## Slide 1: Disciplined Approximate Computing: From Language to Hardware and Beyond
University of Washington
Adrian Sampson, Hadi Esmaelizadeh,1 Michael Ringenburg, Reneé St. Amant,2 Luis Ceze, Dan Grossman, Mark Oskin, Karin Strauss,3 and Doug Burger 3
1 Now at Georgia Tech
2 UT-Austin
3 Microsoft Research

## Slide 2
Approximation with HW eyes...

## Slide 3
Approximation with SW eyes...
Approximation is yet another complexity
  Most of a code base can’t handle it
But many expensive kernels are naturally error-tolerant
  Multiple “good enough” results

## Slide 4
Language
Compiler
Architecture
Circuits
Algorithm
Must work across the stack…
Devices
Application
User
From above: Where approximation acceptable
From below: More savings for less effort
Working at one level is inherently limiting

## Slide 6
Energy
Errors
Energy
Errors
Energy
Errors
Energy
Errors
Notes: Which one would you choose?

## Slide 7
Notes: JPEG HEADER: The hardware doesn’t know which bits are important and which are unimportant!
Without a good way to separate these things, this is a programmability nightmare.

## Slide 8: Across the stack
Higher level knows pixel buffer vs. header bits and control flow
Lower level knows how to save energy for approximate pixel buffer
We are working on:
Expressing and monitoring disciplined approximation
Exploiting approximation in architectures and devices
Much, much more…

## Slide 9
Compiler
Architecture
Circuits
Application
EnerJ
Truffle
NPU
traditional
architecture
neural
networks
as accelerators
Approximate
Storage
Plan for today
language for where-to-approximate
Monitoring
mention in passing
give high-level results
dynamic quality evaluation
Approximate
Wi-Fi

## Slide 10
EnerJ
language for where-to-approximate
EnerJ: Approximate Data Types for Safe and
General Low-Power Computation, PLDI 2011
Application

## Slide 11
Safety
Statically separate critical and non-critical program components
Precise
Approximate
✗
✓
Generality
Various approximation strategies encapsulated
Storage
Logic
Disciplined Approximate Programming
Algorithms
λ
Comunication

## Slide 12: Type qualifiers
✓
✗
int a = ...;
int p = ...;
@approx
@precise
p = a;
a = p;
Notes: Precise-by-default: Java backward compatibility (every Java program is an EnerJ program; every EnerJ program is a Java program when the qualifiers are ignored)
***SEMANTICS***
Precise = normal, strong guarantees
Approx = no guarantees; pathological is legal, but expectation of best effort

## Slide 13: Control flow: implicit flows
✗
int a = ...;
int p = ...;
@approx
@precise
if (
p = 2;
}
a == 10
) {
Notes: This is information flow, so what about implicit flows? Lots of sophisticated ways to deal with them, but for our purposes something simple suffices: disallow approximate conditionals.
THE RESULT OF THIS EQUALITY : @APPROX BOOL

## Slide 14: Endorsement: escape hatch
endorse(a);
✓
int a = expensive();
int p;
@approx
@precise
p =
quickChecksum(p);
output(p);
Notes: Escape hatch. Terminology comes from info flow for security.
A common pattern: big approx computation followed by precise reduction/output.
**Explicit CONVERSION** (not “ignoring”)

## Slide 15: Algorithmic approximation with Polymorphism
float mean() {
calculate mean
}
float[] nums = ...;
class FloatSet {
@context
}
@approx float mean_APPROX() {
calculate mean of half
}
@approx FloatSet someSet = ...;
someSet.mean();
Also in the PLDI’11 paper:
Formal semantics
Noninterference claim
Object-layout issues
Simulation results
…
Notes: ALGORITHMIC APPROXIMATION as proposed in GREEN

## Slide 16
EnerJ
language for where-to-approximate
Monitoring
dynamic quality evaluation
[under submission]
Application

## Slide 17: Controlling approximation
EnerJ: approximate cannot interfere with precise
But semantically, approximate results are unspecified “best effort”
  “Worst effort” of “skip; return 0” is “correct”
Only higher levels can measure quality: inherently app-specific
Lower levels can make monitoring convenient

## Slide 18: Quality of Result (QoR) monitoring
Offline: Profile, auto-tune
  Pluggable energy model
Online: Can react – recompute or decrease approximation-level
  Handle situations not seen during testing
  But needs to be cheap!
First design space of online monitors
  Identify several common patterns
  And apps where they work well

## Slide 19: Online monitoring approaches
General Strawman: Rerun computations precisely; compare. More energy than no approximation.
Sampling: Rerun some computations precisely; compare.
Verification Functions: Run a cheap check after every computation (e.g., within expected bounds, solves equation, etc.)
Fuzzy Memoization: Record past inputs and outputs of computations. Check that “similar” inputs produce “similar” outputs.

## Slide 20: Results
[See paper for energy model, benchmarks, etc.]
Application | Monitor Type
Ray Tracer | Sampling
Asteroids | Verifier
Triangle  | Verifier
Sobel | Fuzzy Memo
FFT | Fuzzy Memo

## Slide 21: Results
[See paper for energy model, benchmarks, etc.]
Application | Monitor Type | Precise | Approx No Monitor
Ray Tracer | Sampling | 100% | 67%
Asteroids | Verifier | 100% | 91%
Triangle  | Verifier | 100% | 83%
Sobel | Fuzzy Memo | 100% | 86%
FFT | Fuzzy Memo | 100% | 73%

## Slide 22: Results
[See paper for energy model, benchmarks, etc.]
Application | Monitor Type | Precise | Approx No Monitor | Approx Monitor | Retained Savings
Ray Tracer | Sampling | 100% | 67% | 85% | 44%
Asteroids | Verifier | 100% | 91% | 95% | 56%
Triangle  | Verifier | 100% | 83% | 87% | 78%
Sobel | Fuzzy Memo | 100% | 86% | 93% | 49%
FFT | Fuzzy Memo | 100% | 73% | 82% | 70%

## Slide 23
Compiler
EnerJ
Truffle
traditional
architecture
language for where-to-approximate
Monitoring
dynamic quality evaluation
Architecture Support for Disciplined
Approximate Programming, ASPLOS 2012
Application

## Slide 24: Hardware support for disciplined approximate execution
Truffle
Core
Compiler
int p = 5;
@approx int a = 7;
for (int x = 0..) {
a += func(2);
@approx int z;
z = p * 2;
p += 4;
}
a /= 9;
func2(p);
a += func(2);
@approx int y;
z = p * 22 + z;
p += 10;
VDDH
VDDL

## Slide 25: Approximation-aware ISA
ld 0x04 r1
ld 0x08 r2
add r1 r2 r3
st 0x0c r3

## Slide 26: Approximation-aware ISA
ld 0x04 r1
ld 0x08 r2
add.a r1 r2 r3
st.a 0x0c r3
operations
ALU
storage
registers
caches
main memory

## Slide 27: Approximate semantics
add.a r1 r2 r3:
Informally: r3 gets something approximating r1 + r2
Actual error pattern depends on approximation technique, microarchitecture, voltage, process, variation, …
  writes the sum of r1 and r2 to r3
  some value
Still guarantee:
No other register modified
No floating point trap raised
Program counter doesn’t jump
No missiles launched
…
Notes: **FROM ENERJ: APPROXIMATE SEMANTICS ARE USEFUL**
ABSTRACTS the approximations performed by uarch
**TUNE VOLTAGE TO WORK FOR EACH APPLICATION**

## Slide 28: Dual-voltage pipeline
Fetch
Decode
Reg Read
Execute
Memory
Write Back
Branch Predictor
Instruction Cache
ITLB
Decoder
Register File
Integer FU
FP FU
Data Cache
DTLB
Register File
replicated functional units
dual-voltage SRAM arrays
7–24% energy saved on average
(fft, game engines, raytracing, QR code readers, etc)
(scope: processor + memory)

## Slide 29: Diminishing returns on data
Fetch
Decode
Reg Read
Execute
Memory
Write Back
Branch Predictor
Instruction Cache
ITLB
Decoder
Register File
Integer FU
FP FU
Data Cache
DTLB
Register File
Instruction control cannot be approximated
  Can we eliminate instruction bookkeeping?

## Slide 30
Compiler
Architecture
EnerJ
Truffle
NPU
traditional
architecture
neural
networks
as accelerators
language for where-to-approximate
Monitoring
dynamic quality evaluation
Neural Acceleration for General-Purpose
Approximate Programs, MICRO 2012
Application

## Slide 31
CPU
Very efficient hardware implementations!
Trainable to mimic many computations!
Recall is imprecise.
Using Neural Networks as Approximate Accelerators
Fault tolerant
[Temam, ISCA 2012]
Map entire regions of code to an (approximate) accelerator:
Get rid of instruction processing (von Neumann bottleneck)
Notes: hardware neural networks have been around for a long time -- approximate computing is a way we can use them in ordinary programs

## Slide 32
Program
Neural acceleration
Notes: HERE IS THE NEW CONTRIBUTION

## Slide 33
Program
Find an approximable
program component
Neural acceleration

## Slide 34
Program
Compile the program
and train a neural network
Find an approximable
program component
Neural acceleration
Notes: THIS IS THE KEY: an algorithmic transformation
In the compilation step, we LEARN FROM THE IMPLEMENTATION provided by the programmer
the function can be COMPLEX, lots of CONTROL FLOW

## Slide 35
Program
Compile the program
and train a neural network
Execute on a fast Neural Processing Unit (NPU)
Find an approximable
program component
Neural acceleration

## Slide 36: Example: Sobel filter
edgeDetection()
@approx float grad(approx float[3][3] p) {
…
}
void edgeDetection(aImage &src,
aImage &dst) {
for (int y = …) {
for (int x = …) {
dst[x][y] = grad(window(src, x, y));
}
}
}
@approx float dst[][];
Notes: good target: approximate outputs, well defined inputs

## Slide 37: Code region criteria
Approximable
Well-defined inputs and outputs
small errors do not corrupt output
no side effects
√
√
Notes: wouldn’t work on the whole edgeDetection() function because inputs & outputs are large & unbounded

## Slide 38: Code observation
[[NPU]]
float grad(float[3][3] p) {
…
}
void edgeDetection(Image &src,
Image &dst) {
for (int y = …) {
for (int x = …) {
dst[x][y] =
grad(window(src, x, y));
}
}
}
+
=>
test cases
instrumented program
sample
arguments & outputs
323, 231, 122, 93, 321, 49
53.2
➝
p
grad(p)
49, 423, 293, 293, 23, 2
94.2
➝
34, 129, 493, 49, 31, 11
1.2
➝
21, 85, 47, 62, 21, 577
64.2
➝
7, 55, 28, 96, 552, 921
18.1
➝
5, 129, 493, 49, 31, 11
92.2
➝
49, 423, 293, 293, 23, 2
6.5
➝
34, 129, 72, 49, 5, 2
120
➝
323, 231, 122, 93, 321, 49
53.2
➝
6, 423, 293, 293, 23, 2
49.7
➝
record(p);
record(result);
Notes: one test input -> lots of data

## Slide 39: Training
Backpropagation
Training
Training Inputs
Notes: different shapes and sizes

## Slide 40: Training
Training Inputs
Training Inputs
Training Inputs
faster
less robust
slower
more accurate
70%
98%
99%
Notes: the smallest NN that meets an accuracy criterion
Different,code,regions,require,different, neural,networks
➙

## Slide 41: Neural Processing Unit (NPU)
Core
NPU
Notes: a neural network tightly coupled with the core -- more like a functional unit than a discrete GPU

## Slide 42: Software interface: ISA extensions
Core
NPU
input
output
configuration
enq.c
deq.c
enq.d
deq.d
Notes: deq.d: ONLY ISSUES when data is available

## Slide 43: A digital NPU
Bus
Scheduler
Processing Engines
input
output
scheduling
Notes: each processing engine represents one or more of the neurons in the NN topology
can implement many different sizes

## Slide 44: A digital NPU
Bus
Scheduler
Processing Engines
input
output
scheduling
multiply-add unit
accumulator
sigmoid LUT
neuron
weights
input
output
Many other implementations
FPGAs
Analog
Hybrid HW/SW
SW only?
...
Notes: each processing engine represents one or more of the neurons in the NN topology
can implement many different sizes

## Slide 45: How does the NN look in practice?
1,079
static x86-64
instructions
60 neurons
2 hidden layers
88 static
instructions
18
neurons
triangle intersection
edge detection
56% of dynamic
instructions
97% of dynamic
instructions
Notes: jmeint: 32 function calls, 23 IFs
sobel: 3 calls, 2 loops, 1 IF
LOGAL NEURAL TOPOLOGIES mapped on the PEs of the NPU

## Slide 46: Results Summary
2.3x average speedup
Ranges from 0.8x to 11.1x
3.0x average energy reduction
All benchmarks benefit
Quality loss below 10% in all cases
As always, quality metrics application-specific
Also in the MICRO paper:
Sensitivity to communication latency
Sensitivity to NN evaluation efficiency
Sensitivity to PE count
Benchmark statistics
All-software NN slowdown
Notes: Ranged from 11.1x (inverse kinematics) to 20% slowdown for kmeans
These results incorporate the communication & recall latency

## Slide 47: Ongoing effort
Disciplined Approximate Programming
(EnerJ, EnerC,...)
Approximate Compiler
X86, ARM
off-the-shelf
Truffle:
dual-Vdd uArch
Approximate Accelerators
Approximate Wireless Networks and Storage
Approximate compiler (no special HW)
Analog components
Storage via PCM
Wireless communication
Approximate HDL

## Slide 48: Conclusion
Goal: approximate computing across the system
Key: Co-design programming model with approximation techniques: disciplined approximate programming
Early results encouraging
Approximate computing can potentially save our bacon in a post-Dennard era and be in the survival kit for dark silicon

## Slide 49: Disciplined Approximate Computing: From Language to Hardware and Beyond
University of Washington
Adrian Sampson, Hadi Esmaelizadeh, Michael Ringenburg, Reneé St. Amant, Luis Ceze, Dan Grossman, Mark Oskin, Karin Strauss, and Doug Burger
Thanks!
Notes: hadi will be on the job market