## Slide 1: The ARM Architecture
Notes: v10: 28/04/03, Chris Shore
slide 4: added China to text (already on graphic). Updated employee count and geographical distribution.
slide 19: added V6
slides 32: Imported from RV Overview to replace original ADS slide.
slide 33: New general debug architecture diagram
slide 34: new product montage (crib in notes)
slide 35: New question about embedded trace.
v09: 19/11/02, Chris Shore
slides 6-8: New slides showing IP deployment (imported from 926 core module)
v08: 08/02, Rob Levy
- Style update, black & white view amended
v07: 12/01, CJS
Main changes:
- ARM Development Boards slide removed (now in Debug Solutions module)
- Register set slides re-ordered so that the animated graphic comes first
- slide 12: Q bit in v5TEJ as well as v5TE
- slide 14: CPSR changes rephrased slightly
- slide 16: reference to v5T removed.
- slide 27: EASY/Micropack replaced with ADK/ACT
- slide 30: Trace slide updated

## Slide 2: Agenda
Introduction to ARM Ltd
Programmers Model
Instruction Set
System Design
Development Tools
Notes: Introduction to ARM
  Background to who ARM Ltd are, what we do, and how our business model works.
Programmers Model
  The structure of the ARM architecture
  How it has developed
  Register set, modes and exceptions
  The endian issue
Instruction Sets
  Overview of the features of the ARM instruction set
  The coprocessor mechanism
  Overview of Thumb - Why it was designed and the benefits it gives.
System Design
  Overview of some of the hardware and software technologies that ARM has to support the design in of the ARM core into real products.
  Also looks at some of the issues involved with memory maps in ARM based systems.

## Slide 3: ARM Ltd
Founded in November 1990
  Spun out of Acorn Computers
Designs the ARM range of RISC processor cores
Licenses ARM core designs to semiconductor partners who fabricate and sell to their customers.
  ARM does not fabricate silicon itself
Also develop technologies to assist with the design-in of the ARM architecture
  Software tools, boards, debug hardware, application software, bus architectures, peripherals etc
Notes: The ARM processor core originates within a British computer company called Acorn. In the mid-1980s they were looking for replacement for the 6502 processor used in their BBC computer range, which were widely used in UK schools. None of the 16-bit architectures becoming available at that time met their requirements, so they designed their own 32-bit processor.
Other companies became interested in this processor, including Apple who were looking for a processor for their PDA project (which became the Newton). After much discussion this led to Acorn’s processor design team splitting off from Acorn at the end of 1990 to become Advanced RISC Machines Ltd, now just ARM Ltd.
Thus ARM Ltd now designs the ARM family of RISC processor cores, together with a range of other supporting technologies.
One important point about ARM is that it does not fabricate silicon itself, but instead just produces the design - we are an Intellectual Property (or IP) company. Instead silicon is produced by companies who license the ARM processor design.

## Slide 4: ARM Partnership Model
Notes: ARM’s business model centres around the principle of partnership. At the centre of this are ARM’s semiconductor partners who design, manufacture and market ARM-compliant products.
Having so many partner companies producing silicon executing the same instruction set is a very important part of ARM’s strength in the market place.
However each of our semiconductor partners bring their own unique strengths to the partnership - each having their own technologies, applications knowledge, product focus, culture, geography, and key customers.
In addition to our partnering with semiconductor companies, we also partner with a large number of other third parties to ensure that operating systems, EDA and software development tools, application software and design services are available for doing ARM based designs.
“ATAP” stands for ARM Technology Access Program. Creates a network of independent design service companies and equips them to deliver ARM-powered designs. Members get access to ARM technology, expertise and support. Members sometimes referred to as “Approved Design Centers”.

## Slide 5: ARM Powered Products

## Slide 6
ARM provides hard and soft views to licencees
  RTL and synthesis flows
  GDSII layout
Licencees have the right to use hard or soft views of the IP
  soft views include gate level netlists
  hard views are DSMs
OEMs must use hard views
  to protect ARM IP
Intellectual Property
Notes: Soft Intellectual Property
This just sums up the whole IP stuff.
ARM provides IP to licencees and also the synthesis flows to allow the partner to synthesise the processor to their technology.
Internally the partner can use soft or hard views. This will depend on their own strategy.
OEMs using a synthesisable processor can not use a soft view. They must use a DSM with some high level timing view. This is to protect ARMs IP.
So, while the core is a “-S” and is therefore synthesisable, the end user won’t necessarily be synthesising the core themselves.

## Slide 7: Agenda
Introduction to ARM Ltd
Programmers Model
Instruction Sets
System Design
Development Tools
Notes: Programmers Model
  The structure of the ARM architecture
  How it has developed
  Register set, modes and exceptions
  The endian issue

## Slide 8: Data Sizes and Instruction Sets
The ARM is a 32-bit architecture.
When used in relation to the ARM:
  Byte means 8 bits
  Halfword means 16 bits (two bytes)
  Word means 32 bits (four bytes)
Most ARM’s implement two instruction sets
  32-bit ARM Instruction Set
  16-bit Thumb Instruction Set
Jazelle cores can also execute Java bytecode
Notes: The cause of confusion here is the term “word” which will mean 16-bits to people with a 16-bit background.
In the ARM world 16-bits is a “halfword” as the architecture is a 32-bit one, whereas “word” means 32-bits.
Java bytecodes are 8-bit instructions designed to be architecture independent. Jazelle transparently executes most bytecodes in hardware and some in highly optimized ARM code. This is due to a tradeoff between hardware complexity (power consumption & silicon area) and speed.

## Slide 9: The Registers
ARM has 37 registers all of which are 32-bits long.
  1 dedicated program counter
  1 dedicated current program status register
  5 dedicated saved program status registers
  30 general purpose registers
The current processor mode governs which of several banks is accessible. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (the stack pointer, sp) and r14 (the link register, lr)
  the program counter, r15 (pc)
  the current program status register, cpsr
Privileged modes (except System) can also access
  a particular spsr (saved program status register)
Notes: The ARM architecture provides a total of 37 registers, all of which are 32-bits long. However these are arranged into several banks, with the accessible bank being governed by the current processor mode. We will see this in more detail in a couple of slides. In summary though, in each mode, the core can access:
  a particular set of 13 general purpose registers (r0 - r12).
  a particular r13 - which is typically used as a stack pointer. This will be a different r13 for each mode, so allowing each exception type to have its own stack.
  a particular r14 - which is used as a link (or return address) register. Again this will be a different r14 for each mode.
  r15 - whose only use is as the Program counter.
The CPSR (Current Program Status Register) - this stores additional information about the state of the processor:
And finally in privileged modes, a particular SPSR (Saved Program Status Register). This stores a copy of the previous CPSR value when an exception occurs. This combined with the link register allows exceptions to return without corrupting processor state.

## Slide 10: Processor Modes
The ARM has seven basic operating modes:
  User : unprivileged mode under which most tasks run
  FIQ : entered when a high priority (fast) interrupt is raised
  IRQ : entered when a low priority (normal) interrupt is raised
  Supervisor : entered on reset and when a Software Interrupt
  instruction is executed
  Abort : used to handle memory access violations
  Undef : used to handle undefined instructions
  System : privileged mode using the same registers as user mode
Notes: The Programmers Model can be split into two elements - first of all, the processor modes and secondly, the processor registers. So let’s start by looking at the modes.
Now the typical application will run in an unprivileged mode know as “User” mode, whereas the various exception types will be dealt with in one of the privileged modes : Fast Interrupt, Supervisor, Abort, Normal Interrupt and Undefined (and we will look at what causes each of the exceptions later on).
NB - spell out the word FIQ, otherwise you are saying something rude in German!
One question here is what is the difference between the privileged and unprivileged modes? Well in reality very little really - the ARM core has an output signal (nTRANS on ARM7TDMI, InTRANS, DnTRANS on 9, or encoded as part of HPROT or BPROT in AMBA) which indicates whether the current mode is privileged or unprivileged, and this can be used, for instance, by a memory controller to only allow IO access in a privileged mode. In addition some operations are only permitted in a privileged mode, such as directly changing the mode and enabling of interrupts.
All current ARM cores implement system mode (added in architecture v4). This is simply a privileged version of user mode. Important for re-entrant exceptions because no exceptions can cause system mode to be entered.

## Slide 11: The ARM Register Set
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
IRQ
SVC
Undef
Abort
User Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
FIQ
IRQ
SVC
Undef
Abort
r0
r1
r2
r3
r4
r5
r6
r7
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
IRQ
SVC
Undef
Abort
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
FIQ Mode
IRQ Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
SVC
Undef
Abort
r13 (sp)
r14 (lr)
Undef Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Abort
r13 (sp)
r14 (lr)
SVC Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
Undef
Abort
r13 (sp)
r14 (lr)
Abort Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Undef
r13 (sp)
r14 (lr)
Notes: This animated slide shows the way that the banking of registers works. On the left the currently visible set of registers are shown for a particular mode.
On the right are the registers that are banked out whilst in that mode.
Each key press will switch mode:
user -> FIQ ->user -> IRQ -> user ->SVC -> User -> Undef -> User -> Abort and then back to user.
The following slide then shows this in a more static way that is more useful for reference

## Slide 12: Register Organization Summary
User mode r0-r7, r15, and cpsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r0
r1
r2
r3
r4
r5
r6
r7
User
r13 (sp)
r14 (lr)
spsr
IRQ
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Undef
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
SVC
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Abort
User mode r0-r12, r15, and cpsr
Thumb state
Low registers
Thumb state
High registers
Note: System mode uses the User mode register set
Notes: This slide shows the registers visible in each mode - basically in a more static fashion than the previous animated slide that is more useful for reference.
The main point to state here is the splitting of the registers in Thumb state into Low and High registers.
ARM register banking is the minimum necessary for fast handling of overlapping exceptions of different types (e.g. ABORT during SWI during IRQ). For nested exceptions of the same type (e.g. re-entrant interrupts) some additional pushing of registers to the stack is required.

## Slide 13: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carried out
  V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
  Architecture 5TE/J only
  Indicates if saturation has occurred
J bit
  Architecture 5TEJ only
  J = 1: Processor in Jazelle state
Interrupt Disable bits.
  I = 1: Disables the IRQ.
  F = 1: Disables the FIQ.
T Bit
  Architecture xT only
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
Notes: Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 14: Program Counter (r15)
When the processor is executing in ARM state:
  All instructions are 32 bits wide
  All instructions must be word aligned
  Therefore the pc value is stored in bits [31:2] with bits [1:0] undefined (as instruction cannot be halfword or byte aligned).
When the processor is executing in Thumb state:
  All instructions are 16 bits wide
  All instructions must be halfword aligned
  Therefore the pc value is stored in bits [31:1] with bit [0] undefined (as instruction cannot be byte aligned).
When the processor is executing in Jazelle state:
  All instructions are 8 bits wide
  Processor performs a word access to read 4 instructions at once
Notes: ARM is designed to efficiently access memory using a single memory access cycle. So word accesses must be on a word address boundary, halfword accesses must be on a halfword address boundary. This includes instruction fetches.
Point out that strictly, the bottom bits of the PC simply do not exist within the ARM core - hence they are ‘undefined’. Memory system must ignore these for instruction fetches.
In Jazelle state, the processor doesn’t perform 8-bit fetches from memory. Instead it does aligned 32-bit fetches (4-byte prefetching) which is more efficient. Note we don’t mention the PC in Jazelle state because the ‘Jazelle PC’ is actually stored in r14 - this is technical detail that is not relevant as it is completely hidden by the Jazelle support code.

## Slide 15: Exception Handling
Vector Table
When an exception occurs, the ARM:
  Copies CPSR into SPSR_<mode>
  Sets appropriate CPSR bits
    Change to ARM state
    Change to exception mode
    Disable interrupts (if appropriate)
  Stores the return address in LR_<mode>
  Sets PC to vector address
To return, exception handler needs to:
  Restore CPSR from SPSR_<mode>
  Restore PC from LR_<mode>
This can only be done in ARM state.
Vector table can be at 0xFFFF0000 on ARM720T and on ARM9/10 family devices
FIQ
IRQ
(Reserved)
Data Abort
Prefetch Abort
Software Interrupt
Undefined Instruction
Reset
0x1C
0x18
0x14
0x10
0x0C
0x08
0x04
0x00
Notes: Exception handling on the ARM is controlled through the use of an area of memory called the vector table. This lives (normally) at the bottom of the memory map from 0x0 to 0x1c. Within this table one word is allocated to each of the various exception types.
This word will contain some form of ARM instruction that should perform a branch. It does not contain an address.
Reset - executed on power on
Undef - when an invalid instruction reaches the execute stage of the pipeline
SWI - when a software interrupt instruction is executed
Prefetch - when an instruction is fetched from memory that is invalid for some reason, if it reaches the execute stage then this exception is taken
Data - if a load/store instruction tries to access an invalid memory location, then this exception is taken
IRQ - normal interrupt
FIQ - fast interrupt
When one of these exceptions is taken, the ARM goes through a low-overhead sequence of actions in order to invoke the appropriate exception handler. The current instruction is always allowed to complete (except in case of Reset).
IRQ is disabled on entry to all exceptions; FIQ is also disabled on entry to Reset and FIQ.

## Slide 16: Development of the ARM Architecture
SA-110
ARM7TDMI
4T
1
Halfword and signed halfword / byte support
System mode
Thumb instruction set
2
4
ARM9TDMI
SA-1110
ARM720T
ARM940T
Improved ARM/Thumb Interworking
CLZ
5TE
Saturated maths
DSP multiply-accumulate instructions
XScale
ARM1020E
ARM9E-S
ARM966E-S
3
Early ARM architectures
ARM9EJ-S
5TEJ
ARM7EJ-S
ARM926EJ-S
Jazelle
Java bytecode execution
6
ARM1136EJ-S
ARM1026EJ-S
SIMD Instructions
Multi-processing
V6 Memory architecture (VMSA)
Unaligned data support
Notes: This slide is aimed at showing the development of the ARM Architecture.
  The “Stars” mark each relevant Architecture Level.
  The “Boxes” give examples of ARM products implementing each particular Architecture level. This is not meant to be a complete list of products, what they offer, or a product roadmap.
  Within each Architecture
    The “Notes by the Stars” give the major enhancements specified by this particular Architecture over the previous one.
Note architectures 1,2,3 have been removed - these are obsolete (the only part which contains arch 3 core is ARM7500FE).
ARM1020T was architecture v5T, however we are rapidly transitioning to ARM1020E and 1022E.
Jazelle adds Java bytecode execution, which increases Java performance by 5-10x and also reduces power consumption accordingly. 9EJ - Harvard - 200MIPS 7EJ - Von Neumann - 70MIPS
Brief notes on V6:
SIMD instructions provide greatly increased audio/video codec performance
LDREX/STREX instructions improve multi-processing support
VMSA (Virtual Memory System Architecture): Complete L1 cache and TCM definition; physically-tagged cache; ASID for improved task-switching
SRS and RFE instructions to improve exception handling performance
Hardware and instruction set support for mixed-endianness
1136JF-S has integral VFP coprocessor

## Slide 17: Agenda
Introduction to ARM Ltd
Programmers Model
Instruction Sets
System Design
Development Tools
Notes: Instruction Sets
  Overview of the features of the ARM instruction set
  The coprocessor mechanism
  Overview of Thumb - Why it was designed and the benefits it gives.

## Slide 18: Conditional Execution and Flags
ARM instructions can be made to execute conditionally by postfixing them with the appropriate condition code field.
  This improves code density and performance by reducing the number of forward branch instructions.
  CMP r3,#0 CMP r3,#0 BEQ skip ADDNE r0,r1,r2 ADD r0,r1,r2 skip
By default, data processing instructions do not affect the condition code flags but the flags can be optionally set by using “S”. CMP does not need “S”.
  loop … SUBS r1,r1,#1 BNE loop
if Z flag clear then branch
decrement r1 and set flags
Notes: Unusual but powerful feature of the ARM instruction set. Other architectures normally only have conditional branches.
Some recently-added ARM instructions (in v5T and v5TE) are not conditional (e.g. v5T BLX offset)
Core compares condition field in instruction against NZCV flags to determine if instruction should be executed.

## Slide 19: Condition Codes
Not equal
Unsigned higher or same
Unsigned lower
Minus
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Less than
Greater than
Less than or equal
Always
Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N=!V
The possible condition codes are listed below:
    Note AL is the default and does not need to be specified
Notes: Condition codes are simply a way of testing the ALU status flags.

## Slide 20: Examples of conditional execution
Use a sequence of several conditional instructions
  if (a==0) func(1);
    CMP r0,#0 MOVEQ r0,#1 BLEQ func
Set the flags, then use various condition codes
  if (a==0) x=0; if (a>0) x=1;
    CMP r0,#0 MOVEQ r1,#0 MOVGT r1,#1
Use conditional compare instructions
  if (a==4 || a==10) x=0;
    CMP r0,#4 CMPNE r0,#10 MOVEQ r1,#0
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).

## Slide 21: Branch instructions
Branch : B{<cond>} label
Branch with Link : BL{<cond>} subroutine_label
The processor core shifts the offset field left by 2 positions, sign-extends it and adds it to the PC
  ± 32 Mbyte range
  How to perform longer branches?
28
31
24
0
Cond 1 0 1 L Offset
Condition field
Link bit 0 = Branch
1 = Branch with link
23
25
27
Notes: PC-relative to allow position independent code, and allows restricted branch range to jump to nearby addresses.
How to access full 32-bit address space? Can set up LR manually if needed, then load into PC
MOV lr, pc
LDR pc, =dest
ADS linker will automatically generate long branch veneers for branches beyond 32Mb range.

## Slide 22: Data processing Instructions
Consist of :
  Arithmetic: ADD ADC SUB SBC RSB RSC
  Logical: AND ORR EOR BIC
  Comparisons: CMP CMN TST TEQ
  Data movement: MOV MVN
These instructions only work on registers, NOT memory.
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
    Comparisons set flags only - they do not specify Rd
    Data movement does not specify Rn
Second operand is sent to the ALU via barrel shifter.
Notes: BIC bit clear
ORR bit set
AND bit mask
EOR bit invert
Comparisons produce no results - just set condition codes.
CMP like SUB
CMN like ADD (subtract of a negative number is the same as add)
TST like AND
TEQ like EOR (eor of identical numbers gives result of zero)
Generally single-cycle execution (except write to PC and register-controlled shift). Mention ARM NOP & Thumb NOP.
Explain RSB and RSC which do subtract in other order (e.g. y-x not x-y)
Does not include multiply (separate instr format). No divide - compiler uses run-time library or barrel shifter to perform division.
Can combine “S” bit with conditional execution, e.g.
ADDEQS r0, r1, r2

## Slide 23: The Barrel Shifter
Destination
CF
0
Destination
CF
LSL : Logical Left Shift
ASR: Arithmetic Right Shift
Multiplication by a power of 2
Division by a power of 2, preserving the sign bit
Destination
CF
...0
Destination
CF
LSR : Logical Shift Right
ROR: Rotate Right
Division by a power of 2
Bit rotate with wrap around from LSB to MSB
Destination
RRX: Rotate Right Extended
Single bit rotate with wrap around from CF to MSB
CF
Notes: Rotate left can be implemented as rotate right (32-number), e.g. rotate left of 10 is performed using rotate right of 22.
RRX shifts by 1 bit position, of a 33 bit amount (includes carry flag). Very specialized application (e.g. encryption algorithms). Cannot be generated by C compiler. We have used it for 64/64 bit divide. RRX allows you to shift multiprecision values right by one efficiently. Also used in ARM’s MPEG code in a very tricky piece of code.
ANSI C does not have a rotate operation (it only has “<<“ and “>>” which are the equivalent of LSL, LSR and ASR). However the ARM compiler recognizes rotate type expresssions and optimizes these to use ROR, e.g.
int f(unsigned int a)
{
return (a << 10) | (a >>22) ;
}
=> MOV a1,a1,ROR #22
Carry flag set out of the shifter for *logical* data processing operations

## Slide 24: Using the Barrel Shifter: The Second Operand
Register, optionally with shift operation
  Shift value can be either be:
    5 bit unsigned integer
    Specified in bottom byte of another register.
  Used for multiplication by constant
Immediate value
  8 bit number, with a range of 0-255.
    Rotated right through even number of positions
  Allows increased range of 32-bit constants to be loaded directly into registers
Result
Operand 1
Barrel Shifter
Operand 2
ALU
Notes: Mention A bus and B bus on 7TDMI core.
Give examples:
ADD r0, r1, r2
ADD r0, r1, r2, LSL#7
ADD r0, r1, r2, LSL r3
ADD r0, r1, #0x4E

## Slide 25: Immediate constants (1)
No ARM instruction can contain a 32 bit immediate constant
  All ARM instructions are fixed as 32 bits long
The data processing instruction format has 12 bits available for operand2
4 bit rotate value (0-15) is multiplied by two to give range 0-30 in steps of 2
Rule to remember is “8-bits shifted by an even number of bit positions”.
0
7
11
8
immed_8
Shifter ROR
rot
x2
Quick Quiz: 0xe3a004ff MOV r0, #???
Notes: Could have used 12 bits directly for immediate value - this would allow 0-4095. But this does not allow any large numbers, which are useful for:
base address of memory devices in target system
large, but simple hex constants (0x10000)
Research has shown there is a need for a large range of small numbers (frequently needed) but also some large numbers. 50% of all constants lie between the range -15 and +15 and 90% lie in the range -511 and +511. Will vary depending on the application.
ROR #n is confusing… but can be considered as ROL #32-n
Opcode 0xe3a004ff = MOV r0, #0xff, 8
Core rotates 0xff right by 4 pairs of bits
=> MOV r0, #0xff000000

## Slide 26: Immediate constants (2)
Examples:
The assembler converts immediate values to the rotate form:
  MOV r0,#4096 ; uses 0x40 ror 26
  ADD r1,r2,#0xFF0000 ; uses 0xFF ror 16
The bitwise complements can also be formed using MVN:
  MOV r0, #0xFFFFFFFF ; assembles to MVN r0,#0
Values that cannot be generated in this way will cause an error.
0
31
ror #0
range 0-0xff000000 step 0x01000000
ror #8
range 0-0x000000ff step 0x00000001
range 0-0x000003fc step 0x00000004
ror #30
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Notes: Point out that it is 8-bit value shifted to anywhere within the 32-bit word (but must be an even number of bits). Other bits are zeros.
Mention that ROR#2,4,6 (not shown) will split the 8-bit immediate with some bits at bottom of word and some at top.
mov r0, #256 ; mov r0, #0x100
mov r1, #0x40, 30 ; mov r1, #0x100
etc.
This method of generating constants allows 3073 distinct values, about 25% fewer than if 12-bits were used without modification. They are, however, a much more useful set of values.

## Slide 27: Loading 32 bit constants
To allow larger constants to be loaded, the assembler offers a pseudo-instruction:
  LDR rd, =const
This will either:
  Produce a MOV or MVN instruction to generate the value (if possible).
or
  Generate a LDR instruction with a PC-relative address to read the constant from a literal pool (Constant data area embedded in the code).
For example
  LDR r0,=0xFF => MOV r0,#0xFF
  LDR r0,=0x55555555 => LDR r0,[PC,#Imm12] … … DCD 0x55555555
This is the recommended way of loading constants into a register
Notes: 26
Literal pools
  These are constant data areas embedded in the code at the end of assembler modules, and at other locations if specified by the user using LTORG. Data value must not be executed (will probably be an undefined instruction), assembly programmer must ensure this by placing LTORG at an appropriate location. ARM C compilers will handle placement of literal pools automatically.

## Slide 28: Multiply
Syntax:
  MUL{<cond>}{S} Rd, Rm, Rs Rd = Rm * Rs
  MLA{<cond>}{S} Rd,Rm,Rs,Rn Rd = (Rm * Rs) + Rn
  [U|S]MULL{<cond>}{S} RdLo, RdHi, Rm, Rs RdHi,RdLo := Rm*Rs
  [U|S]MLAL{<cond>}{S} RdLo, RdHi, Rm, Rs RdHi,RdLo := (Rm*Rs)+RdHi,RdLo
Cycle time
  Basic MUL instruction
    2-5 cycles on ARM7TDMI
    1-3 cycles on StrongARM/XScale
    2 cycles on ARM9E/ARM102xE
  +1 cycle for ARM9TDMI (over ARM7TDMI)
  +1 cycle for accumulate (not on 9E though result delay is one cycle longer)
  +1 cycle for “long”
Above are “general rules” - refer to the TRM for the core you are using for the exact details
Notes: Variable number of cycles for some processors which implement ‘early termination’. The multiply is faster for smaller values in Rs.
ARM7TDMI and ARM9TDMI use 8-bit Booth’s algorithm which takes 1 cycle for each byte in Rs. Terminates when rest of Rs is all zeros or all ones.
MUL/MLA don’t need signed/unsigned specified - because they return the low 32-bit of the result which is the same whatever the sign of the arguments.
Cycle information is general and specific cores have some specific variations from this, specifically with respect to result delays where accumulation is involved. Refer to TRM for exact details if required.
XScale and StrongARM have a split pipeline with multiple execution units - so can issue multiplies in 1 or 2 cycles and continue with following instructions, assuming no resource or result dependencies.
XScale can issue MUL/MLA/MULL in one cycle (MLAL requires 2 cycles), providing multiplier is not already in use. Cycle timing is dependent on result latency - the core will stall if an instruction tries to use the result before multiplier has completed.
Note that there is no form of the multiply instruction which has an immediate constant operand - registers only.
For the interested student - C flag is unpredictable if S is set in architectures prior to V5.
MULS/MLAS always take 4 cycles; MULLS, MLALS always take 5.

## Slide 29: Single register data transfer
  LDR STR Word
  LDRB STRB Byte
  LDRH STRH Halfword
  LDRSB Signed byte load
  LDRSH Signed halfword load
Memory system must support all access sizes
Syntax:
  LDR{<cond>}{<size>} Rd, <address>
  STR{<cond>}{<size>} Rd, <address>
  e.g. LDREQB
Notes: Point out destination (reg) first for LDR, but destination (mem) last for STR. Different to Motorola, but it keeps the instruction mnemonic format consistent. Always have register loaded/stored first, then address accessed second
Size specifier comes out on MAS (memory access size) signal. Important that memory supports full range of accesses - especially important for writes where only the specified size should be written.
Special types of sign extended load - this is needed because ARM registers only hold 32-bit values. Draw diagram. No need for special store instructions though.
Instruction cycle timing:
STR LDR
7TDMI 2 cycles 3 cycles
9TDMI 1 cycle 1 cycle - interlock if used in next cycle
StrongARM1 1 cycle 1 cycle - interlock if used in next cycle
Xscale 1 cycle 1 cycle - interlock if used in next 2 cycles
Note size specifier comes after condition code.
Link: <address> explained on next slide.
Note that load/store instructions never set condition codes.

## Slide 30: Address accessed
Address accessed by LDR/STR is specified by a base register plus an offset
For word and unsigned byte accesses, offset can be
  An unsigned 12-bit immediate value (ie 0 - 4095 bytes). LDR r0,[r1,#8]
  A register, optionally shifted by an immediate value LDR r0,[r1,r2] LDR r0,[r1,r2,LSL#2]
This can be either added or subtracted from the base register: LDR r0,[r1,#-8] LDR r0,[r1,-r2] LDR r0,[r1,-r2,LSL#2]
For halfword and signed halfword / byte, offset can be:
  An unsigned 8 bit immediate value (ie 0-255 bytes).
  A register (unshifted).
Choice of pre-indexed or post-indexed addressing
Notes: Halfword access and signed halfword/byte accesses were added to the architecture in v4T, this is the reason the offset field is not as flexible as the normal word/byte load/store - not a problem because these accesses are less common.
Link: diagram on next slide

## Slide 31: Pre or Post Indexed Addressing?
0x5
0x5
r1
0x200
Base Register
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x200
Original Base Register
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x20c
Updated Base Register
Auto-update form: STR r0,[r1,#12]!
Pre-indexed: STR r0,[r1,#12]
Post-indexed: STR r0,[r1],#12
Notes: “!” indicates “writeback” i.e. the base register is to be updated after the instruction.
No “!” for post-indexed because post-increment of base register always happens (otherwise the offset field would not be used at all).
Give C example:
int *ptr;
x = *ptr++;
Compiles to a single instruction:
LDR r0, [r1], #4

## Slide 32: LDM / STM operation
Syntax:
  <LDM|STM>{<cond>}<addressing_mode> Rb{!}, <register list>
4 addressing modes:
  LDMIA / STMIA increment after
  LDMIB / STMIB increment before
  LDMDA / STMDA decrement after
  LDMDB / STMDB decrement before
IA
r1
Increasing Address
r4
r0
r1
r4
r0
r1
r4
r0
r1
r4
r0
r10
IB
DA
DB
LDMxx r10, {r0,r1,r4}
STMxx r10, {r0,r1,r4}
Base Register (Rb)
Notes: Always lowest register first.
Always ascending memory address order.
Uses sequential cycles to take advantage of faster access.
‘addressing_mode’ just determines whether up/down with respect to the base pointer and if value at base pointer address is accessed or skipped. It isn’t possible to add any offset to the base pointer.
Note address and registers loaded/stored are the other way around compared with LDM/STM.
Note the base pointer is not loaded or stored, unless it is in the reg list.

## Slide 33: Software Interrupt (SWI)
Causes an exception trap to the SWI hardware vector
The SWI handler can examine the SWI number to decide what operation has been requested.
By using the SWI mechanism, an operating system can implement a set of privileged operations which applications running in user mode can request.
Syntax:
  SWI{<cond>} <SWI number>
28
31
24
27
0
Cond 1 1 1 1
SWI number (ignored by processor)
23
Condition Field
Notes: In effect, a SWI is a user-defined instruction.
Used for calling the operating system (switches to privileged mode).
SWI number field can be used to specify the operation code, e.g. SWI 1 start a new task, SWI 2 allocate memory, etc. Using a number has the advantage that the O.S. can have different revisions, and the same application code will work on each O.S. rev.

## Slide 34: PSR Transfer Instructions
MRS and MSR allow contents of CPSR / SPSR to be transferred to / from a general purpose register.
Syntax:
  MRS{<cond>} Rd,<psr> ; Rd = <psr>
  MSR{<cond>} <psr[_fields]>,Rm ; <psr[_fields]> = Rm
where
  <psr> = CPSR or SPSR
  [_fields] = any combination of ‘fsxc’
Also an immediate form
  MSR{<cond>} <psr_fields>,#Immediate
In User Mode, all bits can be read but only the condition flags (_f) can be written.
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
Notes: The status registers are split into four 8-bit fields that can be individually written:
bits 31 to 24 : the flags field (NZCV flags and 4 unused bits)
bits 23 to 16 : the status field (unused in Arch 3, 4 & 4T)
bits 15 to 8 : the extension field (unused in Arch 3, 4 & 4T)
bits 7 to 0 : the control field (I & F interrupt disable bits, 5 processor mode bits, and the T bit on ARMv4T.)
Immediate form of MSR can actually be used with any of the field masks, but care must be taken that a read-modify-write strategy is followed so that currently unallocated bits are not affected. Otherwise the code could have distinctly different effect on future cores where such bits are allocated. When used with the flag bits, the immediate form is shielded from this as bits 27-24 can be considered to be read only.
For MSR operations, we recommend that only the minimum number of fields are written, because future ARM implementations may need to take extra cycles to write specific fields; not writing fields you don't want to change reduces any such extra cycles to a minimum.
For example, an MRS/BIC/ORR/MSR sequence whose purpose is to change processor mode (only) is best written with the last instruction being MSR CPSR_c,Rm, though any other set of fields that includes "c" will also work.

## Slide 35: ARM Branches and Subroutines
B <label>
  PC relative. ±32 Mbyte range.
BL <subroutine>
  Stores return address in LR
  Returning implemented by restoring the PC from LR
  For non-leaf functions, LR will have to be stacked
STMFD sp!,{regs,lr}
:
BL func2
:
LDMFD sp!,{regs,pc}
func1
func2
:
:
BL func1
:
:
:
:
:
:
:
MOV pc, lr
Notes: This slide shows the way that ARM branch instructions work
It also shows the need to stack the LR (using STM/LDM instructions) when making subroutine calls within subroutines.

## Slide 36: Thumb
Thumb is a 16-bit instruction set
  Optimised for code density from C code (~65% of ARM code size)
  Improved performance from narrow memory
  Subset of the functionality of the ARM instruction set
Core has additional execution state - Thumb
  Switch between ARM and Thumb using BX instruction
0
15
31
0
ADDS r2,r2,#1
ADD r2,#1
32-bit ARM Instruction
16-bit Thumb Instruction
For most instructions generated by compiler:
Conditional execution is not used
Source and destination registers identical
Only Low registers used
Constants are of limited size
Inline barrel shifter not used
Notes: The Thumb instruction set was designed by looking at the instructions produced by the ARM C compiler from real application code to see which instructions were most often used. This subset of instructions was then compressed into 16-bit opcodes to give better code density and better performance from narrow memory
A Thumb compatible processor is still a 32-bit processor, but it has the ability to execute either sections of ARM code or sections of Thumb code. The two instruction sets cannot be interleaved though, a special form of branch has to be used to change “state”.
The diagram then shows the way that a typical 32-bit ARM instruction might be “compressed” into a 16-bit Thumb one.

## Slide 37: Agenda
Introduction
Programmers Model
Instruction Sets
System Design
Development Tools
Notes: System Design
  Overview of some of the hardware and software technologies that ARM has to support the design in of the ARM core into real products.
  Also looks at some of the issues involved with memory maps in ARM based systems.

## Slide 38: Example ARM-based System
16 bit RAM
8 bit ROM
32 bit RAM
ARM
Core
I/O
Peripherals
Interrupt
Controller
nFIQ
nIRQ
Notes: This slides shows a very generic ARM based design, that is actually fairly representative of the designs that we see being done.
On-chip there will be an ARM core (obviously) together with a number of system dependant peripherals. Also required will be some form of interrupt controller which receives interrupts from the peripherals and raised the IRQ or FIQ input to the ARM as appropriate. This interrupt controller may also provide hardware assistance for prioritizing interrupts.
As far as memory is concerned there is likely to be some (cheap) narrow off-chip ROM (or flash) used to boot the system from. There is also likely to be some 16-bit wide RAM used to store most of the runtime data and perhaps some code copied out of the flash. Then on-chip there may well be some 32-bit memory used to store the interrupt handlers and perhaps stacks.

## Slide 39: AMBA
Bridge
Timer
On-chip
RAM
ARM
Interrupt
Controller
Remap/
Pause
TIC
Arbiter
Bus Interface
External
ROM
External
RAM
Reset
System Bus
Peripheral Bus
AMBA
  Advanced Microcontroller Bus Architecture
ADK
  Complete AMBA Design Kit
ACT
  AMBA Compliance Testbench
PrimeCell
  ARM’s AMBA compliant peripherals
AHB or ASB
APB
External
Bus
Interface
Decoder
Notes: AMBA is ARM’s on-chip bus specification. The aims of AMBA are to:
Make life easier for Systems designers
Standardise the bus interface
Reduce the support required from ARM and between internal design teams
Allows increased re-use of IP in designs
Enable the creation of upgrades and families of devices
Why use AMBA not the original ARM Bus
  Improved Tools support
  Modularity
  Upgrading to other ARM cores
ADK is ARM’s AMBA design kit. A generic, stand-alone development environment enabling rapid creation of AMBD-based components and designs.
ACT is a complete environment for testing compliance to the AMBA spec.
The PrimeCell peripherals are a set of AMBA-compliant peripherals that are available for licensing from ARM. They include a UART, real time clock, keyboard & mouse interface, GPIO and a generic IR interface. Consult the ARM website for more details - a selection of reference manuals are also on the technical documentation CD.

## Slide 40: FriendlyArm micro2440-35

## Slide 41: FriendlyArm micro2440

## Slide 42: Specification: SDK-Board
Dimension: 180 x 130 mm
EEPROM: 1024 Byte (I2C)
Ext. Memory: SD-Card socket
Serial Ports: 3x DB9 connector (RS232)
USB: 4x USB-A Host, 1x USB-B Device
Audio Output: 3.5 mm stereo jack
Audio Input: 3.5mm jack (mono) + Condenser microphone
Ethernet: RJ-45 10/100M (DM9000)
RTC: Real Time Clock with battery
Beeper: PWM buzzer
Camera: 20 pin Camera interface (2.0 mm)
LCD: 41 pin connector for FriendlyARM Displays (3.5" and 7") and VGA Board
Touch Panel: 4 pin
User Inputs: 6x push buttons and 1x A/D pot
Expansion headers (2.0 mm)
Power: 5V connector, power switch and LED
Power Supply: regulated 5V

## Slide 43: Stamp Module

## Slide 44: Specification: Stamp Module
Dimension: 63 x 52 mm
CPU: 400 MHz Samsung S3C2440A ARM920T (max freq. 533 MHz)
RAM: 64 MB SDRAM, 32 bit Bus
Flash: 64 MB / 128 MB / 256 MB / 1GB NAND Flash and 2 MB NOR Flash with BIOS
LCD Interface
  STN Displays:
    Monochrome, 4 gray levels, 16 gray levels, 256 colors, 4096 colors
    Max: 1024x768
  TFT Displays:
    Monochrome, 4 gray levels, 16 gray levels, 256 colors, 64k colors, true color
    Max: 1024x768
Touch Panel: 4 wire resistive
User Outputs: 4x LEDs
Expansion headers (2.0 mm)
Debug: 10 pin JTAG (2.0 mm)
OS Support
  Windows CE 5 and 6
  Linux 2.6
  Android

## Slide 45
FriendlyArm Processor
Samsung S3C2440A
ARM920T