## Slide 1: Part I - DMA Part II - Introduction to Processes
Lecture 12

## Slide 2: Summary of Previous Lecture
Details of UART
Interrupts (continued)
Quiz #2

## Slide 3: Administrivia
Quiz #3
  Will be open book/open notes
Midterm Exam
  Will be open book/open notes
  Midterm grades will be based on Quizzes #1-3 and Labs 1-2

## Slide 4: Outline of This Lecture
Part I
  Continuation of Last Lecture
  Nested interrupts, critical sections
  Direct Memory Access (DMA)
  Double buffering
Part II
  Foreground/Background systems
  Processes
Detours signify material outside of, but indirect/direct background/review material for, the main lecture

## Slide 5: Concurrency between I/O and Processing
Keyboard command processing
      The “B” key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        ch <­ Read keyboard input register
        switch (ch) {
        case ‘b’ : startGame(); break;
        case ‘x’ : doSomeProcessing(); break;
        ...
        }
        }
return from ISR
How long does this processing take?

## Slide 6: Will Events Be Missed?
How fast is the keyboard_ISR()?
      The “B” key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR(){
        ch <­ Read keyboard input register
        switch (ch) {
        case ‘b’ : startGame(); break;
        case ‘x’ : doSomeProcessing(); break;
        ...
        }
        }
What happens if another key is pressed ­ or if a timer interrupt occurs?
return from ISR

## Slide 7: A More Elegant Solution
Add a buffer (in software or hardware) for input characters.
  This decouples the time for processing from the time between keystrokes, and provides a computable upper bound on the time required to service a keyboard interrupt.
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        input_buffer[tail++ % BUF_SIZE] = ch;
        ...
        }
Stores the input and then quickly returns to the “main program” (process)
return from ISR

## Slide 8: What Can Go Wrong?
1. Buffer could overflow (bigger buffer helps, but there is a limit)
2. Could another interrupt occur while adding the current keyboard character to the input_buffer?
Key is pressed in the middle of incrementing tail
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        input_buffer[tail++ % BUF_SIZE] = ch;
        ...
        }
return from ISR
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        input_buffer[tail++
        % BUF_SIZE] = ch;
        ...
        }
return from ISR

## Slide 9: Masking Interrupts
If interrupts are masked (IRQ and FIQ disabled), nothing will be processed until the ISR completes and returns.
  Remember: entering IRQ mode masks IRQs and entering FIQ mode masks FIQs and IRQs
Key is pressed in the middle of incrementing tail
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        MASK_INTERRUPTS();
        input_buffer[tail++ % BUF_SIZE] = ch;
        UNMASK_INTERRUPTS();
        ...
        }
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        MASK_INTERRUPTS();
        input_buffer[tail++ % BUF_SIZE]
        = ch;
        UNMASK_INTERRUPTS();
        ...
        }
return from ISR
return from ISR

## Slide 10: Buffer Processing
Must be careful when modifying the buffer with interrupts turned on.
  while (!quit){
  if (tail != head){
  process_command(input_buffer);
  remove_command(input_buffer);
  }
  }
  keyboard_ISR(){
  MASK_INTERRUPTS();
  ch <­ Read ACIA input register
  input_buffer[tail++ % BUF_SIZE] = ch;
  UNMASK_INTERRUPTS();
  }
return from ISR
What happens if another command is entered as you remove one from the input_buffer?

## Slide 11: Buffer Processing
How about the print buffer?
  printStr(char *string) {
  while (*string) {
  outputBuffer[tail++ % BUF_SIZE] = *string++;
  }
}
  timer_ISR(){
  clockTicks++;
  printStr(convert(clockTicks));
  }
printStr(“this is a line”);
  T H I S I S 2 : 3 0
  T H I S I S
Jump to timer_ISR
tail points here ­ and a timer interrupt occurs

## Slide 12: Critical Sections of Code
Pieces of code that must appear as an atomic action
  T H I S I S
  printStr(char * string) {
  MASK_INTERRUPTS;
  while (*string){
  outputBuffer[tail++ % BUF_SIZE] = *string++;
}
UNMASK_INTERRUPTS();
}
  timer_ISR(){
  clockTicks++;
  printStr(convert(clockTicks));
  }
printStr(“this is a line”);
  T H I S I S A L I N E
Jump to timer_ISR happens after printStr() completes
tail points here ­ and a timer interrupt occurs
Atomic action ­ action that “appears”' to take place in a single indivisible operation

## Slide 13: Increasing Concurrency Between I/O and Programs
So far today, we have seen how to use buffers to de-couple the speed of input/output devices from that of programs executing on the CPU
  And how to deal with the corresponding concurrency problems with masking of interrupts
Now, how can we push this further??
  In particular, can we get the I/O to happen without needing the CPU for every single operation?!

## Slide 14: Programmed I/O
All of our examples so far have used programmed I/O
  Programmed I/O: a program running on the processor moves data to/from the device using instructions.
  Either interrupts or polling are used to discover when devices are ready.
Processor
device
On-chip
cache
Memory
buffer
program
Bus
Processor grabs data from device and copies to buffer “by hand” (manually)

## Slide 15: Direct Memory Access (DMA)
What if we make the device a little smarter??
  Make the device capable of moving data to/from memory itself
  Advantage: it would no longer need the processor to move the data
  Disadvantage: more complicated
Processor
device
On-chip
cache
Memory
buffer
program
Bus
... while the processor executes instructions for another process
DMA reads/writes memory

## Slide 16: Direct Memory Access – How?
The device can “steal” memory access cycles from the bus while the processor is not reading or writing
Generally a “block” move is set up ­­ maybe 512 bytes per block
  A setup routine is used to initialize the move
  The DMA move is done
  A signal bit is set indicating completion of the move.
There are other DMA methods
  Sometimes there is a DMA­only device that moves the data to/from other devices

## Slide 17: Direct Memory Access – Why?
Higher performance
Only one interrupt per N bytes moved, rather than one interrupt per byte
Stealing a cycle from the bus and doing the transfer is faster than doing a single move instruction
  Each byte potentially goes over the bus fewer times
  Used for high performance, block-oriented devices: disks, tapes, networks, etc.

## Slide 18: Direct Memory Access ­­ DMA Read example
Operations on processor
  Load starting address of buffer
  Load max word count
  Start device
  Wait for interrupt
  Process buffer
Operations on DMA device
Processor
device
On-chip
cache
Memory
buffer
program
Bus
... while the processor executes instructions from another process
DMA reads/writes memory
  struct dmaDevice { /* device registers */
    unsigned int startingAddressOfBuffer;
    unsigned int wordCount;
    unsigned char controlAndStatus;
  }
wait for start signal
while (wordcount­­)
mem(address++) = deviceData;
signal done (IRQ)

## Slide 19: Are We Missing Something?
The processor and the I/O device cannot safely access the memory buffer at the same time
If they have to take turns
  Then, the amount of overlapping may be much lower (unless the program does not really need the data)
Is there any hope?

## Slide 20: Double Buffering
A double-buffered system
  producer writes to one buffer while DMA consumer empties another
    or vice-versa ­­ the DMA could be the producer
  switch to alternate buffer when both done
    could have N parallel buffers
    Q: What is the right value for N?
Data Buffer 1
Data Buffer 2
Producer
Consumer
Active
transfer
Alternate
transfer
Active
transfer
Alternate
transfer

## Slide 21: Why is Double Buffering Better?
Why is double buffering usually better?
  Overlap processing ­­ Two “processes” run concurrently ­­ their activity overlaps.
    The application process and the device are both active at the same time.
      Application software and the device state machine do useful work at the same time.
        i.e. at the same time that the producer calculates data and fills a buffer, the DMA consumes another.
  Device utilization ­­ it is easier to keep the consumer DMA busy
    Shorter delay between completion of one buffer and the availability of next
But, it takes more memory and time to set up
  So, it is not worth it for small, quick and infrequent I/O activities...

## Slide 22: Overlapped Processing
Win:
  With overlap of the two processes, there is higher throughput
Single Buffer Scenario
Double Buffer Scenario
fill_it
empty_it
empty_it
fill_it
fill_B
empty_A
fill_A
empty_B
fill_B
empty_A
fill_A
wait
Execution of the two activities overlap
Program
activity
DMA device
activity

## Slide 23: Foreground/Background Systems
Small, simple systems usually don't have an OS
Instead, an application consists of an infinite loop that calls modules (functions) to perform various actions in the “Background”.
Interrupt Service Routines (ISRs) handle asynchronous events in the “Foreground”
Foreground = interrupt level
Background = task level

## Slide 24: Foreground/Background System
Code
Execution
while
loop
time
ISR
ISR
ISR
“Foreground”
“Background”

## Slide 25: Process
Informally, a program in execution
Process is more than just the code
It includes the current activity of the program, as represented by the PC and the contents of the processor's registers.
Generally includes a stack and data section
Program is a passive entity
Process is an active entity

## Slide 26: Process Control Block (PCB)
Process Control Block
  OS structure which holds the pieces of information associated with a process
Process state: new, ready, running, waited, halted, etc.
Program counter: contents of the PC
CPU registers: contents of the CPU registers
CPU scheduling information: information on priority and scheduling parameters
Memory­management information: Pointers to page or segment tables
Accounting information: CPU and real time used, time limits, etc.
I/O status information: which I/O devices (if any) this process has allocated to it, list of open files, etc.

## Slide 27: Process Control Block
Nothing more than a structure maintained by the OS
Example PCB from OSF/1:
  struct pcb {
    char *pcb_usp; /* User stack pointer */
    char *pcb_ssp; /* System stack pointer */
    int pcb_r0;
    int pcb_r1;
    int pcb_r2;
    int pcb_r3;
    int pcb_r4;
    int pcb_r5;
    int pcb_r6;
    int pcb_r7;
    int pcb_fp;
    int pcb_pc; /* program counter */
    int pcb_modpsr; /* program status register
    and mod register */
  #if MMAX_XPC || MMAX_APC
    short pcb_isrv; /* ISRV Register in ICU
    (interrupt state) */
  #endif MMAX_XPC || MMAX_APC
    quad pcb_f0;
    quad pcb_f1;
    ...
    quad pcb_f7;
    int pcb_fsr; /* FPU status register */
    struct pt_entry *pcb_ptbr;
    int pcb_sigc[5];
  #if MMAX_XPC
    int pcb_dcr; /* Debug Condition Register */
    int pcb_dsr; /* Debug Status Register */
    int pcb_car; /* Compare Address Register */
    int pcb_bpc; /* Breakpoint Program Counter */
  #endif MMAX_XPC
  };

## Slide 28: PCB in Linux (1/3)
struct task_struct {
/* these are hardcoded - don't touch */
volatile long state; /* -1 unrunnable, 0 runnable, >0 stopped */
unsigned long flags; /* per process flags, defined below */
int sigpending;
mm_segment_t addr_limit; /* thread address space; 0-0xBFFFFFFF for user-thead
0-0xFFFFFFFF for kernel-thread */
struct exec_domain *exec_domain;
long need_resched;
/* various fields */
long counter;
long priority;
cycles_t avg_slice;
/* SMP and runqueue state */
int has_cpu;
int processor;
int last_processor;
int lock_depth; /* Lock depth. We can context switch in/out of holding a syscall*/
struct task_struct *next_task, *prev_task;
struct task_struct *next_run, *prev_run;
/* task state */
struct linux_binfmt *binfmt;
int exit_code, exit_signal;
int pdeath_signal; /* The signal sent when the parent dies */

## Slide 29: PCB in Linux (2/3)
unsigned long personality;
int dumpable:1;
int did_exec:1;
pid_t pid;
pid_t pgrp;
pid_t tty_old_pgrp;
pid_t session;
int leader; /* boolean value for session group leader */
/* pointers to (original) parent process, youngest child, younger sibling, older sibling, respectively.(p->father can be replaced with p->p_pptr->pid) */
struct task_struct *p_opptr, *p_pptr, *p_cptr, *p_ysptr, *p_osptr;
/* PID hash table linkage. */
struct task_struct *pidhash_next;
struct task_struct **pidhash_pprev;
/* Pointer to task[] array linkage. */
struct task_struct **tarray_ptr;
struct wait_queue *wait_chldexit; /* for wait4() */
struct semaphore *vfork_sem; /* for vfork() */
unsigned long policy, rt_priority;
unsigned long it_real_value, it_prof_value, it_virt_value;
unsigned long it_real_incr, it_prof_incr, it_virt_incr;
struct timer_list real_timer;
struct tms times;
unsigned long start_time;
long per_cpu_utime[NR_CPUS], per_cpu_stime[NR_CPUS];
/* mm fault and swap info: this can be seen as either mm-specific or thread-specific */
unsigned long min_flt, maj_flt, nswap, cmin_flt, cmaj_flt, cnswap;
int swappable:1;

## Slide 30: PCB in Linux (3/3)
/* process credentials */
uid_t uid,euid,suid,fsuid;
gid_t gid,egid,sgid,fsgid;
int ngroups;
gid_t groups[NGROUPS];
kernel_cap_t cap_effective, cap_inheritable, cap_permitted;
struct user_struct *user;
/* limits */
struct rlimit rlim[RLIM_NLIMITS];
unsigned short used_math;
char comm[16];
/* file system info */
int link_count;
struct tty_struct *tty; /* NULL if no tty */
/* ipc stuff */
struct sem_undo *semundo;
struct sem_queue *semsleeping;
/* tss for this task */
struct thread_struct tss;
/* filesystem information */
struct fs_struct *fs;
/* open file information */
struct files_struct *files;
/* memory management info */
struct mm_struct *mm;
/* signal handlers */
spinlock_t sigmask_lock; /* Protects signal and blocked */
struct signal_struct *sig;
sigset_t signal, blocked;
struct signal_queue *sigqueue, **sigqueue_tail;
unsigned long sas_ss_sp;
size_t sas_ss_size;
};

## Slide 31: Process vs. Task vs. Thread
The terms, process and task, are often used interchangeably
Threads, sometimes called lightweight processes, consist of
  Program counter
  Register set
  Stack space
A single process (task) can have multiple threads
These multiple threads share the text and data segments (physical memory), file descriptors and process priority
Each thread has its own private register set (including PC) and stack

## Slide 32: Multiple Processes
stack
task priority
CPU registers
CPU registers
Processor
Memory
stack
task priority
CPU registers
stack
task priority
CPU registers
...
}
context

## Slide 33: Summary of Lecture
Buffer processing
  Nested interrupts
  Critical sections
  Double buffering
DMA
OS “Scheduling”
  Foreground/Background systems
  Processes
  Process Control Block (PCB)