## Slide 1: Memory Management: Overlays and Virtual Memory
Lecture 14

## Slide 2: How Does a Program Start Running?
00111101
01101010
11010101
10101010
10101101
11010101
0x0000
0x3fff
RAM
CPU’s Program Counter is then set to the starting address of the program and the program begins execution.
OS (loader) copies a program from permanent storage into RAM ­ on PCs and workstations, the “operating system” copies the program (bits) from disk.

## Slide 3: What if the program is too big?
Some machines won't let you run the program
  Original DOS
  Why this limitation?
0011100
0010101
0010101
1001101
0011100
0010101
0010101
1001101
0011100
0010101
0010101
1101011
0x0000
0x3fff
RAM
1011000101101011110101010110

## Slide 4: Solution: Only Load Part of the Program
One option: programmer breaks code into pieces that fit into RAM
Pieces, called overlays, are loaded and unloaded by the program
Does not require OS help
RAM
0xff
0x00
0x00ff
0x0000
0x01ff
0x0100
load one overlay and run
until other overlay
is needed
Program

## Slide 5: ARM Linker Supports Overlays
Overlay manager loads an overlay segment when it is not in RAM
Supports Static and Dynamic Overlays
Static overlays
  One root segment
  2 or more memory partitions (1 for the root partition which is always in RAM)
  Within each partition, any number of overlay segments
  Only 1 overlay segment can be in a partition at a given time
  Application writer specifies what is in each partition and segment
root segment
2_1
2_2
2_3
2_4
1_1
1_2
1_3
1_4
low address
high address
segments 1_1 .. 1_4 share the same memory area
so do segments 2_1 .. 2_4

## Slide 6: What Happens if ...
A function in one overlay calls a function in another ­ and vice-versa
RAM
0xff
0x00
0x00ff
0x0000
0x01ff
0x0100
define foo2(){
call foo1();
}
define foo1(){
call foo2();
}
both segments statically
allocated to the same
physical partition

## Slide 7: Dynamic Overlay
Include re-location information with each overlay segment
Have overlay manager allocate memory for an overlay segment when it is first loaded
Load and unload overlay segments by explicit calls to overlay manager
Each overlay segment is given its own name ­ linker links each as if it were in its own partition

## Slide 8: Problems with Overlays
Difficult for programmer to manage
Not general ­ management of resources (RAM) is an operating system issue
  But many embedded systems do not have the space or power for a “real” OS

## Slide 9: Solution: Virtual Memory
What is virtual memory?
  Technique that allows execution of a program that may not completely reside in memory (RAM)
Allows the computer to “fake”' a program into believing that its memory space is larger than physical RAM
Why is VM important?
  Cheap ­ no longer have to buy lots of RAM
  Removes burden of memory resource management from the programmer
  Other benefits ...

## Slide 10: The Memory Pyramid

## Slide 11: How Does VM Work ?
Two memory “spaces”
  Virtual memory space ­ what the program “sees”
  Physical memory space ­ what the program runs in (size of RAM)
On program startup
  OS copies program into RAM
  If there is not enough RAM, OS stops copying program and starts it running with only a portion of the program loaded in RAM
  When the program touches a part of the program not in physical memory (RAM), OS catches the memory abort (called a page fault) and copies that part of the program from disk into RAM
  In order to copy some of the program from disk to RAM, OS must evict parts of the program already in RAM
    OS copies the evicted parts of the program back to disk

## Slide 12: Example: Virtual and Physical Address Spaces
Virtual Address Space Physical Address Space
bne 0x00
add r10,r1,r2
sub r3,r4,r1
sw r5,0x0c
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5

## Slide 13: Example (con'td): Need VA­to­PA mappings
bne 0x00
add r10,r1,r2
sub r3,r4,r1
sw r5,0x0c
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
Virtual Address Space Physical Address Space
VA->PA

## Slide 14: Example (con'td): After handling a page fault
bne 0x00
add r10,r1,r2
sub r3,r4,r1
sw r5,0x0c
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
bne 0x00
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
Virtual Address Space Physical Address Space
VA->PA

## Slide 15: Example (con'td): After a second page fault
bne 0x00
add r10,r1,r2
sub r3,r4,r1
sw r5,0x0c
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
bne 0x00
add r1,r2,r3
lw r2, 0x04
mult r3,r4,r5
Virtual Address Space Physical Address Space
VA->PA

## Slide 16: Basic VM Algorithm
Program asks for virtual address
Computer translates virtual address (VA) to physical address (PA)
Computer reads PA from RAM, returning it to program
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
RAM
VA->PA
Processor
(running program)
Instructions
(or data)
Virtual
address

## Slide 17: Page Tables
Table which holds VA ­> PA translations is called the page table
In our current scheme, each word is translated from a virtual address to a physical address
  How big is the page table?
0x00
0x04
0x08
0x0C
add r1,r2,r3
sub r2,r3,r4
lw r2, 0x04
mult r3,r4,r5
RAM
VA->PA
Processor
(running program)
Instructions
(or data)
Virtual
address

## Slide 18: Real Page Tables
Instead of the fine­grained VM where any virtual word can map to any RAM word location, partition memory into chunks called pages
  Typical page size today is 4 or 8 KBytes
This reduces the number of VA­> PA translation entries
  Only one translation per page
  For a 4 KByte page, that's one VA­> PA translation for every 1,024 words
Within a page, the virtual address == physical address
Virtual Page Number
Page Offset
Physical Page #
Page Offset
Translation
Virtual
Address
Physical
Address
0
11
12
31
0
11
12
24

## Slide 19: Virtual Pages & Physical Page Frames
0x7fff
0x6fff
0x5fff
0x4fff
0x3fff
0x2fff
0x1fff
0x0fff
0x0000
0x3fff
0x2fff
0x1fff
0x0fff
0x0000
Virtual Address Space Physical Address Space
virtual page
0x000-0xfff = 4KB
physical page frame

## Slide 20: Page Frames
Every address within a virtual page maps to the same location within a physical page frame
  In other words, bottom log 2(page size in bytes) is not translated

## Slide 21: Page Table Entries
A real page table entry (PTE) contains a number of fields
  Physical page number
  Access control bits (e.g., writeable bit)
  Status bits (e.g., accessed and dirty bits)
  MMU control bits (e.g., cacheable and bufferable bits)
Why is the virtual page number not in the page table entry?
Physical Page Number (PPN)
Access Control
0
11
12
31
Status
MMU
2
3
5
6

## Slide 22: Interactions with Instruction/Data Cache
Page table entry has bits to determine if region is
  cacheable vs . uncacheable
  write­through vs. write­back
  Why control caching?
  Some regions, such as for memory­mapped I/O devices, should not be cached. Why?
    Because cache doesn't know if I/O device register has changed value

## Slide 23: Interactions with Write Buffer
Page table entry has bits to determine if region
  Allows write buffer to buffer writes
Why would one not want to buffer writes?
  Possible problems with memory­mapped I/O devices that require a write to complete before subsequent commands (instructions) are issued

## Slide 24: Two­level Page Tables
Virtual
Address
0
11
12
31
21
22
page
directory
page
table
page
frame
data

## Slide 25: ARM MMU
Complex VM and protection mechanisms
Presents 4 GB address space (why?)
Memory granularity: 3 options supported
  1MB sections
  Large pages (64 KBytes) ­ access control within a large page on 16 KBytes
  Small pages (4 KBytes) ­ access control within a large page on 1 Kbytes
Puts processor in Abort Mode when virtual address not mapped or permission check fails
Change pointer to page tables (called the translation table base, in ARM jargon) to change virtual address space
  useful for context switching of processes

## Slide 26: Example: Single-Level Page Table
Virtual
Address
0
11
12
31
page
table
page
frame
data
value = y
y
220
entries
32 bits
212
entries
Size of page table
= 220 * 32 bits = 4 Mbytes
value = x
x
8 bits
Size of page
= 212 * 8 bits = 4 Kbytes

## Slide 27: Single-Level Page Table
Assumptions
  32-bit virtual addresses
  4 Kbyte page size = 212 bytes
  32-bit address space
How many virtual page numbers?
  232 / 212 = 220 = 1,048,576 virtual page numbers = number of entries in the page table
If each page table entry occupies 4 bytes, how much memory is needed to store the page table?
  220 entries * 4 bytes = 222 bytes = 4 Mbytes

## Slide 28: Example: Two­level Page Table
Virtual
Address
0
11
12
31
21
22
page
directory
page
table
page
frame
data
value = z
value = y
y
210
entries
32 bits
32 bits
Size of page directory
= 210 * 32 bits = 4 Kbytes
value = x
x
z
210
entries
Size of page table
= 210 * 32 bits = 4 Kbytes
212
entries
8 bits
Size of page
= 212 * 8 bits = 4 Kbytes

## Slide 29: Two-Level Page Table
Assumptions
  210 entries in page directory (= max number of page tables)
  210 entries in page table
  32 bits allocated for each page directory entry
  32 bits allocated for each page table entry
How much memory is needed?
  Page table size = 210 entries * 32 bits = 212 bytes = 4 Kbytes
  Page directory size = 210 entries * 32 bits = 212 bytes = 4 Kbytes

## Slide 30: Two-Level Page Table
Small (typical) system
  One page table might be enough
    Page directory size + Page table size = 8 Kbytes of memory would suffice for virtual memory management
  How much physical memory could this one page table handle?
    Number of page tables * Number of page table entries * Page size =
    1 * 210 * 212 bytes = 4 Mbytes
Large system
  You might need the maximum number of page tables
    Max number of page tables * Page table size =
    210 directory entries * 212 bytes = 222 bytes = 4 Mbytes of memory would be needed for virtual memory management
  How much physical memory could these 210 page tables handle?
    Number of page tables * Number of page table entries * Page size =
    210 * 210 * 212 bytes = 4 Gbytes

## Slide 31: Summary of Lecture
How do programs run in memory?
  What happens on “overflows”?
  Memory Overlays
    static overlays and dynamic overlays
    Problems with overlays
Virtual Memory (VM)
  What is VM?
  How does VM work?
  Virtual address to physical address mappings
  Page faults
  VM Schemes
    page tables
    virtual pages and physical page frames
    page table entries
    interactions with the rest of the system
    two-level page tables