## Slide 1: ARM Exception Handling and SoftWare Interrupts (SWI)
Lecture #4

## Slide 2: Recommended Readings
Sections 5.1-5.4 (Exceptions) of the ARM Developer Guide
Chapter 12 (Implementing SWIs) of Jumpstart Programming Techniques
Chapters 17 ARM Demon Routines of Jumpstart Reference Manual
Catch up on your readings!

## Slide 3: Thought for the Day
I can accept failure.
Everyone fails at something.
But I cannot accept not trying.
- Michael Jordan

## Slide 4: Summary of Previous Lecture
The ARM Programmer’s Model
Introduction to ARM Assembly Language
Assembly Code from C Programs (7 Examples)
Dealing With Structures
Interfacing C Code with ARM Assembly
ARM libraries and armsd

## Slide 5: Outline of This Lecture
Frame pointers and backtrace structures
Normal program flow vs. exceptions
  Exceptions vs. interrupts
Software Interrupts
  What is an SWI?
  What happens on an SWI?
  Vectoring SWIs
  What happens on SWI completion?
  What do SWIs do?
  A Complete SWI Handler
  A C_SWI_Handler (written in C)
Loading the Software Interrupt Vector Table

## Slide 6: The Frame Pointer
fp points to top of the stack area for the current function
  Or zero if not being used
By using the frame pointer and storing it at the same offset for every function call, it creates a singly­linked list of activation records
  The fp register points to the stack backtrace structure for the currently executing function.
  The saved fp value is (zero or) a pointer to a stack backtrace structure created by the function which called the current function.
  The saved fp value in this structure is a pointer to the stack backtrace structure for the function that called the function that called the current function; and so on back until the first function.
(saved) pc
(saved) lr
(saved) sb
SPbefore
address
0x90
0x8c
0x88
0x84
0x80
0x7c
0x78
0x74
0x70
0x6c
0x68
0x64
0x60
0x5c
0x58
0x54
0x50
(saved) ip
(saved) fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
SPcurrent
FPcurrent

## Slide 7: Example Backtrace
(saved) pc
(saved) lr
(saved) sb
(saved) ip
(saved) fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
(saved) pc
(saved) lr
(saved) sb
(saved) ip
(saved) fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
(saved) pc
(saved) lr
(saved) sb
(saved) ip
(saved) fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
fp
bar’s frame
foo’s frame
main’s frame
If main calls foo which calls bar

## Slide 8: Creating the “backtrace” structure
MOV ip, sp
STMFD sp!,{a1­a4,v1­v5,sb,fp,ip,lr,pc}
SUB fp, ip, #4
…
…
LDMFD fp, {fp,sp,sb,pc}
(saved) pc
(saved) lr
(saved) sb
SPbefore
address
0x90
0x8c
0x88
0x84
0x80
0x7c
0x78
0x74
0x70
0x6c
0x68
0x64
0x60
0x5c
0x58
0x54
0x50
(saved) ip
(saved) fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
SPcurrent
FPafter

## Slide 9: Normal Program Flow vs. Exceptions
Normally, programs execute sequentially (with a few branches to make life interesting)
Normally, programs execute in user mode (see next slide)
Exceptions and interrupts break the sequential flow of a program, jumping to architecturally­defined memory locations
In ARM, SoftWare Interrupt (SWI) is the “system call” exception
Types of ARM exceptions
  reset when CPU reset pin is asserted
  undefined instruction when CPU tries to execute an undefined op-code
  software interrupt when CPU executes the SWI instruction
  prefetch abort when CPU tries to execute an instruction pre-fetched from an illegal addr
  data abort when data transfer instruction tries to read or write at an illegal address
  IRQ when CPU's external interrupt request pin is asserted
  FIQ when CPU's external fast interrupt request pin is asserted

## Slide 10: ARM Processor Modes (of interest to us)
User: the “normal” program execution mode.
IRQ: used for general-purpose interrupt handling.
Supervisor: a protected mode for the operating system.
  (there are also Abort, FIQ and Undef modes)
The ARM Register Set
Registers R0-R15 + CPSR (Current Program Status Register)
  R13: Stack Pointer (by convention)
  R14: Link Register (hardwired)
  R15: Program Counter where bits 0:1 are ignored (hardwired)

## Slide 11: Terminology
The terms exception and interrupt are often confused
Exception usually refers to an internal CPU event such as
  floating point overflow
  MMU fault (e.g., page fault)
  trap (SWI)
Interrupt usually refers to an external I/O event such as
  I/O device request
  reset
In the ARM architecture manuals, the two terms are mixed together

## Slide 12: What do SWIs do?
SWIs (often called software traps) allow a user program to “call” the OS ­­ that is, SWIs are how system calls are implemented.
When SWIs execute, the processor changes modes (from User to Supervisor mode on the ARM) and disables interrupts.
Types of SWIs in ARM Angel (axd or armsd)
  SWI_WriteC(SWI 0) Write a byte to the debug channel
  SWI_Write0(SWI 2) Write the null­terminated string to debug channel
  SWI_ReadC(SWI 4) Read a byte from the debug channel
  SWI_Exit(SWI 0x11) Halt emulation ­ this is how a program exits
  SWI_EnterOS(SWI 0x16) Put the processor in supervisor mode
  SWI_Clock(SWI 0x61) Return the number of centi­seconds
  SWI_Time(SWI 0x63) Return the number of secs since Jan. 1, 1970
Read more in Chapter 17 of the JumpStart Reference Manual
  See Recommended Readings

## Slide 13: What Happens on an SWI? (1)
The ARM architecture defines a Vector Table indexed by exception type
One SWI, CPU does the following: PC <­­0x08
Also, sets LR_svc, SPSR_svc, CPSR (supervisor mode, no IRQ)
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
SWI Handler
1
1

## Slide 14: What Happens on an SWI? (2)
Not enough space in the table (only one instruction per entry) to hold all of the code for the SWI handler function
This one instruction must transfer control to appropriate SWI Handler
Several options are presented in the next slide
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
SWI Handler
2
2

## Slide 15: “Vectoring” Exceptions to Handlers
Option of choice: Load PC from jump table (shown below)
Another option: Direct branch (limited range)
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
LDR pc, pc, 0x100
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
SWI Handler
(S_Handler)
2
&A_Handler
&U_Handler
&S_Handler
&P_Handler
...
“Jump” Table
0x108
0x10c
0x110
0x114
...
Why 0x110?

## Slide 16: What Happens on SWI Completion?
Vectoring to the S_Handler starts executing the SWI handler
When the handler is done, it returns to the program ­­ at the instruction following the SWI
MOVS restores the original CPSR as well as changing pc
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
3
MOVS pc, lr
3
SWI Handler
(S_Handler)

## Slide 17: How Do We Determine the SWI number?
All SWIs go to 0x08
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
SWI Handler must
serve as clearing
house for different
SWIs
MOVS pc, lr
SWI Handler
(S_Handler)

## Slide 18: SWI Instruction Format
24-bit “comment” field (ignored by processor)
1 1 1 1
Example: SWI 0x18
cond
0
23
24
27
31
28
SWI number

## Slide 19: SWI Handler Uses the “Comment” Field
On SWI, the processor
    (1) copies CPSR to SPSR_SVC
    (2) set the CPSR mode bits to supervisor mode
    (3) sets the CPSR IRQ to disable
    (4) stores the value (PC + 4) into LR_SVC
    (5) forces PC to 0x08
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
LDR r0,[lr,#­4]
BIC r0,r0,#0xff000000
R0 holds SWI number
MOVS pc, lr
SWI Handler
(S_Handler)
24-bit “comment” field (ignored by processor)
1 1 1 1
cond

## Slide 20: Use The SWI # to Jump to “Service Routine”
On SWI, the processor
    (1) copies CPSR to SPSR_SVC
    (2) set the CPSR mode bits to supervisor mode
    (3) sets the CPSR IRQ to disable
    (4) stores the value (PC + 4) into LR_SVC
    (5) forces PC to 0x08
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
LDR r0,[lr,#­4]
BIC r0,r0,#0xff000000
switch (r0){
case 0x00: service_SWI1();
case 0x01: service_SWI2();
case 0x02: service_SWI3();
…
}
MOVS pc, lr
SWI Handler
(S_Handler)
24-bit “comment” field (ignored by processor)
1 1 1 1
cond

## Slide 21: Problem with The Current Handler
On SWI, the processor
    (1) copies CPSR to SPSR_SVC
    (2) set the CPSR mode bits to supervisor mode
    (3) sets the CPSR IRQ to disable
    (4) stores the value (PC + 4) into LR_SVC
    (5) forces PC to 0x08
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
to R_Handler
to U_Handler
to S_Handler
to P_Handler
to D_Handler
...
to I_Handler
to F_Handler
Vector Table (spring board)
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
(Reset
(Undef instr.)
(SWI)
(Prefetch abort)
(Data abort)
(Reserved)
(IRQ)
(FIQ)
LDR r0,[lr,#­4]
BIC r0,r0,#0xff000000
switch (r0){
case 0x00: service_SWI1();
case 0x01: service_SWI2();
case 0x02: service_SWI3();
…
}
MOVS pc, lr
SWI Handler
(S_Handler)
What was in R0? User program may have been using this register. Therefore, cannot just use it ­ must first save it

## Slide 22: Full SWI Handler
S_Handler
  SUB sp,sp, #4 ; leave room on stack for SPSR
  STMFD sp!, {r0­r12, lr} ; store user's gp registers
  MRS r2, spsr[_csxf] ; get SPSR into gp registers
  STR r2, [sp, #14*4] ; store SPSR above gp registers
  MOV r1, sp ; pointer to parameters on stack
  LDR r0, [lr, #­4] ; extract the SWI number
  BIC r0,r0,#0xff000000 ; get SWI # by bit-masking
  BL C_SWI_handler ; go to handler (see next slide)
  LDR r2, [sp, #14*4] ; restore SPSR (NOT “sp!”)
  MSR spsr_csxf, r2 ; csxf flags (see XScale QuickRef Card)
  LDMFD sp!, {r0­r12, lr} ; unstack user's registers
  ADD sp, sp, #4 ; remove space used to store SPSR
  MOVS pc, lr ; return from handler
gp = general-purpose
SPSR is stored above gp registers since the registers may contain system call parameters (sp in r1)

## Slide 23: C_SWI_Handler
void C_SWI_handler(unsigned number, unsigned *regs)
{
  switch (number){
  case 0: /* SWI number 0 code */ break;
  case 1: /* SWI number 1 code */ break;
  ...
  case XXX: /* SWI number XXX code */ break;
  default:
  } /* end switch */
} /* end C_SWI_handler() */
spsr_svc
lr_svc
r4
r3
r12
r11
r10
r9
r8
r7
r6
r5
r2
r1
r0
Previous sp_svc
sp_svc
regs[12]
regs[0] (also *regs)

## Slide 24: Loading the Vector Table
/* For 18-349, the Vector Table will use the ``LDR PC, PC,
* offset'' springboard approach */
unsigned Install_Handler(unsigned int routine, unsigned int *vector)
{
  unsigned int pcload_instr, old_handler, *soft_vector;
  pcload_instr = *vector; /* read the Vector Table instr (LDR ...) */
  pcload_instr &= 0xfff; /* compute offset of jump table entry */
  pcload_instr += 0x8 + (unsigned)vector; /* == offset adjusted by PC
  and prefetch */
  soft_vector = (unsigned *)pcload_instr; /* address to load pc from */
  old_handler = *soft_vector; /* remember the old handler */
  *soft_vector = routine; /* set up new handler in jump table */
  return (old_handler); /* return old handler address */
} /* end Install_Handler() */
Called as
  Install_Handler ((unsigned) C_SWI_Handler, swivec);
where,
  unsigned *swivec = (unsigned *) 0x08;

## Slide 25: Calling SWIs from C Code
char __swi(4) SWI_ReadC(void);
void readline (char *buffer)
{
  char ch;
  do {
  *buffer++ = ch = SWI_ReadC();
  while (ch != 13);
}
*buffer = 0;
} /* end readline() */
readline
STMDF sp!,{lr}
MOV lr, a1
readagain
SWI &4
STRB a1,[lr],#1
CMP a1,#&d
BNE readagain
MOV a1,#0
STRB a1, [lr, #0]
LDMIA sp!, {pc}
Assembly code produced by compiler
User-Level C Source Code

## Slide 26: Summary of Lecture
Software Interrupts (SWIs)
  What is an SWI?
  What happens on an SWI?
  Vectoring SWIs
  What happens on SWI completion?
  What do SWIs do?
  A Full SWI Handler
  A C_SWI_Handler (written in C)
Loading Software Interrrupt Vectors

## Slide 27: Looking Ahead
Program Monitor, Loading and Initialization