## Slide 1: Operating systems for embedded systems
CSE 466
Wireless Sensor Networks
<number>
Embedded operating systems
  How do they differ from desktop operating systems?
Programming model
  Process-based
  Event-based
  How is concurrency handled?
  How are resource conflicts managed?
Programming languages
  C/C++
  Java/C#
  Memory management
  Atomicity in the presence of interrupts
Notes: <number>

## Slide 2: Embedded Operating Systems
CSE 466
Wireless Sensor Networks
<number>
Features of all operating systems
  Abstraction of system resources
  Managing of system resources
  Concurrency model
  Launch applications
Desktop operating systems
  General-purpose – all features may be needed
  Large-scale resources – memory, disk, file systems
Embedded operating systems
  Application-specific – just use features you need, save memory
  Small-scale resources – sensors, communication ports
Notes: <number>

## Slide 3: System Resources on Typical Sensor Nodes
CSE 466
Wireless Sensor Networks
<number>
Timers
Sensors
Serial port
Radio communications
Memory
Power management
Notes: <number>

## Slide 4: Abstraction of System Resources
CSE 466
Wireless Sensor Networks
<number>
Create virtual components
  E.g., multiple timers from one timer
Allow them to be shared by multiple threads of execution
  E.g., two applications that want to share radio communication
Device drivers provide interface for resource
  Encapsulate frequently used functions
  Save device state (if any)
  Manage interrupt handling
Notes: <number>

## Slide 5: Very simple device driver
CSE 466
Wireless Sensor Networks
<number>
Turn LED on/off
Parameters:
  port pin
API:
  on(port_pin) - specifies the port pin (e.g., port D pin 3)
  off(port_pin)
Interactions:
  only if other devices want to use the same port
Notes: <number>

## Slide 6: Simple device driver
CSE 466
Wireless Sensor Networks
<number>
Turning an LED on and off at a fixed rate
Parameters:
  port pin
  rate at which to blink LED
API:
  on(port_pin, rate)
    specifies the port pin (e.g., port D pin 3)
    specifies the rate to use in setting up the timer (what scale?)
  off(port_pin)
Internal state and functions:
  keep track of state (on or off for a particular pin) of each pin
  interrupt service routine to handle timer interrupt
Notes: <number>

## Slide 7: Interesting interactions
CSE 466
Wireless Sensor Networks
<number>
What if other devices also need to use timer (e.g., PWM device)?
  timer interrupts now need to be handled differently depending on which device’s alarm is going off
Benefits of special-purpose output compare peripheral
  output compare pins used exclusively for one device
  output compare has a separate interrupt handling routine
What if we don’t have output compare capability or run out of output compare units?
Notes: <number>

## Slide 8: Sharing timers
CSE 466
Wireless Sensor Networks
<number>
Create a new device driver for the timer unit
  Allow other devices to ask for timer services
  Manage timer independently so that it can service multiple requests
Parameters:
  Time to wait, address to call when timer reaches that value
API:
  set_timer(time_to_wait, call_back_address)
    Set call_back_address to correspond to time+time_to_wait
    Compute next alarm to sound and set timer
    Update in interrupt service routine for next alarm
Internal state and functions:
  How many alarms can the driver keep track of?
  How are they organized? FIFO? priority queue?
Notes: <number>

## Slide 9: Concurrency
CSE 466
Wireless Sensor Networks
<number>
Multiple programs interleaved as if parallel
Each program requests access to devices/services
  e.g., timers, serial ports, etc.
Exclusive or concurrent access to devices
  allow only one program at a time to access a device (e.g., serial port)
  arbitrate multiple accesses (e.g., timer)
State and arbitration needed
  keep track of state of devices and concurrent programs using resource
  arbitrate their accesses (order, fairness, exclusivity)
  monitors/locks (supported by primitive operations in ISA - test-and-set)
Interrupts
  disabling may effect timing of programs
  keeping enabled may cause unwanted interactions
Notes: <number>

## Slide 10: Handling concurrency
CSE 466
Wireless Sensor Networks
<number>
Traditional operating system
  multiple threads or processes
  file system
  virtual memory and paging
  input/output (buffering between CPU, memory, and I/O devices)
  interrupt handling (mostly with I/O devices)
  resource allocation and arbitration
  command interface (execution of programs)
Embedded operating system
  lightweight threads
  input/output
  interrupt handling
  real-time guarantees
Notes: <number>

## Slide 11: Embedded operating systems
CSE 466
Wireless Sensor Networks
<number>
Lightweight threads
  basic locks
  fast context-switches
Input/output
  API for talking to devices
  buffering
Interrupt handling (with I/O devices and UI)
  translate interrupts into events to be handled by user code
  trigger new tasks to run (reactive)
Real-time issues
  guarantee task is called at a certain rate
  guarantee an interrupt will be handled within a certain time
  priority or deadline driven scheduling of tasks
Notes: <number>

## Slide 12: Some Examples
CSE 466
Wireless Sensor Networks
<number>
embedded operating systems typically reside in ROM (flash) - changed rarely
Pocket PC/WindowsCE/WindowsMobile
  PDA operating system
  spin-off of Windows NT
  portable to a wide variety of processors (e.g., Xscale)
  full-featured OS modularized to only include features as needed
Wind River Systems VxWorks
  one of the most popular embedded OS kernels
  highly portable to an even wider variety of processors (tiny to huge)
  modularized even further than the ones above (basic system under 50K)
TinyOS
  Open-source development environment specifically for small sensors
  Simple (and tiny) operating system
    Scheduler/event model of concurrency
    Software components for efficient modularity
    Software encapsulation for resources of sensor networks
  Programming language and model – nesC
Notes: <number>

## Slide 13: Metrics in Real-Time Systems (1/2)
End-to-end latency:
  E.g. worst-case, average-case, variance, distribution
  Can involve multiple hops (across nodes, links, switches and routers)
  Behavior in the presence or absence of failures
Jitter
Throughput:
  How many X can be processed?
  How many messages can be transmitted?
Survivability:
  How many faults can be tolerated before system failures?
  What functionality gets compromised?

## Slide 14: Metrics in Real-Time Systems (2/2)
Security:
  Can the system’s integrity be compromised?
  Can violations be detected?
Safety:
  Is the system “safe”?
    Can the system get into an ‘unsafe’ state? Has it been ‘certified’?
Maintainability:
  How does one fix problems?
  How does the system get upgraded?
Dynamism and Adaptability:
  What happens when the system mission changes?
  What happens when individual elements fail?
  Can the system reconfigure itself dynamically?
  How does the system behave after re-configuration?

## Slide 15: RTOS Considerations
What processor(s) does it run on?
  8-bit, 16-bit, 32-bit, …
  Intel Pentium® Processor, PowerPC, Arm/StrongArm Intel Xscale®, MIPS, SuperH, …
  IBM and Intel® Network Processors
What board(s) does it run on?
  Complete software package for a particular hardware board is called a BSP (Board Support Package)
What is the software environment?
  Compilers and debuggers
  IDE
    Cross-compilation + symbolic debugging on target?
  Profilers (CPU, memory)
  Test coverage tools
  Native simulation/emulation support?

## Slide 16: Real-Time Operating Systems
Windows platforms
  Embedded XP, Windows CE, Pocket Windows
VxWorks from Wind River Systems (www.windriver.com)
Linux variants
  Blue Cat Linux (www.lynuxworks.com)
  (Embedded) Red Hat Linux (www.redhat.com)
  FSM RT-Linux (www.fsmlabs.com)
  Monta Vista Linux (www.mvista.com)
  TimeSys Linux (www.timesys.com)
LynxOS (www.lynuxworks.com)
QNX (www.qnx.com)
Solaris real-time extensions
TRON
  Embedded OS specification in Japan
  Has multiple profiles for different classes of devices

## Slide 17: Common RTOS Features
Utilities
Bootstrapping support
“Headless” operation
  Display not necessary
APIs (Application Programming Interfaces)
Multiple threads and/or processes
  Fixed priority scheduling is most popular
Mutex/semaphore support likely with priority inheritance support
Inter-process communications
  Message queues
Timers/clock
Graphics support
Device drivers
Network protocol stack

## Slide 18: Emerging RTOS Requirements
Full-featured operating system
Support for new processors and devices
Support for Internet protocols and standards
Support for Multimedia protocols and standards
Support for File Systems
Memory protection
Resource protection, security
Development tools and libraries
GUI Environment
Do this with low and predictable overheads.

## Slide 19
CSE 466
Wireless Sensor Networks
<number>
Future??? Android Layer Cake