## Slide 1: Communication methods
CSE 466
Communication
<number>
Communication methods
  Media and signalling conventions used to transmit data between digital devices
  Different physical layers methods including:
    wires, radio frequency (RF), optical (IR)
  Different encoding schemes including:
    amplitude, frequency, and pulse-width modulation
Modulation Technique | Waveform
No encoding (Baseband) | 
On-Off Keying (OOK) | 
Frequency Shift Keying (FSK) | 
Binary Phase Shift Keying (BPSK) | 

## Slide 2: Communication methods
CSE 466
Communication
<number>
Dimensions to consider
  bandwidth – number of wires – serial/parallel
  speed – bits/bytes/words per second
  timing methodology – synchronous or asynchronous
  number of destinations/sources
  arbitration scheme – daisy-chain, centralized, distributed
  protocols – provide some guarantees as to correct communication

## Slide 3: Bandwidth
CSE 466
Communication
<number>
Serial
  Single wire or channel to trasmit information one bit at a time
  Requires synchronization between sender and receiver
  Sometimes includes extra wires for clock and/or handshaking
  Good for inexpensive connections (e.g., terminals)
  Good for long-distance connections (e.g., LANs)
  Examples: RS-232, Ethernet, I2C, IrDA, USB, Firewire, Bluetooth
Parallel
  Multiple wires to transmit information one byte or word at a time
  Good for high-bandwidth requirements (CPU to disk)
  More expensive wiring/connectors/current requirements
  Examples: SCSI-2, PCI bus (PC), PCMCIA (Compact Flash)
Issues
  Encoding, data transfer rates, cost of connectors and wires, modularity, error detection and/or correction

## Slide 4: Speed
CSE 466
Communication
<number>
Serial
  low-speed, cheap connections
    RS-232 1K–20K bits/sec, copper wire
  medium-speed efficient connections
    I2C 10K-400K bits/sec, board traces
    IrDA 9.6K-4M bits/sec, line-of-sight, 0.5-6.0m
  high-speed, expensive connections
    USB 1.5M bytes/sec, USB2 60M bytes/sec
    Ethernet 1.5M-1G bits/sec, twisted-pair or co-axial
    Firewire 12.5-50M bytes/sec
Parallel
  low-speed, not too wide
    SCSI-2 10M bytes/sec, 8 bits wide
    PCI bus, 250M bytes/sec, 32 bits wide
    PCMCIA (CF+), 9-10M bytes/sec, 16 bits wide
  high-speed, very wide – memory systems in large multi-processors
    200M-2G bytes/sec, 128-256 bits wide

## Slide 5: Speed
CSE 466
Communication
<number>
Issues
  length of the wires (attenuation, noise, capacitance)
  connectors (conductors and/or transducers)
  environment (RF/IR interference, noise)
  current switching (spikes on supply voltages)
  number and types of wires (cost of connectors, cross-talk)
  flow-control (if communicating device can’t keep up)

## Slide 6: Timing methodology
CSE 466
Communication
<number>
Asynchronous
  less wires (no clock)
  no skew concerns
  synchronization overhead
  appropriate for loosely-coupled systems (CPU and peripherals)
  common in serial schemes
Synchronous
  clock wires and skew concerns
  no synchronization overhead
  can be high-speed if delays are small and can be controlled
  appropriate for tightly-couple systems (CPU and memory/disk)
  common in parallel schemes

## Slide 7: Timing methodology
CSE 466
Communication
<number>
Issues
  clock period and wire delay
  synchronization and skew
  encoding of timing and data information
  handshaking
  flow-control
  power consumption

## Slide 8: Number of devices communicating
CSE 466
Communication
<number>
Single source – single destination
  point-to-point
  cheap connections, no tri-stating necessary
Single source – multiple destination
  fanout limitations
  addressing scheme to direct data to one destination
Multiple source – multiple destination
  arbitration between senders
  tri-stating capability is necessary
  collision detection
  addressing scheme
  priority scheme
  fairness considerations

## Slide 9: Arbitration schemes
CSE 466
Communication
<number>
Daisy-chain or token passing
  devices either act or pass to next
  fixed priority order
  as many wires as devices
  fairness issues
Centralized
  request to central arbiter
  central arbiter implements priority scheme
  wires from/to each device can be costly
  can be dynamically changing priority/fairness
Distributed
  no central arbiter
  common set of wires (or ether) observed by all devices
  fixed priority/fairness scheme

## Slide 10: Serial case studies
CSE 466
Communication
<number>
RS-232 (IEEE standard)
  serial protocol for point-to-point, low-cost, low-speed applications for PCs
I2C (Philips) TWI (Atmel)
  up to 400Kbits/sec, serial bus for connecting multiple components
Ethernet (popularized by Xerox)
  most popular local area network protocol with distributed arbitration
IrDA (Infrared Data Association)
  up to 115kbps wireless serial (Fast IrDA up to 4Mbs)
Firewire (Apple – now IEEE1394)
  12.5-50Mbytes/sec, consumer electronics (video cameras, TVs, audio, etc.)
SPI (Motorola)
  10Mbits/sec, commonly used for microcontroller to peripheral connections
USB (Intel – followed by USB-2)
  12-480Mbits/sec, isochronous transfer, desktop devices
Bluetooth (Ericsson – cable replacement)
  700Kbits/sec, multiple portable devices, special support for audio

## Slide 11: RS-232 (standard serial line)
CSE 466
Communication
<number>
Point-to-point, full-duplex
Synchronous or asynchronous
Flow control
Variable baud (bit) rates
Cheap connections (low-quality and few wires)
Variations: parity bit; 1, 1.5, or 2 stop bits
start bit
8 data bits
parity bit
stop bit

## Slide 12: RS-232 wires
CSE 466
Communication
<number>
all wires active low "0" = -12v, "1" = 12v
special driver chips that generate ±12v from 5v
TxD – transmit data
TxC – transmit clock
RTS – request to send
CTS – clear to send
RxD – receive data
RxC – receive clock
DSR – data set ready
DTR – data terminal ready
Ground

## Slide 13: Transfer modes
CSE 466
Communication
<number>
Synchronous
  clock signal wire is used by both receiver and sender to sample data
Asynchronous
  no clock signal in common
  data must be oversampled (16x is typical) to find bit boundaries
Flow control
  handshaking signals to control rate of transfer

## Slide 14: Inter-Integrated Circuit Bus (I2C)
CSE 466
Communication
<number>
+Vcc
device 1
device 2
device n
SCL
SDA
Modular connections on a printed circuit board
Multi-point connections (needs addressing)
Synchronous transfer (but adapts to slowest device)
Similar to Controller Area Network (CAN) protocol used in automotive applications
Similar to TWI (Two-Wire Interface) on ATmegas

## Slide 15: Serial data format
CSE 466
Communication
<number>
SDA
SCL
START
STOP
SDA going low while SCL high signals start of data
SDA going high while SCL high signals end of data
SDA can change when SCL low
SCL high (after start and before end) signals that a data bit can be read

## Slide 16: Byte transfer
CSE 466
Communication
<number>
SDA
SCL
1
3
4
5
6
7
8
ack
2
Byte followed by a 1 bit acknowledge from receiver
Open-collector wires
  sender allows SDA to rise
  receiver pulls low to acknowledge after 8 bits
Multi-byte transfers
  first byte contains address of receiver
  all devices check address to determine if following data is for them
  second byte usually contains address of sender

## Slide 17: Clock synchronization
CSE 466
Communication
<number>
clk 1
clk 2
SCL
Synchronous data transfer with variable speed devices
  go as fast as the slowest device involved in transfer
Each device looks at the SCL line as an input as well as driving it
  if clock stays low even when being driven high then another device needs more time, so wait for it to finish before continuing
  rising clock edges are synchronized

## Slide 18: Arbitration
CSE 466
Communication
<number>
Devices can start transmitting at any time
  wait until lines are both high for some minimum time
  multiple devices may start together - clocks will be synchronized
All senders will think they are sending data
  possibly slowed down by receiver (or another sender)
  each sender keeps watching SDA - if ever different (driving high, but its really low) then there is another driver
  sender that detects difference gets off the bus and aborts message
Device priority given to devices with early 0s in their address
  00….111 has higher priority than 01…111

## Slide 19: Inter-Integrated Circuit Bus (I2C)
CSE 466
Communication
<number>
Supports data transfers from 0 to 400KHz
Philips (and others) provide many devices
  microcontrollers with built-in interface
  A/D and D/A converters
  parallel I/O ports
  memory modules
  LCD drivers
  real-time clock/calendars
  DTMF decoders
  frequency synthesizers
  video/audio processors

## Slide 20: Ethernet (Xerox local area network)
CSE 466
Communication
<number>
Local area network
  up to 1024 stations
  up to 2.8 km distance
  10Mbits/sec serially on shielded co-axial cable
  1.5Mbits/sec on twisted pair of copper pair
Developed by Xerox in late 70s
  still most common LAN right now
  being displaced by fiber-optics (can't handle video/audio rates or make required service guarantees)
High-level protocols to ensure reliable data transmission
CSMA-CD: carrier sense multiple access with collision detection

## Slide 21: The ISO OSI Reference Model
<number>
Application
Data Link
Presentation
Network
Physical
Session
Transport
Physical Medium
Application
Data Link
Presentation
Network
Physical
Session
Transport
Host A
Host B
Notes: CHAPTER1
Sami S.Al-Wakeel
<number>

## Slide 22: The ISO OSI Reference Model
<number>
Application
Data Link
Presentation
Network
Physical
Session
Transport
Physical Medium
Application
Data Link
Presentation
Network
Physical
Session
Transport
Layer 7 Protocol
Layer 1 Protocol
Layer 2 Protocol
Layer 3 Protocol
Layer 4 Protocol
Layer 5 Protocol
Layer 6 Protocol
Layer 6/7 Interface
Layer 5/6 Interface
Layer 4/5 Interface
Layer 3/4 Interface
Layer 2/3 Interface
Layer 1/2 Interface
Host A
Host B
Notes: CHAPTER1
Sami S.Al-Wakeel
<number>

## Slide 23: The ISO OSI Reference Model
<number>
Interface: It defines which primitive operations and services the lower layer offers to the upper layer.
Peer: The similar layer on a different machine.
Protocol: It is a set of rules and conventions used by the layer to communicate with similar peer layer in another (remote) system.
The peer processes communicate with each other using a protocol.
A set of layers and protocols is called a network architecture.
Notes: CHAPTER1
Sami S.Al-Wakeel
<number>

## Slide 24: The ISO OSI Reference Model
<number>
In reality, no data are directly transferred from layer i on one machine to layer i on another machine. Instead, each layer passes data and control information to the layer immediately below it, until the lowest layer is reached. Below layer 1 is the physical medium through which actual communication occurs.
Send-To-Other-side ( )
Get-From-Other-side ( )
Protocol
(Virtual Communication)
Host A
Host B
Layer i
Layer i
Notes: CHAPTER1
Sami S.Al-Wakeel
<number>

## Slide 25: Ethernet layered organization
CSE 466
Communication
<number>
Transmit
and
Receive Electrical Interface
Serial
Encode
and
Decode
Link Management
Data
Encapsulation
Physical Channel
Data-link Controller
Ethernet Controller Board
Transceiver
Host-specific Interface
To Host
Ethernet Cable
Physical Layer
Data-link Layer
Transport Layer
Client Layer
parallel data
serial data
Physical and data-link layers are our focus

## Slide 26: Serial data format
CSE 466
Communication
<number>
0
1
0
1
0
0
1
1
0
Manchester encoding
  signal and clock on one wire (XORed together)
  "0" = low-going transition
  "1" = high-going transition
Extra transitions between 00 and 11 need to be filtered
  preamble at beginning of data packet contains alternating 1s and 0s
  allows receivers to get used to where important transitions should be and ignore extra ones (this is how synchronization is achieved)
  preamble is 48 bits long: 10101. . . 01011

## Slide 27: Ethernet packet
CSE 466
Communication
<number>
preamble (6 bytes)
destination address (6 bytes)
source address (6 bytes)
type (2 bytes)
data (46-1500 bytes)
checksum (4 bytes) compute from data
Packets size: 64 to 1518 bytes + 6 bytes of preamble

## Slide 28: Arbitration
CSE 466
Communication
<number>
Wait for line to be quiet for a while then transmit
  detect collision
  average value on wire should be exactly between 1 and 0
  if not, then two transmitters are trying to transmit data
If collision, stop transmitting
  wait a random amount of time and try again
  if collide again, pick a random number from a larger range (2x) and try again
Exponential backoff on collision detection
Try up to 16 times before reporting failure

## Slide 29: Extending Ethernet
CSE 466
Communication
<number>
Segments, repeaters, and gateways
  segment: a single cable
  repeater: transfers all messages on one segment to another and vice-versa
  gateway: selectively forwards messages to other segments and helps isolate traffic
  Segment
  Repeater
  Gateway

## Slide 30: Infrared Data Association
CSE 466
Communication
<number>
Consortium of over 160 companies
Meet needs of the “mobile professional”
  Short interactions with other devices (file transfer, printing)
  Possibly using others’ peripherals (visiting a customer’s office)
Goals:
  Suitable replacement for cables
  Interoperability
  Minimal cost
  “Point-and-shoot” model (intended use and to reduce interference)
History:
  First standard developed in 1994
  Revisions as recently as late 1998 (i.e., still active)

## Slide 31: IrDA: Infrared Data Association
CSE 466
Communication
<number>
Radio (RF)
Microwaves
Infrared (IR)
Visible
Ultraviolet
X-Rays
Gamma
Rays
FCC
$
109
1012
1014
1015
1017
1020
Freq.
(Hz)
Characteristics of IR:
  Implementation costs rise significantly around 1-10 GHz
    one important exception is IR at around 100 THz – very inexpensive
  Signals above 100 GHz cannot penetrate walls
  Most signals below 300 GHz are regulated by the FCC

## Slide 32: Speed
CSE 466
Communication
<number>
Components include:
  Transmitter (LED) and paired receiver (photodiode)
IrDA supports wide range of speeds
  2400 bps to 4 Mbps
  Exact physical-layer protocol used depends on speed of IrDA connection
  Uses highest speed available on both devices
    determined when connection is established
Future promises even higher speeds:
  16-50 Mbps is not too far off
Comparison to other wireless technologies:
  Low-power RF (e.g., Bluetooth) slightly slower (.5 - 2 Mbps max)
  Bound by walls, easy to control, intentional aspect
  Much lower-power than high-speed RF (e.g., 802.11a at 50Mbps)

## Slide 33: Low-speed Modulation
CSE 466
Communication
<number>
0
0
1
0
0
1
Speed: 2400 bps - 115 kbps (“Serial Infrared”, or SIR)
  Only 0’s require pulse (and thus power) ; pulse < full bit time
  Standard UART byte framing
  Pulse is constant 1.6 s long (so duty cycle varies with speed)
  Average duty cycle:  9%
Speed: 576 kbps - 1 Mbps
  similar to SIR (pulse only for 0’s ; pulse < full bit time)
  pulse lasts 1/4 of bit time (so pulse varies with speed)
  Average duty cycle: 12.5%
Speed: 4 Mbps (“Fast Infrared”, or FIR)
  uses four-pulse-position-modulation scheme (4PPM)
  pulse during exactly 1/4 of each symbol boundary
  4PPM makes synchronization easier to maintain
  Duty cycle: 25% (independent of data)
  Lowest power/bit
0
0
1
0
0
1
0
0
0
1
1
0
1
1

## Slide 34: Range
CSE 466
Communication
<number>
0 - 1 m
Linear:
  IrDA standard requires 0-1 m
  Realistically, some transceivers work at up to 10 m
Angular:
  Limited to a narrow cone (15 half-angle)
  Done to help reduce interference between devices

## Slide 35: IrDA Protocol Stack
CSE 466
Communication
<number>
Physical Layer
Data-link Layer
Network Layer
Transport Layer
Application Layer
Standard Network Model
IrDA Protocol Stack
Physical Layer
IrLAP
IrLMP
TinyTP
IrCOMM
IrLAN
IrOBEX
Analogous to the standard layered network model
Consists of both required and optional components
  Handle connections/disconnections
  Implement reliable transfer
Multiplexes several “virtual” connections on a single IrLAP connection (logical service access points – LSAPs)
Segmentation and re-assembly automatically break-up large packets (and put back together correctly)
Per-channel flow control
Serial and parallel port emulation
IrDA interface acts as a local-area network
IR “Object Exchange” – transfer of objects

## Slide 36: Protocol Overhead
CSE 466
Communication
<number>
Total: 5 bytes
Total: 58 bytes (minimum)
Very simple model (point-to-point), so can expect reduced protocol overhead
For layers in IrDA protocol stack, overhead per packet/frame is:
  IrLAP = 2 bytes
  IrLMP = 2 bytes
  TinyTP = 1 byte
For perspective, compare to TCP/IP over Ethernet:
  Ethernet = 18 bytes minimum
  IP = 20 bytes
  TCP = 20 bytes
IrDA takes advantage of its simpler model, and keeps protocol overhead very low.

## Slide 37: Firewire
CSE 466
Communication
<number>
Interconnection for high-bandwidth consumer electronic devices
  e.g., still and video cameras, MP3 players, digital video recorders
  IEEE 1394a standard
  12.5-400 Mbits/sec (800 Mbits/sec with 1394b)
    Most consumer devices use 100 Mbits/sec
  Up to 63 devices connected at once on 4.5m cables
    Up to 16 cables can be daisy-chained to 72m
  Devices connect for power as well as communication
  Hot-swappable devices
  Asynchronous and isochronous data transfers

## Slide 38: Firewire Electrical/Mechanical Spec
CSE 466
Communication
<number>
4-6 wires depending on whether device needs power
Tree arrangement
  each branch is bandwidth limited
Digital VCR
Digital Camcorder
Digital Camcorder
DV Monitor
PC with IEEE 1394
IEEE 1394 Hard Drive

## Slide 39: Firewire data format
CSE 466
Communication
<number>
Data is transferred in addressed packets, and is transaction-based
Transfers can be asynchronous or isochronous
  Asynchronous transfers are used mainly for bus configuration, setting up transfers and handshaking, but are also used for bulk data transfer to and from hard disk drives, etc.
  Isochronous transfers are used for transporting time-sensitive data like digital video and audio
Data packets have a 64-bit address header
  10-bit network address
  6-bit node address
  48 bits for data memory addresses at the receiving node
Ability to address 1023 networks of 63 nodes, each with up to 281TB (terabytes) of data addresses

## Slide 40: Firewire data format (cont’d)
CSE 466
Communication
<number>
Bus manager
  One device on the bus (usually a PC)
Isochronous resource manager
  Allocates bus bandwidth for isochronous data transfers based on time-domain multiplexing (TDM) that guarantees a proportion of the total time slots to each device
    Bandwidth allocation unit is 20.3ns, 6144 of them in a basic cycle of 125us
    25us of every cycle is always reserved for asynchronous control data transfers, so a maximum of 4195 units is available for isochronous transfers
    Typically a stream from a DV camcorder to a PC or digital VCR might need to be allocated a channel of ~1800 bandwidth units, for about 30Mb/s
  Asynchronous transfers can have multiple data packets per basic cycle, within the 25us reserved for this type of signalling

## Slide 41: Firewire signalling
CSE 466
Communication
<number>
Data-strobe signalling
  Avoids two signals where both change at the same time
  Keeps noise levels low
Strobe easily derived at transmitter
  Strobe = Clock xor Data
Clock is easily recovered at receiver
  Clock = Data xor Strobe
Data Strobe Clock
1 0 1 1 0 1 1

## Slide 42: Serial Peripheral Interface
CSE 466
Communication
<number>
Common serial interface on many microcontrollers
Simple 8-bit exchange between two devices
  Master initiates transfer and generates clock signal
  Slave device selected by master
One-byte at a time transfer
  Data protocols are defined by application
  Must be in agreement across devices

## Slide 43: SPI Block Diagram
CSE 466
Communication
<number>
8-bits transferred in each direction every time
Master generates clock
Shift enable used to select one of many slaves

## Slide 44: MSP430 USART (larger MSPs)

## Slide 45: SPI on the MS430 USART
CSE 466
Communication
<number>
Prescaler for clock rate
Interrupt on receive and on send complete
TXMT and RCV are separate registers

## Slide 46: MSP430F2013 USI

## Slide 47: Using SPI as a Master
CSE 466
Communication
<number>
// MSP430F20x2/3 Demo - SPI full-Duplex 3-wire Master
//
// Description: SPI Master communicates full-duplex with SPI Slave using
// 3-wire mode. The level on P1.4 is TX'ed and RX'ed to P1.0.
// Master will pulse slave reset for synch start.
// ACLK = n/a, MCLK = SMCLK = Default DCO
//
// Slave Master
// MSP430F20x2/3 MSP430F20x2/3
// ----------------- -----------------
// | XIN|- /|\| XIN|-
// | | | | |
// | XOUT|- --|RST XOUT|-
// | | /|\ | |
// | RST/NMI|--+<----|P1.2 |
// LED <-|P1.0 | | P1.4|<-
// ->|P1.4 | | P1.0|-> LED
// | SDI/P1.7|<-------|P1.6/SDO |
// | SDO/P1.6|------->|P1.7/SDI |
// | SCLK/P1.5|<-------|P1.5/SCLK |
//

## Slide 48: Using SPI as a Master
CSE 466
Communication
<number>
#include <msp430x20x3.h>
void main(void)
{
volatile unsigned int i;
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer
P1OUT = 0x10; // P1.4 set, else reset
P1REN |= 0x10; // P1.4 pullup
P1DIR = 0x01; // P1.0 output, else input
USICTL0 |= USIPE7 + USIPE6 + USIPE5 + USIMST + USIOE; // Port, SPI master
USICTL1 |= USIIE; // Counter interrupt, flag remains set
USICKCTL = USIDIV_4 + USISSEL_2; // /16 SMCLK
USICTL0 &= ~USISWRST; // USI released for operation
USISRL = P1IN; // init-load data
P1DIR |= 0x04; // Reset Slave
P1DIR &= ~0x04;
for (i = 0xFFF; i > 0; i--); // Time for slave to ready
USICNT = 8; // init-load counter
_BIS_SR(LPM0_bits + GIE); // Enter LPM0 w/ interrupt
}
// USI interrupt service routine
#pragma vector=USI_VECTOR
__interrupt void universal_serial_interface(void)
{
if (0x10 & USISRL)
P1OUT |= 0x01;
else
P1OUT &= ~0x01;
USISRL = P1IN;
USICNT = 8; // re-load counter
}

## Slide 49: Using SPI as a Slave
CSE 466
Communication
<number>
#include <msp430x20x3.h>
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer
P1OUT = 0x10; // P1.4 set, else reset
P1REN |= 0x10; // P1.4 pullup
P1DIR = 0x01; // P1.0 output, else input
USICTL0 |= USIPE7 + USIPE6 + USIPE5 + USIOE; // Port, SPI slave
USICTL1 |= USIIE; // Counter interrupt, flag remains set
USICTL0 &= ~USISWRST; // USI released for operation
USISRL = P1IN; // init-load data
USICNT = 8; // init-load counter
_BIS_SR(LPM0_bits + GIE); // Enter LPM0 w/ interrupt
}
// USI interrupt service routine
#pragma vector=USI_VECTOR
__interrupt void universal_serial_interface(void)
{
if (0x10 & USISRL)
P1OUT |= 0x01;
else
P1OUT &= ~0x01;
USISRL = P1IN;
USICNT = 8; // re-load counter
}

## Slide 50: Data Payload on SPI
CSE 466
Communication
<number>
Data is exchanged between master and slave
  Master always initiates
  May need to poll slave (or interrupt-driven)
Decide on how many bytes of data have to move in each direction
  Transfer the maximum for both directions
  One side may get more than it needs
Decide on format of bytes in packet
  Starting byte and/or ending byte?
  Can they be distinguished from data in payload?
  Length information or fixed size?
SPI buffer
  Write into buffer, specify length, master sends it out, gets data
  New data arrives at slave, slave interrupted, provides data to go to master, reads data from master in buffer

## Slide 51: Universal Serial Bus
CSE 466
Communication
<number>
Connecting peripherals to PCs
  Ease-of-use
  Low-cost
  Up to 127 devices (optionally powered through bus)
  Transfer rates up to 480 Mb/s
    Variable speeds and packet sizes
    Full support for real-time data for voice, audio, and video
    Protocol flexibility for mixed-mode isochronous data transfers and asynchronous messaging
  PC manages bus and allocates slots (host controller)
    Can have multiple host controllers on one PC
    Support more devices than 127

## Slide 52: USB Peripherals
CSE 466
Communication
<number>

## Slide 53: USB
CSE 466
Communication
<number>
Tree of devices – one root controller

## Slide 54: USB Data Transfer
CSE 466
Communication
<number>
Data transfer speeds
  Low is <0.8v, high is >2.0v differential
  480Mb/sec, 12Mb/sec, 1.5Mb/sec
  Data is NRZI encoded (data and clock on one wire)
  SYNC at beginning of every packet

## Slide 55: NRZI Encoding
CSE 466
Communication
<number>
NRZI – Non-return to zero inverted
  Toggles a signal to transmit a “0” and leaves the signal unchanged for a “1”
  Also called transition encoding
  Long string of 0s generates a regular waveform with a frequency half the bit rate
  Long string of 1s generates a flat waveform – bit stuff a 0 every 6 consecutive 1s to guarantee activity on waveform

## Slide 56: NRZI Encoding (cont’d)
CSE 466
Communication
<number>

## Slide 57: USB Data Transfer Types
CSE 466
Communication
<number>
Control Transfers:
  Used to configure a device at attach time and can be used for other device-specific purposes, including control of other pipes on the device.
Bulk Data Transfers:
  Generated or consumed in relatively large and bursty quantities and have wide dynamic latitude in transmission constraints.
Interrupt Data Transfers:
  Used for timely but reliable delivery of data, for example, characters or coordinates with human-perceptible echo or feedback response characteristics.
Isochronous Data Transfers:
  Occupy a prenegotiated amount of USB bandwidth with a prenegotiated delivery latency. (Also called streaming real time transfers)

## Slide 58: USB Packet Format
CSE 466
Communication
<number>
Sync + PID + data + CRC
Basic data packet
  Sync: 8 bits (00000001)
  PID: 8 bits (packet id – type)
  Data: 8-8192 bits (1K bytes)
  CRC: 16 bits (cyclic redundancy check sum)
Other data packets vary in size
  May be as short as only 8 bits of PID

## Slide 59: USB Protocol Stack
CSE 466
Communication
<number>
FTDI USB chip implements right side
Communicates to physical device through SPI

## Slide 60: More Communication Later
CSE 466
Communication
<number>
Bluetooth
  Popular radio frequency protocol
  We’ll discuss after looking at wireless sensors
PCMCIA/CompactFlash
  Popular parallel bus protocol
  We’ll discuss (time permitting) at end of quarter