## Slide 1: Basics of Feedback Control
Lecture 21

## Slide 2: Summary of Previous Lecture
Basics of A/D and D/A converters
Fundamentals of sampling
  Why and how often?
  Aliasing effects
Example A/D and D/A converters
Drift and Jitter
Examining code snippets for potential drift and jitter

## Slide 3: Announcements
Lab #4 due tonight
Lab #5 out tonight
  Please plan your time carefully
  Requires building parts of an embedded operating system to run on the X-Board

## Slide 4: Outline of This Lecture
The Feedback Control Problem
Proportional Control
Derivative Control
Integral Control

## Slide 5: Feedback Control – Why Should You Care?
Happens in everyday life, even in our 18-349 lectures
Remember the “howling” we hear when we sometimes have the microphones on for our videoconferencing?
Microphone Amplifier  Speaker  Microphone
This loop happens so fast that it generates its own frequency
Microphone-to-speaker distance dictates the frequency
  Decides how quickly sound “feedback” occurs through the system
This feedback problem happens in public address systems

## Slide 6: Want To Try This Out Yourself?
Attach a set of speakers to your computer
“Un-mute” and set microphone and speakers to maximum volume
Tap microphone and hear it in the speakers
Place speakers near microphone, turn up the volume and hear feedback
Change distance between microphone and speakers to see the effect
Caution: Not to be used as revenge on instructors, labmates, etc.

## Slide 7: Feedback in Embedded Systems
Many real-time embedded systems make control decisions
These decisions are usually made by software and based on feedback from the hardware under its control (termed the plant)
Such feedback commonly takes the form of an analog sensor that can be read via an A/D converter
A sample from the sensor might represent position, voltage, temperature, or any other appropriate parameter
Each sample provides the software with additional information upon which to base its control decisions

## Slide 8: Closed-Loop vs. Open-Loop
Open-loop systems doesn’t necessarily use feedback
Closed-loop systems use feedback
After reading each new sample from the sensor
  Software reacts to the plant's changed state by recalculating and adjusting the drive signal
  Plant responds to this change, another sample is taken, and the cycle repeats
Eventually, the plant should reach the desired state and the software will cease making changes

## Slide 9: On-Off Control – Your Thermostat
How much should the software increase or decrease the drive signal?
  Set the drive signal to its minimum value when you want the thermostat to decrease its temperature
  Set the drive signal to its maximum value when you want the thermostat to increase its temperature

## Slide 10: Proportional Control
If the difference between the current output and its desired value (the current error) is large
  Software should probably change the drive signal a lot
If the error/difference is small
  Software should change drive signal only a little
We want the change to look like this
  K * (desired – current)
  K called the proportional gain
If K is well chosen
  Time taken to reach a new setpoint will be as short as possible, with overshoot (or undershoot) and oscillation minimized
Is there a problem here?

## Slide 11: Proportional-Derivative (PD) Control
Problems with Proportional Control
  You want to reach the desired value quickly (higher K)
  You want to settle down once you’re near the desired value (low K)
We have (or can discover) information about the rate of change of the plant's output
  Rate of change of a signal = its derivative
  If output is changing rapidly, overshoot/undershoot may lie ahead
We can then reduce the size of the change suggested by the proportional controller
  Subtract a derivative-based term from the proportional term
PD Controllers
  Slower response time and far less overshoot and ripple than proportional controller

## Slide 12: Proportional-Integral-Derivative (PID) Control
Problems with PD Control
  Change in drive signal triggered by error = difference in desired and current values of output
  Derivative only tells you how two consecutive output values differ
  What if the error is not sufficient to trigger any action?
Something else needs to drive the plant toward the setpoint
Integral term
  Sum of all past errors in the plant output
  A persistent error will eventually cause the sum to grow large
  The integral term then forces a change in the drive signal
Proportional, Integral and Derivative combination = PID

## Slide 13: A Simple System with Proportional Control
Consider a marble on a flat and perfectly level table.
  Any point can be an equilibrium point (just pick one)
  Motion can be described by Newton’ s law F = ma, or x’’ = F/m
  Suppose that we want to keep the marble at x = 0,
    By applying proportional control: F = -Kp x.
  The feedback is negative since if the marble position error is negative, it pushes with a positive force and vice versa.
  Kp is a positive integer known as proportional control constant.
F = -Kpx
x
acceleration

## Slide 14: Concepts of Stability
The objective of controlling the marble is to put it at rest at the origin (set point). i.e. X = 0, and x’ = 0, from any initial condition. Or for that matter, after the marble was disturbed by some force.
  This intuition is formalized as the notion of stability
  Or more precisely, asymptotic stability, i.e. the errors will converge to zero over time.
The opposite of stability is instability, meaning that the error will grow larger and larger without bound.
  That is, the marble will leave the origin for good.
In-between is marginal stability, the errors stay within some bound.

## Slide 15: Cartoon Laws of Physics
Any body passing through solid matter will leave a perforation conforming to its perimeter
Any body suspended in space will remain in space until made aware of its situation
Certain bodies can pass through solid walls painted to resemble tunnel entrances; others cannot
For every vengeance there is an equal and opposite “revengeance”

## Slide 16: Review
From your calculus courses, we know that the solution of Linear Partial Differential Equations is a sum of exponentials:
  y(t) = c1exp(1t) + c2exp(2t) + ....
  Exponents 1 , 1 ... are known as eigenvalues of the system.
  Eigenvalues can be complex, e.g., exp(Re(l) t)*exp(Im(l) jt)
Solving LPDEs using the Laplace Transform
  3*y’’ + 4*y’ + 5*y = 0 (replace nth derivative with sn )
  3s2 + 4s + 5 = 0
  Solve for s and you will get the eigenvalues

## Slide 17: Stability and Eigenvalues
What is the relationship between
  The magnitude of eigenvalues and
  The notion of (asymptotic) stability, marginal stability and instability?
Stability
  All real parts are negative
Instability
  At least one eigenvalue’s real part is greater than zero.
Marginal stability
  None greater than zero but some eigenvalues equal to zero.

## Slide 18: Back To The Marbles
Now, let us analyze the stability of our marble under proportional control.
From Newton’s law, we have F = m x’’
From proportional control, we have F = -Kp x
Hence, we have mx’’ = -Kpx, with m > 0 and Kp > 0,
  s = ______________
The marble under proportional control is
  Stable?
  Unstable?
  Marginally stable?
Why?

## Slide 19: Marble under Proportional Control
The system trajectories can be obtained by solving the differential equations by using Laplace transform
    L(x”) = s2 , L(x’) = s, L(x) = 1
Let’s start with x’’ = (-Kp/m) x 
    x’’ + (Kp/m) x = 0
    Apply Laplace transforms
    s2 + Kp /m = 0
    s = +/- j sqrt(Kp /m) are the eigenvalues
As you might have guessed, the marble will oscillate with frequency
     = sqrt(Kp /m) radians/sec
System is marginally stable since real part of eigenvalue is zero

## Slide 20: Marble Under P + D control
F = m x’’ // where m is the mass of the marble
F = -Kpx // proportional control
F = -Kpx - Kdx’ // proportional + derivative control
mx’’ + Kdx’ + Kpx = 0 // putting it together
ms2 +Kds + Kp = 0 // applying Laplace transforms
s = (-Kd ± sqrt(Kd2 - 4mKp)) / 2m
m > 0, Kp > 0 and Kd > 0
Is this system stable? Why?
  Since sqrt(Kd2 - 4m*Kp) < Kd, the real part of s is always < 0
  It follows that the system is stable.

## Slide 21: Intuition
When the position error x is positive, the proportional control force is negative.
  It pushes the marble back to the origin (setpoint) at 0.
  What will be the force and the speed when marble reaches the origin if we use only proportional control?
When the marble is moving towards the setpoint, the velocity is negative. So the force due to derivative control -Kdx’ is positive.
  This counters the proportional force and slows down the marble’ s motion towards the origin.
Proportional control is like your car’s gas pedal
  Moves the car towards the setpoint (a chosen origin)
Derivative control is like your brake

## Slide 22: Tuning a Simple PD Controller - I
Experimental tuning procedure
  First set the derivative gain to zero
  Slowly increase the proportional gain until the device oscillates around the set point with a speed that is satisfactory
    At this point, the real part of the eigenvalue is _________
    The imaginary part of the eigenvalue determines the __________ of oscillation
  Slowly increase the derivative gain until the device settles down at the setpoint
    At this point, the real part of the eigenvalue is ________

## Slide 23: Tuning a Simple PD Controller - II
Fine-tuning
  If the motion towards the setpoint is too slow, we can __________ the proportional gain or ___________ the derivative gain
  If the motion overshoots the setpoint too much, we can __________ the derivative gain or __________ the proportional gain
Avoid using too large a proportional gain and too large a derivative gain at the same time
  This will saturate the actuator
  It is like slamming on your gas pedal and the brake together

## Slide 24: Integral Control
A system often has friction or changing workloads that you may not be able to model in advance
In auto-cruise control, we cannot know how many passengers will be in the car
Friction may change due to machine conditions (worn-out tires, loss of engine conditioning)
Unmodeled heavy load often results in steady-state error, the system will settle “near”, rather than at, the setpoint

## Slide 25: What Does Integral Control Do?
Integral control adds up (integrates) the past errors and then adds a force that is proportional to the cumulative errors
If the marble gets stuck near a setpoint due to some friction
  The position error adds up over time
  This eventually generates a force large enough to help get the marble going
If the car has a heavier load and the velocity settles at a value lower than the setpoint for a while
  The error adds up and
  The integral control leads to increased throttle

## Slide 26: The Dark Side of Integral Control
Integral control acts on cumulative errors
  It takes a while to reach a large sum
  It will also take time to reduce the sum
Consider the following case
  The marble gets stuck on the left side of the set-point
  After 10 sec, the integral control is large enough to help get the marble moving
  The integral will keep increasing until the marble crosses the origin
  It will take a while to “wash out” the cumulative error
An overdose of integral control is a common source of overshoot, oscillation and even instability.
  What can you do to offset this?

## Slide 27: Using Integral Control
As a rule of thumb, start from zero and use it lightly
Check the eigenvalue of the system to make sure all of them are sufficiently negative.
  X’’ = F/m, where F = -Kp x - Kd x’ - Ki*x
  s2 + (Kd/m) s + Kp/m + (Ki/m) 1/s = 0 (because Laplace transform of integral is 1/s)
  s3 + Kd/m s2 + Kp/m s + Ki/m = 0
Effect of integral is to add an order to the system. A large value of Ki will lead to a positive eigenvalue (bad!)
We can solve the equation to see if the real part of the eigenvalues are still negative (Best done using MATLAB)

## Slide 28: How to Tune a Simple PID Controller
Experimental tuning procedure
First set derivative gain and integral gains to zero.
Slowly increase the proportional gain until the device oscillates around the set point with a speed that is satisfactory.
  At this point, the real part of the eigenvalue is _________
  Imaginary part of the eigenvalue determines the __________ of oscillation
Slowly increase the derivative gain until the device settles down at the setpoint
  At this point, the real part of the eigenvalue is ____________
If there is a steady-state error, slightly increase the integral gain until the steady state error is corrected and yet does not cause serious oscillation.
  This means that the real part of the eigenvalues are still _______

## Slide 29: How to Tune a Simple PID Controller
Fine-tuning
  If the motion towards the setpoint is too slow
    We can __________ proportional gain or ___________ derivative gain
    Do not play with integral gain
  If there is a steady-state error
    We can add a little __________ gain
  If the motion overshoots the setpoint and oscillates
    We can __________ the derivative gain or
    We can reduce __________ gain and __________ gain

## Slide 30: Basic Simulation Diagram Concepts
Mass is a double-integrator with weight 1/m, which transforms
force to acceleration, acceleration to velocity, and then velocity to position.
(1/s denotes integration)
Proportional Control of Marble

## Slide 31: Marble Under PID Control

## Slide 32: Cruise Control – PID In Action
Cruise control controls the speed of the car by adjusting the throttle position (throttle valve controls engine power and speed)
Good cruise control system would accelerate aggressively to the desired speed without overshooting, and then maintain that speed with little deviation, even if you go over a hill
Proportional control
  Difference in ideal and current speeds dictates proportional control
  Cruise control set at 60mph; car traveling at 50mph has twice the throttle opening than when it gets to 55mph
Integral control (time integral of speed is distance)
  Helps the car deal with hills, and settle into the correct speed
  If car goes up a hill, proportional control helps, but may still slow the car down; the longer the car stays at a slower speed, the more the integral control, and therefore the throttle opening increases
Derivative control (time derivative of speed is acceleration)
  Helps to respond quickly to changes, such as hills
  If speeds changes, cruise control can sense this acceleration even before speed changes too much, and increases throttle opening

## Slide 33: Summary of Lecture
Feedback control
  stability
  instability
  marginal stability
Feedback controllers
  proportional control
  proportional + derivative control
  proportional + derivative + integral control
Simulation diagram concepts