## Slide 1
CSE 466
<number>
As the tines move back and forth they exert pressure on the air around them.
(a) The first displacement of the tine compresses the air molecules causing high
pressure.
(b) Equal displacement of the tine in the opposite direction forces the molecules to
widely disperse themselves and so, causes low pressure.
(c) These rapid variations in pressure over time form a pattern which propogates
itself through the air as a wave. Points of high and low pressure are sometimes
reffered to as ’compression’ and ’rarefaction’ respectively.
What is Sound?
(a) compression
(b) rarefaction
(c) wave propagation of a tuning fork
as seen from above
Notes: <number>

## Slide 2
CSE 466
<number>
When a pendulum approaches equlibrium it doesn’t slow down;
it simply travels a smaller distance from the point of rest.
Any body undergoing simple harmonic motion moves periodically
with uniform speed.
If the tuning fork is moving periodically
then the pressure variations it creates will also be periodic.
Maximum displacement
at 0 seconds
Maximum displacement
after say, 3 seconds
Maximum displacement
after say, 6 seconds
a
b
a
a
b
b
The time taken to get from position a to b in all three cases is the same
Simple Harmonic Motion -- a Pendulum
Notes: <number>

## Slide 3
CSE 466
<number>
The Unit Circle
These pressure patterns can be represented using as a circle.
Imagine the journey of the pendulum or the tine in four stages:
1) from its point of rest to its first point of maximum displacement...
2) its first point of maximum displacement back through the point of rest...
3) ... to its second point of maximum displacement...
4) ... and back from there through its point of rest again
We can map that journey to a circle. This is called the Unit Circle. The sine wave
represents this journey around and around the unit circle over time.
1
2
3
4
Time
Notes: <number>

## Slide 4
CSE 466
<number>
The sine wave or sinusoid or sinusoidal signal is probably the most commonly used graphic representation of sound waves.
Pressure or density
of air molecules;
’Amplitude’ in
deciBels
0
+ 1
-1
Time in seconds
1
0.5
high pressure
or ’compression’
low pressure
or ’rarefaction’
Sine Waves
Notes: <number>

## Slide 5
CSE 466
<number>
1 second
Frequency = the number of cycles per second (this wave has a frequency of 6 hertz)
Amplitude = variations in air pressure (measured in decibels)
Phase = The starting point of a wave along the y-axis (measured in degrees)
The specific properties of a sine wave are described as follows.
Sine Waves
Wavelength = physical length of 1 period of a wave (measured in metres per second)
Notes: <number>

## Slide 6
CSE 466
<number>
Frequency
Frequency refers to the number of cycles of a wave per second. This is measured in Hertz. So if a sinusoid has a frequency of 100hz then one period of that wave repeats itself every 1/100th of a second. Humans can hear frequencies between 20hz and 20,000hz (20Khz).
Frequency is closely related to, but not the same as!!!, pitch.
2) Frequency does not determine the speed a wave travels at. Sound waves travel at approximately 340metres/second regardless of frequency.
3) Frequency is inherent to, and determined by the vibrating body – not the amount of energy used to set that body vibrating. For example, the tuning fork emits the same frequency regardless of how hard we strike it.
(a) 800hz
(b) 100hz
Notes: <number>

## Slide 7
CSE 466
<number>
Amplitude
Amplitude describes the size of the pressure variations.
Amplitude is measured along the vertical y-axis.
Amplitude is closely related to but not the same as!!!, loudness.
(a) Two signals of equal frequency and
varying amplitude
(b) Two signals of varying frequency and
equal amplitude
Notes: <number>

## Slide 8
CSE 466
<number>
Amplitude Envelope
Attack
Decay
Sustain
Release
The amplitude of a wave changes or ’decays’ over time as it loses energy.
These changes are normally broken down into four stages;
Attack , Decay, Sustain and Release.
Collectively, the four stages are described as the amplitude envelope.
100
200
400
300
500
600
700
0
0.2
0.4
0.6
0.8
Notes: <number>

## Slide 9: Quantization
CSE 466
<number>
  The digital signal is defined only at the points at which it is sampled.
Notes: <number>

## Slide 10: Quantization
CSE 466
<number>
  The height of each vertical bar can take on only certain values, shown by horizontal dashed lines, which are sometimes higher and sometimes lower than the original signal, indicated by the dashed curve.
Notes: <number>

## Slide 11: Quantization
CSE 466
<number>
  The difference between a quantized representation and an original analog signal is called the quantization noise.
  The more bits for quantization of a signal, the more closely the original signal is reproduced.
Notes: <number>

## Slide 12: Quantization
CSE 466
<number>
  Using higher sampling frequency and more bits for quantization will produce better quality digital audio.
  But for the same length of audio, the file size will be much larger than the low quality signal.
Notes: <number>

## Slide 13: Quantization
CSE 466
<number>
The number of bits available to describe sampling values determines the resolution or accuracy of quantization.
For example, if you have 8-bit analog to digital converters, the varying analog voltage must be quantized to 1 of 256 discrete values;
a 16-bit converter has 65,536 values.
Notes: <number>

## Slide 14: Nyquist Theorem
CSE 466
<number>
A theorem which states that an analog signal waveform may be uniquely reconstructed, without error, from samples taken at equal time intervals.
Notes: <number>

## Slide 15: Nyquist Theorem
CSE 466
<number>
The sampling rate must be equal to, or greater than, twice the highest frequency component in the analog signal.
Notes: <number>

## Slide 16: Nyquist Theorem
CSE 466
<number>
Stated differently:
The highest frequency which can be accurately represented is one-half of the sampling rate.
Notes: <number>

## Slide 17: Error
CSE 466
<number>
Sampling an analog signal can introduce ERROR.
ERROR is the difference between a computed, estimated, or measured value and the true, specified, or theoretically correct value.
Notes: <number>

## Slide 18: Nyquist Theorem
CSE 466
<number>
By sampling at TWICE the highest frequency:
  One number can describe the positive transition, and…
  One number can describe the negative transition of a single cycle.
Notes: <number>

## Slide 19: upper => sampling 6 times per cycle(fs=6f); middle => sampling 3 times per cycle(fs=3f); lower=> sampling 6 times in 5 cycles
CSE 466
<number>
Nyquist Error-- aliasing
Notes: <number>

## Slide 20: Digital Synthesis Overview
CSE 466
<number>
Sound is created by manipulating numbers, converting those numbers to an electrical current, and amplifying result.
Numerical manipulations are the same whether they are done with software or hardware.
Same capabilities (components) as analog synthesis, plus significant new abilities
Notes: <number>

## Slide 21: Digital Oscillators
CSE 466
<number>
Everything is a Table
  A table is an indexed list of elements (or values)
  The index is the address used to find a value
Notes: <number>

## Slide 22: Generate a Sine Tone Digitally (1)
CSE 466
<number>
Compute the sine in real time, every time it is needed.
  equation:
  t = a point in time; r = the radius, or amplitude of the signal;
  w (omega) = 2pi*f the frequency
  Advantages: It’s the perfect sine tone. Every value that you need will be the exact value from the unit circle.
  Disadvantages: must generate every sample of every oscillator present in a synthesis patch from an algorithm. This is very expensive computationally, and most of the calculation is redundant.
Notes: <number>
t = a point in time; r = the radius, or amplitude of the signal; w (omega) = 2pi*f the frequency

## Slide 23: Generate a Sine Tone Digitally (2)
CSE 466
<number>
Compute the sine tone once, store it in a table, and have all oscillators look in the table for needed values.
  Advantages: Much more efficient, hence faster, for the computer. You are not, literally, re-inventing the wheel every time.
  Disadvantages: Table values are discrete points in time. Most times you will need a value that falls somewhere in between two already computed values.
Notes: <number>

## Slide 24: Table Lookup Synthesis
CSE 466
<number>
Sound waves are very repetitive.
For an oscillator, compute and store one cycle (period) of a waveform.
Read through the wavetable repeatedly to generate a periodic sound.
Notes: <number>
Example:
  Wavetable with 100 values for one period.
  If sampling rate is 100 Hz (playback 100 samples every second), resulting frequency is 1 Hz (freq = sampF/tableL )
  If sampling rate is 200 Hz (playback 200 samples/s), resulting frequency is 2 Hz.
  SR = tableL x freq. 440 Hz x 100 = 44000
  Audio example from MSP (with buffer~)

## Slide 25: Changing Frequency
CSE 466
<number>
The Sample Rate doesn’t change within a synthesis algorithm.
You can change the speed that the table is scanned by skipping samples.
skip size is the increment, better known as the phase increment. ***phase increment is a very important concept***
Notes: <number>

## Slide 26: Algorithm for a Digital Oscillator
CSE 466
<number>
Basic, two-step program:
  phase_index = modL(previous_phase + increment)
  output = amplitude x wavetable[phase_index]
increment = (TableLength x DesiredFrequency)
SampleRate
Notes: <number>

## Slide 27: If You’re Wrong, it’s Noise
CSE 466
<number>
What happens when the phase increment doesn’t land exactly at an index location in the table?
  It simply looks at the last index location passed for a value. In other words, the phase increment is truncated to the integer.
Quantization
Noise
The greater the error, the more the noise.
Notes: <number>
512 - 440 - 44100 gives 5.1 blah.
If I give you six questions on a quiz, I can’t ask for question 5.1.

## Slide 28: Interpolation
CSE 466
<number>
Rather than truncate the phase location…
  look at the values stored before and after the calculated phase location
  calculate what the value would have been at the calculated phase location if it had been generated and stored. Interpolate
More calculations, but a much cleaner signal.
Notes: <number>

## Slide 29: Linear interpolation
CSE 466
<number>
Interpolate between two audio samples
More accurate, yet still efficient
double inbetween = fmod(sample, 1);
return (1. – inbetween) * wave[int(sample)] +
inbetween * wave[int(sample) + 1];
1021
1022
1021.35
Notes: <number>

## Slide 30: Envelopes
CSE 466
<number>
We commonly will make samples with fixed amplitudes, then make a synthetic envelope for the sound event.
Notes: <number>

## Slide 31: Attack and Release
CSE 466
<number>
Time
Amplitude
Attack
Release
Notes: <number>

## Slide 32: ADSR
CSE 466
<number>
ADSR: Attack, decay, sustain, release
Amplitude
Attack
Decay
Sustain
Release
Sustain level
Notes: <number>

## Slide 33: Frequency Modulation
CSE 466
<number>
Notes: <number>

## Slide 34: FM: General Description
CSE 466
<number>
Simple FM: carrier oscillator has its frequency modulated by the output of a modulating oscillator.
Sidebands produced around carrier at multiples of modulating frequency.
  Number generated depends on the amplitude of the modulator.
Notes: <number>
  Both are technically angle modulation.
  Slight spectrum differences, but no real musical difference
  Output equals amplitude
Sum and difference on the modulating frequency and multiples

## Slide 35: Modulator : Carrier Ratio
CSE 466
<number>
Sidebands at C + and - (n * Modulator)
Ratio of M:C determines whether spectrum is harmonic or not.
  Simple integer ratio = harmonic
  Non-integer ratio = inharmonic
Notes: <number>
N = multiples of the modulator frequency
Example
Literature usually describes C:M, I learned M:C

## Slide 36: Modulation Index and Bandwidth
CSE 466
<number>
The bandwidth of the FM spectrum is the number of sidebands present.
The bandwidth is determined by the Modulation Index
  I = depth of modulation / modulator
  D depth of modulation, which depends on the amount of amplitude applied to modulating oscillator. (D = A x M)
If the index is above zero, then sidebands occur.
Notes: <number>
Index of Modulation
Depth of Modulation depends on the amount of amplitude applied to modulating
Amplitude applied to modulator is on the order several thousand, usually scaled by an amplitude envelope at a later point with the typical range of 0. — 1. (although it is not necesssary to restrict yourself to this scale)

## Slide 37: FM Voices
CSE 466
<number>
Case 1: if ƒc is equal to any integer and ƒm is equal to 1, 2, 3 or 4, then the resulting timbre will have a distinctive pitch, because the offset carrier frequency will always be prominent.
Case 2: if ƒc is equal to any integer and ƒm is equal to any integer higher than 4, then the modulation produces harmonic partials but the fundamental may not be prominent.
Case 3: if ƒc is equal to any integer and ƒm is equal to 1, then the modulation produces a spectrum composed of harmonic partials; e.g. the ratio 1:1 produces a sawtooth-like wave.
Case 4: if ƒc is equal to any integer and ƒm is equal to any even number, then the modulation produces a spectrum with some combination of odd harmonic partials; e.g. the ratio 2:1 produces a square-like wave.
Case 5: if ƒc is equal to any integer and ƒm is equal to 3, then every third harmonic partial of the spectrum will be missing; e.g. the ratio 3:1 produces narrow pulse -like waves.
Case 6: if ƒc is equal to any integer and ƒm is not equal to an integer, then the modulation produces non-harmonic partials; e.g. 2:1.29 produces a "metallic" bell sound
Notes: <number>

## Slide 38: FM examples
CSE 466
<number>
Gong:
Bells:
Notes: <number>

## Slide 39: What we’re going to do:
CSE 466
<number>
This week:
  Talk to the sound driver
  Play sound sample files
  Build a table-driven oscillator
Next week:
  Connect your Chronos via RF dongle
  Control sine generator as a Theremin
Notes: <number>