## Slide 1: Resource Management in (Embedded) Real-Time Systems - II
Lecture 18

## Slide 2: Summary of Previous Lecture
Introduction to Real-Time Systems
  Terminology
  Example Categories
  Metrics
  Scheduling Policies

## Slide 3: Thought For the Day
You will become as small as your controlling desire, as great as your dominant aspiration.
  James Allen

## Slide 4: Rate Monotonic Scheduling (RMS)
Priorities of periodic tasks are based on their rates: highest rate gets highest priority.
Theoretical basis
  optimal fixed scheduling policy (when deadlines are at end of period)
  analytic formulas to check schedulability
Must distinguish between scheduling and analysis
  rate monotonic scheduling forms the basis for rate monotonic analysis
  however, we consider later how to analyze systems in which rate monotonic scheduling is not used
  any scheduling approach may be used, but all real-time systems should be analyzed for timing
Notes: <number>
<footer>
<header>
<date/time>
7
In 1973, Liu and Leyland published a paper called “ Scheduling Algorithms for Multiprogrammimg in a Hard-Real-Time Environment.” In this paper, they introduce the rate monotonic scheduling (RMS) algorithm. The RMS algorithm is an optimal static-priority scheduling algorithm, which gives higher priority to tasks with shorter periods (in other words, higher priority to tasks with higher frequencies, or rates).
It is important to emphasize that tasks are assigned priorities based strictly on their periods. Semantic importance does not play a role in priority assignment.
The algorithm is optimal in the sense that a task set that cannot meet its deadlines with a rate monotonic priority assignment will not be able to be scheduled with any fixed-priority assignment.
The original 1973 work on rate monotonic scheduling theory assumed that RMS was used and all tasks were periodic and non-interacting. Given these assumptions, a simple formula could be used to check for task schedulability, i.e. if each task is guaranteed to meet all its deadlines.
It is important to distinguish between rate monotonic scheduling (RMS) and rate monotonic analysis (RMA). Although the analysis approach has grown out of RMS theory, RMA can be done on a system even if RMS is not the scheduling approach used

## Slide 5: Rate Monotonic Analysis (RMA)
Rate-monotonic analysis is a set of mathematical techniques for analyzing sets of real-time tasks.
Basic theory applies only to independent, periodic tasks, but has been extended to address
  priority inversion
  task interactions
  aperiodic tasks
Focus is on RMA, not RMS
Notes: <number>
<footer>
<header>
<date/time>
8
RMA is a mathematical approach for analyzing real-time tasks to determine their schedulability. Again, the original theory was only able to analyze independent, periodic tasks. However, the basic theory has been extended to analyze cases that include inversion, task interactions, and aperiodic tasks.
In this tutorial, we will first introduce the mechanics of the analysis based on the original RMS theory assumptions, which are very restrictive. We will then systematically relax the assumptions and extend the basic theory.
Remember that the analysis can be done on systems that are scheduled by other algorithms. Again, this is the strength in rate monotonic theory. The analysis can be applied to any system, providing insight to its timing behavior. From now on, our focus is on rate monotonic analysis (RMA) of systems, which may or may not use the rate monotonic scheduling (RMS) algorithm.
In this tutorial we will cover priority inversion. We will cover task interactions and aperiodics as time allows

## Slide 6: Why Are Deadlines Missed?
For a given task, consider
  preemption: time waiting for higher priority tasks
  execution: time to do its own work
  blocking: time delayed by lower priority tasks
The task is schedulable if the sum of its preemption, execution, and blocking is less than its deadline.
Focus: identify the biggest hits among the three and reduce, as needed, to achieve schedulability
Notes: <number>
<footer>
<header>
<date/time>
9
Note:
For a task to meet its deadline, it must accommodate
Preemption from higher-priority tasks,
Its own execution time, and
Delays caused by lower-priority tasks (known as priority inversion or blocking).
Remember that higher-priority tasks, from a rate monotonic perspective, are those with higher rates (or shorter periods). These can occur more than once in a task’s period. A task’s execution occurs once during its period. And blocking can occur at most once during the task’s period; blocking comes from lower-priority tasks, those that have slower rates (or longer periods).
Preemption and execution are unavoidable. If these exceed capacity, one is faced with a classical throughput problem and the only remedy is to reduce the workload (which means changing the system requirements) or to increase the capacity by using a faster computer. Experience has shown that priority inversion (blocking), delay from lower-priority tasks, is a major source of missed deadlines. So we focus on identifying sources of priority inversion and try to reduce their blocking effects to enhance schedulability.

## Slide 7: Example of Priority Inversion
B
Collision check: {... P ( ) ... V ( ) ...}
Update location: {... P ( ) ... V ( ) ...}
Collision
check
Refresh
screen
Update
location
Attempts to lock data
resource (blocked)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Rate Monotonic Theory - Experience
Supported by several standards
  POSIX Real-time Extensions
    Various real-time versions of Linux
  Java (Real-Time Specification for Java and Distributed Real-Time Specification for Java)
  Real-Time CORBA
  Real-Time UML
  Ada 83 and Ada 95
  Windows 95/98
  …
Notes: <number>
<footer>
<header>
<date/time>
22
IBM System Integration Division (SID) Manassas developed and delivered a “schedulable” real-time network to the Navy.
RMA was successfully used by IBM to improve the performance of the BSY-1 Trainer while under development. (A case study in this tutorial reviews this.)
RMA principles were used to design real-time scheduling support in the IEEE FutureBus+ standard.
The NASA Space Station program has decided to adopt RMA in their development effort. They are currently implementing management practices for the use of RMA.
The European Space Agency is requiring that RMS theory be used as the baseline theory for its hard real-time operating system (OS) contract.
Various software vendors are offering products and services that support RMA: Compiler and runtime vendors; Real-time operating system vendors; Commercial training firms.
IBM's response-time analysis effort is using several of the same techniques detailed in the handbook to determine which parts of the system will meet its response-time requirements, even under worst-case system conditions, and which need modification to meet requirements. The analysis is being done by several IBM engineers on an initial release of over 1 million lines of code, allowing its response-time characteristics to be established early enough to take corrective action before full-scale testing and deployment. The analysis effort is expected to be a continuous activity throughout the development and deployment of the system.

## Slide 9: Summary
Real-time goals are:
  fast response,
  guaranteed deadlines, and
  stability in overload.
Any scheduling approach may be used, but all real-time systems should be analyzed for timing.
Rate monotonic analysis
  based on rate monotonic scheduling theory
  analytic formulas to determine schedulability
  framework for reasoning about system timing behavior
  separation of timing and functional concerns
Provides an engineering basis for designing real-time systems
Notes: <number>
<footer>
<header>
<date/time>
24
Use of rate monotonic theory provides the ability to predict timeliness and guarantee that deadlines will always be met. But more importantly, it provides insight into the hardware and software design that affect system timing performance and helps to identify possible bottlenecks and errors that degrade schedulability, i.e. the ability to meet deadlines.
Performing the analysis provides predictability of system performance during system design and allows the separation of timing and functional concerns. In essence, RMA provides an engineering approach to designing real-time systems, in the way that physics provides predictability in building bridges.

## Slide 10: Plan for Lectures
Present basic theory for periodic task sets
Extend basic theory to include
  context switch overhead
  preperiod deadlines
  interrupts
Consider task interactions:
  priority inversion
  synchronization protocols (time allowing)
Extend theory to aperiodic tasks:
  sporadic servers (time allowing)
Notes: <number>
<footer>
<header>
<date/time>
25
The approach that we will take with this tutorial is to start with very simple concepts and gradually build onto this foundation with more practical, real-world considerations.
We will first introduce the mechanics of RMA, applying the basic theory for independent, periodic tasks.
We will then extend the basic theory to include practical issues, such as context switch overhead, interrupts, and non-rate-monotonic priority assignments.
We will present a case study that incorporates the strategies covered and demonstrates the benefits of using RMA.
There will be exercises associated with some sections to practice the concepts discussed in those modules.
Next, as time allows, we will consider task interaction and aperiodic events, incorporating these issues into the analysis

## Slide 11: A Sample Problem
Periodics Servers Aperiodics

1

2

3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
’s deadline is 20 msec before the end of each period
Notes: <number>
<footer>
<header>
<date/time>
26
We will use this sample problem throughout the tutorial as a common thread, starting with the periodic tasks, then gradually adding the other components in the task set. This sample task set is simple and yet embodies many different types of real-time requirements. The task set is completely analyzable using the methods outlined in this tutorial.
Task set characteristics:
Periodic task t1: execution time = 20 msec; period = 100 msec; deadline is at the end of each period.
In addition, t3 may block t1 for 10 msec by using a shared communication server, and task t2 may block t1 for 20 msec by using a shared data object.
Periodic task t2: execution time = 40 msec; period = 150 msec; deadline is 20 msec before the end of each period.
Periodic task t3: execution time = 100 msec; period = 350 msec; deadline is at the end of each period.
Emergency event handling task: execution time = 5 msec; worst-case interarrival time = 50 msec; deadline is 6 msec after arrival.
Routine event handling task: average execution time = 2 msec; average interarrival time = 40 msec; 4 msec average response time is needed.

## Slide 12: Rate Monotonic Analysis
Introduction
Periodic tasks
Extending basic theory
Synchronization and priority inversion
Aperiodic servers
Notes: <number>
<footer>
<header>
<date/time>
1

## Slide 13: A Sample Problem - Periodics
Periodics Servers Aperiodics

1

2

3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
’s deadline is 20 msec before the end of each period
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Concepts and Definitions - Periodics
Periodic task
  initiated at fixed intervals
  must finish before start of next cycle
Task’s CPU utilization:
  Ci = worst-case compute time (execution time) for task i
  Ti = period of task i
CPU utilization for a set of tasks
U = U1 + U2 +...+ Un
Ui =
Ci
Ti
Notes: <number>
<footer>
<header>
<date/time>
3
A periodic task becomes ready to execute at fixed intervals. The time between task initiations is called the period of the task. When we say a periodic task meets its deadline, we mean that it finishes its execution before the start of the next period (i.e. the end of the current period). This is not always the most appropriate definition for a periodic task’s deadline. For example, a requirement to minimize jitter means that a task must perform some action at a specific time, not simply before a specific time. Jitter can be minimized by several design approaches. One approach is to trigger a very high priority task by an accurate clock to meet a jitter requirement.
Ci and Ti represent the execution time and period respectively for task ti. A task’s utilization of the CPU is Ci/Ti. Total CPU utilization is the sum of the utilizations of all the tasks

## Slide 15: Example of Priority Assignment
IP: U
IP
=
VIP: U
VIP
=
1
10
11
25
= 0.10
= 0.44
0
25
VIP:
0
10
20
30
IP:
Semantics-Based Priority Assignment
misses deadline
0
10
20
30
IP:
0
25
VIP:
Policy-Based Priority Assignment
Notes: <number>
<footer>
<header>
<date/time>
5
This example provides some motivation for using the rate monotonic scheduling algorithm. In the example we have 2 tasks, named IP and VIP, with the following descriptions:
Task IP: CIP = 1; TIP = 10; UIP = 0.10
Task VIP: CVIP = 11; TVIP = 25; UVIP = 0.44
Total utilization: 54%
If we assign higher priority to task VIP, then task IP will miss its deadline, even though the total utilization is only 54%. But if priorities are assigned according to the rate monotonic algorithm, then both tasks will meet their deadlines. Notice that, as VIP’s period increases, total utilization decreases to 10%, since UVIP approaches zero for large TVIP; yet deadlines are still missed

## Slide 16: Schedulability: UB Test
Utilization bound (UB) test: a set of n independent periodic tasks scheduled by the rate monotonic algorithm will always meet its deadlines, for all task phasings, if
U(1) = 1.0 U(4) = 0.756 U(7) = 0.728
U(2) = 0.828 U(5) = 0.743 U(8) = 0.724
U(3) = 0.779 U(6) = 0.734 U(9) = 0.720
For harmonic task sets, the utilization bound is U(n)=1.00 for all n.
--- + .... + --- < U(n) = n(2 - 1)
C1 Cn 1/ n
T1 Tn
Notes: <number>
<footer>
<header>
<date/time>
6
We say a set of tasks is schedulable if the task set is guaranteed to meet all its deadlines. The utilization bound test says that a task set is schedulable if its total utilization is less than a certain bound, called the Liu & Leyland bound. The utilization bound test provides the basic formula underlying the theory. More complex formulas provide better bounds. This test is the application of a theorem, which was proved by Liu and Leyland in “Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment”, JACM, 1973.
The utilization bound test assumes that:
1. The processor always executes the highest priority task.
2. Task priorities are assigned according to rate monotonic policy.
3. Tasks do not synchronize with each other.
4. Each task’s deadline is at the end of its period.
5. Tasks do not suspend themselves in the middle of computations.
The test takes into account the preemption time and execution time for each task under a worst-case combination of periods and execution times. As the number of tasks goes to infinity, the bound approaches ln(2) = 0.693; in other words, any number of independent periodic tasks will meet their deadlines if the total system utilization is under 69%
For a harmonic task set (in which the period of each task is a multiple of all higher-frequency tasks), the utilization bound is 1.0 for all task sets.

## Slide 17: Sample Problem: Applying UB Test
Total utilization is .200 + .267 + .286 = .753 < U(3) = .779
The periodic tasks in the sample problem are schedulable according to the UB test
 | C | T | U
Task 1 | 20 | 100 | 0.200
Task 2 | 40 | 150 | 0.267
Task 3 | 100 | 350 | 0.286
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 18: Timeline for Sample Problem
0
100
200
300
400
Scheduling Points

2

3

1
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 19: Exercise: Applying the UB Test
a. What is the total utilization?
b. Is the task set schedulable?
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
Given:
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 20: Solution: Applying the UB Test
a. What is the total utilization? .25 + .34 + .10 = .69
b. Is the task set schedulable? Yes: .69 < U(3) = .779
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
.25 + .34 + .20 = .79 > U(3) = .779
0
5
10
15
20
Task 
Task 
Task 
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 21: Toward a More Precise Test
UB test has three possible outcomes:
0 < U < U(n)  Success
U(n) < U < 1.00  Inconclusive
1.00 < U  Overload
UB test is conservative.
A more precise test can be applied.
Notes: <number>
<footer>
<header>
<date/time>
9
The results of applying the UB test can be:
0<U<u(n) success, task set is schedulable
U9n)<U<1.0 inconclusive, task set may or may not be schedulable
1.0 < U overload, task set exceeds capacity
When the UB test is inconclusive, a more precise test can be applied.
The previous schedulability test (utilization bound test) is very conservative. Schedulable system utilization can often exceed 90%. In fact, for tasks with harmonic periods, where each period is evenly divisible into all longer periods (e.g. 100 ms, 200 ms, 800 ms, 1600 ms), the utilization bound is 100%.

## Slide 22: Schedulability: RT Test
Theorem: The worst-case phasing of a task occurs when it arrives simultaneously with all its higher priority tasks.
Theorem: for a set of independent, periodic tasks, if each task meets its first deadline, with worst-case task phasing, the deadline will always be met.
Response time (RT) or Completion Time test: let an = response time of task i. an of task I may be computed by the following iterative formula:
Test terminates when an+1 = an.
Task i is schedulable if its response time is before its deadline: an < Ti
The above must be repeated for every task i from scratch
a
n+1
C
i
a
n
T
j
C
j
j
1

i
1



where a
0
C
j
j
1

i



This test must be repeated for every task i if required
  i.e. the value of i will change depending upon the task you are looking at
Stop test once current iteration yields a value of an+1 beyond the deadline (else, you may never terminate).
The ‘square bracketish’ thingies represent the ‘ceiling’ function, NOT brackets
Notes: <number>
<footer>
<header>
<date/time>
10
This remarkable theorem was proved by Liu and Leyland and assumes:
Tasks are scheduled according to the rate monotonic algorithm.
Tasks are independent and do not interact.
Tasks do not suspend during execution.
The iterative formula for task response time was introduced in Joseph and Pandya, “Finding Response Times in a Real-Time System,” BCS Computing Journal, October 1986 (vol 29 no 5) pp 390-395.
The iterative formula is an application of fixed point iteration. Since the successive iterates are non-decreasing and approach the response time from below, the iterative formula is known to converge if there is a solution.
There is an alternative approach that we call the scheduling point version of the response time test (see slide 29). The mathematical characterization of this scheduling point version is presented in The Rate Monotonic Scheduling Algorithm -- Exact Characterization and Average Case Behavior, by Lehoczky, Sha, and Ding, Technical Report, Department of Statistics, Carnegie Mellon University, 1987. Also presented in this paper is the fact that for randomly generated task sets, the actual utilization bound is 88% rather than the worst-case bound of 69% presented in the UB test.

## Slide 23: Example: Applying RT Test -1
C T U
Task  20 100 0.200
Task 40 150 0.267
Task 100 350 0.286
Taking the sample problem, we increase the compute time of 1 from 20 to 40; is the task set still schedulable?
0.4
40
Utilization of first two tasks: 0.667 < U(2) = 0.828
  first two tasks are schedulable by UB test
Utilization of all three tasks: 0.953 > U(3) = 0.779
  UB test is inconclusive
  need to apply RT test
Notes: <number>
<footer>
<header>
<date/time>
11
The following data is the same as the sample problem. However, we have changed C1 from 20 to 40 to illustrate the use of the RT test.
Task t1: C1 = 40; T1 = 100; U1 = 0.4
Task t2: C2 = 40; T2 = 150; U2 = 0.267
Task t3: C3 = 100; T3 = 350; U3 = 0.286
Utilization of first two tasks: .4 + .267 = .667 < U(2) = .828
Total utilization: .4 + .267 + .286 = .953 > U(3) = .779
When we change C1 from 20 to 40, CPU utilization changes. Since the utilization of the first two tasks is under the utilization bound of the UB test, these tasks will always meet their deadlines. When the third task is considered, the total utilization is above the utilization bound (Liu & Leyland), so we must look further to see if the third task can nonetheless meet its deadline.
We will now apply the response time test to task t3

## Slide 24: Example: Applying RT Test -2
Use RT test to determine if 3 meets its first deadline: i = 3
100
180
100
40


180
150
40




100
80
80


260



a
1
C
i
a
0
T
j
C
j
j
1

i
1



C
3
a
0
T
j
C
j
j
1

2




3
a
0
C
j
j
1


C
1
C
2
C
3


40
40
100


180




Notes: <number>
<footer>
<header>
<date/time>
12
To apply the RT test, we do two steps
Use the iterative formula to compute the first response time W3 of t3.
Compare W3 to the first deadline for t3, namely T3.
If W3 < T3, then t3 is schedulable according to the RT test.
We start with an initial guess W3 = 0. This is labeled as the “zero-ith” iteration W3(0) = 0. To compute the first iteration, W3(1), we use the iteration formula with n = 0.
Substitute 0 for W3(0). All the terms in the summation drop out, so the first iteration is
W3(1) = C3 = 100.
Next we apply the formula with n=1 and n=2, and compute, respectively, W3(2) and W3(3). Since each successive iteration is different, the computation has not yet converged and we must continue.

## Slide 25: Example: Applying the RT Test -3
Task 3 is schedulable using RT test
a
3
300

T

350

a
2
C
3
a
1
T
j
C
j
j
1

2



100
260
100
(40)
260
150
(40)




a
3
a
2
300
Done!


a
3
C
3
a
2
T
j
C
j
j
1

2



100
300
100
(40)
300
150
(40)




Notes: <number>
<footer>
<header>
<date/time>
13
We continue by applying the iteration formula for n=3 and n=4.
Finally, the computed value for W3(5) is the same as W3(4).
W3(5) = W3(4) = 300.
The iteration has converged, and the first response time for t3 is
W3 = 300.
This must be compared to the first deadline for t3.
We have W3 < T3 since 300 < 350.
So t3 is schedulable using the response time test.

## Slide 26: Timeline for Example

2

3
0
100
200
300

1

3
completes its work at t = 300
Notes: <number>
<footer>
<header>
<date/time>
14
This slide illustrates an alternate version of the response time test based on scheduling points. Again, the test is being applied only to t3.
A scheduling point is a point in time when new work arrives; the beginning of a new period for some task in the task set. This version of the CT test checks to see if there exists a scheduling point (at or before the deadline of t3) at which all work initiated up to that point has been completed. Since the workload includes the compute time of t3 as well as all higher-priority tasks, if the work is completed, then t3 has met its deadline.
In this graphical representation of task execution under worst-case phasing, we can see that, when all tasks are ready to execute at t=0, task t3 cannot begin execution until t=80. As t3 tries to complete its work it gets preempted at the next scheduling point at t=100, where t1 introduces more work. Each time t3 resumes its work it is preempted before completion, until t=300. In this example, task t3 completes all its work at exactly the fourth scheduling point. It completes all its work before its first deadline at t=350, and is therefore schedulable.
The reason for introducing two ways to find the response time is that the iteration formula is easier to program, while the scheduling points are easier to visualize

## Slide 27: Exercise: Applying RT Test
Task 1: C1 = 1 T1 = 4
Task 2: C2 = 2 T2 = 6
Task 3: C3 = 2 T3 = 10
a) Apply the UB test
b) Draw timeline
c) Apply RT test
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 28: Solution: Applying RT Test
a) UB test
  and OK -- no change from previous exercise
  .25 + .34 + .20 = .79 > .779  Test inconclusive for 
b) RT test and timeline
0
5
10
15
20
Task 
Task 
Task 
All work completed at t = 6
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 29: Solution: Applying RT Test (cont.)
c) RT test
3
a
0
C
j
j
1


C
1
C
2
C
3


1
2
2


5




a
1
C
3
a
0
T
j
C
j
j
1

2




2
5
4
1

5
6
2


2 + 2 + 2 = 6
a
2
C
3
a
1
T
j
C
j
j
1

2




2
6
4
1

6
6
2


2 + 2 + 2 = 6
Done
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 30: Summary
UB test is simple but conservative.
RT test is more exact but also more complicated.
To this point, UB and RT tests share the same limitations:
  all tasks run on a single processor
  all tasks are periodic and noninteracting
  deadlines are always at the end of the period
  there are no interrupts
  Rate-monotonic priorities are assigned
  there is zero context switch overhead
  tasks do not suspend themselves
Notes: <number>
<footer>
<header>
<date/time>
15
Although the UB test is conservative, it is useful in providing insight into timing issues. The BSY-1 case study will illustrate this.
Step-by-step algorithms are available in the A Practitioner's Handbook for Real-Time Analysis (published by Kluwer).
Up to this point in the tutorial, the schedulability tests have the following limiting assumptions:
All tasks run on a single processor.
All tasks are periodic and noninteracting.
Deadlines of all tasks are at the end of the period.
No interrupts are used.
Rate monotonic priorities are assigned.
There is no context switch overhead.
Tasks do not suspend themselves.
We will relax some of these assumptions in the next several sections.

## Slide 31: Sample Problem: Applying UB Test
Total utilization is .200 + .267 + .286 = .753 < U(3) = .779
The periodic tasks in the sample problem are schedulable according to the UB test
C T U
Task  20 100 0.200
Task 40 150 0.267
Task 100 350 0.286
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 32: Timeline for Sample Problem
0
100
200
300
400
Scheduling Points

2

3

1
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 33: Exercise: Applying the UB Test
a. What is the total utilization?
b. Is the task set schedulable?
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
Given:
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 34: Solution: Applying the UB Test
a. What is the total utilization? .25 + .34 + .10 = .69
b. Is the task set schedulable? Yes: .69 < U(3) = .779
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
.25 + .34 + .20 = .79 > U(3) = .779
0
5
10
15
20
Task 
Task 
Task 
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 35: Towards a More Precise Test
UB test has three possible outcomes:
0 < U < U(n)  Success
U(n) < U < 1.00  Inconclusive
1.00 < U  Overload
UB test is conservative.
A more precise test can be applied.
Notes: <number>
<footer>
<header>
<date/time>
9
The results of applying the UB test can be:
0<U<u(n) success, task set is schedulable
U9n)<U<1.0 inconclusive, task set may or may not be schedulable
1.0 < U overload, task set exceeds capacity
When the UB test is inconclusive, a more precise test can be applied.
The previous schedulability test (utilization bound test) is very conservative. Schedulable system utilization can often exceed 90%. In fact, for tasks with harmonic periods, where each period is evenly divisible into all longer periods (e.g. 100 ms, 200 ms, 800 ms, 1600 ms), the utilization bound is 100%.

## Slide 36: Schedulability: RT Test
Theorem: The worst-case phasing of a task occurs when it arrives simultaneously with all its higher priority tasks.
Theorem: for a set of independent, periodic tasks, if each task meets its first deadline, with worst-case task phasing, the deadline will always be met.
Response time (RT) or Completion Time test: let an = response time of task i. an may be computed by the following iterative formula:
Test terminates when an+1 = an.
Task i is schedulable if its response time is before its deadline: an < Ti
a
n+1
C
i
a
n
T
j
C
j
j
1

i
1



where a
0
C
j
j
1

i



This test must be repeated for every task i (if required)
  i.e. the value of i will change depending upon the task you are looking at
Stop test once current iteration yields a value of an+1 beyond the deadline (else, you may never terminate).
The ‘square bracketish’ thingies constitute the ‘ceiling’ function:
  ceiling (x) = smallest integer greater than or equal to x
Notes: <number>
<footer>
<header>
<date/time>
10
This remarkable theorem was proved by Liu and Leyland and assumes:
Tasks are scheduled according to the rate monotonic algorithm.
Tasks are independent and do not interact.
Tasks do not suspend during execution.
The iterative formula for task response time was introduced in Joseph and Pandya, “Finding Response Times in a Real-Time System,” BCS Computing Journal, October 1986 (vol 29 no 5) pp 390-395.
The iterative formula is an application of fixed point iteration. Since the successive iterates are non-decreasing and approach the response time from below, the iterative formula is known to converge if there is a solution.
There is an alternative approach that we call the scheduling point version of the response time test (see slide 29). The mathematical characterization of this scheduling point version is presented in The Rate Monotonic Scheduling Algorithm -- Exact Characterization and Average Case Behavior, by Lehoczky, Sha, and Ding, Technical Report, Department of Statistics, Carnegie Mellon University, 1987. Also presented in this paper is the fact that for randomly generated task sets, the actual utilization bound is 88% rather than the worst-case bound of 69% presented in the UB test.

## Slide 37: Example: Applying RT Test -1
C T U
Task  20 100 0.200
Task 40 150 0.267
Task 100 350 0.286
Taking the sample problem, we increase the compute time of 1 from 20 to 40; is the task set still schedulable?
0.4
40
Utilization of first two tasks: 0.667 < U(2) = 0.828
  first two tasks are schedulable by UB test
Utilization of all three tasks: 0.953 > U(3) = 0.779
  UB test is inconclusive
  need to apply RT test
Notes: <number>
<footer>
<header>
<date/time>
11
The following data is the same as the sample problem. However, we have changed C1 from 20 to 40 to illustrate the use of the RT test.
Task t1: C1 = 40; T1 = 100; U1 = 0.4
Task t2: C2 = 40; T2 = 150; U2 = 0.267
Task t3: C3 = 100; T3 = 350; U3 = 0.286
Utilization of first two tasks: .4 + .267 = .667 < U(2) = .828
Total utilization: .4 + .267 + .286 = .953 > U(3) = .779
When we change C1 from 20 to 40, CPU utilization changes. Since the utilization of the first two tasks is under the utilization bound of the UB test, these tasks will always meet their deadlines. When the third task is considered, the total utilization is above the utilization bound (Liu & Leyland), so we must look further to see if the third task can nonetheless meet its deadline.
We will now apply the response time test to task t3

## Slide 38: Example: Applying RT Test -2
Use RT test to determine if 3 meets its first deadline: i = 3
100
180
100
40


180
150
40




100
80
80


260



a
1
C
i
a
0
T
j
C
j
j
1

i
1



C
3
a
0
T
j
C
j
j
1

2




3
a
0
C
j
j
1


C
1
C
2
C
3


40
40
100


180




Notes: <number>
<footer>
<header>
<date/time>
12
To apply the RT test, we do two steps
Use the iterative formula to compute the first response time W3 of t3.
Compare W3 to the first deadline for t3, namely T3.
If W3 < T3, then t3 is schedulable according to the RT test.
We start with an initial guess W3 = 0. This is labeled as the “zero-ith” iteration W3(0) = 0. To compute the first iteration, W3(1), we use the iteration formula with n = 0.
Substitute 0 for W3(0). All the terms in the summation drop out, so the first iteration is
W3(1) = C3 = 100.
Next we apply the formula with n=1 and n=2, and compute, respectively, W3(2) and W3(3). Since each successive iteration is different, the computation has not yet converged and we must continue.

## Slide 39: Example: Applying the RT Test -3
Task 3 is schedulable using RT test
a
3
300

T

350

a
2
C
3
a
1
T
j
C
j
j
1

2



100
260
100
(40)
260
150
(40)




a
3
a
2
300
Done!


a
3
C
3
a
2
T
j
C
j
j
1

2



100
300
100
(40)
300
150
(40)




Notes: <number>
<footer>
<header>
<date/time>
13
We continue by applying the iteration formula for n=3 and n=4.
Finally, the computed value for W3(5) is the same as W3(4).
W3(5) = W3(4) = 300.
The iteration has converged, and the first response time for t3 is
W3 = 300.
This must be compared to the first deadline for t3.
We have W3 < T3 since 300 < 350.
So t3 is schedulable using the response time test.

## Slide 40: Timeline for Example

2

3
0
100
200
300

1

3
completes its work at t = 300
Notes: <number>
<footer>
<header>
<date/time>
14
This slide illustrates an alternate version of the response time test based on scheduling points. Again, the test is being applied only to t3.
A scheduling point is a point in time when new work arrives; the beginning of a new period for some task in the task set. This version of the CT test checks to see if there exists a scheduling point (at or before the deadline of t3) at which all work initiated up to that point has been completed. Since the workload includes the compute time of t3 as well as all higher-priority tasks, if the work is completed, then t3 has met its deadline.
In this graphical representation of task execution under worst-case phasing, we can see that, when all tasks are ready to execute at t=0, task t3 cannot begin execution until t=80. As t3 tries to complete its work it gets preempted at the next scheduling point at t=100, where t1 introduces more work. Each time t3 resumes its work it is preempted before completion, until t=300. In this example, task t3 completes all its work at exactly the fourth scheduling point. It completes all its work before its first deadline at t=350, and is therefore schedulable.
The reason for introducing two ways to find the response time is that the iteration formula is easier to program, while the scheduling points are easier to visualize

## Slide 41: Exercise: Applying RT Test
Task 1: C1 = 1 T1 = 4
Task 2: C2 = 2 T2 = 6
Task 3: C3 = 2 T3 = 10
a) Apply the UB test
b) Draw timeline
c) Apply RT test
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 42: Solution: Applying RT Test
a) UB test
  and OK -- no change from previous exercise
  .25 + .34 + .20 = .79 > .779  Test inconclusive for 
b) RT test and timeline
0
5
10
15
20
Task 
Task 
Task 
All work completed at t = 6
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 43: Solution: Applying RT Test (cont.)
c) RT test
3
a
0
C
j
j
1


C
1
C
2
C
3


1
2
2


5




a
1
C
3
a
0
T
j
C
j
j
1

2




2
5
4
1

5
6
2


2 + 2 + 2 = 6
a
2
C
3
a
1
T
j
C
j
j
1

2




2
6
4
1

6
6
2


2 + 2 + 2 = 6
Done
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 44: Summary
UB test is simple but conservative.
RT test is more exact but also more complicated.
To this point, UB and RT tests share the same limitations:
  all tasks run on a single processor
  all tasks are periodic and noninteracting
  deadlines are always at the end of the period
  there are no interrupts
  Rate-monotonic priorities are assigned
  there is zero context switch overhead
  tasks do not suspend themselves
Notes: <number>
<footer>
<header>
<date/time>
15
Although the UB test is conservative, it is useful in providing insight into timing issues. The BSY-1 case study will illustrate this.
Step-by-step algorithms are available in the A Practitioner's Handbook for Real-Time Analysis (published by Kluwer).
Up to this point in the tutorial, the schedulability tests have the following limiting assumptions:
All tasks run on a single processor.
All tasks are periodic and noninteracting.
Deadlines of all tasks are at the end of the period.
No interrupts are used.
Rate monotonic priorities are assigned.
There is no context switch overhead.
Tasks do not suspend themselves.
We will relax some of these assumptions in the next several sections.

## Slide 45: Rate Monotonic Analysis
Introduction
Periodic tasks
Extending the basic theory
Synchronization and Priority Inversion
Aperiodic servers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 46: A Sample Problem
’s deadline is 20 msec before the end of each period
Periodics Servers Aperiodics

1

2

3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
Notes: <number>
<footer>
<header>
<date/time>

## Slide 47: Extensions to Basic Theory
This section extends the schedulability tests to address
  nonzero task switching times
  preperiod deadlines
  interrupts and non-rate-monotonic priorities
Notes: <number>
<footer>
<header>
<date/time>
To this point we have assumed that there was no context (or task) switching overhead, that all deadlines were at the end of the period, and that tasks were scheduled according to the rate monotonic algorithm. In particular, we have assumed perfect preemption for the priority-based scheduler and we have assumed that priorities are assigned rate monotonically. Lack of preemption has the effect of delaying (or blocking) higher-priority tasks until the lower-priority task finishes its nonpreemptive execution. This situation in which a higher-priority task is ready to run, yet is prevented from running by a lower-priority task, we call priority inversion. Another source of priority inversion (from the standpoint of rate monotonic theory) is when priorities are assigned to tasks in violation of the rate monotonic algorithm. In this situation, a longer-period task (with a higher scheduling priority) will delay the execution of a task with a higher rate monotonic priority

## Slide 48: Modeling Task Switching as Execution Time
time
S
S
S
S
S
C
1
C
2
C
2






40
0
100
200
C
1
C
2
C
2
C
1
C
1
T
1
T
2
2T
1
C
i
+ 2S
T
i
U
i =
Two scheduling actions per task
(start of period and end of period)
40
C
1
C
1
Notes: <number>
<footer>
<header>
<date/time>
When a task preempts a lower-priority task, the execution state of the lower-priority task is saved and the execution state of the higher-priority task is established. When the higher- priority task completes its processing and relinquishes the CPU to a lower-priority task, its execution state is saved and the state of the lower-priority task is reestablished. The context switches for (1) preemption of the lower-priority process and (2) subsequent resumption of its execution account for the 2S added to the execution time of the preempting process.
Consider a given task, t3, which may be preempted by higher-priority tasks, t1 and t2. Worst case is that t3 will be preempted by t1 (and t2) every time t1 (or t2) is ready to run. Each preemption causes two context switches; one from t3 to run t1 and one from t1 back to resume t3. These two context switch times are charged to the higher-rate preempting task.

## Slide 49: Modeling Preperiod Deadlines
Suppose task , with compute time C and period T, has a preperiod deadline D (i.e. D < T ).
Compare total utilization to modified bound:
where i is the ratio (Di / Ti).
U(n, i) =
n
2

i


1
n

1



1

i



1
2

i
1.0




i

i
1
2










U
total
C
1
T
1
...
C
n
T
n
U
n

i







Notes: <number>
<footer>
<header>
<date/time>
It is common in control applications to set a task’s deadline to be prior to the end of its period. This is done to account for the transport delay.
Don’t worry about this formula. Just look up the utilization bound in Table 4-4 of the handbook. We will not go into any detail on preperiod deadlines or task switching. This is only made available to show that the situations can be analyzed using RMA.

## Slide 50: Schedulability with Interrupts
Interrupt processing can be inconsistent with rate-monotonic priority assignment.
  interrupt handler executes with high priority despite its period
  interrupt processing may delay execution of tasks with shorter periods
Effects of interrupt processing must be taken into account in schedulability model.
Question is: how to do that?
Notes: <number>
<footer>
<header>
<date/time>
To this point we have assumed that all tasks run in rate monotonic order. Interrupt processing is common in real-time applications and often violates this assumption. Typically, interrupt processing is higher in priority than application-level processing. So although it may have a lower rate monotonic priority than an application-level task (i.e., it has a longer period), it will have a higher runtime priority and preempt the application-level tasks. To this point, the schedulability tests have not addressed this situation.
To clarify some definitions;
Runtime priority - the priority actually assigned to a task.
Rate monotonic priority - the priority of a task, if assigned according to its rate.
Runtime preemption - seizing of the CPU by a task with a higher runtime priority.
Rate monotonic preemption - delay of a task by a higher-rate task. (Generally when we use the term preemption, we mean rate monotonic preemption.)
Rate monotonic blocking (or rate monotonic priority inversion) - delay of a task by a lower-rate task. (In general, we will simply use the terms blocking and priority inversion for rate monotonic blocking and rate monotonic priority inversion.)
We will now explore how the basic rate monotonic schedulability model can be extended to account for interrupt processing.

## Slide 51: Example: Determining Schedulability with Interrupts
3 is an interrupt handler
C T U
Task 120 100 0.200
Task 2: 40 150 0.267
Task 360 200 0.300
Task 440 350 0.115
Notes: <number>
<footer>
<header>
<date/time>
We will illustrate the way we address priority inversion with the above example.
Note that in this example, the interrupt has a lower rate monotonic priority than tasks t1 and t2.

## Slide 52: Example: Execution with Rate-Monotonic Priorities













Notes: <number>
<footer>
<header>
<date/time>
This timeline shows how the tasks would execute under worst-case phasing if they ran in rate monotonic order. All tasks are clearly schedulable according to the “visual” CT test.
Unfortunately, this timeline is not how the tasks execute. Since t3 is an interrupt handler, it executes before the other tasks, causing additional delays to t1 and t2.

## Slide 53: Example: Execution with an Interrupt Priority




Interrupt







Notes: <number>
<footer>
<header>
<date/time>
This timeline shows the actual execution order, where t3 is an interrupt handler and executes with a runtime priority that is higher than the other three tasks, in spite of its longer period. Notice the impact that the interrupt has on the completion time of the other three tasks. Both t1 and t2 are severely affected, being delayed by interrupt processing. However, t4 is not affected.
Execution is clearly inconsistent with the rate monotonic scheduling policy.

## Slide 54: Resulting Table for Example
Task (i) | Period (T) | Execution Time (C) | Priority (P) | Deadline (D)
3 | 200 | 60 | Hardware (highest) | 200
1 | 100 | 20 | High | 100
2 | 150 | 40 | Medium | 150
4 | 350 | 40 | Low | 350
Notes: <number>
<footer>
<header>
<date/time>
Task Period Execution prior Deadline
Time
TskE 50 5 very high 0 6
TskR 24 2 High 0 24
Tsk1 100 20 Medium 20 100
Tsk2 150 40 Low 10 150
Tsk3 350 100 very low 0 350

## Slide 55: UB Test with Interrupt Priority
Test is applied to each task.
Determine effective utilization (fi) of each task i using
j Hn
f
C
T

C
T
1
T
C




i
j
j
i
i
k
i
k H1
Preemption
from tasks that
can “hit” more than once
(with period less than Di)
Execution of
task under test
Preemption
from tasks that
can hit only once
(with period greater than Di)
Compare effective utilization against bound U(n).
  n = num(Hn) + 1
  num(Hn) = the number of tasks in the set Hn


Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: UB Test with Interrupt Priority: t3
For 3, no tasks have a higher priority:
  H = Hn = H1 = { }
f
0

C
T
0





3
3
3
Note:
num(Hn) = 0; therefore, utilization bound is U(1).
Plugging in the numbers:
f
C
T
60
200
0.3
1.0




3
3
3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: UB Test with Interrupt Priority: 1
To 1, 3 has higher priority: H = {3 }; Hn = { }; H1 = {3 }
f
0

C
T
1
T
C





1
1
1
k
k=3
1
Note:
num(Hn) = 0; therefore, utilization bound is U(1).
Plugging in the numbers:


0.800 <
1.0



20
100
60
100
f
1
C
T
1
1
C
T
1
3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: UB Test with Interrupt Priority: 2
To 2: H = {}; Hn = {}; H1 = {}.
f

C
T
1
T
C





2
2
2
k
k=3
2
C
T
j
j
j = 1
f
C
T
C
T

20
100
60
150

0.867 > 0.828



2
1
1
2
3
C
T
2
2

40
150

Note:
num(Hn) = 1; therefore, utilization bound is U(2).
Plugging in the numbers:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: UB Test with Interrupt Priority: 4
To 4: H = {123}; Hn = {123}; H1 = { }.
f

C
T
0




4
4
4
C
T
j
j
j = 1,2,3
f
C
T
C
T

20
100



4
1
1
3
3
C
T
2
2

C
T
4
4

40
150

60
200
350

40

Note:
num(Hn) = 3; therefore, utilization bound is U(4).
Plugging in the numbers:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Exercise: Schedulability with Interrupts
Use the UB test to determine which tasks are schedulable
Given the following tasks:
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 61: Solution: Schedulability with Interrupts
0.334 < 1.0
U
1

(
)
Cint
Tint

U
1, .75)

(
C1
T1
Cint
T1

U
3)

(
C1
T1
Cint
Tint

C2
T2
0.250 + 0.500 = 0.750 = U(1, .75)
0. 334 + 0. 250 + 0.100 = 0.684 < 0.779
{H1}
{Hn}
Notes: <number>
<footer>
<header>
<date/time>

## Slide 62: Basic Theory: Where Are We?
We have shown how to handle
  task context switching time: include 2S in C
  Pre-period deadlines: change bound to U(n, Di)
  non-rate-monotonic priority assignments
We still must address
  task interactions
  aperiodic tasks
We still assume
  single processor
  priority-based scheduling
  a task does not suspend itself voluntarily
Notes: <number>
<footer>
<header>
<date/time>
The schedulability model is now as complex as it will get. By adding blocking, as well as context switching and dormant time, we have extended the model to address the issues we will cover in this tutorial. We still have to cover task interactions through synchronization, which does not change the schedulability model but gives additional sources of blocking effects that must be included. Finally, we will add aperiodic tasks, which are handled by making them pseudo-periodic.
Remember that we still assume that all tasks run on a single CPU, that priority-based scheduling is used, and that tasks do not suspend themselves. However, later we will study a case in which priority-based scheduling is not used and look at its schedulability.