## Slide 1: Introduction to Embedded (Real Time) Systems Lecture 1

## Slide 2: Thoughts for the Day
Have a vision not clouded by fear.
- Cherokee proverb
The greatest virtues are those which
are most useful to other persons.
- Aristotle, 384-322 B.C.

## Slide 3: Course Support
• TAs
• Course Administrative Support
• Lectures
• Labs
– A few evening lectures (likely Monday or Wednesday evenings 7-9 pm)
– 24hour
• Textbooks
– None!

## Slide 4: Pre-requisites
Pre-requisites
– CS 211: Fundamental Data Structures and Algorithms
– ECE 240: Fundamentals of Computer Engineering
– CS 213: Introduction to Computer Systems
Or ECE 347: Introduction to Computer Architecture
• Knowledge of C programming
– just knowing Java could actually be harmful!
• Need to know, understand and manipulate “pointers”
• Basic knowledge of digital logic
– basic gates and their truth tables
• Assembly-language programming
– the Intel Xscale® instruction set will be used in 18-349
– knowledge of instruction sets of other modern microprocessors (x86, ARM,
PowerPC, 680x0, MIPS) should be a sufficient and necessary starting point
• If you do not know assembly language programming, you need to spend
Extra (ordinary?) effort in coming up to speed as soon as you can
– Learning materials are available online on course web-site

## Slide 5: Lab online
• 5 Lab projects
– 100 points each
– the 1st will be an individual project
– labs 2, 3 and 4 will likely be in groups of 4 (or less)
• all members must be present for project demonstrations and will
be asked questions
– the 5th project will be an individual project (a group-based version
may be available as an alternative)
– Most labs will have two parts

## Slide 6: Miscellaneous Lab Information
Introducing…. The 18-349 X-board
– Intel Xscale® Prototype board from Intel® + PCI Sound card + Keypad
• Intel Xscale® Simulation software
• New hardware and software
• Real world tools: industrial grade (means there will be bugs!)
• You probably will spend (waste) time because the environment is still relatively new
• Most labs cannot be done in a day
• We will require small group sizes

## Slide 7: What are Embedded Systems?
Anything that uses a microprocessor but isn't a general-purpose computer
– PDAs
– Set-top boxes
– Televisions
– Video Games
– Refrigerators
– Cars
– Planes
– Elevators
– Remote Controls
– Alarm Systems
• The user “sees” a smart (special-purpose) system as opposed to the computer inside the system
• “how does it do that?”
• “it has a computer inside it!”
• “oh! BTW, it does not or cannot run Windows or MacOS!”
– the end-user typically does not or cannot modify or upgrade the internals

## Slide 8: Why are Embedded Systems important?
Engineering reasons
– Why does a satellite need a Windows prompt ?
– Does the McDonald’s POS (point-of-sale) terminal need MacOS?
– Any device that needs to be controlled can be controlled by a microprocessor
• Market reasons
– The general-purpose computing market is in billions of US $
– The embedded systems market is also in billions of $
– In year 2000, about $2,700 of every car went to electronics
• Pedagogical reasons
– General-purpose system designers specialize
– HW vs. SW
• Embedded system designers are often
– jackofmanytrades
– Need to know hardware, software, and some combination of networking,
control theory and signal processing
– business models

## Slide 9: What Are You Going to Learn?
  • Hardware
  – I/O, memory, busses, devices, control logic, interfacing hardware to software
  • Software
  – Lots of C and assembly, device drivers, low level
  OS issues, scheduling,
  – Concurrency
  • Software/Hardware interactions
  – Where is the best place to put functionality hardware
  or software?
  – What are the costs:
  • performance,
  • memory requirements (RAM and/or ROM)
  • Integration of hardware and software courses
  – Programming, logic design, architecture,
  – Algorithms, mathematics and common sense

## Slide 10: Where Could You End Up?
Automotive systems
– perhaps designing and developing “drive-by-wire” systems
• Telecommunications
• Consumer electronics
– cellular phones, MP3 devices, integrated cellular/walkman/PDA/kitchen sink
– Set-top boxes and HDTV
– Home appliances
– Internet appliances
• your washer will be on the internet more than you are!
• Defense and weapon systems
• Process control
– gasoline processing, chemical refinement
• Automated manufacturing
– Supervisory Control and Data Acquisition (SCADA)
• Space applications
– Satellite communications

## Slide 11: Goals of the Course
High-Level Goals
1. Understand the scientific principles and concepts behind embedded systems,
and
2. Obtain hands-on experience in programming embedded systems.
By the end of the course, you must be able to
• Understand the "big ideas" in embedded systems
• Obtain direct hands-on experience on both hardware and software elements
commonly used in embedded system design.
• Understand basic real-time resource management theory
• Understand the basics of embedded system application concepts such as signal
processing and feedback control
• Understand, and be able to discuss and communicate intelligently about
– embedded processor architecture and programming
– I/O and device driver interfaces to embedded processors with networks, multimedia cards and disk drives
– OS primitives for concurrency, timeouts, scheduling, communication and synchronization

## Slide 12: The Big Ideas
HW/SW Boundary
• Non processor centric view of architecture
• Bowels of the operating system
– specifically, the lower half of the OS
– Concurrency
• Realworld design
– performance vs. cost tradeoffs
• Analyzability
– how do you “know” that your drive-by-wire system will function correctly?
• Application-level techniques
– signal processing, control theory

## Slide 13: Grading Criteria
Assignments
– 200 points from 5 quizzes (50 points each, we drop the lowest score)
– 300 points from 2 in-class exams
– 500 points from 5 projects
• ~50 points extra credit course development
• Grading Scale
– 90% 100% A
– 80% 89% B
– 70% 79% C
– 60% 69% D
– 0 59% R

## Slide 14: Questions and Feedback
Grades will be available online
• Post to the class discussion board from the web-page.
• Talk to the professor if you have any concerns regarding anything related to the course.
• The professor will want to talk with you if you are not doing well in class.
• Mid-term survey to get your feedback.
• You can also provide anonymous feedback anytime.

## Slide 15
What are Embedded Systems anyway?

## Slide 16: Embedded Systems: An Introduction
• What is an embedded system?
– More than just a computer
• What makes embedded systems different?
– Real-time operation
– Many sets of constraints on designs
• size
• cost
• time
• reliability
• safety
• energy
• security
• What embedded system designers need to know?
– The “big” picture
– Skills required to be an “expert” in this area

## Slide 17: What is an Embedded System?
  • Computer purchased as part of some other piece of equipment
  – Typically dedicated software (may be user customizable)
  – Often replaces previously electromechanical components
  – Often no “real” keyboard
  – Often limited display or no general purpose display device
  • But, every system is unique there are always exceptions

## Slide 18: CPU: An All-Too-Common View of Computing
• Measured by:
– Performance

## Slide 19: An Advanced Computer Engineer's View
• Measured by: Performance
• Compilers matter too...

## Slide 20: An Enlightened Computer Engineer's View
• Measured by: Performance, Cost
Compilers & OS matters

## Slide 21: An Embedded Computer Designer's View
• Measured by: Cost, I/O connections, Memory Size, Performance

## Slide 22: An Embedded Control System Designer's View
• Measured by:
Cost, Time to market, Cost, Functionality, Cost & Cost.

## Slide 23: A Customer View
– Reduced Cost
– Increased Functionality
– Improved Performance
– Increased Overall Dependability

## Slide 24: Some Embedded System Examples
• Pocket remote control RF transmitter
– 100 KIPS, water/crushproof, fits in pocket, 5year battery life
– Software handcrafted for small size (less than 1 KB)
• Industrial equipment controller (e.g., elevator; jet engine)
– 110 MIPS for 1 to 10 CPUs, 1 8MB memory
– Safety critical software; real time control loops
• Military signal processing (e.g., Radar/Sonar)
– 1 GFLOPS, 1 GB/sec I/O, 32 MB memory
– Software handcrafted for extremely high performance

## Slide 25: Embedded Computers Rule the Marketplace
• ~80 Million PCs vs. ~3 Billion Embedded CPUs annually
– Embedded market growing; PC market mostly saturated

## Slide 26: Why Are Embedded Systems Different?
Four General Categories of Embedded Systems
• General Computing
– Applications similar to desktop computing, but in an embedded package
– Video games, set top boxes, wearable computers, automatic tellers
• Control Systems
– Closed loop feedback control of real time system
– Vehicle engines, chemical processes, nuclear power, flight control
• Signal Processing
– Computations involving large data streams
– Radar, Sonar, video compression
• Communication & Networking
– Switching and information transmission
– Telephone system, Internet

## Slide 27: Types of Embedded System Functions
• Control Laws
– PID control
– Fuzzy logic, ...
• Sequencing logic
– Finite state machines
– Switching modes between control laws
• Signal processing
– Multimedia data compression
– Digital filtering
• Application specific interfacing
– Buttons, bells, lights,...
– High speed I/O
• Fault response
– Detection & reconfiguration
– Diagnosis
• ...

## Slide 28: Distinctive Embedded System Attributes
• Reactive: computations occur in response to external events
– Periodic events (e.g., rotating machinery and control loops)
– Aperiodic events (e.g., button closures)
• Real-Time: timing correctness is part of system correctness
– Hard real-time
• Absolute deadline, beyond which answer is useless
• May include minimum time as well as maximum time
– Soft real-time
• Missing a deadline is not catastrophic
• Utility of answer degrades with time difference from deadline
– Example:
• a train is entering an urban area...
• the railway gate in the city allows automotive traffic to go over the tracks
• when should the railway gate close?
In general,
Real Time != “Real Fast”

## Slide 29: Typical Embedded System Constraints
• Small Size, Low Weight
– Handheld electronics
– Transportation applications weight costs money
• Low Power
– Battery power for 8+ hours (laptops often last only 2 hours)
– Limited cooling may limit power even if AC power available
• Harsh environment
– Heat, vibration, shock
– Power fluctuations, RF interference, lightning
– Water, corrosion, physical abuse
• Safety critical operation
– Must function correctly
– Must not function incorrectly
• Extreme cost sensitivity
– $.05 adds up over 1,000,000 units

## Slide 30: Embedded System Design World-View
A complex set of tradeoffs:
• Optimize for more than just speed
• Consider more than just the computer
• Take into account more than just initial product design
Multi-Discipline
• Electronic Hardware
• Software
• Mechanical Hardware
• Control Algorithms
• Humans
• Society/Institutions
MultiObjective
• Dependability
• Affordability
• Safety
• Security
• Scalability
• Timeliness
MultiPhase
• Requirements
• Design
• Manufacturing
• Deployment
• Logistics
• Retirement
x
x

## Slide 31: Mission Critical Applications Require Robustness
• Loss of Arianne inaugural flight in June, 1996
– Lost a $400 million scientific payload (the rocket was extra)
• Efforts to reduce system costs led to the failure
– Reuse of Inertial Reference System software from Ariane 4
– Improperly handled exception caused by variable overflow during
– new flight profile (that wasn't simulated because of cost/schedule)
– 64bit float converted to 16bit int assumed not to overflow
• Exception caused dual hardware shutdown (software doesn't fail!)
• What really happened?
– The narrow view: it was a software bug fix it
– The broad view: the loss was caused by a lack of system robustness in an
exceptional (unanticipated) situation
Many embedded systems must be robust

## Slide 32: Software Drives Designs
• Hardware is mostly a recurring cost
– Cost proportional to number of units manufactured
• Software is a “one time” nonrecurring engineering design cost (NRE)
– Paid for ``only once''
• But bug fixes may be expensive, or impossible
– Cost is related to complexity & number of functions
– Market pressures lead to feature creep
• Software Is NOT free!!!!!

## Slide 33: Life Cycle Concerns Figure Prominently
• “Let's use a CAD system to re-synthesize designs for cost optimization”
– Automatically use whatever components are cheap that month
– Would permit quick responses to bids for new variants
– Track record of working fine for PC motherboards
• Why wouldn't it work for an automotive application?
– Embedded systems had more analog than digital mostly digital synthesis tool
– Cost of recertification for safety, FCC, warrantee repair rate
– Design optimized for running power, not idle power
• Car batteries must last a month in a parking lot
– Parts cost didn't take into account lifecycle concerns
• Price breaks for large quantities
• Inventory, spares, end of life buy costs
– Tool didn't put designs on a single sheet of paper
• Archive system paper-based -- how else do you read
– 20 year old files?

## Slide 34: Embedded System Designer Skill Set
• Appreciation for multidisciplinary nature of design
– Both hardware & software skills
– Understanding of engineering beyond digital logic
– Ability to take a project from specification through production
• Communication & teamwork skills
– Work with other disciplines, manufacturing, marketing
– Work with customers to understand the real problem being solved
– Make a good presentation; even better write ``trade rag'' articles
• And, by the way, technical skills too...
– Low-level: Microcontrollers, FPGA/ASIC, assembly language, A/D, D/A
– High-level: Object oriented Design, C/C++, Real Time Operating Systems
– Meta-level: Creative solutions to highly constrained problems
– Likely in the future: Unified Modeling Language, embedded networks
– (Un)certain future: Java, Windows CE

## Slide 35: Review
• What is an embedded system?
– More than just a computer it's a complete system
• What makes embedded systems different?
– Many sets of constraints on designs
– Four general types:
• General-Purpose
• Control
• Signal Processing
• Communications
• What embedded system designers need to know ?
– Multi-objective: cost, dependability, performance, etc.
– Multidiscipline: hardware, software, electromechanical, etc.
– Life-cycle: specification, design, prototyping, deployment, support, retirement