## Slide 1: Memory, I/O and Microcomputer Bus Architectures
Lecture 7

## Slide 2: Summary of Previous Lecture
Improving program performance
Standard compiler optimizations
  Common sub-expression elimination
  Dead-code elimination
  Induction variables
Aggressive compiler optimizations
  In-lining of functions
  Loop unrolling
Using the CodeWarrior IDE for profiling and optimization
Architectural code optimizations

## Slide 3: Administrivia
Supplemental Required Readings (available under Course Documents  Readings)
  How does ROM work?
  How does RAM work?
  How does Flash memory work?

## Slide 4: Quote of the Day
The empires of the future are the empires of the mind.
  Winston Churchill

## Slide 5: Outline of This Lecture
The many levels of computer systems
The CPU-Memory Interface
The Memory Subsystem and Technologies
CPU-Bus-I/O
Bus Protocols

## Slide 6: Understanding Computer Systems at Many Levels
A computer system can be viewed, understood and manipulated at many different levels, each built on those below
CPU + main memory as a big array of bytes
  this is the view/level we've been working with so far
CPU + memory controllers/chips + I/O controllers/devices
  this is the view/level we're going to work with during the next few weeks
  think of the system as a bunch of independent components talking to each other
  of course, there must be a communication medium and a common language

## Slide 7: CPU ­ Memory Interface
CPU ­ Memory Interface usually consists of:
  uni­directional address bus
  bi­directional data bus
  read control line
  write control line
  ready control line
  size (byte, word) control line
Memory access involves a memory bus transaction
  read:
    (1) set address, read and size,
    (2) copy data when ready is set by memory
  write:
    (1) set address, data, write and size,
    (2) done when ready is set
address bus
data bus
CPU
Memory
Read
Write
Ready
size

## Slide 8: Memory Subsystem Components
Memory subsystems generally consist of chips+controller
Each chip provides few bits (e.g., 1­4) per access
  Bits from multiple chips are accessed in parallel to fetch bytes and words
  Memory controller decodes/translates address and control signals
  Controller can also be on memory chip
Example:
  contains 8 16x1­bit chips and very simple controller
address bus
data bus
CPU
Memory
Read
Write
Ready
Size
1-of-16
decoder
1 0 1 1 0 0 1 0
1 0 0 0 0 0 0 1
0 1 0 1 0 0 1 1
address
0000
0001
1111
16x1-bit memory chip
16x8-bit memory array
D7 D6 D5 D4 D3 D2 D1 D0

## Slide 9: Memory
Memories come in many shapes, sizes and types
  Shapes and sizes we've discussed already (e.g., 16x1­bit)

## Slide 10: Memory Technologies
DRAM: Dynamic Random Access Memory
  upside: very dense (1 transistor per bit) and inexpensive
  downside: requires refresh and often not the fastest access times
  often used for main memories
SRAM: Static Random Access Memory
  upside: fast and no refresh required
  downside: not so dense and not so cheap
  often used for caches
ROM: Read­Only Memory
  often used for bootstrapping and such

## Slide 11: Storage Basics
Just because the CPU sees RAM as one long, thin line of bytes doesn't mean that it's actually laid out that way
Real RAM chips don't store whole bytes, but rather they store individual bits in a grid, which you can address one bit at a time

## Slide 12: SRAM Chip

## Slide 13: SRAM Memory Timing for Read Accesses
Address and chip select signals are provided tAA before data is available
Outputs reflect new data
2147H
2147H High-Speed 4096x1-bit static RAM
A11-A0
Din
WE
CS
Dout
tRC = Read cycle time
tAA = Address access time
tACS = Chip select access time
tHZ = Chip deselections to high­Z out
old address
high
impedance
undef
Data Valid
tRC
tAA
tACS
tHz
new address
Address
A11-A0
CS
WE
Dout
Address Bus

## Slide 14: SRAM Memory Timing for Write Accesses
Address and data must be stable tS time-units before write enable signal falls
2147H
2147H High-Speed 4096X1-bit static RAM
A11-A0
Din
WE
CS
Din
tS = Signal setup time
tRC = Read cycle time
tAA = Address access time
tACS = Chip select access time
tHZ = Chip deselections to high­Z out
old address
old data
new data
tWC
tAA
tACS
tHz
new address
Address
A11-A0
CS
WE
Din
tS
Address Bus

## Slide 15: DRAM Organization and Operations
In the traditional DRAM, any storage location can be randomly accessed for read/write by inputting the address of the corresponding storage location.
  A typical DRAM of bit capacity 2N * 2M consists of an array of memory cells arranged in 2N rows (word-lines) and 2M columns (bit-lines).
  Each memory cell has a unique location represented by the intersection of word and bit line.
  Memory cell consists of a transistor and a capacitor. The charge on the capacitor represents 0 or 1 for the memory cell. The support circuitry for the DRAM chip is used to read/write to a memory cell.

## Slide 16: DRAM Organization and Operations
Address decoders
  to select a row and a column
(b) Sense amps
  to detect and amplify the charge in the capacitor of the memory cell.
(c) Read/Write logic
  to read/store information in the memory cell.
(d) Output Enable logic
  controls whether data should appear at the outputs.
(e) Refresh counters
  to keep track of refresh sequence.

## Slide 17: DRAM Memory Access
DRAM Memory is arranged in a XY grid pattern of rows and columns.
First, the row address is sent to the memory chip and latched, then the column address is sent in a similar fashion.
This row and column-addressing scheme (called multiplexing) allows a large memory address to use fewer pins.
The charge stored in the chosen memory cell is amplified using the sense amplifier and then routed to the output pin.
Read/Write is controlled using the read/write logic.

## Slide 18: How DRAM Works

## Slide 19: DRAM Memory Access
Hardware Diagram of
Typical DRAM (2 N x 2N x 1)
A typical DRAM read operation:
1. The row address is placed on the address pins visa the address bus
2. RAS pin is activated, which places the row address onto the Row Address Latch.
3. The Row Address Decoder selects the proper row to be sent to the sense amps.
4. The Write Enable is deactivated, so the DRAM knows that it’s not being written to.
5. The column address is placed on the address pins via the address bus
6. The CAS pin is activated, which places the column address on the Column Address Latch
7. The CAS pin also serves as the Output Enable, so once the CAS signal has stabilized, the sense amps place the data from the selected row and column on the Data Out pin so that it can travel the data bus back out into the system.
8. RAS and CAS are both deactivated so that the cycle can begin again.

## Slide 20: Aligned DRAM Block Copy
The source and destination block are in the same DRAM chip.
There is no overlap between the source and destination blocks.
Blkcp operation does use register file and is not cacheable.
Add two new components in DRAM chip: a Buffer Register and a MUX (multiplexer). The Buffer Register is used to temporarily store the source row, and the MUX is used to choose the write back data used in refresh period: under normal condition, column latch should be chosen to refresh, but during row copy mode, WS is raised and Buffer Register is chosen.

## Slide 21: DRAM Performance Specs
Important DRAM Performance Considerations
  Random access time: time required to read any random single cell
  Fast Page Cycle time: time required for page mode access ­­ read/write to memory location on the most recently­accessed page (no need to repeat RAS in this case)
  Extended Data Out (EDO): allows setup of next address while current data access is maintained
  SDRAM ­ Burst Mode: Synchronous DRAMs use a self­incrementing counter and a mode register to determine the column address sequence after the first memory location accessed on a page ­­ effective for applications that usually require streams of data from one or more pages on the DRAM
  Required refresh rate: minimum rate of refreshes

## Slide 22: Turning Bits Into Bytes (2x This Picture)

## Slide 23: Critical Thinking
It’s a commonly held belief that adding more RAM increases your performance. If you wanted to speed up your computer, what kind of RAM would you buy and why?

## Slide 24: CPU ­ Bus ­ I/O
CPU needs to talk with I/O devices such as keyboard, mouse, video, network, disk drive, LEDs
Memory­mapped I/O
  Devices are mapped to specific memory locations just like RAM
  Uses load/store instructions just like accesses to memory
Ported I/O
  Special bus line and instructions
Address
CPU
Memory
I/O Device
Data
Read
Write
CPU
Memory
I/O Device
Data
Read
Write
Address
I/O Port
Memory I/O

## Slide 25: I/O Register Basics
I/O Registers are NOT like normal memory
  Device events can change their values (e.g., status registers)
  Reading a register can change its value (e.g., error condition reset)
    so, for example, can't expect to get same value if read twice
  Some are read­only (e.g., receive registers)
  Some are write­only (e.g., transmit registers)
  Sometimes multiple I/O registers are mapped to same address
    selection of one based on other info (e.g., read vs. write or extra control bits)
The bits in a control register often each specify something different and important ­­ and have significant side effects
Cache must be disabled for memory­mapped addresses
When polling I/O registers, should tell compiler that value can change on its own
  volatile int *ptr;

## Slide 26: Up Next - Bus Architectures

## Slide 27: Bus Protocols
Protocol refers to the set of rules agreed upon by both the bus master and bus slave
  Synchronous bus ­ transfers occur in relation to successive edges of a clock
  Asynchronous bus ­ transfers bear no particular timing relationship
  Semi­synchronous bus ­ Operations/control initiate asynchronously, but data transfer occurs synchronously
CPU
Device 1
Device 2
Device 3
Bus

## Slide 28: Synchronous Bus Protocol
Transfer occurs in relation to successive edges of the system clock
Example:
  Memory address is placed on the address bus within a certain time, relative to the rising edge of the clock
  By the trailing edge of this same clock pulse, the address information has had time to stabilize, so the READ line is asserted
  Once the chip has been selected, then the memory can place the contents of the specified location on the data bus
Clock
Address
Master (CPU) RD
Master (CPU) CS
Data
stable
stable
stable
stable
unstable
unstable
Instruction Addr
Data Addr
I-fetch
data
access time
decoding delay

## Slide 29: Asynchronous Bus Protocol
No system clock used
Useful for systems where CPU and I/O devices run at different speeds
Example:
  Master puts address and data on the bus and then raises the Master signal
  Slave sees master signal, reads the data and then raises the Slave signal
  Master sees Slave signal and lowers Master signal
  Slave sees Master signal lowered and lowers Slave signal
write
read
Address
Master
Slave
Data
there's
some
data
I’ve
got
it
I see you
got it
I see you
see I got it
We call this exchange “handshaking”

## Slide 30: Bus Arbitration
What happens if multiple devices want access to the bus?
Scheme 1: Every device connects to the bus request line and the first one there gets it
Scheme 2: daisy chain the devices ­ devices further down the daisy chain pass the request to the CPU ­ device's priority decreases further down the daisy chain
Scheme 3: one bus request line per bus and arbitrator applies arbitration policy to decide who gets bus next
CPU
Device 1
Device 2
Device 3
Bus
Bus request line
CPU
Device 3
Bus
Device 1
Device 2
Request
Grant

## Slide 31: Summary of Lecture
The many levels of computer systems
The CPU-Memory Interface
The Memory Subsystem and Technologies
  SRAM
  DRAM
CPU-Bus-I/O
  I/O Register Basics
Bus Protocols
  Synchronous bus protocol
  Asynchronous bus protocol
  Bus arbitration