## Slide 1: Interfacing
Connecting the computation capabilities of a microcontroller to external signals
  Transforming variable values into voltages and vice-versa
  Digital and analog
Issues
  How many signals can be controlled?
  How can digital and/or analog inputs be used to measure different physical phenomena?
  How can digital and/or analog inputs be used to control different physical phenomena?

## Slide 2: Controlling and reacting to the environment
To control or react to the environment we need to interface the microcontroller to peripheral devices
  Microcontroller may contain specialized interfaces to sensors and actuators
Things we want to measure or control
  light, temperature, sound, pressure, velocity, position
Sensors
  e.g., switches, photoresistors, accelerometers, compass, sonar
Actuators
  e.g., motors, relays, LEDs, sonar, displays, buzzers

## Slide 3: Typical control system
controller
actuators
sensors
physical
system
interfaces

## Slide 4: Analog to digital conversion
Map analog inputs to a range of binary values
  8-bit A/D has outputs in range 0-255
What if we need more information?
  linear vs. logarithmic mappings
  larger range of outputs (16-bit a/d)
0
64
128
192
255
1
10
100
1000
.1
1
10
100
1000
.1
analog
analog
digital

## Slide 5: Logarithm of a signal
Usually use an op-amp circuit
Often found as a pre-amplifier to ADC circuitry
Simple circuit to computer natural logarithm
VIN
VOUT = loge ( VIN )

## Slide 6: Digital to analog conversion
Map binary values to analog outputs (voltages)
Most devices have a digital interface – use time to encode value
Time-varying digital signals – almost arbitrary resolution
  pulse-code modulation (data = number or width of pulses)
  pulse-width modulation (data = duty-cycle of pulses)
  frequency modulation (data = rate at which pulses occur)
V
t
V
t
V
t

## Slide 7: Pulse-width modulation
Pulse a digital signal to get an average “analog” value
The longer the pulse width, the higher the voltage
Pulse-width ratio =
ton
tperiod
t
t
t
average
value
tperiod
ton

## Slide 8: Why pulse-width modulation works
Most mechanical systems are low-pass filters
  Consider frequency components of pulse-width modulated signal
  Low frequency components affect components
    They pass through
  High frequency components are too fast to fight inertia
    They are “filtered out”
Electrical RC-networks are low-pass filters
  Time constant ( = RC) sets “cutoff” frequency that separates low and high frequencies

## Slide 9: Anti-lock brake system
Rear wheel controller/anti-lock brake system
  Normal operation
    Regulate velocity of rear wheel
  Brake pressed
    Gradually increase amount of braking
    If skidding (front wheel is moving much faster than rear wheel) then temporarily reduce amount of braking
Inputs
  Brake pedal
  Front wheel speed
  Rear wheel speed
Outputs
  Pulse-width modulation rear wheel velocity
  Pulse-width modulation brake on/off

## Slide 10: Rear wheel controller/anti-lock brake system
micro controller
brake pedal pressed
front wheel velocity
rear wheel velocity
brake on/off
move rear wheel

## Slide 11: Basic I/O ports (brakes)
Check if brake pedal pressed – or interrupt
  brakePressed = read (brakePedalPort)
Turn brake on/off
  write (brakePort, onOff)
Move rear wheel
  write (rearWheel, onOff)
micro
controller
brake on/off
move rear wheel
GPIO
port
brake pedal pressed
front wheel velocity
rear wheel velocity
GPIO
port

## Slide 12: Polling vs. interrupts
Software must repeatedly check
  Brake pedal port
  How often?
  Need to make sure not to forget to do so (use timer)
Use automatic detection capability of processor
  Connect brake pedal to input capture or external interrupt pin
  Interrupt on level change
  Interrupt handler for brake pedal
micro
controller
GPIO
port
brake pedal pressed

## Slide 13: Pulse-width modulation for brakes
To pump the brakes gradually increase the duty-cycle (ton) until car stops
t
t

## Slide 14: Brake pump setup
Use timer to turn brake on and off
  Apply brake
  Set timer to interrupt after “on” time
  Disengage brake
  Set time to interrupt after “off” time
  Repeat
How do we tell which interrupt is which?
t
start timer running
set timer to go off at each edge

## Slide 15: Brake pump setup (cont’d)
Change value of “on” time to change analog average
  average output = ( on + off ) / ( period )
How do we decide on the period of the pulses?
Using two timers
  One to set period (auto-reload)
  One to turn it off at the right duty cycle
t
start timer running
set timer to go off at each edge

## Slide 16: Shaft encoders
Need to determine the rear wheel velocity
  Use sensor to detect wheel moving
Determine speed of a bicycle
  Attach baseball card so it pokes through spokes
  Number of spokes is known
  Count clicks per unit time to get velocity
Baseball card sensor is a shaft encoder
bike wheel
baseball card
click!

## Slide 17: Shaft encoders
Instead of spokes we’ll use black and white segments
Black segments absorb infrared light, white reflects
Count pulses instead of clicks
emitter
detector
wheel
infrared light
pulse

## Slide 18: IR reflective patterns
How many segments should be used?
  More segments give finer resolution
  Fewer segments require less processing
  Tradeoff resolution and processing

## Slide 19: Interfacing shaft encoders
Use interrupt on GPIO pin
  Every interrupt, increment counter
Use timer to set period for counting
  When timer interrupts, read GPIO pin counter
  velocity = counter  “known distance per click” / “judiciously chosen period”
  Reset counter
Pulse accumulator function
  Common function
  Some microcontrollers have this in a single peripheral device
  Basically a counter controlled by an outside signal
    Signal might enable counter to count at rate of internal clock – to measure time
    Signal might be the counter’s clock – to measure pulses
  ATmega16 has external clock source for timer/counter

## Slide 20: General interfaces to microcontrollers
Microcontrollers come with built-in I/O devices
  Timers/counters
  GPIO
  ADC
  Etc.
Sometimes we need more . . .
Options
  Get a microcontroller with a different mix of I/O
  Get a microcontroller with expansion capability
    Parallel memory bus (address and data) exposed to the outside world
    Serial communication to the outside world

## Slide 21: I/O ports
The are never enough I/O ports
Techniques for creating more ports
  port sharing with simple glue logic
  decoders/multiplexors
  memory-mapped I/O
  port expansion units
Direction of ports is important
  single direction port easier to implement
  timing important for bidirectional ports

## Slide 22: Port sharing
RS RW DB E
RS RW DB E
RS RW DB E
RS RW DB E
RS RW DB E
If signals all in same direction and have a separate guard signal, then able to share without glue logic
Example: connect 5 LCD displays to microcontroller
  can share connections to RS, RW, and DB but not E
  changes on E affect display – must guarantee only one is active

## Slide 23: Forced sharing
Conflict on device signals (e.g., one signal affects both)
  solution is to insert intervening registers that keep signals stable
  registers require enable signals which now need ports as well
µ C
device A
device B
µ C
D
Q
EN
D
Q
EN
device A
device B

## Slide 24: Decoders and multiplexors
Encode n single-bit device ports using log n bits of a controller port
  enabled decoder: one-hot, input-only device ports
  registered decoder: input-only (but not one-hot) device ports
  multiplexor: output-only device ports
n one-hot signals
log(n)
bits
enable
µC
enabled decoder
n signals
µC
log(n)
bits
enable
D
Q
EN
n register
select lines
registered decoder
µC
log(n)
select bits
n signals
data
multiplexor

## Slide 25: Memory-mapped I/O
Address bus selects device
Data bus contains data
addr
data
=
Device addr
E
Da
Db
latch

## Slide 26: Memory-mapped I/O
Partition the address space
Assign memory-mapped locations
Software
  loads read from the device
  stores write to the device
Can exploit unused bits for device input-only ports
device select
can be used as inputs
lsb
msb
address

## Slide 27: Port expansion units
Problem of port shortage so common port expansion chips exist
Easily connect to the microprocessor
Timing on ports may be slightly different
May not support interrupts
uC
port
expansion
data
ctrl
newPort1
newPort2
newPort3
addr

## Slide 28: Connecting to the outside world
Exploit specialized functions (e.g., UART, timers)
Attempt to connect directly to a device port without adding interface hardware (e.g., registers), try to share registers if possible but beware of unwanted interactions if a signal goes to more than one device
If out of ports, must force sharing by adding hardware to make a dedicated port sharable (e.g., adding registers and enable signals for the registers)
If still run out of ports, then most encode signals to increase bandwidth (e.g., use decoders)
If all else fails, then backup position is memory-mapped I/O, i.e., what we would have done if we had a bare microprocessor

## Slide 29: 64-bit General-purpose I/O port
Suppose we wanted a 64-bit I/O port
If EN is true, then we have an output pin
If EN is false, then we have an input pin

## Slide 30: 64-bit I/O port software
We need 8 8-bit registers to store/write the 64 bits
  Select the EN addresses to be $...000 to $...007
  Select OUT addresses to be $...010 to $...017
Read 15th bit
  load value at address $...011 (2nd set of OUT regs)
  logical AND with 0x80
  bit position 7 of result is 15th bit
Write the 47th bit
  read OUT register at $...015
  set bit position 7 to desired value ( or with 0x80)
  store in $...015
  load EN register at $...005
  set bit to output
  store value back to $...005

## Slide 31: External PWM Unit
Design a system to control a digital
Solution: design a PWM unit

## Slide 32: External PWM FSM Controller
if (onOff == OFF)
nextState = MotorLow
else if (highTime Expired)
nextState = MotorLow
else if (highTime NOT Expired)
nextState = MotorHigh
if (onOff == OFF)
nextState = MotorLow
reset counter
else if (period NOT Expired)
nextState = MotorLow
else if (period Expired)
nextState = MotorHigh
reset counter
Motor High State
Motor Low State

## Slide 33: External PWM software
// in initialization code
Write off to onOff register
// do some stuff
// set up PWM
Repeat for each motor
Write highTime and period registers
// turn motors on
Repeat for each motor
Write on to the onOFF register
// more stuff

## Slide 34: Some example I/O devices
Sonar range finder
Compass
IR proximity detector
Accelerometer
Bright LED

## Slide 35: Sonar range finder
Uses ultra-sound (not audible) to measure distance
Time echo return
Sound travels at approximately 343m/sec
  need at least a 34.3kHz timer for cm resolution
One simple echo not enough
  many possible reflections
  want to take multiple readings for high accuracy

## Slide 36: Polaroid 6500 sonar range finder
Commonly found on old Polaroid cameras, now a frequently used part in mobile robots
Transducer (gold disc)
  charged up to high voltage and “snapped”
  disc stays sentisized so it can detect echo (acts as microphone)
Controller board
  high-voltage circuitry to prepare disc for transmitting and then receiving

## Slide 37: Polaroid 6500 sonar range finder (cont’d)
Only need to connect two pins to microcontroller
  INIT - start transmitting
  ECHO - return signal
Some important information from data sheet
  INIT requires large current (greater than microcontroller can provide – add external buffer/amplifier)
  ECHO requires a pull-up resistor (determine current that needs to flow into microcontroller pin - size resistor so proper voltage is on pin

## Slide 38: Compass
Four compass directions (each has three pins)
One-hot/two-hot encoding
  one-hot for N, E, S, W
  two-hot for NE, SE, SW, NW
3 2 1
TOP
3
2
1
.5M
680
5V
12V
inside compass

## Slide 39: Compass (cont’d)
Detecting a change in compass direction
  4 bits change from 0001 to 0011 to 0010 to 0110 to 0100 …
  Always alternating between one bit on and two bits on
Parity tree can detect difference between one and two bits being asserted
  XOR tree of four bits (one TTL SSI package)
  Output must change at least once for every change in orientation
  Use interrupts to detect changes
N
E
S
W
e.g., NE  E  SE
1100  0100  0110 0  1  0

## Slide 40: IR proximity detector
micro controller
Oscillator must be set to match detector

## Slide 41: IR frequency modulation

## Slide 42: Proximity code
turn on emitter
sleep for 600us timer goes off
val_on = read detector wake
turn off emitter
sleep for 600us timer goes off
val_off = read detector wake
return ( val_on & ~val_off )
turn on emitter
set timer
sleep timer goes off
val_on = read detector
turn off emitter
reset timer
sleep timer goes off (again)
val_off = read detector
return ( val_on & ~val_off ) wake
Mostly in main
Using interrupt handlers

## Slide 43: More integrated proximity detector
Always sending out IR
Detector drives LED (guaranteed to match frequency)

## Slide 44: Accelerometer
Micro-electro-mechanical system that measures force
  F = ma (I. Newton)
  Measured as change in capacitance between moving plates
  Designed for a maximum g-force (e.g., 2-10g)
  2-axis and 3-axis versions
  Used in airbags, laptop disk drives, etc.

## Slide 45: Accelerometer output
Analog output too susceptible to noise
Digital output requires many pins for precision
Use pulse-width modulation
What about gravity?

## Slide 46: Analog Devices ADXL202
2-axis accelerometer
  Set 0g at 50% duty-cycle
  Positive acceleration increases duty cycle
  Negative acceleration decreases duty cycle
  12.5% per g in either direction

## Slide 47: Typical measurement for ADXL202
Noisy data – all forces are aggregated by accelerometer
Sample trace at 250Hz
Walking down six flights of stairs
Elevator ride

## Slide 48: Typical signal from ADXL202
Cause interrupts at Ta, Tb, and Tc from X-axis output
1. Look for rising edge, reset counter: Ta = 0
2. Look for falling edge, record timer: Tb = positive duty cycle
3. Look for rising edge, record timer, reset counter: Tc = period
Repeat from 2
Same for Y-axis output (T2 is the same for both axes)

## Slide 49: What to do about noise/jitter?
Average over time – smoothing
  Software filter – like switch debouncing
Take several readings
  use average for Tb and Tc or their ratio
Running average so that a reading is available at all times
  e.g., update running average of 4 readings current average = ¾ * current average + ¼ * new reading
Take readings of both Tb and Tc to be extra careful
  Tc changes with temperature
  Usually can do Tc just once

## Slide 50: Built-in filter
Filter capacitors limited noise frequency
  bandwidth limiting

## Slide 51: ADXL202 Output
Accelerometer duty cycle varies with force
12.5% for each g
RSET determines duration of period
At 1g duty-cycle will be 62.5% (37.5%)

## Slide 52: ADXL202 Orientation
Sensitivity (maximum duty cycle change per degree) is highest when accelerometer is perpendicular to gravity

## Slide 53: PWM Calculations
How big a counter do you need?
Assume 7.37MHz clock
1ms period yields a count of 7370
  This fits in a 16-bit timer/counter
Should you use a prescaler for the counter?
Bit precision issues
    unsigned int positive;
    unsigned int period;
    unsigned int pos_duty_cycle;
    BAD:
    pos_duty_cycle = positive/period;
    BAD:
    pos_duty_cycle = ( positive * 1000 ) / period;
    OKAY:
    pos_duty_cycle = ( (long) positive * 1000 ) / period;

## Slide 54: Bright LED
Easy to control intensity of light through pulse-width modulation
Duty-cycle is averaged by human eye
  Light is really turning on and off each period
  Too quickly for human retina (or most video cameras)
  Period must be short enough (< 1ms is a sure bet)
LED output is low to turn on light, high to turn it off
  Active low output

## Slide 55: Sample code for LED
Varying PWM output
volatile uint8_t width; /* positive pusle width */
volatile uint8_t delay; /* used to slow the pulse width changing */
SIGNAL (SIG_OVERFLOW2)
{
if(delay++ == 20) { OCR2 = width++; delay = 0; }
}
int main (void)
{
/* must make OC2 pin an output for the PWM to visible */
DDRD = _BV(DDD7);
/* use Timer 2 FastPWM and the overflow interrupt to update duty-cycle */
TCCR2 = _BV (WGM21) | _BV (WGM20) | _BV (COM21) | _BV(COM20) | _BV(CS21) | _BV(CS20);
TIMSK = _BV (TOIE2);
/* setup initial conditions */
delay = 0;
/* enable interrupts */
sei ();
for (;;)
{ ; /* LOOP FOREVER as the interrupt will make necessary adjustment */ }
return (0);
}

## Slide 56: Fast PWM