## Slide 1: Timers and Interrupts
Lecture 9

## Slide 2: Summary of Previous Lecture
The lab 80200 Big-Endian Evaluation Board
  80200 Intel Xscale® processor
  Xilinx FPGA
  PCI
The X-Board and accessories
  Seven-segment LED, Serial ports
Preparing you for Lab 2
  Flash memory
  Serial ports

## Slide 3: Administrivia
Lab 2 is out on the street
Lab 2 – Individual (and not a group) project

## Slide 4: Outline of This Lecture
Timers
Interrupt vs. polled I/O
  Examples
IRQ and FIQ
Detours signify material outside of, but indirect/direct background/review material for, the main lecture

## Slide 5: Questions on X-Board
What kind of power supply (wattage) are we using?
  We are using the standard ATX PC power supply
  Maximum of 300 W
  The voltages required by the board are 3.3V or 5V (if the PCI card is connected)
  The ATX can supply 3.3/5/12 V (the original adaptor could supply only 3.3V)

## Slide 6: Quote of the Day
The penalty of success is to be bored by the people who used to snub you.
  Lady Astor

## Slide 8: How Oscillators Work
Some form of energy needs to move back and forth
Capacitor stores energy in an electrostatic form
Inductor stores energy in a magnetic form
Oscillation cycle
  Capacitor starts off charged
  Capacitor discharges through inductor, creating a magnetic field
  Inductor tries to keep current moving and charges other plate of capacitor
  Inductor field collapses, but capacitor charged in opposite polarity
  Capacitor re-starts the cycle
Question: When does this stop?
Timer = oscillator + counter

## Slide 9: X-Board System Clocks
Two oscillators
  50 MHz and 66.6 MHz
  Connected to FPGA
All clocks are derived from these sources
  80200 Processor
    Multiplies 66.6 MHz clock by 6 at power-up (~ 400 MHz)
    Firmware multiplies this by an integer ranging from 5 (~333 MHz) to 11 (~733 MHz)
  Memory
    Multiplies the 50 MHz clock by 2 (~100 MHz)
  PCI and Serial Ports
    Divides the 50 MHz clock by 1.5 (~33.3 MHz)
  Ethernet
    Divides the 50 MHz clock by 2 (~25 MHz)

## Slide 10: X-Board System Clocks

## Slide 11: What is a Timer?
A device that uses high­speed clock input to provide a series of time or count-related events
÷
000000
0x1206
I/O Control
Clock Divider
Counter Register
Reload on Zero
Countdown Register
Interrupt to Processor
System Clock

## Slide 12: X-Board Timers
The X-Board has two timers
Timer A and Timer B
These timers can interrupt the 80200 processor
  Interrupt will be held active until cleared by the 80200
32-bit timers
33.3MHz peripheral bus clock is the time base
128 seconds maximum timing interval
Each timer consists of
  A down counter which reloads itself when it hits underflow
Can be programmed for one-shot operation
  Disables itself when it hits zero

## Slide 13: What Kinds of Timers Exist?
What is a timeout?
Pause Function
  Suspends task for a specified amount of time
One-shot timer
  Single one-time-only timeout
Periodic timer
  Multiple renewable timeouts
Time-slicing
  Chunks of time to each task
Watchdog timer

## Slide 14: X-Board Timer Status/Control Registers
Timer Status/Control Register
  One for each of the two timers
  To control the features of the timer

## Slide 15: X-Board Timer Preload Registers

## Slide 16: X-Board Timer Current Value

## Slide 17: Which Timers to Use for Lab 2?
We use all the 3 registers
Status-control register
  Used for control operations
  Enable/disable, clearing interrupts, etc.
Preload register
  Generally set to the highest possible value to get the longest possible time
Current value register
  Contains the current value while the timer is enabled.
There is some sample "timer" code in the appendix of the Lab2 handout.

## Slide 18: Inside the Timer
High Byte
Low Byte
Counter Register
at offsets 0x04, 0x00 (write only)
Current Counter
(not directly readable by software)
GO Register
offset 0x08, immediately moves
Counter Reg value into Current Counter
Latch Register
offset 0x0C, write a ``1'' to immediately write
Current Counter value to readable Latch Reg
Latched Counter
at offsets 0x04, 0x00 (read only)

## Slide 19: Structs for the Timer
In ANSI C, structs are laid out in RAM in ascending order
  Example for the timer
#define TIMER0 0x10200040
#define TIMER1 0x10200050
volatile struct timer_s {
  unsigned char countLow;
  unsigned char space1[3];
  unsigned char countHigh;
  unsigned char space2[3];
  unsigned char go;
  unsigned char space3[3];
  unsigned char latch;
  unsignec char space4[3];
};
typedef timer_s *timer_p;
timer_p timer;
timer = (timer_p) TIMER1;

## Slide 20: Setting the Timer's Counter Registers
Counter is usually programmed to reach zero X times per second
  To program the timer to reach zero 100 times per second
  Example: For a 2 MHz-based timer, 2MHz / 100 = 20,000
  #define TIMER1 0x10200050
  int time;
  time = 2000000 / 100;
  timer = (timer_p) TIMER1;
  timer­>countLow = (unsigned char) (time & 0xff);
  timer­>countHigh = (unsigned char) ((time > 8) & 0xff);
  timer­>go = (unsigned char) 0x1;

## Slide 21: Reading the Timer's Current Value
Must first dump the current value so that it can be read
  Why?
  #define TIMER1 0x10200050
  int time;
  timer = (timer_p) TIMER1;
  timer­>latch = (unsigned char) 1;
  time = (unsigned int) timer­>countLow;
  time = time | (unsigned int) (timer­>countHigh << 8);
How do we know when the timer has reached zero?
  while (1){
    timer­>latch = (unsigned char) 1;
    time = (unsigned int) timer­>countLow;
    time = time | (unsigned int) (timer­>countHigh << 8);
  }

## Slide 22: Interrupt vs. Polled I/O
Polled I/O requires the CPU to ask a device (e.g. toggle switches) if the device requires servicing
  For example, if the toggle switches have changed position
  Software plans for polling the devices and is written to know when a device will be serviced
Interrupt I/O allows the device to interrupt the processor, announcing that the device requires attention
  This allows the CPU to ignore devices unless they request servicing (via interrupts)
  Software cannot plan for an interrupt because interrupts can happen at any time ­­ therefore, software has no idea when an interrupt will occur
  This makes it more difficult to write code
Processors can be programmed to ignore interrupts
  We call this masking of interrupts
  Different types of interrupts can be masked (IRQ vs. FIQ)

## Slide 23: X-Board Interrupt Controller

## Slide 24: Polling Example
Polling the switches
#define SWITCH_BASE 0x18200000
int main(int argc, char * argv[])
{
  volatile unsigned int *switchBank = (unsigned int *) SWITCH_BASE;
  unsigned int tmpSwitchState;
  unsigned int prevSwitchState;
  /* get the current state of the switches */
  prevSwitchState = *switchBank & 0xff;
  while (1) {
    /* loop until a switch is pressed */
    while (prevSwitchState ==
    (tmpSwitchState = (*switchBank & 0xff))) {};
  }
} /* end main() */

## Slide 25: Polling vs. Interrupt­Driven I/O
Polling requires code to loop until device is ready
  Consumes lots of CPU cycles
  Can provide quick response (guaranteed delay)
Interrupts don't require code to loop until the device is ready
  Device interrupts processor when it needs attention
  Code can go off and do other things
  Interrupts can happen at any time
    Requires careful coding to make sure other programs (or your own) don't get messed up

## Slide 26: Polling the Serial Port - I
// Function to read from the serial keypad
unsigned char* my_gets(void)
{
unsigned char* char_ptr;
volatile unsigned char* UART_ptr;
unsigned int i;
static unsigned char char_buffer[116];
char_ptr = char_buffer;
*(volatile unsigned char*)UART2_FIFO_CNTRL = 0x06; // Clear FIFO
*char_ptr = *(volatile unsigned char*)UART2_RX_REG; // Empty any trash in the RX
for(i=0; i<sizeof(char_buffer); i++) {
char_buffer[i] = (unsigned char)NULL;
}
UART_ptr = (volatile unsigned char*)UART2_LINE_STAT;

## Slide 27: Polling the Serial Port - II
// Keep looking at characters until '\r'
while(1){
// Wait for Rx character forever
while ((*UART_ptr & 0x01) == 0) {
;
}
*char_ptr = *(volatile unsigned char*)UART2_RX_REG; // Read the character
if(*char_ptr != BACKSPACE) {
printf("%d",*char_ptr&0xffff); // Echo char back
if ((*char_ptr&0xffff) == 125)
sendchar("v");
}

## Slide 28: Polling the Serial Port - III
// Exit the 'while' when we see '\r' or the buffer fills
if((*char_ptr == '\r') || (char_ptr == &char_buffer[sizeof(char_buffer)-1]))
break;
// If Backspace, backup char_ptr so next char will overwrite bad input
if(*char_ptr == BACKSPACE){
if(char_ptr > char_buffer){
// If at least 1 character, backup cursor, delete character on screen, backup cursor
char_ptr--; // delete char from buffer
}
} else {
char_ptr++;
}
}
*char_ptr = '\000'; // Terminate the string
return(char_buffer);
}

## Slide 29: Windows NT Interrupt Architecture
When a device raises an interrupt, the interrupt-controller automatically masks all interrupts of lower priority
IRQL (Interrupt Request Level)
  Level of interrupt that the CPU is currently masking
HAL (Hardware Abstraction Layer)
  Maps interrupt-controller’s interrupt levels onto hardware interrupts
  IRQL Table
ISR (Interrupt Service Routine)
  Interrupt handlers registered with the interrupt-controller
Spinlock
  Synchronization primitive to prevent simultaneous ISR execution on multiple processors
DPC (Deferred procedure call)
  ISR indicates that it can do work at a lower priority level

## Slide 30: Windows NT Interrupt Architecture

## Slide 31: Interrupts and the Blue Screen of Death?
Two kinds of ISRs: Default system ISRs and user-registered ISRs
Unregistered interrupts made to point at ISRs that indicate that an illegal system interrupt has been generated
Illegal system interrupts often lead to the Blue Screen of Death

## Slide 32: IRQ and FIQ
Program Status Register
  To disable interrupts, set the corresponding “F” or “I” bit to 1
On interrupt, processor switches to FIQ32_mode registers or IRQ32_mode registers
  On any interrupt (or SWI Trap)
    Switch register banks
    Copy PC and CPSR to R14 and SPSR
    Change new CPSR mode bits
N
31 30 29 28 27 … 8 7 6 5 4 3 2 1 0
Z
C
V
I
F
M4
M3
M2
M1
M0

## Slide 33: Interrupt Example
Address Bus
D0
ARM 7500 Processor
D7
D6
D5
D4
D3
D2
D1
A0
A2
A4
A6
A8
A10
A12
A14
A16
A18
A20
A22
A24
A26
A28
A30
Vcc
Data Bus
8-bit register
31 30 29 28 27 … 8 7 6 5 4 3 2 1 0
N
Z
C
V
I
F
M4
M3
M2
M1
M0

## Slide 34: Summary of Lecture
Timers
  What is a timer?
  A peek inside the timers
  C structs for the timer
  Using the timer
Interrupt vs. polled I/O
  polling example
  interrupt example
IRQ and FIQ