## Slide 1: Buffering and DMA (Direct Memory Access)
Lecture 11

## Slide 2: Summary of Previous Lecture
Interrupts
  Interrupt handlers
  Nested interrupts
  Interrupt timing and metrics
  Interrupts on the X-Board
  Installing and writing interrupt handlers
Serial Communications
  Data communications and modulation
  Asynchronous protocols
  Serial port and bit transmission
  Serial I/O from device drivers

## Slide 3: Quote of the Day
I am grateful for all my problems. After each one was overcome, I became stronger and more able to meet those that were still to come. I grew in all my difficulties.
  J. C. Penney

## Slide 4: Lessons Learned From Lab 1
Some Common Mistakes from Part 1
Very little error checking
What happens when MOVS pc, lr instruction is executed in the SWIHandlerEntry.s assembly file ?
When does the stack pointer get initialized ?

## Slide 5: Common Misunderstanding
Loop unrolling not very clear. Assumed that only constant sized loops can be FULLY unrolled for loop unrolling and variable sized loops cannot easily be unrolled. e.g. A bad example of loop-unrolling for (i = 1; i < n; i++) foo; to for (i = 1; i < n - 1; i++) foo; foo;

## Slide 6: Outline of This Lecture
Concurrency between I/O and processing activities: An Introduction
Buffering
  dealing with nested interrupts
  critical sections and masking interrupts

## Slide 7: Interfacing Serial Data to Microprocessor
Processor has parallel buses for data ­­ need to convert serial data to parallel (and vice versa)
Standard way is with UART
UART ­ Universal asynchronous receiver and transmitter
  USART ­ Universal synchronous and asynchronous receiver and transmitter
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
Buffers
D0-D7

## Slide 8: Serial I/O
High­level I/O call
  printf(“the number is %d\n”, someNumber);
Low­level details
  printf() is a library call which formats the output (e.g., converts %d formats) and then makes system call to output the formatted string
    Formatted string is nothing more than an array of characters
    Low­level routines then output the string one character at a time using UART
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
D0-D7

## Slide 9: Conceptual View of Device Driver
while (*string != `\0')
printChar(*string++);
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
D0-D7
string

## Slide 10: Conceptual View of Device Driver (con't)
while (*string != '\0')
printChar(*string++);
string
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
D0-D7
One problem
the while loop can execute a lot faster than the UART can transmit characters

## Slide 11: Check UART for space
while (*string != '\0'){
  if (UART is empty()){
    printChar(*string++);
  }
}
string
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
D0-D7
1
2

## Slide 12: Device Driver (pseudo code)
output_string(char *string)
{
  while (*string != `\0')
  writeChar(*string++);
} /* end output_string() */
UARTBASE EQU 0x10010BE0
  LSR EQU 0x14
  LSR_Transmit EQU 0x20
writeChar
  LDR R1,= UARTBASE
  LDRB R3, [R1,#LSR]
B1 TST R3, #LSR_Transmit
  BEQ B1
  STRB R0, [R1]
  AND R0, R0, #0xff
  TEQ R0, #'\n'
  MOVENE PC,LR
  MOV R0, #'\r'
  B B01

## Slide 13: Concurrency between I/O and Processing
Keyboard command processing
      The “B” key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        ch <­ Read keyboard input register
        switch (ch) {
        case ‘b’ : startGame(); break;
        case ‘x’ : doSomeProcessing(); break;
        ...
        }
        }
return from ISR
How long does this processing take?

## Slide 14: Will Events Be Missed?
How fast is the keyboard_ISR()?
      The “B” key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR(){
        ch <­ Read keyboard input register
        switch (ch) {
        case ‘b’ : startGame(); break;
        case ‘x’ : doSomeProcessing(); break;
        ...
        }
        }
What happens if another key is pressed ­ or if a timer interrupt occurs?
return from ISR

## Slide 15: A More Elegant Solution
Add a buffer (in software or hardware) for input characters.
  This decouples the time for processing from the time between keystrokes, and provides a computable upper bound on the time required to service a keyboard interrupt.
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        *input_buffer++ = ch;
        ...
        }
Stores the input and then quickly returns to the “main program” (process)
return from ISR

## Slide 16: What Can Go Wrong?
1. Buffer could overflow (bigger buffer helps, but there is a limit)
2. Could another interrupt occur while adding the current keyboard character to the input_buffer?
Keyboard is pressed in the middle of incrementing *input_buffer++
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        *input_buffer++ = ch;
        ...
        }
return from ISR
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        *input_buffer++ = ch;
        ...
        }
return from ISR

## Slide 17: Masking Interrupts
If interrupts are masked (IRQ and FIQ disabled), nothing will be processed until the ISR completes and returns.
  Remember: entering IRQ mode masks IRQs and entering FIQ mode masks IRQs and FIQs
UART interrupts the processor
      A key is pressed by the user
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        MaskInterrupts();
        ch <­ Read keyboard input register
        *input_buffer++ = ch;
        UnmaskInterrupts();
      }
return from ISR
      The “keyboard” interrupts the processor
      Jump to keyboard ISR
        keyboard_ISR() {
        MaskInterrupts();
        ch <­ Read kbd in register
        *input_buffer++ = ch;
        UnmaskInterrupts();
        }
return from ISR
Keyboard is pressed in the middle of incrementing *input_buffer++

## Slide 18: Buffer Processing
Must be careful when modifying the buffer with interrupts turned on.
  while (!quit){
  if (*input_buffer){
  processCommand(*input_buffer);
  removeCommand(*input_buffer);
  }
  }
  keyboard_ISR(){
  MaskInterrupts();
  ch <­ Read ACIA input register
  *input_buffer++ = ch;
  UnmaskInterrupts();
  }
return from ISR
What happens if another command is entered as you remove one from the inputBuffer?

## Slide 19: Buffer Processing
How about the print buffer?
  printStr(*string)
  char *string;
  {
  while (*string) {
  outputBuffer[tail++] = *string++;
  }
}
  timer_ISR(){
  clockTicks++;
  printStr(convert(clockTicks));
  }
printStr(“this is a line”);
  T H I S I S 2 : 3 0
  T H I S I S
Jump to timer_ISR
tail points here ­ and a timer interrupt occurs

## Slide 20: Critical Sections of Code
Pieces of code that must appear as an atomic action
  T H I S I S
  printStr(*string)
  char *string;
  {
  MaskInterrupts();
  while (*string){
  outputBuffer[tail++] = *string++;
}
UnmaskInterrupts();
}
  timer_ISR(){
  clockTicks++;
  printStr(convert(clockTicks));
  }
printStr(“this is a line”);
  T H I S I S A L I N E
Jump to timer_ISR happens after printStr() completes
tail points here ­ and a timer interrupt occurs
Atomic action ­ action that “appears”' to take place in a single indivisible operation

## Slide 21: Increasing Concurrency Between I/O and Programs
So far today, we have seen how to use buffers to de-couple the speed of input/output devices from that of programs executing on the CPU
  and how to deal with the corresponding concurrency problems with masking of interrupts
Now, how can we push this farther??
  In particular, can we get the I/O to happen without needing the CPU for every single operation?!

## Slide 22: Summary of Lecture
Concurrency between I/O and processing activities
Buffering
  dealing with nested interrupts
  critical sections and masking interrupts