## Slide 1: A/D & D/A Conversion
Lecture 20

## Slide 2: Moving on...
We now move on from OS constructs to higher-level constructs for embedded systems
  with a minor detour through D/A and A/D conversion.

## Slide 3: Outline of This Lecture
Traditional Unix Scheduling
Analog to Digital Conversion
Digital to Analog Conversion
Periodic tasks
  Drift and jitter problems
  Timing problems in “traditional” implementations
  POSIX support

## Slide 4: Back to Basics
An A/D converter is a circuit that changes analog signals to digital signals
  Why do we need one?
A D/A converter is a circuit that changes digital signals to analog signals

## Slide 5: Sampling
To recover a signal function exactly, it is necessary to sample the signal at a rate greater than twice its highest frequency component
  What’s the fancy term for this sampling frequency?
What if we don’t respect this?
  Aliasing: Frequency may be mistaken for another when signal is recovered
Real-world signals contain a spectrum of frequencies
  Recovering such signals would require unreasonably high sample rates
How do we get around this?
  Precondition the signal to prevent aliasing
  Band-limiting filters
  Attenuation

## Slide 6: The Big Picture

## Slide 7: A/D and D/A Card Architecture
A modern A/D and D/A card has multiple ports starting from a selectable base address. These ports are organized as
  data register
  control and configuration
  status registers
A DAS-1600 Card’s base address may be set at 300H (using jumpers). Some of the entries in the port function table can be:
Address Read Function Write Function
Base A/D (bits 0 - 3) starts A/D conversion
(stores in bits 4..7)
Base + 1 A/D (bits 4 - 11) N/A
(stores in bits 0..7)
Base + 2 Channel Mux selection Set Channel Mux select
Base + 4 N/A D/A Ch 0 bits 0 - 3
Base + 5 N/A D/A Ch 0 bits 4 - 11
Base + 8 status clear interrupt
Base + 9 status sets card configuration

## Slide 8: High Byte and Low Byte
The A/D and D/A conversion logic may support 12-bit conversion. However, its data register is only 8 bits wide. Thus, it uses 2 registers. For example, input Ch 0’s 12 bits are stored in Base and Base + 1.
Base 3 2 1 0 x x x x
Base + 1 11 10 9 8 7 6 5 4
You need to
  Get HighByte from base+1 (bits 4 .. 11 of the 12 bit data)
  data = (HighByte << 8) to move the data into high byte
    = 11 10 9 8 7 6 5 4 x x x x x x x x
  Get LowByte from base (bits 0 .. 3 of the 12 bit data plus 4 bits of junk
  data = (HighByte | LowByte)
  = 11 10 9 8 7 6 5 4 3 2 1 0 x x x x
  data = (data >> 4) to get rid of the 4 bits of junk
  = 0 0 0 0 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 9: Control and Status Register
We need to initialize the card
  Set BASEADDR+9 to 0 disables interrupt and DMA.
  Set BASEADDR+8 to 0 clears trigger-flip flop for interrupt
  Set BASEADDR+2 to 0 selects analog input channel 0 (pin 37).
To sample the analog voltage and start the A/D conversion
  Set BASEADDR to 0
Once the A/D conversion starts, your program must wait for the A/D conversion to complete.
Bit 7 of BASEADDR+8 says whether the conversion is complete. Thus we AND the value with 0x80 (27 ) to get Bit 7 and wait until the conversion is done.
while (hw_input(BaseADDR+8) & 0x80 != 0) {}
Note: for certain cards, you may need to re-initialize it for every read.

## Slide 10: Digital Representation of Analog Voltage - 1
The N = 12 bits can be configured by jumpers/switches or software to represent different analog voltage ranges, e.g.
  -2.5 V to +2.5 V
  -5 V to +5 V and
  -10 V to +10 V.
What are these ranges for?
What should be the rule in picking a range?

## Slide 11: The General Conversion Rule
Converting the analog voltages to a N-bit digital representation is a special case of measurement conversion. The general rule is
  ((measure_1 – Measure_1_Lower_Limit)/range_1) * range_2 + Measure_2_Lower_Limit
Let’ s take the range between water freezing and boiling points at sea level. The measure using Celsius is from 0 to 100 while the measure using Fahrenheit is from 32 to 212.
Example: convert 600C to Fahrenheit:
  (60/(100 - 0))*(212 - 32) + 32 = 60 (180/100) + 32 = 60 * 9/5 + 32 0F
The general conversion rule is derived from the observation that since two different measures measure the same physical quantity.
  50% in measure_1 must correspond to 50% in measure_2.

## Slide 12: A/D and D/A Mapping
A/D: ((_______ - _______)/(________))*(__________) + __________
  ((V – V_lower_limit)/(analog_range))*digital_range + digital_lower_limit
D/A: ((________ - _______)/(________))*(__________) + __________
  ((digital_level)/digital_range)*analog_range + V_lower_limit
Example:
Analog voltage range is -1 to +2v The analog range is 2 – (-1) = 3
Digital levels are from 0 to (2n - 1) = 3 The digital range is 3 - 0 = 3
A/D: V = 1 maps to ((1 – (-1))/3)*3 = 2  10b
D/A: 10b maps to (2/3)*3 + (-1) = 1

## Slide 13: Single-Ended Input
External voltage can be connected with A/D cards via single-ended inputs or differential inputs.
Single-ended input measures the difference between ground and the input signal.
  It is susceptible to EMI interference
  It is susceptible to voltage differences between grounds of the A/D card and the ground of the signal source.
  They are fine in a low-noise lab environment.

## Slide 14: Differential Inputs
Differential connections are insensitive (e.g. up to 10 v) to ground differences and EMI.
However, electronically differential connections require twice the number of input lines.
For example,
  DAS 1600 may have 16 single-ended A/D inputs or 8 differential A/D inputs.

## Slide 15: Simultaneous A/D Converter

## Slide 16: Stair-Step A/D Converters

## Slide 17: Tracking A/D Converter

## Slide 18: Weighted D/A Converter

## Slide 19: Ladder D/A Converter

## Slide 20: Periodic Tasks
Periodic tasks are commonly used in embedded real time systems,
  e.g., a 10 Hz task updates the display and a 20 Hz task for sampling the temperature.
The Rate-Monotonic Scheduling (RMS) algorithm is commonly used in practice.
  RMS assigns high priorities to tasks with higher rates,
  e.g., the 20 Hz task should be given higher priority than the 10 Hz task.
If every instance of a periodic task has the same priority, it is called a fixed-priority scheduling method
Commercial RTOSs typically support only fixed priority scheduling
  RMS is an optimal fixed priority scheduling method
The timing behavior of a real time system scheduled by RMS, can be fully analyzed and predicted by Rate-Monotonic Analysis (RMA). We will study this subject in depth later (done already!)
  We will study the design and implementation of periodic tasks today.

## Slide 21: Periodic Tasks
A periodic task should repeat regularly according to a given period. For example, a periodic task with period 10 starting at t = 0.
Drift can be eliminated completely but one can only hope to minimize
jitter in general.

## Slide 22: Preemption: Potential Cause of Jitter & Drift
Tasks 1 and 2 are supposed to be ready to execute at time t = 0

## Slide 23: Evaluation: Sources of Jitter and Drifts
Suppose that we want to control a device using a 20 msec task starting at START_TIME:
1. current_time = read_clock()
2. If (START_TIME - current_time < 10 msec) { // report too late and exit }
3. sleep(START_TIME - current_time)
loop
4. current_time = read_clock()
5. wake_up_time = current_time + 20 msec
6. // read sensor data from the device
7. // do work
8. current_time = read_clock()
9. // send control data to the device
10. sleep(wake_up_time - current_time)
end_loop
Can you identify the 6 places that can introduce drift or jitter?
Hint: think of paging, multi-tasking and preemption.

## Slide 24: Potential Timing Problems
E1. It could be swapped out of memory (drift and jitter) pin it down in memory!
1. current_time = read_clock()
2. If (START_TIME - current_time < 10 msec) {//report too late and exit}
3. sleep(START_TIME - current_time) // E2: if preempted, drift
loop
4. current_time = read_clock() // E3: if preempted, drift
5. wake_up_time = current_time + 20 msec
6. Read sensor data // E4: if preempted input jitter
7. // do work
8. current_time = read_clock()
9. // send control data to the device // E5: output jitter (caused by
preemption or variable execution time)
10.sleep(wake_up_time - current_time) // E6: if preempted, drift
end_loop

## Slide 25: Solution Approach
To solve the drift problem, use a periodic, hardware-based timer to kick-start each instance of a periodic task. It will be ready at the correct time instants
To solve the jitter problem, do the I/O in the timer interrupt handler. As long as each task finishes before its end of period, I/O can be done at the regular instants of timer interrupt, the highest regularity.
Timer_interrupt handler()
//by convention, executes before application tasks
{
// do I/O ONLY
} // why not do both work and I/O in handler?
Task
{
loop
// wait for timer interrupt
// do computation
end_loop
}

## Slide 26: POSIX RT Time and Clocks
In POSIX-RT defines the structure of time representation. There must be at least 1 real-time clock.
  POSIX: IEEE 1003.1 Portable Operating System Interface standard
Clock resolution is hardware-dependent (typically 10 msec)
...
#include time.h
...
struct timespec current_time, clock_resolution
return_code = clock_gettime(CLOCK_REALTIME, &current_time);
// check return_code...
printf(“%d %d current time in CLOCK_REALTIME is \n”,
current_time.tv_sec, // the seconds portion
current_time.tv_nsec); // the nanoseconds portion
return_code = clock_getres(CLOCK_REALTIME, &clock_resolution)
// check return_code...
printf(“%d %d CLOCK_REALTIME’s resolution is \n”,
clock_resolution.tv_sec, clock_resolution.tv_nsec);

## Slide 27: POSIX RT Interval Timer (itimer) Structure
#include <signal.h>
#include <time.h>
...
struct timer_t timer_id;
// under POSIX, each thread defines its own timer for itself.
struct itimerspec timer_spec, old_timer_spec;
// old timer allows saving old timer definition to simulate multiple timers
return_code = timer_create(CLOCK_REALTIME, NULL, &timer_1_id);
// NULL: “no signal” mask used to block other signals, if any, sent to this task
timer_1_spec.it_value.tv_sec = 10; // 1st expiration time
timer_1_spec.it_value.tv_nsec = 0;
timer_1_spec.it_interval.tv_sec = 0; // task period
timer_1_spec.it_interval.tv_nsec = 20000000;
timer_settime(timer_1_id, 0, &timer_spec, &old_timer_spec) //initialize the periodic timer

## Slide 28: POSIX RT Timer Interrupt Handler
POSIX Timer generates signal (software interrupts), SIGALRM.
Action (ISR) for SIGALRM is therefore needed.
By POSIX coding conventions, you define a generic action and then bind the action to a specific handler you wrote
...
struct sigaction action, old_action //actions to catch a given signal arrives
...
// establish signal handler for SIGALRM
memset(&action, 0, sizeof(action));
// clear up the memory location to install the handler
action.sa_handler = (void *) timer_handler;
// the action is to be performed by timer_handler
return_code = sigaction(SIGALRM, &action, &old_action);
// binding the action to signal

## Slide 29: Putting it Together
// include header files signal.h, time.h, errno.h, stdio.h
// errno.h allows decoding of the return code
void timer_handler( )
// it is invoked by the timer, not called by your software
{ do your device I/O } // use global variables to communicate between main and handler
void main () {
// ask user to input the task rate, max volt and min volt. Check for validity whether the resolution is too high and whether the voltages are too high/low
// create your timer and initialize it
// set up your SIGALRM handler
while (1) {
sigpause(SIGALRM); // wait for signal SIGALRM
// do your computation, make the handler code as small as possible to reduce jitter.
}

## Slide 30: Summary of Lecture
Analog to Digital Conversion
  single-ended inputs
  differential inputs
Digital to Analog Conversion
  Voltage ranges and conversion between representations
Periodic tasks
  Rate-Monotonic Scheduling
  Drift and jitter
  Timing problems in “traditional” implementations
  POSIX timers and clocks
  POSIX interval structures