## Slide 1: ARM Monitor, Program Loading and Initialization
Lecture #5

## Slide 2: Summary of Previous Lecture
• Exception handling
• SWI (SoftWare Interrupts)
– what they are
– what they do
– what happens when they complete
– how to install one

## Slide 3: Announcement
Quiz #1 on Friday 2nd half of lecture
  Bring a calculator to any quiz (just in case)
  Materials included: beginning of the course to this lecture
  Open notes (any document/notes that are part of this course)
  Recommendation: Know your Intel Xscale® assembly language

## Slide 4: Outline of This Lecture
Overview of the ARM Debug Monitor
Loading a Program
The ARM Image Format
What happens on program startup?

## Slide 5: Thoughts for the Day
Associate yourself with [people] of good quality if you esteem your own reputation for 'tis better to be alone than in bad company.
–George Washington
Group yourself with students of good quality if you esteem your own grade for 'tis better to be alone than in bad company.
-Raj

## Slide 6: Recommended Readings
• ARM ELF
– Available on blackboard
•Course Documents Readings and ARM Manuals ARM ELF Spec
– “Detailed” document: use as ‘handy’ reference to clarify doubts

## Slide 7: Suggested Reading (not required)
backtrace structures
  – http://www.heyrick.co.uk/assembler/apcsintro.html

## Slide 8: Overview of ARM Debug Monitor
The ARM Debug Monitor is called “Angel” (earlier versions called it the “Demon” – get it?)
Provides
– lowlevel programming C library and debugging environment
When the X-board first boots, they load the demon from flash memory (emulator pretends that this happens)
–This activity is called “bootstrapping”

## Slide 9: Memory Map of Demon
  0x0000 CPU reset vector
  0x0004 ...0x1c CPU undefined instruction ... CPU Fast Interrupt Vector
  0x0020 ~1K Bytes for FIQ and FIQ mode stack
  0x0400 256 bytes for IRQ mode stack
  0x0500 256 bytes for Undefined mode stack
  0x0600 256 bytes for Abort mode stack
  0x0700 256 bytes for SVC mode stack
  0x0800 Debug monitor private workspace
  0x1000 Free for user-supplied Debug Monitor
  0x2000 Floating Point Emulation Space
  0x8000 Application Space
  top of memory SWI_Getenv returns top of memory = 0x08000000

## Slide 10: Monitor Program
Provide Capability to
  Setup Hardware on startup
  Load and run programs
  Debug code
  Minimal OS functionality
Many embedded systems are just
  Monitor + application
  Monitor still handles other types of interrupts (we'll cover this later)
  l timer, I/O (e.g., keypad, switches, LED, LCD)

## Slide 11: Example System
Interrupts from We refer to each piece of external devices software as a process
  such as keyboards, • codes
  timers, disk drives • program counters • registers
  • stacks
  Other terms:
  • task
  • thread

## Slide 12: Debug Monitor SWIs
• Angel provides a number of SWIs that you can use
SWI_WriteC (0) Write a byte to the debug channel
SWI_Write0(2) Write the null-terminated string to debug channel
SWI_ReadC(4) Read a byte from the debug channel
SWI_Exit (0x11) Halt emulation this is how a program exits
SWI_EnterOS (0x16) Put the processor in supervisor mode
SWI_GetErrno (0x60) Returns (r0) the value of the C library err-no variable
SWI_Clock (0x61) Return the number of centi-seconds
SWI_Time (0x63) Return the number of secs since Jan. 1, 1970
SWI_Remove (0x64) Deletes the file named by pointer in r0
SWI_Rename (0x65) Renames a file
SWI_Open (0x66) Open file (or device)
SWI_Close (0x68) Close a file (or device)
SWI_Write (0x69) Read a file
SWI_Read (0x6a) Write a file
SWI_Seek (0x6b) Seek to a specific location in a file
SWI_Flen (0x6c) Returns length of the file object
SWI_InstallHandler(0x70) installs a handler for a hardware exception

## Slide 13: Loading a program
Monitor (or you, in project 1, part 2) reads program from ???
  and puts it into RAM
  Does it just copy the executable into RAM??
  Where does it put it??
  Who sets up the user stack??
  Who sets up the user heap??

## Slide 14: ARM File Formats
ARM supports many formats for executables (see Chapter 21 of the Reference Manual)
Executable ARM Image Format (AIF)
  Nonexecutable ARM Image Format (AIF)
  ARM Object Format (AOF)
  ARM Object Library Format
  ARM Symbolic Debug Table Format
  AXF: ARM Executable Format (specialized version of ELF)
  ELF: Executable and Linking Format
Each provides code + data + other information
We will focus on the AXF: ARM Executable Format (AXF)

## Slide 15: ARM Executive Format (AXF)
ARM Executable Format (AXF)
  ELF (Executable and Link Format) header
  image's code
  image's initialized static data
  debug and relocation information (optional)
        We will use static linking
        (no dynamic linking or shared libraries)
ELF Header
Program Header Table
Segment 1
Segment 2
… …
Section Header Table optional
AXF File

## Slide 16: AXF ELF Header
#define EI_NIDENT 16
typedef struct {
unsigned char e_ident[EI_NIDENT]; // file info
Elf32_Half e_type; // type of file
Elf32_Half e_machine; // target processor
Elf32_Word e_version; // version #
Elf32_Addr e_entry; // program entry point
Elf32_Off e_phoff; // offset of program header
Elf32_Off e_shoff; // offset of section header table
Elf32_Word e_flags; // processor-specific flags
Elf32_Half e_ehsize; // ELF header’s size
Elf32_Half e_phentsize; // entry size in pgm header tbl
Elf32_Half e_phnum; // # of entries in pgm header
Elf32_Half e_shentsize; // entry size in sec header tbl
Elf32_Half e_shnum; // # of entries in sec header tbl
Elf32_Half e_shstrndx; // sec header tbl index of str tbl
} Elf32_Ehdr;
        See Section 3.2 of ARM ELF document.

## Slide 17: Sample File Layout

## Slide 18: Loading an Executive AIF Program
• Read the file from ???
– ARMulator gets stuff from the native file system
– Loader uses the SWI_Open and SWI_Read Monitor system calls
• Parse the header to determine the size of the image and its
– Starting Location
– Image Base
• Read the executable’s text and data segments into RAM
– Image Readonly size (text or code segment – SHF_EXECINSTR flag)
– Image ReadWrite size (initialized data segment – SHF_WRITE flag)
• Zeroinit the un-initialized data
• Determine the starting PC
– entryAddress = ImageEntryPoint + ?? (for prefetch) << ?? (word-aligned)
– Code + data + debug + offset (offset is determined empirically)
• Check offset of main in memory map after image has been read in
• Hard-wire offset in your program
• Recompile and run (works only for this program!)

## Slide 19: Memory Layout
Memory Layout for Loaded Executive AXF File

## Slide 20: Other “Gotcha”’s
• Who sets up the application's initial PC?
– The loader gets it from the header
• Who sets up the application's stack and heap?
– Loader (monitor) by convention
• Who cleans up after a program completes?
– Monitor can, when program executes SWI_Exit

## Slide 21: Optional AXF Components
• Compression
– self-decompression code included in image
• Relocation
– self relocation code included in image
• Debugging
– symbol table for debugger use
• String tables for efficient allocation of strings
• Can have more than one section per segment

## Slide 22: Starting a Program
We discussed how an application's initial PC is set
  The loader gets the address of the starting instruction from the object file (AXF) header
  To start the program, the loader moves the specified address into the PC
Is main() the starting point?
  In other words, does the PC initially get set to the address of main()?
  Let's look at an example

## Slide 23: Starting a Program
• Example based on the following C program
#include <stdio.h>
int foo(int);
int main (){
int i; int a[100], b, c; b = 2; c = 4; for (i = 0; i < 10; i++){ a[i] = b*c; c = a[i] * b; b = foo(c);
  }
} int foo (int c){
c = 2 * c;
return (c);
}

## Slide 24: Listing from AXD (1/11)

## Slide 25: AXD Listing (2/11)

## Slide 26: AXD Listing (3/11)

## Slide 27: AXD Listing (4/11)

## Slide 28: AXD Listing (5/11)

## Slide 29: Listing from AXD (6/11)

## Slide 30: Listing from AXD (7/11)

## Slide 31: Listing from AXD (8/11)

## Slide 32: Listing from AXD (9/11)

## Slide 33: Listing from AXD (10/11)

## Slide 34: Listing from AXD (11/11)

## Slide 35: Starting a Program
To get to main() takes hundreds of instructions!
  In a modern OS, it can take several thousands of instructions!
  Why? Because the C compiler generates code for a number of setup routines before the call to main().
  These setup routines handle the stack, data segments, heap and other miscellaneous functions.
What about assembly code?
  If the assembly code interfaces to C code and the ENTRY point is the C function main(), then the C compiler will generate the setup code
  But, if the entire program is written in assembly OR there is no C function called main(), then the setup code is not generated.
What does this mean for you?
– What's the SP register pointing to when you start your program?

## Slide 36: Complete Assembly Program Example

## Slide 37: Listing from ARMSD

## Slide 38: Summary of Lecture
• The ARM Debug Monitor
• Loading programs
• The ARM Image Format (AIF)
• What happens on program startup?