## Slide 1: Intel Xscale® Assembly Language and C
Lecture #3

## Slide 2: Summary of Previous Lectures
Course Description
What is an embedded system?
  More than just a computer ­­ it's a system
What makes embedded systems different?
  Many sets of constraints on designs
  Four general types:
    General-Purpose
    Control
    Signal Processing
    Communications
What embedded system designers need to know?
  Multi­objective: cost, dependability, performance, etc.
  Multi­discipline: hardware, software, electromechanical, etc.
  Multi-Phase: specification, design, prototyping, deployment, support, retirement

## Slide 3: Thought for the Day
The expectations of life depend upon diligence; the mechanic that would perfect his work must first sharpen his tools.
- Confucius
The expectations of this course depend upon diligence; the student that would perfect his grade must first sharpen his assembly language programming skills.

## Slide 4: Outline of This Lecture
The Intel Xscale® Programmer’s Model
Introduction to Intel Xscale® Assembly Language
Assembly Code from C Programs (7 Examples)
Dealing With Structures
Interfacing C Code with Intel Xscale® Assembly
Intel Xscale® libraries and armsd
Handouts:
  Copy of transparencies

## Slide 5: Documents available online
Course Documents  Lab Handouts  XScale Information  Documentation on ARM
  Assembler Guide
  CodeWarrior IDE Guide
  ARM Architecture Reference Manual
  ARM Developer Suite: Getting Started
  ARM Architecture Reference Manual

## Slide 6: The Intel Xscale® Programmer’s Model (1)
(We will not be using the Thumb instruction set.)
Memory Formats
  We will be using the Big Endian format
    the lowest numbered byte of a word is considered the word’s most significant byte, and the highest numbered byte is considered the least significant byte .
Instruction Length
  All instructions are 32-bits long.
Data Types
  8-bit bytes and 32-bit words.
Processor Modes (of interest)
  User: the “normal” program execution mode.
  IRQ: used for general-purpose interrupt handling.
  Supervisor: a protected mode for the operating system.

## Slide 7: The Intel Xscale® Programmer’s Model (2)
The Intel Xscale® Register Set
  Registers R0-R15 + CPSR (Current Program Status Register)
  R13: Stack Pointer
  R14: Link Register
  R15: Program Counter where bits 0:1 are ignored (why?)
Program Status Registers
  CPSR (Current Program Status Register)
    holds info about the most recently performed ALU operation
      contains N (negative), Z (zero), C (Carry) and V (oVerflow) bits
    controls the enabling and disabling of interrupts
    sets the processor operating mode
  SPSR (Saved Program Status Registers)
    used by exception handlers
Exceptions
  reset, undefined instruction, SWI, IRQ.

## Slide 8: Intro to Intel Xscale® Assembly Language
“Load/store” architecture
32-bit instructions
32-bit and 8-bit data types
32-bit addresses
37 registers (30 general-purpose registers, 6 status registers and a PC)
  only a subset is accessible at any point in time
Load and store multiple instructions
No instruction to move a 32-bit constant to a register (why?)
Conditional execution
Barrel shifter
  scaled addressing, multiplication by a small constant, and ‘constant’ generation
Co-processor instructions (we will not use these)

## Slide 9: The Structure of an Assembler Module
  AREA Example, CODE, READONLY ; name of code block
  ENTRY ; 1st exec. instruction
start
  MOV r0, #15 ; set up parameters
  MOV r1, #20
  BL func ; call subroutine
  SWI 0x11 ; terminate program
func ; the subroutine
  ADD r0, r0, r1 ; r0 = r0 + r1
  MOV pc, lr ; return from subroutine
  ; result in r0
  END ; end of code
Chunks of code or data manipulated by the linker
Minimum required block (why?)
First instruction to be executed

## Slide 10: Intel Xscale® Assembly Language Basics
Conditional Execution
The Intel Xscale® Barrel Shifter
Loading Constants into Registers
Loading Addresses into Registers
Jump Tables
Using the Load and Store Multiple Instructions
Check out Chapters 1 through 5 of the ARM Architecture Reference Manual

## Slide 11: Generating Assembly Language Code from C
Use the command-line option –S in the ‘target’ properties in Code Warrior.
  When you compile a .c file, you get a .s file
  This .s file contains the assembly language code generated by the compiler
    When assembled, this code can potentially be linked and loaded as an executable

## Slide 12: Example 1: A Simple Program
int a,b;
int main()
{
a = 3;
b = 4;
} /* end main() */
AREA ||.text||, CODE, READONLY
main PROC
|L1.0|
LDR r0,|L1.28|
MOV r1,#3
STR r1,[r0,#0] ; a
MOV r1,#4
STR r1,[r0,#4] ; b
MOV r0,#0
BX lr // subroutine call
|L1.28|
DCD ||.bss$2||
ENDP
AREA ||.bss||
a
||.bss$2||
% 4
b
% 4
EXPORT main
EXPORT b
EXPORT a
END
label “L1.28” ­ compiler tends to make the labels equal to the address
declare one or more words
loader will put the address of |||.bss$2| into this memory location
declares storage (1 32-bit word) and initializes it with zero

## Slide 13: Example 1 (cont’d)
AREA ||.text||, CODE, READONLY
main PROC
|L1.0|
LDR r0,|L1.28|
MOV r1,#3
STR r1,[r0,#0] ; a
MOV r1,#4
STR r1,[r0,#4] ; b
MOV r0,#0
BX lr // subroutine call
|L1.28|
DCD 0x00000020
ENDP
AREA ||.bss||
a
||.bss$2||
DCD 00000000
b
DCD 00000000
EXPORT main
EXPORT b
EXPORT a
END
This is a pointer to the |x$dataseg| location
address
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000014
0x00000018
0x0000001C
0x00000020
0x00000024

## Slide 14: Example 2: Calling A Function
int tmp;
void swap(int a, int b);
int main()
{
int a,b;
a = 3;
b = 4;
swap(a,b);
} /* end main() */
void swap(int a,int b)
{
tmp = a;
a = b;
b = tmp;
} /* end swap() */
AREA ||.text||, CODE, READONLY
swap PROC
LDR r2,|L1.56|
STR r0,[r2,#0] ; tmp
MOV r0,r1
LDR r2,|L1.56|
LDR r1,[r2,#0] ; tmp
BX lr
main PROC
STMFD sp!,{r4,lr}
MOV r3,#3
MOV r4,#4
MOV r1,r4
MOV r0,r3
BL swap
MOV r0,#0
LDMFD sp!,{r4,pc}
|L1.56| DCD ||.bss$2|| ; points to tmp
END
STMFD ­ store multiple,
full descending
sp  sp ­ 4
mem[sp] = lr ; linkreg
sp  sp – 4
mem[sp] = r4 ; linkreg
contents of lr
SP
contents of r4

## Slide 15: Example 3: Manipulating Pointers
int tmp;
int *pa, *pb;
void swap(int a, int b);
int main()
{
int a,b;
pa = &a;
pb = &b;
*pa = 3;
*pb = 4;
swap(*pa, *pb);
} /* end main() */
void swap(int a,int b)
{
tmp = a;
a = b;
b = tmp;
} /* end swap() */
AREA ||.text||, CODE, READONLY
swap LDR r1,|L1.60| ; get tmp addr
STR r0,[r1,#0] ; tmp = a
BX lr
main STMFD sp!,{r2,r3,lr}
LDR r0,|L1.60| ; get tmp addr
ADD r1,sp,#4 ; &a on stack
STR r1,[r0,#4] ; pa = &a
STR sp,[r0,#8] ; pb = &b (sp)
MOV r0,#3
STR r0,[sp,#4] ; *pa = 3
MOV r1,#4
STR r1,[sp,#0] ; *pb = 4
BL swap ; call swap
MOV r0,#0
LDMFD sp!,{r2,r3,pc}
|L1.60| DCD ||.bss$2||
AREA ||.bss||
||.bss$2||
tmp DCD 00000000
pa DCD 00000000
pb DCD 00000000

## Slide 16: Example 3 (cont’d)
AREA ||.text||, CODE, READONLY
swap LDR r1,|L1.60|
STR r0,[r1,#0]
BX lr
main STMFD sp!,{r2,r3,lr}
LDR r0,|L1.60| ; get tmp addr
ADD r1,sp,#4 ; &a on stack
STR r1,[r0,#4] ; pa = &a
STR sp,[r0,#8] ; pb = &b (sp)
MOV r0,#3
STR r0,[sp,#4]
MOV r1,#4
STR r1,[sp,#0]
BL swap
MOV r0,#0
LDMFD sp!,{r2,r3,pc}
|L1.60| DCD ||.bss$2||
AREA ||.bss
||.bss$2||
tmp DCD 00000000
pa DCD 00000000 ; tmp addr + 4
pb DCD 00000000 ; tmp addr + 8
contents of lr
SP
address
0x90
0x8c
0x88
0x84
0x80
1
1
contents of lr
a
b
SP
address
0x90
0x8c
0x88
0x84
0x80
main’s local variables a and b are placed on the stack
2
2
contents of r3
contents of r2

## Slide 17: Example 4: Dealing with “struct”s
typedef struct
testStruct {
unsigned int a;
unsigned int b;
char c;
} testStruct;
testStruct *ptest;
int main()
{
ptest­>a = 4;
ptest­>b = 10;
ptest­>c = 'A';
} /* end main() */
AREA ||.text||, CODE, READONLY
main PROC
|L1.0|
MOV r0,#4 ; r0  4
LDR r1,|L1.56|
LDR r1,[r1,#0] ; r1  &ptest
STR r0,[r1,#0] ; ptest->a = 4
MOV r0,#0xa ; r0  10
LDR r1,|L1.56|
LDR r1,[r1,#0] ; r1  ptest
STR r0,[r1,#4] ; ptest->b = 10
MOV r0,#0x41 ; r0  ‘A’
LDR r1,|L1.56|
LDR r1,[r1,#0] ; r1  &ptest
STRB r0,[r1,#8] ; ptest->c = ‘A’
MOV r0,#0
BX lr
|L1.56|
DCD ||.bss$2||
AREA ||.bss||
ptest
||.bss$2||
% 4
r1  M[#L1.56] is the pointer to ptest
watch out, ptest is only a ptr
the structure was never malloc'd!

## Slide 18: Questions?

## Slide 19: Example 5: Dealing with Lots of Arguments
int tmp;
void test(int a, int b, int c, int d, int *e);
int main()
{ int a, b, c, d, e;
a = 3;
b = 4;
c = 5;
d = 6;
e = 7;
test(a, b, c, d, &e);
} /* end main() */
void test(int a,int b,
int c, int d, int *e)
{
tmp = a;
a = b;
b = tmp;
c = b;
b = d;
*e = d;
} /* end test() */
AREA ||.text||, CODE, READONLY
test LDR r1,[sp,#0] ; get &e
LDR r2,|L1.72| ; get tmp addr
STR r0,[r2,#0] ; tmp = a
STR r3,[r1,#0] ; *e = d
BX lr
main PROC
STMFD sp!,{r2,r3,lr} ;  2 slots
MOV r0,#3 ; 1st param a
MOV r1,#4 ; 2nd param b
MOV r2,#5 ; 3rd param c
MOV r12,#6 ; 4th param d
MOV r3,#7 ; overflow  stack
STR r3,[sp,#4] ; e on stack
ADD r3,sp,#4
STR r3,[sp,#0] ; &e on stack
MOV r3,r12 ; 4th param d in r3
BL test
MOV r0,#0
LDMFD sp!,{r2,r3,pc}
|L1.72|
DCD ||.bss$2||
tmp
r0 holds the return value

## Slide 20: Example 5 (cont’d)
AREA ||.text||, CODE, READONLY
test LDR r1,[sp,#0] ; get &e
LDR r2,|L1.72| ; get tmp addr
STR r0,[r2,#0] ; tmp = a
STR r3,[r1,#0] ; *e = d
BX lr
main PROC
STMFD sp!,{r2,r3,lr} ;  2 slots
MOV r0,#3 ; 1st param a
MOV r1,#4 ; 2nd param b
MOV r2,#5 ; 3rd param c
MOV r12,#6 ; 4th param d
MOV r3,#7 ; overflow  stack
STR r3,[sp,#4] ; e on stack
ADD r3,sp,#4
STR r3,[sp,#0] ; &e on stack
MOV r3,r12 ; 4th param d in r3
BL test
MOV r0,#0
LDMFD sp!,{r2,r3,pc}
|L1.72|
DCD ||.bss$2||
tmp
#7
SP
address
0x90
0x8c
0x88
0x84
0x80
2
3
SP
address
0x90
0x8c
0x88
0x84
0x80
1
1
Note: In “test”, the compiler removed the assignments to a, b, and c ­­ these assignments have no effect, so they were removed
contents of lr
contents of r3
contents of r2
#7
0x8c
SP
address
0x90
0x8c
0x88
0x84
0x80
3
2

## Slide 21: Example 6: Nested Function Calls
int tmp;
int swap(int a, int b);
void swap2(int a, int b);
int main(){
int a, b, c;
a = 3;
b = 4;
c = swap(a,b);
} /* end main() */
int swap(int a,int b){
tmp = a;
a = b;
b = tmp;
swap2(a,b);
return(10);
} /* end swap() */
void swap2(int a,int b){
tmp = a;
a = b;
b = tmp;
} /* end swap() */
swap2 LDR r1,|L1.72|
STR r0,[r1,#0] ; tmp  a
BX lr
swap MOV r2,r0
MOV r0,r1
STR lr,[sp,#-4]! ; save lr
LDR r1,|L1.72|
STR r2,[r1,#0]
MOV r1,r2
BL swap2 ; call swap2
MOV r0,#0xa ; ret value
LDR pc,[sp],#4 ; restore lr
main STR lr,[sp,#-4]!
MOV r0,#3 ; set up params
MOV r1,#4 ; before call
BL swap ; to swap
MOV r0,#0
LDR pc,[sp],#4
|L1.72|
DCD ||.bss$2||
  AREA ||.bss||, NOINIT, ALIGN=2
tmp

## Slide 22: Example 7: Optimizing across Functions
int tmp;
int swap(int a,int b);
void swap2(int a,int b);
int main(){
int a, b, c;
a = 3;
b = 4;
c = swap(a,b);
} /* end main() */
int swap(int a,int b){
tmp = a;
a = b;
b = tmp;
swap2(a,b);
} /* end swap() */
void swap2(int a,int b){
tmp = a;
a = b;
b = tmp;
} /* end swap() */
AREA ||.text||, CODE, READONLY
swap2 LDR r1,|L1.60|
STR r0,[r1,#0] ; tmp
BX lr
swap MOV r2,r0
MOV r0,r1
LDR r1,|L1.60|
STR r2,[r1,#0] ; tmp
MOV r1,r2
B swap2 ; *NOT* “BL”
main PROC
STR lr,[sp,#-4]!
MOV r0,#3
MOV r1,#4
BL swap
MOV r0,#0
LDR pc,[sp],#4
|L1.60|
DCD ||.bss$2||
AREA ||.bss||, tmp
||.bss$2||
% 4
Compare with Example 6 ­ in this example, the compiler optimizes the code so that swap2() returns directly to main()
Doesn't return to swap(), instead it jumps directly back to main()

## Slide 23: Interfacing C and Assembly Language
ARM (the company @ www.arm.com) has developed a standard called the “ARM Procedure Call Standard” (APCS) which defines:
  constraints on the use of registers
  stack conventions
  format of a stack backtrace data structure
  argument passing and result return
  support for ARM shared library mechanism
Compiler­generated code conforms to the APCS
  It's just a standard ­ not an architectural requirement
  Cannot avoid standard when interfacing C and assembly code
  Can avoid standard when just writing assembly code or when writing assembly code that isn't called by C code

## Slide 24: Register Names and Use
Register # APCS Name APCS Role
R0 a1 argument 1
R1 a2 argument 2
R2 a3 argument 3
R3 a4 argument 4
R4..R8 v1..v5 register variables
R9 sb/v6 static base/register variable
R10 sl/v7 stack limit/register variable
R11 fp frame pointer
R12 ip scratch reg/ new­sb in inter­link­unit calls
R13 sp low end of current stack frame
R14 lr link address/scratch register
R15 pc program counter

## Slide 25: How Does STM Place Things into Memory ?
STM sp!, {r0­r15}
The XScale processor uses a bit-vector to represent each register to be saved
The architecture places the lowest number register into the lowest address
Default STM == STMDB
pc
lr
sp
SPbefore
address
0x90
0x8c
0x88
0x84
0x80
0x7c
0x78
0x74
0x70
0x6c
0x68
0x64
0x60
0x5c
0x58
0x54
0x50
ip
fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
SPafter

## Slide 26: Passing and Returning Structures
Structures are usually passed in registers (and overflow onto the stack when necessary)
When a function returns a struct, a pointer to where the struct result is to be placed is passed in a1 (first parameter)
Example
  struct s f(int x);
  ­­ is compiled as ­­
  void f(struct s *result, int x);

## Slide 27: Example: Passing Structures as Pointers
typedef struct two_ch_struct{
char ch1;
char ch2;
} two_ch;
two_ch max(two_ch a, two_ch b){
return((a.ch1 > b.ch1) ? a : b);
} /* end max() */
max PROC
STMFD sp!,{r0,r1,lr}
SUB sp,sp,#4
LDRB r0,[sp,#4]
LDRB r1,[sp,#8]
CMP r0,r1
BLS |L1.36|
LDR r0,[sp,#4]
STR r0,[sp,#0]
B |L1.44|
|L1.36|
LDR r0,[sp,#8]
STR r0,[sp,#0]
|L1.44|
LDR r0,[sp,#0]
LDMFD sp!,{r1-r3,pc}
ENDP

## Slide 28: “Frame Pointer”
foo
MOV ip, sp
STMDB sp!,{a1­a3, fp, ip, lr, pc}
<computations go here>
LDMDB fp,{fp, sp, pc}
pc
lr
ip
fp
address
0x90
0x8c
0x88
0x84
0x80
0x7c
0x78
0x74
0x70
fp
1
a3
a2
a1
1
ip
SP
frame pointer (fp) points to the top of stack for function

## Slide 29: The Frame Pointer
fp points to top of the stack area for the current function
  Or zero if not being used
By using the frame pointer and storing it at the same offset for every function call, it creates a singly­linked list of activation records
Creating the stack “backtrace” structure
MOV ip, sp
STMFD sp!,{a1­a4,v1­v5,sb,fp,ip,lr,pc}
SUB fp, ip, #4
pc
lr
sb
SPbefore
address
0x90
0x8c
0x88
0x84
0x80
0x7c
0x78
0x74
0x70
0x6c
0x68
0x64
0x60
0x5c
0x58
0x54
0x50
ip
fp
v7
v6
v5
v4
v3
v2
v1
a4
a3
a2
a1
SPafter
FPafter

## Slide 30: Mixing C and Assembly Language
XScale
Assembly
Code
C Library
C Source
Code
XScale
Executable
Compiler
Linker
Assembler

## Slide 31: Multiply
Multiply instruction can take multiple cycles
  Can convert Y * Constant into series of adds and shifts
  Y * 9 = Y * 8 + Y * 1
  Assume R1 holds Y and R2 will hold the result
  ADD R2, R2, R1, LSL #3 ; multiplication by 9 (Y * 8) + (Y * 1)
  RSB R2, R1, R1, LSL #3 ; multiplication by 7 (Y * 8) - (Y * 1)
  (RSB: reverse subtract - operands to subtraction are reversed)
Another example: Y * 105
  105 = 128 ­ 23 = 128 ­ (16 + 7) = 128 ­ (16 + (8 ­ 1))
  RSB r2, r1, r1, LSL #3 ; r2 <­­ Y*7 = Y*8 ­ Y*1(assume r1 holds Y)
  ADD r2, r2, r1, LSL #4 ; r2 <­­ r2 + Y * 16 (r2 held Y*7; now holds Y*23)
  RSB r2, r2, r1, LSL #7 ; r2 <­­ (Y * 128) ­ r2 (r2 now holds Y*105)
Or Y * 105 = Y * (15 * 7) = Y * (16 ­ 1) * (8 ­ 1)
  RSB r2,r1,r1,LSL #4 ; r2 <­­ (r1 * 16)­ r1
  RSB r3, r2, r2, LSL #3 ; r3 <­­ (r2 * 8)­ r2

## Slide 32: Looking Ahead
Software Interrupts (traps)

## Slide 33: Suggested Reading (NOT required)
Activation Records (for backtrace structures)
  http://www.enel.ucalgary.ca/People/Norman/engg335/activ_rec/