## Slide 1: Resource Management in (Embedded) Real-Time Systems
Lecture 17

## Slide 2: Summary of Previous Lecture
More on Synchronization and Deadlocks
  Mutex and Barrier synchronization
  Deadlocks
  Necessary conditions for deadlock
  Deadlock prevention, avoidance and detection/recovery
  Banker’s algorithm
  Wait-for graphs

## Slide 3: Mid-Term Exam Grades
Scores at Pittsburgh
Mean = 76.23%

## Slide 4: Thought for the Day
All our dreams can come true if we have the courage to pursue them.
  Walt Disney

## Slide 5: Outline of This Lecture
Real-time Systems
  characteristics and mis-conceptions
  the “window of scarcity”
Example real-time systems
  simple control systems
  multi-rate control systems
  hierarchical control systems
  signal processing systems
Terminology
Scheduling algorithms
Rate-Monotonic Analysis (RMA)
  Real time systems and you
  Fundamental concepts
  An Introduction to Rate-Monotonic Analysis: independent tasks
We will zip through these!

## Slide 6: Real-time System
A real-time system is a system whose specification includes both logical and temporal correctness requirements.
  Logical Correctness: Produces correct outputs.
    Can by checked, for example, by Hoare logic.
  Temporal Correctness: Produces outputs at the right time.
    It is not enough to say that “brakes were applied”
    You want to be able to say “brakes were applied at the right time”
      In this course, we spend much time on techniques for checking temporal correctness.
      The question of how to specify temporal requirements, though enormously important, is shortchanged in this course.

## Slide 7: Characteristics of Real-Time Systems
Event-driven, reactive.
High cost of failure.
Concurrency/multiprogramming.
Stand-alone/continuous operation.
Reliability/fault-tolerance requirements.
Predictable behavior.

## Slide 8: Example Real-Time Applications
Many real-time systems are control systems.
Example 1: A simple one-sensor, one-actuator control system.
control-law
computation
A/D
A/D
D/A
sensor
plant
actuator
rk
yk
y(t)
u(t)
uk
reference
input r(t)
The system
being controlled

## Slide 9: Simple Control System (cont’d)
Pseudo-code for this system:
set timer to interrupt periodically with period T;
at each timer interrupt do
do analog-to-digital conversion to get y;
compute control output u;
output u and do digital-to-analog conversion;
end do
T is called the sampling period. T is a key design choice. Typical
range for T: seconds to milliseconds.

## Slide 10: Multi-rate Control Systems
More complicated control systems have multiple sensors and actuators
and must support control loops of different rates.
Example 2: Helicopter flight controller.
Do the following in each 1/180-sec. cycle:
validate sensor data and select data source;
if failure, reconfigure the system
Every sixth cycle do:
keyboard input and mode selection;
data normalization and coordinate
transformation;
tracking reference update
control laws of the outer pitch-control loop;
control laws of the outer roll-control loop;
control laws of the outer yaw- and
collective-control loop
Every other cycle do:
control laws of the inner
pitch-control loop;
control laws of the inner roll- and
collective-control loop
Compute the control laws of the inner
yaw-control loop;
Output commands;
Carry out built-in test;
Wait until beginning of the next cycle
Note: Having only harmonic rates simplifies the system.

## Slide 11: Hierarchical Control Systems
Example 3:
Air traffic-flight
control hierarchy.
state
estimator
state
estimator
state
estimator



air traffic
control
flight
management
flight
control
air data
navigation
virtual plant
virtual plant
operator-system
interface
physical plant
from sensors
responses
commands
sampling
rates may
be minutes
or even
hours
sampling
rates may
be secs.
or msecs.

## Slide 12: Signal-Processing Systems
Signal-processing systems transform data from one form to another.
Examples:
  Digital filtering.
  Video and voice compression/decompression.
  Radar signal processing.
Response times range from a few milliseconds to a few seconds.

## Slide 13: Example: Radar System
DSP
radar
memory
DSP
DSP
signal
processors
data
processor
track
records
track
records
signal
processing
parameters
control
status
sampled
digitized
data

## Slide 14: Other Real-Time Applications
Real-time databases.
    Transactions must complete by deadlines.
    Main dilemma: Transaction scheduling algorithms and real-time scheduling algorithms often have conflicting goals.
    Data may be subject to absolute and relative temporal consistency requirements.
Multimedia.
    Want to process audio and video frames at steady rates.
      TV video rate is 30 frames/sec. HDTV is 60 frames/sec.
      Telephone audio is 16 Kbits/sec. CD audio is 128 Kbits/sec.
    Other requirements: Lip synchronization, low jitter, low end-to-end response times (if interactive).

## Slide 15: Are All Systems Real-Time Systems?
Question: Is a payroll processing system a real-time system?
  It has a time constraint: Print the pay checks every two weeks.
Perhaps it is a real-time system in a definitional sense, but it doesn’t pay us to view it as such.
We are interested in systems for which it is not a priori obvious how to meet timing constraints.

## Slide 16: The “Window of Scarcity”
Resources may be categorized as:
  Abundant: Virtually any system design methodology can be used to realize the timing requirements of the application.
  Insufficient: The application is ahead of the technology curve; no design methodology can be used to realize the timing requirements of the application.
  Sufficient but scarce: It is possible to realize the timing requirements of the application, but careful resource allocation is required.

## Slide 17: Example: Interactive/Multimedia Applications
sufficient
but scarce
resources
abundant
resources
insufficient
resources
Requirements
(performance, scale)
1980
1990
2000
Hardware resources in year X
Remote
Login
Network
File Access
High-quality
Audio
Interactive
Video
The interesting
real-time
applications
are here

## Slide 18: Hard vs. Soft Real Time
  Task: A sequential piece of code.
  Job: Instance of a task.
  Jobs require resources to execute.
      Example resources: CPU, network, disk, critical section.
      We will simply call all hardware resources “processors”.
  Release time of a job: The time instant the job becomes ready to execute.
  Absolute Deadline of a job: The time instant by which the job must complete execution.
  Relative deadline of a job: “Deadline  Release time”.
  Response time of a job: “Completion time  Release time”.

## Slide 19: Example
= job release
= job deadline
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
Job is released at time 3.
Its (absolute) deadline is at time 10.
Its relative deadline is 7.
Its response time is 6.

## Slide 20: Hard Real-Time Systems
A hard deadline must be met.
  If any hard deadline is ever missed, then the system is incorrect.
  Requires a means for validating that deadlines are met.
Hard real-time system: A real-time system in which all deadlines are hard.
  We mostly consider hard real-time systems in this course.
Examples: Nuclear power plant control, flight control.

## Slide 21: Soft Real-Time Systems
A soft deadline may occasionally be missed.
  Question: How to define “occasionally”?
Soft real-time system: A real-time system in which some deadlines are soft.
Examples: Telephone switches, multimedia applications.

## Slide 22: Defining “Occasionally”
One Approach: Use probabilistic requirements.
  For example, 99% of deadlines will be met.
Another Approach: Define a “usefulness” function for each job:
Note: Validation is trickier here.
1
0
relative
deadline

## Slide 23: Reference Model
Each job Ji is characterized by its release time ri, absolute deadline di, relative deadline Di, and execution time ei.
  Sometimes a range of release times is specified: [ri, ri+]. This range is called release-time jitter.
Likewise, sometimes instead of ei, execution time is specified to range over [ei, ei+].
  Note: It can be difficult to get a precise estimate of ei (more on this later).

## Slide 24: Periodic, Sporadic, Aperiodic Tasks
Periodic task:
  We associate a period pi with each task Ti.
  pi is the interval between job releases.
Sporadic and Aperiodic tasks: Released at arbitrary times.
  Sporadic: Has a hard deadline.
  Aperiodic: Has no deadline or a soft deadline.

## Slide 25: Examples
= job release
= job deadline
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18
A periodic task Ti with ri = 2, pi = 5, ei = 2, Di =5 executes like this:

## Slide 26: Classification of Scheduling Algorithms
All scheduling algorithms
static scheduling
(or offline, or clock driven)
dynamic scheduling
(or online, or priority driven)
static-priority
scheduling
dynamic-priority
scheduling

## Slide 27: Summary of Lecture So Far
Real-time Systems
  characteristics and mis-conceptions
  the “window of scarcity”
Example real-time systems
  simple control systems
  multi-rate control systems
  hierarchical control systems
  signal processing systems
Terminology
Scheduling algorithms

## Slide 28: Real Time Systems and You
Embedded real time systems enable us to:
  manage the vast power generation and distribution networks,
  control industrial processes for chemicals, fuel, medicine, and manufactured products,
  control automobiles, ships, trains and airplanes,
  conduct video conferencing over the Internet and interactive electronic commerce, and
  send vehicles high into space and deep into the sea to explore new frontiers and to seek new knowledge.

## Slide 29: Real-Time Systems
Timing requirements
  meeting deadlines
Periodic and aperiodic tasks
Shared resources
Interrupts
Notes: <number>
<footer>
<header>
<date/time>
4
Real-time systems generally consist of independently schedulable threads of control called tasks. Here the term task does not necessarily mean an Ada task; rather, a schedulable unit of processing, like a process or thread.
Tasks may be periodic or aperiodic
Periodic tasks are initiated at regular intervals.
Aperiodic tasks are initiated at irregular intervals.
Tasks have deadlines which may be hard or soft.
Failure to meet hard deadlines results in system failure.
Failure to meet soft deadlines degrades system performance.
For the purposes of this workshop, we assume:
Deadline for periodic task is hard (either at or before end of period).
Deadline for aperiodic task may be hard or soft.
Some investigators further categorize tasks as being critical or non-critical. Failure of a critical task to meet a hard deadline (if one exists) is considered catastrophic

## Slide 30: What’s Important in Real-Time
Metrics for real-time systems differ from that for time-sharing systems.
  schedulability is the ability of tasks to meet all hard deadlines
  latency is the worst-case system response time to events
  stability in overload means the system meets critical deadlines even if all deadlines cannot be met
 | Time-Sharing Systems | Real-Time Systems
Capacity | High throughput | Schedulability
Responsiveness | Fast average response | Ensured worst-case response
Overload | Fairness | Stability

## Slide 31: Scheduling Policies
CPU scheduling policy: a rule to select task to run next
  cyclic executive
  rate monotonic/deadline monotonic
  earliest deadline first
  least laxity first
Assume preemptive, priority scheduling of tasks
  analyze effects of non-preemption later
Notes: <number>
<footer>
<header>
<date/time>
6
Real-time systems use a variety of scheduling policies.
Cyclic executive - where all work (tasks) are fit into a common period (major frame) and executed non-preemptively.
Rate monotonic - preemptive scheduling where tasks are assigned priorities based on rates, or periods.
Deadline monotonic - preemptive execution where tasks are assigned priorities based on fixed deadlines.
Earliest deadline first - preemptive scheduling, where tasks are assigned priorities dynamically, based on closeness of current deadlines.
Least laxity first - preemptive scheduling, where tasks are assigned priorities dynamically, based on the amount of slack time that remains between time needed to complete work and time to the deadline.
Criteria for real-time scheduling policies:
Achieve high utilization and still guarantee hard deadlines.
Provide fast aperiodic response and still guarantee hard deadlines.
Low overhead: fixed versus dynamic priorities; dynamic policies tend to have higher overhead, since they may reorder the run queue at each scheduling decision.
This tutorial will first assume preemptive scheduling, then consider effects of non-preemption.

## Slide 32: Rate Monotonic Scheduling (RMS)
Priorities of periodic tasks are based on their rates: highest rate gets highest priority.
Theoretical basis
  optimal fixed scheduling policy (when deadlines are at end of period)
  analytic formulas to check schedulability
Must distinguish between scheduling and analysis
  rate monotonic scheduling forms the basis for rate monotonic analysis
  however, we consider later how to analyze systems in which rate monotonic scheduling is not used
  any scheduling approach may be used, but all real-time systems should be analyzed for timing
Notes: <number>
<footer>
<header>
<date/time>
7
In 1973, Liu and Leyland published a paper called “ Scheduling Algorithms for Multiprogrammimg in a Hard-Real-Time Environment.” In this paper, they introduce the rate monotonic scheduling (RMS) algorithm. The RMS algorithm is an optimal static-priority scheduling algorithm, which gives higher priority to tasks with shorter periods (in other words, higher priority to tasks with higher frequencies, or rates).
It is important to emphasize that tasks are assigned priorities based strictly on their periods. Semantic importance does not play a role in priority assignment.
The algorithm is optimal in the sense that a task set that cannot meet its deadlines with a rate monotonic priority assignment will not be able to be scheduled with any fixed-priority assignment.
The original 1973 work on rate monotonic scheduling theory assumed that RMS was used and all tasks were periodic and non-interacting. Given these assumptions, a simple formula could be used to check for task schedulability, i.e. if each task is guaranteed to meet all its deadlines.
It is important to distinguish between rate monotonic scheduling (RMS) and rate monotonic analysis (RMA). Although the analysis approach has grown out of RMS theory, RMA can be done on a system even if RMS is not the scheduling approach used

## Slide 33: Rate Monotonic Analysis (RMA)
Rate-monotonic analysis is a set of mathematical techniques for analyzing sets of real-time tasks.
Basic theory applies only to independent, periodic tasks, but has been extended to address
  priority inversion
  task interactions
  aperiodic tasks
Focus is on RMA, not RMS
Notes: <number>
<footer>
<header>
<date/time>
8
RMA is a mathematical approach for analyzing real-time tasks to determine their schedulability. Again, the original theory was only able to analyze independent, periodic tasks. However, the basic theory has been extended to analyze cases that include inversion, task interactions, and aperiodic tasks.
In this tutorial, we will first introduce the mechanics of the analysis based on the original RMS theory assumptions, which are very restrictive. We will then systematically relax the assumptions and extend the basic theory.
Remember that the analysis can be done on systems that are scheduled by other algorithms. Again, this is the strength in rate monotonic theory. The analysis can be applied to any system, providing insight to its timing behavior. From now on, our focus is on rate monotonic analysis (RMA) of systems, which may or may not use the rate monotonic scheduling (RMS) algorithm.
In this tutorial we will cover priority inversion. We will cover task interactions and aperiodics as time allows

## Slide 34: Why Are Deadlines Missed?
For a given task, consider
  preemption: time waiting for higher priority tasks
  execution: time to do its own work
  blocking: time delayed by lower priority tasks
The task is schedulable if the sum of its preemption, execution, and blocking is less than its deadline.
Focus: identify the biggest hits among the three and reduce, as needed, to achieve schedulability
Notes: <number>
<footer>
<header>
<date/time>
9
Note:
For a task to meet its deadline, it must accommodate
Preemption from higher-priority tasks,
Its own execution time, and
Delays caused by lower-priority tasks (known as priority inversion or blocking).
Remember that higher-priority tasks, from a rate monotonic perspective, are those with higher rates (or shorter periods). These can occur more than once in a task’s period. A task’s execution occurs once during its period. And blocking can occur at most once during the task’s period; blocking comes from lower-priority tasks, those that have slower rates (or longer periods).
Preemption and execution are unavoidable. If these exceed capacity, one is faced with a classical throughput problem and the only remedy is to reduce the workload (which means changing the system requirements) or to increase the capacity by using a faster computer. Experience has shown that priority inversion (blocking), delay from lower-priority tasks, is a major source of missed deadlines. So we focus on identifying sources of priority inversion and try to reduce their blocking effects to enhance schedulability.

## Slide 35: Example of Priority Inversion
B
Collision check: {... P ( ) ... V ( ) ...}
Update location: {... P ( ) ... V ( ) ...}
Collision
check
Refresh
screen
Update
location
Attempts to lock data
resource (blocked)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Rate Monotonic Theory - Experience
Supported by several standards
  POSIX Real-time Extensions
    Various real-time versions of Linux
  Java (Real-Time Specification for Java and Distributed Real-Time Specification for Java)
  Real-Time CORBA
  Real-Time UML
  Ada 83 and Ada 95
  Windows 95/98
  …
Notes: <number>
<footer>
<header>
<date/time>
22
IBM System Integration Division (SID) Manassas developed and delivered a “schedulable” real-time network to the Navy.
RMA was successfully used by IBM to improve the performance of the BSY-1 Trainer while under development. (A case study in this tutorial reviews this.)
RMA principles were used to design real-time scheduling support in the IEEE FutureBus+ standard.
The NASA Space Station program has decided to adopt RMA in their development effort. They are currently implementing management practices for the use of RMA.
The European Space Agency is requiring that RMS theory be used as the baseline theory for its hard real-time operating system (OS) contract.
Various software vendors are offering products and services that support RMA: Compiler and runtime vendors; Real-time operating system vendors; Commercial training firms.
IBM's response-time analysis effort is using several of the same techniques detailed in the handbook to determine which parts of the system will meet its response-time requirements, even under worst-case system conditions, and which need modification to meet requirements. The analysis is being done by several IBM engineers on an initial release of over 1 million lines of code, allowing its response-time characteristics to be established early enough to take corrective action before full-scale testing and deployment. The analysis effort is expected to be a continuous activity throughout the development and deployment of the system.

## Slide 37: Summary
Real-time goals are:
  fast response,
  guaranteed deadlines, and
  stability in overload.
Any scheduling approach may be used, but all real-time systems should be analyzed for timing.
Rate monotonic analysis
  based on rate monotonic scheduling theory
  analytic formulas to determine schedulability
  framework for reasoning about system timing behavior
  separation of timing and functional concerns
Provides an engineering basis for designing real-time systems
Notes: <number>
<footer>
<header>
<date/time>
24
Use of rate monotonic theory provides the ability to predict timeliness and guarantee that deadlines will always be met. But more importantly, it provides insight into the hardware and software design that affect system timing performance and helps to identify possible bottlenecks and errors that degrade schedulability, i.e. the ability to meet deadlines.
Performing the analysis provides predictability of system performance during system design and allows the separation of timing and functional concerns. In essence, RMA provides an engineering approach to designing real-time systems, in the way that physics provides predictability in building bridges.

## Slide 38: Plan for Lectures
Present basic theory for periodic task sets
Extend basic theory to include
  context switch overhead
  preperiod deadlines
  interrupts
Consider task interactions:
  priority inversion
  synchronization protocols (time allowing)
Extend theory to aperiodic tasks:
  sporadic servers (time allowing)
Notes: <number>
<footer>
<header>
<date/time>
25
The approach that we will take with this tutorial is to start with very simple concepts and gradually build onto this foundation with more practical, real-world considerations.
We will first introduce the mechanics of RMA, applying the basic theory for independent, periodic tasks.
We will then extend the basic theory to include practical issues, such as context switch overhead, interrupts, and non-rate-monotonic priority assignments.
We will present a case study that incorporates the strategies covered and demonstrates the benefits of using RMA.
There will be exercises associated with some sections to practice the concepts discussed in those modules.
Next, as time allows, we will consider task interaction and aperiodic events, incorporating these issues into the analysis

## Slide 39: A Sample Problem
Periodics Servers Aperiodics

1

2

3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
’s deadline is 20 msec before the end of each period
Notes: <number>
<footer>
<header>
<date/time>
26
We will use this sample problem throughout the tutorial as a common thread, starting with the periodic tasks, then gradually adding the other components in the task set. This sample task set is simple and yet embodies many different types of real-time requirements. The task set is completely analyzable using the methods outlined in this tutorial.
Task set characteristics:
Periodic task t1: execution time = 20 msec; period = 100 msec; deadline is at the end of each period.
In addition, t3 may block t1 for 10 msec by using a shared communication server, and task t2 may block t1 for 20 msec by using a shared data object.
Periodic task t2: execution time = 40 msec; period = 150 msec; deadline is 20 msec before the end of each period.
Periodic task t3: execution time = 100 msec; period = 350 msec; deadline is at the end of each period.
Emergency event handling task: execution time = 5 msec; worst-case interarrival time = 50 msec; deadline is 6 msec after arrival.
Routine event handling task: average execution time = 2 msec; average interarrival time = 40 msec; 4 msec average response time is needed.

## Slide 40: Rate Monotonic Analysis
Introduction
Periodic tasks
Extending basic theory
Synchronization and priority inversion
Aperiodic servers
Notes: <number>
<footer>
<header>
<date/time>
1

## Slide 41: A Sample Problem - Periodics
Periodics Servers Aperiodics

1

2

3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
’s deadline is 20 msec before the end of each period
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Example of Priority Assignment
IP: U
IP
=
VIP: U
VIP
=
1
10
11
25
= 0.10
= 0.44
0
25
VIP:
0
10
20
30
IP:
Semantics-Based Priority Assignment
misses deadline
0
10
20
30
IP:
0
25
VIP:
Policy-Based Priority Assignment
Notes: <number>
<footer>
<header>
<date/time>
5
This example provides some motivation for using the rate monotonic scheduling algorithm. In the example we have 2 tasks, named IP and VIP, with the following descriptions:
Task IP: CIP = 1; TIP = 10; UIP = 0.10
Task VIP: CVIP = 11; TVIP = 25; UVIP = 0.44
Total utilization: 54%
If we assign higher priority to task VIP, then task IP will miss its deadline, even though the total utilization is only 54%. But if priorities are assigned according to the rate monotonic algorithm, then both tasks will meet their deadlines. Notice that, as VIP’s period increases, total utilization decreases to 10%, since UVIP approaches zero for large TVIP; yet deadlines are still missed

## Slide 43: Schedulability: UB Test
Utilization bound (UB) test: a set of n independent periodic tasks scheduled by the rate monotonic algorithm will always meet its deadlines, for all task phasings, if
U(1) = 1.0 U(4) = 0.756 U(7) = 0.728
U(2) = 0.828 U(5) = 0.743 U(8) = 0.724
U(3) = 0.779 U(6) = 0.734 U(9) = 0.720
For harmonic task sets, the utilization bound is U(n)=1.00 for all n.
--- + .... + --- < U(n) = n(2 - 1)
C1 Cn 1/ n
T1 Tn
Notes: <number>
<footer>
<header>
<date/time>
6
We say a set of tasks is schedulable if the task set is guaranteed to meet all its deadlines. The utilization bound test says that a task set is schedulable if its total utilization is less than a certain bound, called the Liu & Leyland bound. The utilization bound test provides the basic formula underlying the theory. More complex formulas provide better bounds. This test is the application of a theorem, which was proved by Liu and Leyland in “Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment”, JACM, 1973.
The utilization bound test assumes that:
1. The processor always executes the highest priority task.
2. Task priorities are assigned according to rate monotonic policy.
3. Tasks do not synchronize with each other.
4. Each task’s deadline is at the end of its period.
5. Tasks do not suspend themselves in the middle of computations.
The test takes into account the preemption time and execution time for each task under a worst-case combination of periods and execution times. As the number of tasks goes to infinity, the bound approaches ln(2) = 0.693; in other words, any number of independent periodic tasks will meet their deadlines if the total system utilization is under 69%
For a harmonic task set (in which the period of each task is a multiple of all higher-frequency tasks), the utilization bound is 1.0 for all task sets.

## Slide 44: Concepts and Definitions - Periodics
Periodic task
  initiated at fixed intervals
  must finish before start of next cycle
Task’s CPU utilization:
  Ci = worst-case compute time (execution time) for task i
  Ti = period of task i
CPU utilization for a set of tasks
U = U1 + U2 +...+ Un
Ui =
Ci
Ti
Notes: <number>
<footer>
<header>
<date/time>
3
A periodic task becomes ready to execute at fixed intervals. The time between task initiations is called the period of the task. When we say a periodic task meets its deadline, we mean that it finishes its execution before the start of the next period (i.e. the end of the current period). This is not always the most appropriate definition for a periodic task’s deadline. For example, a requirement to minimize jitter means that a task must perform some action at a specific time, not simply before a specific time. Jitter can be minimized by several design approaches. One approach is to trigger a very high priority task by an accurate clock to meet a jitter requirement.
Ci and Ti represent the execution time and period respectively for task ti. A task’s utilization of the CPU is Ci/Ti. Total CPU utilization is the sum of the utilizations of all the tasks

## Slide 45: Sample Problem: Applying UB Test
Total utilization is .200 + .267 + .286 = .753 < U(3) = .779
The periodic tasks in the sample problem are schedulable according to the UB test
 | C | T | U
Task 1 | 20 | 100 | 0.200
Task 2 | 40 | 150 | 0.267
Task 3 | 100 | 350 | 0.286
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 46: Timeline for Sample Problem
0
100
200
300
400
Scheduling Points

2

3

1
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 47: Exercise: Applying the UB Test
a. What is the total utilization?
b. Is the task set schedulable?
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
Given:
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 48: Solution: Applying the UB Test
a. What is the total utilization? .25 + .34 + .10 = .69
b. Is the task set schedulable? Yes: .69 < U(3) = .779
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
.25 + .34 + .20 = .79 > U(3) = .779
0
5
10
15
20
Task 
Task 
Task 
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 49: Toward a More Precise Test
UB test has three possible outcomes:
0 < U < U(n)  Success
U(n) < U < 1.00  Inconclusive
1.00 < U  Overload
UB test is conservative.
A more precise test can be applied.
Notes: <number>
<footer>
<header>
<date/time>
9
The results of applying the UB test can be:
0<U<u(n) success, task set is schedulable
U9n)<U<1.0 inconclusive, task set may or may not be schedulable
1.0 < U overload, task set exceeds capacity
When the UB test is inconclusive, a more precise test can be applied.
The previous schedulability test (utilization bound test) is very conservative. Schedulable system utilization can often exceed 90%. In fact, for tasks with harmonic periods, where each period is evenly divisible into all longer periods (e.g. 100 ms, 200 ms, 800 ms, 1600 ms), the utilization bound is 100%.

## Slide 50: Schedulability: RT Test
Theorem: The worst-case phasing of a task occurs when it arrives simultaneously with all its higher priority tasks.
Theorem: for a set of independent, periodic tasks, if each task meets its first deadline, with worst-case task phasing, the deadline will always be met.
Response time (RT) or Completion Time test: let an = response time of task i. an of task I may be computed by the following iterative formula:
Test terminates when an+1 = an.
Task i is schedulable if its response time is before its deadline: an < Ti
The above must be repeated for every task i from scratch
a
n+1
C
i
a
n
T
j
C
j
j
1

i
1



where a
0
C
j
j
1

i



This test must be repeated for every task i if required
  i.e. the value of i will change depending upon the task you are looking at
Stop test once current iteration yields a value of an+1 beyond the deadline (else, you may never terminate).
The ‘square bracketish’ thingies represent the ‘ceiling’ function, NOT brackets
Notes: <number>
<footer>
<header>
<date/time>
10
This remarkable theorem was proved by Liu and Leyland and assumes:
Tasks are scheduled according to the rate monotonic algorithm.
Tasks are independent and do not interact.
Tasks do not suspend during execution.
The iterative formula for task response time was introduced in Joseph and Pandya, “Finding Response Times in a Real-Time System,” BCS Computing Journal, October 1986 (vol 29 no 5) pp 390-395.
The iterative formula is an application of fixed point iteration. Since the successive iterates are non-decreasing and approach the response time from below, the iterative formula is known to converge if there is a solution.
There is an alternative approach that we call the scheduling point version of the response time test (see slide 29). The mathematical characterization of this scheduling point version is presented in The Rate Monotonic Scheduling Algorithm -- Exact Characterization and Average Case Behavior, by Lehoczky, Sha, and Ding, Technical Report, Department of Statistics, Carnegie Mellon University, 1987. Also presented in this paper is the fact that for randomly generated task sets, the actual utilization bound is 88% rather than the worst-case bound of 69% presented in the UB test.

## Slide 51: Example: Applying RT Test -1
C T U
Task  20 100 0.200
Task 40 150 0.267
Task 100 350 0.286
Taking the sample problem, we increase the compute time of 1 from 20 to 40; is the task set still schedulable?
0.4
40
Utilization of first two tasks: 0.667 < U(2) = 0.828
  first two tasks are schedulable by UB test
Utilization of all three tasks: 0.953 > U(3) = 0.779
  UB test is inconclusive
  need to apply RT test
Notes: <number>
<footer>
<header>
<date/time>
11
The following data is the same as the sample problem. However, we have changed C1 from 20 to 40 to illustrate the use of the RT test.
Task t1: C1 = 40; T1 = 100; U1 = 0.4
Task t2: C2 = 40; T2 = 150; U2 = 0.267
Task t3: C3 = 100; T3 = 350; U3 = 0.286
Utilization of first two tasks: .4 + .267 = .667 < U(2) = .828
Total utilization: .4 + .267 + .286 = .953 > U(3) = .779
When we change C1 from 20 to 40, CPU utilization changes. Since the utilization of the first two tasks is under the utilization bound of the UB test, these tasks will always meet their deadlines. When the third task is considered, the total utilization is above the utilization bound (Liu & Leyland), so we must look further to see if the third task can nonetheless meet its deadline.
We will now apply the response time test to task t3

## Slide 52: Example: Applying RT Test -2
Use RT test to determine if 3 meets its first deadline: i = 3
100
180
100
40


180
150
40




100
80
80


260



a
1
C
i
a
0
T
j
C
j
j
1

i
1



C
3
a
0
T
j
C
j
j
1

2




3
a
0
C
j
j
1


C
1
C
2
C
3


40
40
100


180




Notes: <number>
<footer>
<header>
<date/time>
12
To apply the RT test, we do two steps
Use the iterative formula to compute the first response time W3 of t3.
Compare W3 to the first deadline for t3, namely T3.
If W3 < T3, then t3 is schedulable according to the RT test.
We start with an initial guess W3 = 0. This is labeled as the “zero-ith” iteration W3(0) = 0. To compute the first iteration, W3(1), we use the iteration formula with n = 0.
Substitute 0 for W3(0). All the terms in the summation drop out, so the first iteration is
W3(1) = C3 = 100.
Next we apply the formula with n=1 and n=2, and compute, respectively, W3(2) and W3(3). Since each successive iteration is different, the computation has not yet converged and we must continue.

## Slide 53: Example: Applying the RT Test -3
Task 3 is schedulable using RT test
a
3
300

T

350

a
2
C
3
a
1
T
j
C
j
j
1

2



100
260
100
(40)
260
150
(40)




a
3
a
2
300
Done!


a
3
C
3
a
2
T
j
C
j
j
1

2



100
300
100
(40)
300
150
(40)




Notes: <number>
<footer>
<header>
<date/time>
13
We continue by applying the iteration formula for n=3 and n=4.
Finally, the computed value for W3(5) is the same as W3(4).
W3(5) = W3(4) = 300.
The iteration has converged, and the first response time for t3 is
W3 = 300.
This must be compared to the first deadline for t3.
We have W3 < T3 since 300 < 350.
So t3 is schedulable using the response time test.

## Slide 54: Timeline for Example

2

3
0
100
200
300

1

3
completes its work at t = 300
Notes: <number>
<footer>
<header>
<date/time>
14
This slide illustrates an alternate version of the response time test based on scheduling points. Again, the test is being applied only to t3.
A scheduling point is a point in time when new work arrives; the beginning of a new period for some task in the task set. This version of the CT test checks to see if there exists a scheduling point (at or before the deadline of t3) at which all work initiated up to that point has been completed. Since the workload includes the compute time of t3 as well as all higher-priority tasks, if the work is completed, then t3 has met its deadline.
In this graphical representation of task execution under worst-case phasing, we can see that, when all tasks are ready to execute at t=0, task t3 cannot begin execution until t=80. As t3 tries to complete its work it gets preempted at the next scheduling point at t=100, where t1 introduces more work. Each time t3 resumes its work it is preempted before completion, until t=300. In this example, task t3 completes all its work at exactly the fourth scheduling point. It completes all its work before its first deadline at t=350, and is therefore schedulable.
The reason for introducing two ways to find the response time is that the iteration formula is easier to program, while the scheduling points are easier to visualize

## Slide 55: Exercise: Applying RT Test
Task 1: C1 = 1 T1 = 4
Task 2: C2 = 2 T2 = 6
Task 3: C3 = 2 T3 = 10
a) Apply the UB test
b) Draw timeline
c) Apply RT test
Notes: <number>
<footer>
<header>
<date/time>
7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 56: Solution: Applying RT Test
a) UB test
  and OK -- no change from previous exercise
  .25 + .34 + .20 = .79 > .779  Test inconclusive for 
b) RT test and timeline
0
5
10
15
20
Task 
Task 
Task 
All work completed at t = 6
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 57: Solution: Applying RT Test (cont.)
c) RT test
3
a
0
C
j
j
1


C
1
C
2
C
3


1
2
2


5




a
1
C
3
a
0
T
j
C
j
j
1

2




2
5
4
1

5
6
2


2 + 2 + 2 = 6
a
2
C
3
a
1
T
j
C
j
j
1

2




2
6
4
1

6
6
2


2 + 2 + 2 = 6
Done
Notes: <number>
<footer>
<header>
<date/time>
8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 58: Summary
UB test is simple but conservative.
RT test is more exact but also more complicated.
To this point, UB and RT tests share the same limitations:
  all tasks run on a single processor
  all tasks are periodic and noninteracting
  deadlines are always at the end of the period
  there are no interrupts
  Rate-monotonic priorities are assigned
  there is zero context switch overhead
  tasks do not suspend themselves
Notes: <number>
<footer>
<header>
<date/time>
15
Although the UB test is conservative, it is useful in providing insight into timing issues. The BSY-1 case study will illustrate this.
Step-by-step algorithms are available in the A Practitioner's Handbook for Real-Time Analysis (published by Kluwer).
Up to this point in the tutorial, the schedulability tests have the following limiting assumptions:
All tasks run on a single processor.
All tasks are periodic and noninteracting.
Deadlines of all tasks are at the end of the period.
No interrupts are used.
Rate monotonic priorities are assigned.
There is no context switch overhead.
Tasks do not suspend themselves.
We will relax some of these assumptions in the next several sections.