## Slide 1: CSE 466 – Software for Embedded Systems
CSE 466
Introduction
<number>
Instructor:
  Bruce Hemingway
    CSE 464, Office Hours: 1:30-2:30 p.m., Monday, Wednesday,
    or whenever the door is open
    bruceh@cs.washington.edu
  Teaching Assistant:
    Tom Sommerville
Notes: <number>

## Slide 2: CSE 466 – Software for Embedded Systems
CSE 466
Introduction
<number>
Class Meeting Times and Location:
  Lectures: EEB 045, MWF 10:30-11:20
  Labs: CSE 003E, Tuesday/Thursday, 2:30-5:20
Exams
  Midterm: Wednesday, 10 November, EEB 045, 10:30-11:20
  Final: Monday, December 13, 2010, 830-1020, EEB 045
Notes: <number>

## Slide 3: CSE 466 – Software for Embedded Systems
CSE 466
Introduction
<number>
Grading Policy
  There will be two exams, as shown on the class schedule.
  Lab reports: Demo usually required, sometimes questions
Ratios:
  Lab: 50%
  Exams total: 20%
  Homework: 10% (reports)
  Class Participation: 20%
Notes: <number>

## Slide 4: Recommended Textbook:
MSP430 Microcontroller Basics
By John H. Davies
Newnes (2008) - Paperback - 668 pages - ISBN 0750682760
U Bookstore doesn’t have it.
CSE 466
Introduction
<number>

## Slide 5: Embedded systems
CSE 466
Introduction
<number>
Notes: <number>

## Slide 6: Embedded system – from the web
CSE 466
Introduction
<number>
Definitions
  A device not independently programmable by the user.
  Specialized computing devices that are not deployed as general purpose computers.
  A specialized computer system which is dedicated to a specific task.
  An embedded system is preprogrammed to perform a narrow range of functions with minimal end user or operator intervention.
Notes: <number>

## Slide 7: Embedded system – from the web
CSE 466
Introduction
<number>
What it is made of
  Embedded systems range in size from a single processing board to systems with operating systems.
  A combination of computer hardware and software, and perhaps additional mechanical or other parts, designed to perform a dedicated function.
  In some cases, embedded systems are part of a larger system or product, as is the case of an anti-lock braking system in a car.
  A specialized computer system that is part of a larger system or machine.
  Typically, an embedded system is housed on a single microprocessor board with the programs stored in ROM.
  Some embedded systems include an operating system, but many are so small and specialized that the entire logic can be implemented as a single program.
Notes: <number>

## Slide 8: Embedded system – from the web
CSE 466
Introduction
<number>
Examples
  Virtually all appliances that have a digital interface -- watches, microwaves, DVD players, cars -- utilize embedded systems.
  A computer system dedicated to controlling some non-computing hardware, like a washing machine, a car engine or a missile.
  Examples of embedded systems are medical equipment and manufacturing equipment.
  While most consumers aren't aware that they exist, they are extremely common, ranging from industrial systems to DVD players and many net devices.
Notes: <number>

## Slide 9: What is an embedded system?
CSE 466
Introduction
<number>
Different than a desktop system
  Fixed or semi-fixed functionality (not user programmable)
  Different human interfaces than screen, keyboard, mouse, audio
  Usually has sensors and actuators for interface to physical world
  May have stringent real-time requirements
It may:
  Replace discrete logic circuits
  Replace analog circuits
  Provide feature implementation path
  Make maintenance easier
  Protect intellectual property
  Improve mechanical performance
Notes: <number>

## Slide 10: What do these differences imply?
CSE 466
Introduction
<number>
Less emphasis on
  Graphical user interface
  Dynamic linking and loading
  Virtual memory, protection modes
  Disks and file systems
  Processes
More emphasis on
  Real-time support, interrupts (very small OS, if we’re lucky)
  Tasks (threads)
  Task communication primitives
  General-purpose input/output
  Analog-digital/digital-analog converters
  Timers
  Event capture
  Pulse-width modulation
  Built-in communication protocols
Notes: <number>

## Slide 11: What is an embedded system? (cont’d)
CSE 466
Introduction
<number>
Figures of merit for embedded systems
  Reliability – it should never crash
  Safety – controls things that move and can harm/kill a person
  Power consumption – may run on limited power supply
  Cost – engineering cost, manufacturing cost, schedule tradeoffs
  Product life cycle – maintainability, upgradeability, serviceability
  Performance – real-time requirements, power budget
Notes: <number>

## Slide 12: Example: a temperature controller
CSE 466
Introduction
<number>
thermister
TACH (pwm)
SPEED (pwm)
ADC0
INT0
AREF
PD6
PD0
PWM signal
Task: Tachometer (external interrupt)
now = getTime();
period = then - now; //overflow?
then = now;
return;
Task: FanPWM (periodic, hard constraint)
count++;
if (count == 0) PD6 = 1;
if (count > Thi) PD6 = 0;
return;
Task: TempControl (periodic, soft constraint)
if (Temp > setpoint) Thi++;
if (Temp < setpoint) Thi--;
if (period<min || period>max) PD0 = 1;
Task: Main
Thi = 0;
setup timer for 1ms interrupt;
setup timer for 100ms interrupt;
while (1) ;
Notes: <number>

## Slide 13: Capacity
CSE 466
Introduction
<number>
Assume:
  8 MHz processor @ one instruction/cycle
  Assume fan runs between 30Hz and 60Hz
  Assume 256ms period on speed control PWM, with 1ms resolution.
What percent of the the available cycles are used for the temperature controller?
  [total instructions in one second] / (8MInstr/sec)
How much RAM do you need?
How much ROM?
Notes: <number>

## Slide 14: Resource analysis of temp controller
CSE 466
Introduction
<number>
Task | ROM | RAM | Instructions/Sec
Tach | ~4 | 2 (period, then) | 4 * 60 = 240
FanPWM | ~8 | 1 (count) | 8 * 1000 = 8000
TempControl | ~10 | 1 (THI) | 10 * 2 = 20
Total Instructions/Sec = 8260, at 8MIPS, that’s only 0.1% utilization!
Other resources? local variables, stack
Task: Tachometer (external interrupt)
now = getTime();
period = then - now; //overflow?
then = now;
return;
Task: FanPWM (periodic, hard constraint)
count++;
if (count == 0) GP0 = 1;
if (count > Thi) GP0 = 0;
return;
Task: TempControl (periodic, soft constraint)
if (Temp > setpoint) Thi++;
if (Temp < setpoint) Thi--;
if (period<min || period>max) GP4 = 1;
Task: Main
Thi = 0;
setup timer for 1ms interrupt;
setup timer for 100ms interrupt;
while (1) ;
Notes: <number>

## Slide 15: Class logistics – see course web
CSE 466
Introduction
<number>
http://www.cs.washington.edu/education/courses/cse466/10au/
Class structure
Business matters
Grading
Syllabus
What we’ll be doing
Notes: <number>

## Slide 16: Class structure
CSE 466
Introduction
<number>
Lecture
  Closely linked to laboratory assignments
  Cover main concepts, introduce laboratory problems
Lab
  Implementation of two projects
  Lab reports due prior with 30 minutes of start of next lab section
Exams
  Two, based on lecture, lab, and datasheet reading
  Open datasheets, open notes
Final demo
  During last class time – participation required
Notes: <number>

## Slide 17: Business Matters
CSE 466
Introduction
<number>
Lecture slides will be on line after class (links in several places)
Random lab partner assignments, changed mid-quarter
Sign up for CSE466 mailing list (soon)
Notes: <number>

## Slide 18: Grading
CSE 466
Introduction
<number>
Lab reports:
  Demonstration(s) required
  Brief answers to questions embedded in assignment
  Sometimes hand-in code
  Do with your partner
Distribution:
  Labs: 50%
  Exams: 20%
  Homework: 10%
  Class Participation: 20%
Notes: <number>

## Slide 19: CSE466 Lab Projects
CSE 466
Introduction
<number>
Two multi-week projects
  Four lab assignments each
  Different lab partners
First project
  Familiarize with low-power microcontroller
  Learn how to interface various devices, including Chronos
  Testing and debugging
  Solar energy harvesting with MSP430
Second project
  Arm-9 with touch-screen
  Embedded Linux talks to Chronos
  And maybe Android
  Implement an app
Notes: <number>

## Slide 20: Project 1 – power-harvesting w. Chronos
CSE 466
Introduction
<number>
  Platform: MSP430 microcontroller
  Powered via Solar cell- read sensor data
  Send data to Chronos via 915 MHz radio
  Chronos collects data, then dumps it to PC
Notes: <number>

## Slide 21: CSE466 Lab Projects (cont’d)
CSE 466
Introduction
<number>
Project 2 – Using the Micro2440
  Platform: 405 MHz Samsung S3C2440A ARM920T
RAM 64 MBytes SDRAM,
Flash 1 GByte of NAND 2 MBytes of NOR with BIOS
Four USB Host connectors One USB Device connector
Audio Stereo Out with mini phone jack. Audio In with cable connector on PCB Condenser Mic on PCB
One standard SD Card socket. Ethernet RJ-45 10/100M RTC Built in Real Time Clock with battery.
Runs Linux 2.6.31, Android, WinCE, and uC/OS
LCD NEC 3.5 inch with Touch Screen, 240x320
Notes: <number>

## Slide 22: Assignment for Friday:
Review the MSP430x2xx Family User’s Guide
  Chapter 1: Introduction and
  Chapter 2: System Resets, Interrupts, and Operating Modes
  Download here:
  http://www.ti.com/litv/pdf/slau144e
  (link is on the Textbook page...)
CSE 466
Introduction
<number>