## Slide 1: MSP430 Interrupts
Notes: <number>

## Slide 2: Interrupts
CSE 466
Interrupts
<number>
Fundamental concept in computation
Interrupt execution of a program to “handle” an event
  Don’t have to rely on program relinquishing control
  Can code program without worrying about others
Issues
  What can interrupt and when?
  Where is the code that knows what to do?
  How long does it take to handle interruption?
  Can an interruption be, in turn, interrupted?
  How does the interrupt handling code communicate its results?
  How is data shared between interrupt handlers and programs?
Notes: <number>

## Slide 3: What is an Interrupt?
CSE 466
Interrupts
<number>
Reaction to something in I/O (human, comm link)
Usually asynchronous to processor activities
“interrupt handler” or “interrupt service routine” (ISR) invoked to take care of condition causing interrupt
  Change value of internal variable (count)
  Read a data value (sensor, receive)
  Write a data value (actuator, send)
Main Program
  Instruction 1
  Instruction 2
  Instruction 3
  Instruction 4
  …..
ISR
  Save state
  Instruction 1
  Instruction 2
  Instruction 3
  …..
  Restore state
  Return from Interrupt
Notes: <number>

## Slide 4: Interrupts
CSE 466
Interrupts
<number>
Code sample that does not interrupt
    char SPI_SlaveReceive(void)
    {
    /* Wait for reception complete */
    while(!(SPSR & (1<<SPIF)))
    ;
    /* Return data register */
    return SPDR;
    }
Instead of busy waiting until a byte is received the processor can generate an interrupt when it sets SPIF
    SIGNAL(SIG_SPI) {
    RX_Byte = SPDR
    }
Notes: <number>

## Slide 5: Saving and Restoring Context
CSE 466
Interrupts
<number>
Processor and compiler dependent
Where to find ISR code?
  Different interrupts have separate ISRs
Who does dispatching?
  Direct
    Different address for each interrupt type
    Supported directly by processor architecture
  Indirect
    One top-level ISR
    Switch statement on interrupt type
  A mix of these two extremes?
Notes: <number>

## Slide 6: Saving and Restoring Context
CSE 466
Interrupts
<number>
How much context to save?
  Registers, flags, program counter, etc.
  Save all or part?
  Agreement needed between ISR and program
Where should it be saved?
  Stack, special memory locations, shadow registers, etc.
  How much room will be needed on the stack?
  Nested interrupts may make stack reach its limit – what then?
Restore context when ISR completes
Notes: <number>

## Slide 7: Ignoring Interrupts
CSE 466
Interrupts
<number>
Can interrupts be ignored?
  It depends on the cause of the interrupt
  No, for nuclear power plant temperature warning
  Yes, for keypad on cell phone (human timescale is long)
When servicing another interrupt
  Ignore others until done
  Can’t take too long – keep ISRs as short as possible
    Just do a quick count, or read, or write – not a long computation
Interrupt disabling
  Will ignored interrupt “stick”?
    Rising edge sets a flip-flop
  Or will it be gone when you get to it?
    Level changes again and its as if it never happened
  Don’t forget to re-enable
Notes: <number>

## Slide 8: Prioritizing Interrupts
CSE 466
Interrupts
<number>
When multiple interrupts happen simultaneously
  Which is serviced first?
  Fixed or flexible priority?
Priority interrupts
  Higher priority can interrupt
  Lower priority can’t
Maskable interrupts
  “don’t bother me with that right now”
  Not all interrupts are maskable, some are non-maskable
Notes: <number>

## Slide 9: Interrupts in the MSP430
CSE 466
Interrupts
<number>
External interrupts
  From I/O pins of microcontroller
Internal interrupts
  Timers
    Output compare
    Input capture
    Overflow
  Communication units
    Receiving something
    Done sending
  ADC
    Completed conversion
Notes: <number>

## Slide 10: Chain of Events on Interrupt
CSE 466
Interrupts
<number>
Finish executing current instruction
Disable all interrupts
Push program counter on to stack
Jump to interrupt vector table
Jump to start of complete ISR
Save any context that ISR may otherwise change
  Registers and flags must be saved within ISR and restored before it returns – this is very important!
Re-enable interrupts if nested interrupts are ok
Complete ISR’s code
Re-enable interrupts upon return
Jump back to next instruction before interruption
Automatic
RETI
Compiler
Notes: <number>

## Slide 11: Shared Data Problem
CSE 466
Interrupts
<number>
When you use interrupts you create the opportunity for multiple sections of code to update a variable.
This might cause a problems in your logic if an interrupt updates a variable between two lines of code that are directly dependent on each other (e.g. if statement)
One solution is to create critical sections where you disable the interrupts for a short period of time while you complete your logic on the shared variable clear (GIE) bit ; …..critical section code goes here….. set (GIE) bit ;
Notes: <number>

## Slide 12: Interrupts
Execution of a program proceeds predictably, with interrupts being the exception
Interrupts are usually generated by hardware
  Processor stops what it is doing,
  Stores enough information to later resume,
  Executes an interrupt service routine (ISR),
  Restores saved information,
  Resumes execution.
An interrupt is an asynchronous signal indicating the need for attention
CSE 466
MSP430 Interrupts
<number>
Notes: <number>

## Slide 13: Interrupts
Interrupts preempt normal code execution
  Interrupt code runs in the foreground
  Normal (e.g. main()) code runs in the background
Interrupts can be enabled and disabled
  Globally
  Individually on a per-peripheral basis
  Non-Maskable Interrupt (NMI)
The occurrence of each interrupt is unpredictable
  When an interrupt occurs
  Where an interrupt occurs
Interrupts are associated with a variety of on-chip and off-chip peripherals.
  Timers, Watchdog, D/A, Accelerometer
  NMI, change-on-pin (Switch)
CSE 466
MSP430 Interrupts
<number>

## Slide 14: Interrupts
Interrupts commonly used for
  Urgent tasks w/higher priority than main code
  Infrequent tasks to save polling overhead
  Waking the CPU from sleep
  Call to an operating system (software interrupt).
Event-driven programming
  The flow of the program is determined by events—i.e., sensor outputs or user actions (mouse clicks, key presses) or messages from other programs or threads.
  The application has a main loop with event detection and event handlers.
CSE 466
MSP430 Interrupts
<number>

## Slide 15: Interrupt Flags
Each interrupt has a flag that is raised (set) when the interrupt occurs.
Each interrupt flag has a corresponding enable bit – setting this bit allows a hardware module to request an interrupt.
Most interrupts are maskable, which means they can only interrupt if
  1) enabled and
  2) the general interrupt enable (GIE) bit is set in the status register (SR).
CSE 466
MSP430 Interrupts
<number>

## Slide 16: Interrupt Vectors
The CPU must know where to fetch the next instruction following an interrupt.
The address of an ISR is defined in an interrupt vector.
The MSP430 uses vectored interrupts where each ISR has its own vector stored in a vector table located at the end of program memory.
Note: The vector table is at a fixed location (defined by the processor data sheet), but the ISRs can be located anywhere in memory.
CSE 466
MSP430 Interrupts
<number>

## Slide 17: MSP430 Memory
  Unified 64KB continuous memory map
  Same instructions for data and peripherals
  Program and data in Flash or RAM with no restrictions
  Designed for modern programming techniques such as pointers and fast look-up tables
CSE 466
MSP430 Interrupts
<number>

## Slide 18: Serving Interrupt Request
CSE 466
MSP430 Interrupts
<number>
0100 0011 0001 0101
user program
1111 1000 0000 0000
interrupt vector
0001 0011 0000 0000
interrupt service routine
RETI
0xF800
Lookup interrupt vector for ISR starting address.
Store information (PC and SR on Stack)
Transfer to service routine.
Restore information
Return (RETI: get old PC from stack).

## Slide 19: MSP430x2xx Interrupt Vectors
INTERRUPT SOURCE | INTERRUPT FLAG | SYSTEM INTERRUPT | ADDRESS | SECTION | PRIORITY
Power-up External reset Watchdog | PORIFG RSTIFG WDTIFG | Reset | 0xFFFE | .reset | 15, highest
NMI Oscillator fault Flash memory violation | NMIIFG OFIFG ACCDVIFG | Non-maskable | 0xFFFC | .int14 | 14
Timer_B3 | TBCCR0 CCIFG | Maskable | 0xFFFA | .int13 | 13
Timer_B3 | TBCCR1 CCIFG TBCCR2 CCIFG, TBIFG | Maskable | 0xFFF8 | .int12 | 12
 |  |  | 0xFFF6 | .int11 | 11
Watchdog Timer | WDTIFG | Maskable | 0xFFF4 | .int10 | 10
Timer_A3 | TACCR0 CCIFG | Maskable | 0xFFF2 | .int09 | 9
Timer_A3 | TACCR1 CCIFG, TACCR2 CCIFG, TAIFG | Maskable | 0xFFF0 | .int08 | 8
USCI_A0/USCI_B0 Rx | UCA0RXIFG, USB0RXIFG | Maskable | 0xFFEE | .int07 | 7
USCI_Z0/USCI_B0 Tx | UCA0TXIFG, UCB0TXIFG | Maskable | 0xFFEC | .int06 | 6
ADC10 | ADC10IFG | Maskable | 0xFFEA | .int05 | 5
 |  |  | 0xFFE8 | .int04 | 4
I/O Port P2 | P2IFG.0 – P2IFG.7 | Maskable | 0xFFE6 | .int03 | 3
I/O Port P1 | P1IFG.0 – P1IFG.7 | Maskable | 0xFFE4 | .int02 | 2
 |  |  | 0xFFE2 | .int01 | 1
 |  |  | 0xFFE0 | .int00 | 0
CSE 466
MSP430 Interrupts
<number>
Higher address = higher priority

## Slide 20: MSP430F2274 Address Space
CSE 466
MSP430 Interrupts
<number>
Byte
8-bit Special Function Registers
0x000F
0x0000
16
Byte
8-bit Peripherals Modules
0x00FF
0x0010
240
Word
16-bit Peripherals Modules
0x01FF
0x0100
256
Word/Byte
Stack
0x05FF
0x0200
1KB
SRAM
Word/Byte
Program Code
0xFFBF
0x8000
Word
Interrupt Vector Table
0xFFFF
0xFFC0
32KB
Flash
Access
Description
Address
Size
Memory

## Slide 21: Processing an Interrupt…
Current instruction completed
MCLK started if CPU was off
Processor pushes program counter on stack
Processor pushes status register on stack
Interrupt w/highest priority is selected
Interrupt request flag cleared if single sourced
Status register is cleared
  Disables further maskable interrupts (GIE cleared)
  Terminates low-power mode
Processor fetches interrupt vector and stores it in the program counter
User ISR must do the rest!
CSE 466
MSP430 Interrupts
<number>

## Slide 22: Interrupt Stack
CSE 466
MSP430 Interrupts
<number>

## Slide 23: Interrupt Service Routines
Look superficially like a subroutine.
However, unlike subroutines
  ISR’s can execute at unpredictable times.
  Must carry out action and thoroughly clean up.
  Must be concerned with shared variables.
  Must return using reti rather than ret.
ISR must handle interrupt in such a way that the interrupted code can be resumed without error
  Copies of all registers used in the ISR must be saved (preferably on the stack)
CSE 466
MSP430 Interrupts
<number>

## Slide 24: Interrupt Service Routines
Well-written ISRs:
  Should be short and fast
  Should affect the rest of the system as little as possible
  Require a balance between doing very little – thereby leaving the background code with lots of processing – and doing a lot and leaving the background code with nothing to do
Applications that use interrupts should:
  Disable interrupts as little as possible
  Respond to interrupts as quickly as possible
CSE 466
MSP430 Interrupts
<number>

## Slide 25: Interrupt Service Routines
Interrupt-related runtime problems can be exceptionally hard to debug
Common interrupt-related errors include:
  Failing to protect global variables
  Forgetting to actually include the ISR - no linker error!
  Not testing or validating thoroughly
  Stack overflow
  Running out of CPU horsepower
  Interrupting critical code
  Trying to outsmart the compiler
CSE 466
MSP430 Interrupts
<number>

## Slide 26: Returning from ISR
MSP430 requires 6 clock cycles before the ISR begins executing
  The time between the interrupt request and the start of the ISR is called latency (plus time to complete the current instruction, 6 cycles, the worst case)
An ISR always finishes with the return from interrupt instruction (reti) requiring 5 cycles
  The SR is popped from the stack
    Re-enables maskable interrupts
    Restores previous low-power mode of operation
  The PC is popped from the stack
  Note: if waking up the processor with an ISR, the new power mode must be set in the stack saved SR
CSE 466
MSP430 Interrupts
<number>

## Slide 27: Return From Interrupt
CSE 466
MSP430 Interrupts
<number>
Single operand instructions:
Emulated instructions:
Mnemonic | Operation | Description
PUSH(.B or .W) src | SP-2SP, src@SP | Push byte/word source on stack
CALL dst | SP-2SP, PC+2@SP dstPC | Subroutine call to destination
RETI | TOSSR, SP+2SP TOSPC, SP+2SP | Return from interrupt
Mnemonic | Operation | Emulation | Description
RET | @SPPC SP+2SP | MOV @SP+,PC | Return from subroutine
POP(.B or .W) dst | @SPtemp SP+2SP tempdst | MOV(.B or .W) @SP+,dst | Pop byte/word from stack to destination

## Slide 28: Summary
By coding efficiently you can run multiple peripherals at high speeds on the MSP430
Polling is to be avoided – use interrupts to deal with each peripheral only when attention is required
Allocate processes to peripherals based on existing (fixed) interrupt priorities - certain peripherals can tolerate substantial latency
Use GIE when it’s shown to be most efficient and the application can tolerate it – otherwise, control individual IE bits to minimize system interrupt latency.
An interrupt-based approach eases the handling of asynchronous events
CSE 466
MSP430 Interrupts
<number>

## Slide 29
CSE 466
MSP430 Interrupts
<number>
// MSP430F20x3 Demo - SD16A, Sample A1+ Continuously, Set P1.0 if > 0.3V
#include <msp430x20x3.h>
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer
P1DIR |= 0x01; // Set P1.0 to output direction
SD16CTL = SD16REFON + SD16SSEL_1; // 1.2V ref, SMCLK
SD16INCTL0 = SD16INCH_1; // A1+/-
SD16CCTL0 = SD16UNI + SD16IE; // 256OSR, unipolar, interrupt enable
SD16AE = SD16AE2; // P1.1 A1+, A1- = VSS
SD16CCTL0 |= SD16SC; // Set bit to start conversion
_BIS_SR(LPM0_bits + GIE);
}
#pragma vector = SD16_VECTOR
__interrupt void SD16ISR(void)
{
if (SD16MEM0 < 0x7FFF) // SD16MEM0 > 0.3V?, clears IFG
P1OUT &= ~0x01;
else
P1OUT |= 0x01;
}

## Slide 30: Multiple Clocks
CSE 466
MSP430 Interrupts
<number>
No crystal on eZ430 tools
Use VLO for ACLK
(mov.w #LFXT1S_2,&BCSCTL3)

## Slide 31: Processor Clock Speeds
Often, the most important factor for reducing power consumption is slowing the clock down
  Faster clock = Higher performance, more power
  Slower clock = Lower performance, less power
Using assembly code:
Using C code:
CSE 466
MSP430 Interrupts
<number>
; MSP430 Clock - Set DCO to 8 MHz:
mov.b #CALBC1_8MHZ,&BCSCTL1 ; Set range
mov.b #CALDCO_8MHZ,&DCOCTL ; Set DCO step + modulation
// MSP430 Clock - Set DCO to 8 MHz:
BCSCTL1 = CALBC1_8MHZ; // Set range 8MHz
DCOCTL = CALDCO_8MHZ; // Set DCO step + modulation

## Slide 32: Processor Clock Speeds
Another method to reduce power consumption is to turn off some (or all) of the system clocks
  Active Mode (AM): CPU, all clocks, and enabled modules are active (300 A)
  LPM0: CPU and MCLK are disabled, SMCLK and ACLK remain active (85 A)
  LPM3: CPU, MCLK, SMCLK, and DCO are disabled; only ACLK remains active (1 A)
  LPM4: CPU and all clocks disabled, RAM is retained (0.1 A)
A device is said to be sleeping when in low-power mode; waking refers to returning to active mode
CSE 466
MSP430 Interrupts
<number>

## Slide 33: MSP430 Clock Modes
CSE 466
MSP430 Interrupts
<number>
Only uses 1A during low clock
Less clocks means less power!
Notes: <number>

## Slide 34: Clocks Off Power Savings
CSE 466
MSP430 Interrupts
<number>
Sleep Modes
No Clocks!
Only ACLK Active
SMCLK and ACLK Active

## Slide 35: Lower Power Savings
Finally, powering your system with lower voltages means lower power consumption as well
CSE 466
MSP430 Interrupts
<number>

## Slide 36: Principles of Low-Power Apps
Maximize the time in LPM3 mode
Use interrupts to wake the processor
Switch on peripherals only when needed
Use low-power integrated peripherals
  Timer_A and Timer_B for PWM
Calculated branches instead of flag polling
Fast table look-ups instead of calculations
Avoid frequent subroutine and function calls
Longer software routines should use single-cycle CPU registers
CSE 466
MSP430 Interrupts
<number>

## Slide 37: Setting Low-Power Modes
Setting low-power mode puts the microcontroller “to sleep” – so usually, interrupts would need to be enabled as well.
Enter LPM3 and enable interrupts using assembly code:
Enter LPM3 and enable interrupts using C code:
CSE 466
MSP430 Interrupts
<number>
; enable interrupts / enter low-power mode 3
bis.b #LPM3+GIE,SR ; LPM3 w/interrupts
// enable interrupts / enter low-power mode 3
__bis_SR_register(LPM3_bits + GIE);

## Slide 38: Timers
System timing is fundamental for real-time applications
The MSP430F2274 has 2 timers, namely Timer_A and Timer_B
The timers may be triggered by internal or external clocks
Timer_A and Timer_B also include multiple independent capture/compare blocks that are used for applications such as timed events and Pulse Width Modulation (PWM)
CSE 466
MSP430 Interrupts
<number>

## Slide 39: Timers
The main applications of timers are to:
  generate events of fixed time-period
  allow periodic wakeup from sleep of the device
  count transitional signal edges
  replace delay loops allowing the CPU to sleep between operations, consuming less power
  maintain synchronization clocks
CSE 466
MSP430 Interrupts
<number>

## Slide 40: TxCTL Control Register
CSE 466
MSP430 Interrupts
<number>
Bit |  | Description
9-8 | TxSSELx | Timer_x clock source: 0 0  TxCLK 0 1  ACLK 1 0  SMCLK 1 1  INCLK
7-6 | IDx | Clock signal divider: 0 0  / 1 0 1  / 2 1 0  / 4 1 1  / 8
5-4 | MCx | Clock timer operating mode: 0 0  Stop mode 0 1  Up mode 1 0  Continuous mode 1 1  Up/down mode
2 | TxCLR | Timer_x clear when TxCLR = 1
1 | TxIE | Timer_x interrupt enable when TxIE = 1
0 | TxIFG | Timer_x interrupt pending when TxIFG = 1
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
(Used by Timer_B) |  |  |  |  |  | TxSSELx |  | IDx |  | MCx |  | - | TxCLR | TxIE | TxIFG

## Slide 41: 4 Modes of Operation
Timer reset by writing a 0 to TxR
Clock timer operating modes:
MCx | Mode | Description
0 0 | Stop | The timer is halted.
0 1 | Up | The timer repeatedly counts from 0x0000 to the value in the TxCCR0 register.
1 0 | Continuous | The timer repeatedly counts from 0x0000 to 0xFFFF.
1 1 | Up/down | The timer repeatedly counts from 0x0000 to the value in the TxCCR0 register and back down to zero.
CSE 466
MSP430 Interrupts
<number>

## Slide 42: Timer Modes
Up Mode
Continuous Mode
Up/Down Mode
CSE 466
MSP430 Interrupts
<number>

## Slide 43: Timer_A Example
Use Timer A to interrupt every 1 ms
CSE 466
MSP430 Interrupts
<number>
SMCLK .set 1200000 ; 1200000 clocks / second
TIME_1MS .set 1000 ; 1 ms = 1/1000 s
TA_CTL .set TASSEL_2+ID_0+MC_1+TAIE ; SMCLK, /1, UP, IE
TA_FREQ .set SMCLK/TIME_1MS ; clocks / 1 ms
clr.w &TAR ; reset timerA
mov.w #TA_CTL,&TACTL ; set timerA control reg
mov.w #TA_FREQ,&TACCR0 ; set interval (frequency)
bis.w #LPM0+GIE,SR ; enter LPM0 w/interrupts
jmp $ ; will never get here! (CPU is off
TA_isr: ; timer A ISR
bic.w #TAIFG,&TACTL ; acknowledge interrupt
; <<add interrupt code here>>
reti
.sect ".int08" ; timer A section
.word TA_isr ; timer A isr

## Slide 44: Pulse Width Modulation (PWM)
Pulse width modulation (PWM) is used to control analog circuits with a processor's digital outputs
PWM is a technique of digitally encoding analog signal levels
  The duty cycle of a square wave is modulated to encode a specific analog signal level
  The PWM signal is still digital because, at any given instant of time, the full DC supply is either fully on or fully off
The voltage or current source is supplied to the analog load by means of a repeating series of on and off pulses
Given a sufficient bandwidth, any analog value can be encoded with PWM.
CSE 466
MSP430 Interrupts
<number>

## Slide 45: PWM Machines
CSE 466
MSP430 Interrupts
<number>

## Slide 46: PWM – Frequency/Duty Cycle
CSE 466
MSP430 Interrupts
<number>
 Frequency
 Duty Cycle
 Time

## Slide 47: Watchdog Timer
The primary function of the watchdog timer+ (WDT+) module is to perform a controlled system restart after a software problem occurs.
If the selected time interval expires, a system reset is generated.
If the watchdog function is not needed in an application, the module can be configured as an interval timer and can generate interrupts at selected time intervals.
CSE 466
MSP430 Interrupts
<number>

## Slide 48: Watchdog Timer
Features of the watchdog timer+ module include:
  Four software-selectable time intervals
  Watchdog mode
  Interval mode
  Access to WDT+ control register is password protected
  Control of RST/NMI pin function
  Selectable clock source
  Can be stopped to conserve power
  Clock fail-safe feature
CSE 466
MSP430 Interrupts
<number>

## Slide 49: Watchdog Power-up
After a power-up cycle (PUC), the WDT+ module is automatically configured in the watchdog mode with an initial 32768 clock cycle reset interval using the DCOCLK.
The user must setup or halt the WDT+ prior to the expiration of the initial reset interval.
CSE 466
MSP430 Interrupts
<number>

## Slide 50: Switch Debounce
CSE 466
MSP430 Interrupts
<number>
Switch “debounded” after signal remains low/high for specified time

## Slide 51: Switch Debounce
What to do?
  Constraints
    As little CPU overhead as possible
    Avoid sampling
    Responsiveness
  Simplest of them all: read the switch once every 500 ms or so, and set a flag indicating the input’s state. No reasonable switch will bounce that long. (Yuck!)
  Counting algorithms
    Reset count on every off/on position
    Switch debounced if count reaches stable number
  Latches
    Latch once
    Reset before looking for next transistion
CSE 466
MSP430 Interrupts
<number>