## Slide 1: Basics of Signal Processing
Lecture 22

## Slide 2: Previous Lecture
Feedback control
  Stability
  Instability
  Marginal stability
Feedback controllers
  Proportional control
  Proportional + Derivative control
  Proportional + Derivative + Integral control
Simulation diagram concepts

## Slide 3: Outline of This Lecture
Signal and data are at the interface of embedded software engineering and ECE.
Objective:
  Understand the basic concepts
  Master issues that a software engineer should do and can do
  Ask for expert-help intelligently
Today: Signals and data acquisition
  Source of deterministic errors and random noises
  Basics of signal spectrum
  Basic filters
    What you can do and when you should ask for help

## Slide 4: Deterministic Errors
Bias adds an offset to the true value. Most analog components have this problem over time
Solution: calibration
  By adjusting resistors or
  By compensating for the bias in software.
Quantization errors: the resolution is not fine enough for the application needs.
  Proper configuration of voltage ranges in A/D and D/A.
    Do you still remember how to do it?
  Standard A/D and D/A card gives 12-bit resolution over a given range. However, higher resolution ones are also available.
Aliasing: discussed briefly before

## Slide 5: Sources of Random Noises
Noise is the electrical signal that you do not want.
  In fact, the music broadcast from radio stations is a common source of EMI problems.
Internal from the electronics of the A/D - D/A card
  It is usually very small.
Environmental :
  Noise from equipment power transformers. Switching transformers are cheap. The very inexpensive ones are quite noisy. A linear transformer is heavy, expensive but quiet.
  Noise from the power line due to power tools, elevators etc. Buy line voltage conditioner or move to another place to do your work.
EMI: electrical shielding and/or using differential mode.
    Do you still remember differential mode inputs?
  The oscilloscope is your best friend to identify the source of noise
Poor grounding is a common source of noise problems. Before trying anything fancy, make sure that your equipment is properly grounded.

## Slide 6: Key Concepts in Signal Processing - 1
Fourier discovered that a signal can be decomposed into a sum of sinusoids.
If you have a set of samples, you can use FFT in tools like MATLAB to take a look at its frequency components.
Bandwidth refers to the frequency components of a signal that have non-negligible magnitudes with respect to the application at hand.
Joseph Fourier, 1768-1830

## Slide 7: Key Concepts in Signal Processing - 1
The most common noises are high-frequency noises and, thus, the popularity of low-pass filters.
Noise in the same frequency range as the signal can only be filtered by model-based filtering, e.g., Kalman filters
If you have significant noise in your signal range, try to prevent them at the source
  Shielding, differential inputs, better transformers, proper grounding, …
If this still does not work, ask a professional in signal processing to help. (How can you know if you have this problem?)

## Slide 8: Basic Signal Processing Concepts
Fourier Series
For any periodic function, whose period is T = 1/ f0

## Slide 9: Basic Signal Processing Concepts
Fourier Transform
The fourier transform of the signal is
Key observation: the narrower the pulse, the wider is the frequency range due to the role played by pulse width t in the transformation.

## Slide 10: Key Concepts in Sampling
Nyquist rate
To correctly capture an analog signal digitally
  The sampling rate must be at least twice the bandwidth of the signal.
This “2 times” result assumes perfection in the sampling and filtering process
You will not have it in practice. So the practical rule of thumb is
  At least 3 times and preferably 5 times if you can afford it.

## Slide 11: Aliasing
Aliasing:
  If you sample too slow, the high frequency components will become irregular noise at the sampling frequency
  They are noises that are in the same frequency range of your signal!!!
Look at the samples alone
Can you tell which of the two frequencies the sampled series represents?
Either of the two signals could produce the samples, i.e., the signals are “aliases” of each other

## Slide 12: Wagon Wheel Effect

## Slide 13: Applications of Nyquist Theorem - 1
“Signal is in the eye of the beholder”
Nyquist was interested in digital samples that capture all the information in the electrical waveform.
The term signal in Nyquist theorem means the total information in the waveform. His signal means the sum of
  The “real signal” that you love and
  The noise that you hate
This “love-hate situation” makes the correct application of the Nyquist theorem interesting.
Suppose that we have a signal which has frequency components in the range of 10 to 60 Hz while noise ranges from 100 to 500 Hz.
  What is a practical lower bound for sampling?

## Slide 14: Applications of Nyquist Theorem - 2
If you are sampling below 1500 Hz, a significant portion of the 500 Hz noise will be transformed into lower frequency noises that you cannot filter away using classical frequency domain filters.
1500 Hz is way too fast for a standard PC with a normal 10 ms timer resolution. You need DSP hardware if you want to digitally filter out the noise after sampling.
Another way is to use an anti-aliasing filter.
  A simple hardware analog filter before the sampling process.

## Slide 15: A/D Sampling
S(t) is a rectangular pulse train, where  is the contact time and s is the sampling rate.

## Slide 16: Modulation Theorem
The effect of chopper sampling is to multiply a harmonic series of cosine functions to the signal.
By the Modulation Theorem, the cosine function splits and frequency-shifts the signal.
The higher the sampling rate, the bigger is the frequency shift and the separation between the shifted signals.

## Slide 17: Basic Signal Processing Concepts
Modulation Theorem
Multiply a signal v(t) by a cosine function with frequency fc splits the signal into two parts and frequency shifted by fc and -fc

## Slide 18: Nyquist Rate and Aliasing
For a signal with bandwidth W, the amount of frequency shift, fs , must be greater than 2W or there will be an overlap between the spectra of the shifted signals.
The overlap, if any, is called aliasing.
It follows that the sampling rate must be at least two times the bandwidth, the highest frequency in the signal, to avoid aliasing. This is known as the Nyquist rate.
  If there is no aliasing, then the signal can be recovered perfectly in theory using ideal low-pass filters.

## Slide 19: Overview of Remainder
Let’s look at the basics of a low-pass filter.
It is reasonable to expect that you can design simple analog filters and simple software digital filters using tools like MATLAB.

## Slide 20: Frequency Domain View of Signals
Fourier discovered that any waveform can be represented as the sum of sinusoids.
  Q1: what does bandwidth mean?
  Q2: Which figure represents a periodic signal and which represents a non-periodic signal (also called energy signal)?

## Slide 21: Review Sampling
According to Nyquist, how fast should you sample?
  What is the rule of thumb in practice?
If you have signal ranges from 1 - 10 Hz and noise ranges from 50 to 1000 Hz, what is the correct practical lower bound in sampling rate if you decide to process the signal digitally?
  A. 20 Hz
  B. 60 Hz
  C. 150 Hz
  D. 3000 Hz
  E. 5000 Hz

## Slide 22: Low Pass Filters – I
Signals are often contaminated by high-frequency noises that need to be removed.
The following is a simple two-stage active filter:
The Op-Amp isolates the interactions between two RC circuits.
This allows a simple analysis. You can get such filters on a chip

## Slide 23: Low Pass Filters – 2
The more the number of stages, the sharper is the rate of reduction of the signal after the cut-off frequency. If you want a sharper rate of reduction, you need more stages.
  In filter literature, the number of stages is called the order of the filter.

## Slide 24: Low Pass Filters – 3
The magnitude attenuation and the phase delay of a N-stage filter illustrated earlier are as follows, where cutoff = R1C1 = R2C2 = …
The formula for the commonly used Butterworth filter is
  SQRT(1 /(1 + (/cutoff)2N ))

## Slide 25: Application Notes
We have two control variables, the cut-off frequency and the order of the filter.
  1. The lower the cutoff frequency, the more effective is the filtering. But if the cutoff frequency is too close to the useful signal, the signal will also be reduced.
  The higher the order, the more powerful is the filter.
The design of a filter is iterative.
  You may need to adjust the cutoff frequency and the order of the filter until the requirements are met.

## Slide 26: Application Example
The frequencies of interest in the signal are from 10 to 60 Hz. There is significant noise with frequencies in the range 500 - 1000 Hz seen on the scope.
  An anti-aliasing filter is used to filter out the high-frequency noises.
Suppose that we pick a cut-off frequency at 100 Hz. What should be the order (stages) of the filter so that the signal will be reduced no more than 30% while the noise will be reduced at least 96%?
Max. magnitude reduction in signal:
Min. magnitude reduction in noise:

## Slide 27: Design a Digital Low Pass Filter
The general structure of a digital filter is:
  y = a1*y1 + a2*y2 + .. + b0*x + b1*x1 + b2*x2, where
    y is the current (filtered) output that you want to compute
    x is the current raw input before filter
    yk and xk are the k-step previous output and input respectively
You can find the a’ s and b’ s using tools like MATLAB
[b, a] = butter[n, wn] gives an nth order (n-stage) Butterworth filter with cut-off frequency wn.
  wn must be in the form of percentage of the Nyquist frequency, which is defined as 0.5 of the sampling rate.
Suppose that the sampling rate is 200 Hz and the cut-off frequency is 20, then the Nyquist frequency is 200/2 = 100 Hz and wn = 20/100 = 0.2

## Slide 28: Digital Filter Design Example
[b,a] = butter[2, 0.2]
  b = 0.0675 0.1349 0.0675
  a = 1.0000 -1.1430 0.4128
  y = -1.143*y1+ 0.4128*y2 + 0.0675*x + 0.1349*x1 + 0.0675*x2
freqz[b,a] // decibel 20 log (v1/v2), the base is 10.

## Slide 29: Summary of Lecture
Source of deterministic errors and random noises
Basics of signal spectrum
  Nyquist sampling
  Fourier transform
Basic filters
  What you can do and when you should ask for help