## Slide 1: Process Scheduling & Concurrency
Lecture 13

## Slide 2: Summary of Previous Lecture
DMA
Single vs. Double buffering
Introduction to Processes
  Foreground/Background systems
  Processes
  Process Control Block (PCB)

## Slide 3: Outline of This Lecture
FOCUS: Multiple processes/tasks running on the same CPU
Context switching = alternating between the different processes or tasks
Scheduling = deciding which task/process to run next
  Various scheduling algorithms
Critical sections = providing adequate memory-protection when multiple tasks/processes run concurrently
  Various solutions to dealing with critical sections

## Slide 4: The Big Picture
stack
task priority
CPU registers
CPU registers
Processor
Memory
stack
task priority
CPU registers
stack
task priority
CPU registers
...
}
context

## Slide 5: Terminology
Batch system  operating system technique where one job completes before the next one starts
Multi-tasking  operating system technique for sharing a single processor between multiple independent tasks
  Cooperative multi-tasking  running task decides when to yield the CPU
  Preemptive multi-tasking  another entity (the scheduler) decides when to make a running task yield the CPU
In both cooperative and preemptive cases
  Scheduler decides the next task to run on the CPU, and starts this next task
  Hardware interrupts and high-priority tasks might cause a task to yield the CPU prematurely
Multitasking vs. batch system
  Multitasking has more overheads – saving the current task, selecting the next task, loading the next task
  Multitasking needs to provide for inter-task memory protection
  Multitasking allows for concurrency – if a task is waiting for an event, another task can grab the CPU and get some work done

## Slide 6: Context Switch
Note: I will use the work “task” interchangeably with “process” in this lecture
The CPU’s replacement of the currently running task with a new one is called a “context switch”
Simply saves the old context and “restores” the new one
  Current task is interrupted
  Processor’s registers for that particular task are saved in a task-specific table
  Task is placed on the “ready” list to await the next time-slice
  Task control block stores memory usage, priority level, etc.
  New task’s registers and status are loaded into the processor
  New task starts to run
This generally includes changing the stack pointer, the PC and the PSR (program status register)

## Slide 7: When Can A Context-Switch Occur?
Time-slicing
  Time-slice: period of time a task can run before a context-switch can replace it
  Driven by periodic hardware interrupts from the system timer
  During a clock interrupt, the kernel’s scheduler can determine if another process should run and perform a context-switch
  Of course, this doesn’t mean that there is a context-switch at every time-slice!
Preemption
  Currently running task can be halted and switched out by a higher-priority active task
  No need to wait until the end of the time-slice
Time-slice
Context switches
Context switches

## Slide 8: Context Switch Overhead
How often do context switches occur in practice?
  It depends – on what?
System context-switch vs. processor context-switch
  Processor context-switch = amount of time for the CPU to save the current task’s context and restore the next task’s context
  System context-switch = amount of time from the point that the task was ready for context-switching to when it was actually swapped in
How long does a system context-switch take?
  System context-switch time is a measure of responsiveness
  Time-slicing  time-slice period + processor context-switch time
  Preemptive  processor context-switch time
  Preemption is mostly preferred because it is more responsive (system context-switch = processor context-switch)

## Slide 9: Process State
A process can be in any one of many different states
Waiting
for
Event
Delayed
Dormant
Ready
Running
Interrupted
task
deleted
interrupted
task create
task
delete
task deleted
context switch
delay
expired
event
occurred
wait for
event
delay task
for n ticks
task delete

## Slide 10: Ready List
Process
Control
Block
Process
Control
Block
Process
Control
Block
Ready
List
NULL

## Slide 11: Process Scheduling
What is the scheduler?
  Part of the operating system that decides which process/task to run next
  Uses a scheduling algorithm that enforces some kind of policy that is designed to meet some criteria
Criteria may vary
  CPU utilization ­ keep the CPU as busy as possible
  Throughput ­ maximize the number of processes completed per time unit
  Turnaround time ­ minimize a process’ latency (run time), i.e., time between task submission and termination
  Response time ­ minimize the wait time for interactive processes
  Real-time ­ must meet specific deadlines to prevent “bad things” from happening

## Slide 12: FCFS Scheduling
First­come, first­served (FCFS)
  The first task that arrives at the request queue is executed first, the second task is executed second and so on
  Just like standing in line for a roller­coaster ride
FCFS can make the wait time for a process very long
        Process Total Run Time
        P1 12 seconds
        P2 3 seconds
        P3 8 seconds
P1
P2
P3
P2
P3
P1
If arrival order is P1, P2, P3
If arrival order is P2, P3, P1

## Slide 13: Shortest­Job­First Scheduling
Schedule processes according to their run-times
      Process Total Run Time
      P1 5 seconds
      P2 3 seconds
      P3 1 second
      P4 8 seconds
May be run­time or CPU burst­time of a process
  CPU burst time is the time a process spends executing in-between I/O activities
  Generally difficult to know the run-time of a process
P3
P2
P1
P4

## Slide 14: Priority Scheduling
Shortest­Job­First is a special case of priority scheduling
Priority scheduling assigns a priority to each process. Those with higher priorities are run first.
  Priorities are generally represented by numbers, e.g., 0..7, 0..4095
  No general rule about whether zero represents high or low priority
  We'll assume that higher numbers represent higher priorities
      Process BurstTime Priority
      P1 5 seconds 6
      P2 3 seconds 7
      P3 1 second 8
      P4 8 seconds 5
P3
P2
P1
P4

## Slide 15: Priority Scheduling (con't)
Who picks the priority of a process?
What happens to low­priority jobs if there are lots of high­priority jobs in the queue?

## Slide 16: Multi­level Round­Robin Scheduling
Each process at a given priority is executed for a small amount of time called a time-slice (or time quantum)
When the time slice expires, the next process in round­robin order at the same priority is executed ­­ unless there is now a higher priority process ready to execute
Each time slice is often several timer ticks
      Process BurstTime Priority
      P1 4 seconds 6
      P2 3 seconds 6
      P3 2 seconds 7
      P4 4 seconds 7
  Quantum is 1 “unit” of time (10ms, 20ms, …)
P3
P4
P1
P2
P4
P4
P4
P3
P1
P1
P1
P2
P2

## Slide 17: Up Next: Interactions Between Processes
Multitasking  multiple processes/tasks providing the illusion of “running in parallel”
  Perhaps really running in parallel if there are multiple processors
A process/task can be stopped at any point so that some other process/task can run on the CPU
At the same time, these processes/tasks running on the same system might interact
  Need to make sure that processes do not get in each other’s way
  Need to ensure proper sequencing when dependencies exist
  Rest of lecture: how do we deal with shared state between processes/tasks running on the same processor?

## Slide 18: Critical Section
Piece of code that must appear as an atomic action
Atomic Action ­ action that “appears” to take place in a single indivisible operation
process one process two
    while (1){ while (1){
    x = x + 1; x = x + 1;
    } }
if “x=x+1” can execute atomically, then there is no race condition
Race condition ­ outcome depends on the particular order in which the operations takes place

## Slide 19: Critical Section

## Slide 20: Solution 1 – Taking Turns
Use a shared variable to keep track of whose turn it is
If a process, Pi , is executing in its critical section, then no other process can be executing in its critical section
Solution 1 (key is initially set to 1)
    process one process two
    while(key != 1); while (key != 2);
    x = x + 1; x = x + 1;
    key = 2; key = 1;
Hmmm…..what if Process 1 turns the key over to Process 2, which then never enters the critical section?
We have mutual exclusion, but do we have progress?

## Slide 21: Solution 1

## Slide 22: The Rip Van Winkle Syndrome
Problem with Solution 1: What if one process sleeps forever?
  while (1){ while (1){
  while(key != 1); while (key != 2);
  x = x + 1; x = x + 1;
  key = 2; key = 1;
  sleep (forever); }
  }
Problem: the right to enter the critical section is being explicitly passed from one process to another
Each process controls the key to enter the critical section

## Slide 23: Solution 2 – Status Flags
Have each process check to make sure no other process is in the critical section
    process one process two
  while (1){ while (1) {
  while(P2inCrit == 1); while (P1inCrit == 1);
  P1inCrit = 1; P2inCrit = 1;
  x = x + 1; x = x + 1;
  P1inCrit = 0; P2inCrit = 0;
  } }
  initially,
  P1inCrit = P2inCrit = 0;
So, we have progress, but how about mutual exclusion?

## Slide 24: Solution 2

## Slide 25: Solution 2 Does not Guarantee Mutual Exclusion
  process one process two
  while (1){ while (1){
  while(P2inCrit == 1); while (P1inCrit == 1);
  P1inCrit = 1; P2inCrit = 1;
  x = x + 1; x = x + 1;
  P1inCrit = 0; P2inCrit = 0;
  } }
P1inCrit P2inCrit
Initially 0 0
P1 checks P2inCrit 0 0
P2 checks P1inCrit 0 0
P1 sets P1inCrit 1 0
P2 sets P2inCrit 1 1
P1 enters crit. section 1 1
P 2 enters crit. Section 1 1
P2 executes
entry

## Slide 26: Solution 3: Enter the Critical Section First
Set your own flag before testing the other one
process one process two
  while (1){ while (1){
  P1inCrit = 1; P2inCrit = 1;
  while (P2inCrit == 1); while (P1inCrit == 1);
  x = x + 1; x = x + 1;
  P1inCrit = 0; P2inCrit = 0;
  } }
P1inCrit P2inCrit
Initially 0 0
P1 sets P1inCrit 1 0
P2 sets P2inCrit 1 1
P1 checks P2inCr 1 1
P2 checks P1inCrit 1 1
Each process waits indefinitely for the other
Deadlock ­ when the computer can do no more useful work
P2 executes
entry

## Slide 27: Solution 4 ­ Relinquish Crit. Section
    process one process two
    while (1){ while (1){
    P1inCrit = 1; P2inCrit = 1;
    while (P2inCrit == 1){ while (P1inCrit == 1){
    P1inCrit = 0; P2inCrit = 0;
    sleep(x); sleep(y);
    P1inCrit = 1; P2inCrit = 1;
    } }
    x = x + 1; x = x + 1;
    P1inCrit = 0; P2inCrit = 0;
    } }
P1inCrit P2inCrit
Initially 0 0
P1 sets P1inCrit 1 0
P2 sets P2inCrit 1 1
P1 checks P2inCrit 1 1
P2 checks P1inCrit 1 1
P1 sets P1inCrit 0 0
P2 sets P2inCrit 0 0
P1 sets P1inCrit 1 0
P2 sets P2inCrit 1 1
Starvation ­ when some process(es) can make progress, but some identifiable process is being indefinitely delayed
Periodically clear and reset your own flag before testing the other one
P2 enters
again as
P1 sleeps

## Slide 28: Dekker's Algorithm – Take Turns & Use Status Flags
process one process two
while (1){ while (1){
P1inCrit = 1; P2inCrit = 1;
while (P2inCrit == 1){ while (P1inCrit == 1){
if (turn == 2){ if (turn == 1){
P1inCrit = 0; P2inCrit = 0;
while (turn == 2); while (turn == 1);
P1inCrit = 1; P2inCrit = 1;
} }
} }
x = x + 1; x = x + 1;
turn = 2; turn = 1;
P1inCrit = 0; P2inCrit = 0;
} }
Initially, turn = 1 and P1inCrit = P2inCrit = 0;

## Slide 29: Dekker's Algorithm

## Slide 30: Mutual Exclusion
Simplest form of concurrent programming
Dekker's algorithm is difficult to extend to 3 or more processes
Semaphores are a much easier mechanism to use

## Slide 31: Semaphores
Semaphore ­ an integer variable (> 0) that normally can take on only non­zero values
Only three operations can be performed on a semaphore ­ all operations are atomic
  init(s, #)
    sets semaphore, s, to an initial value #
  wait(s)
    if s > 0, then s = s ­ 1;
    else suspend the process that called wait
  signal(s)
    s = s + 1;
    if some process P has been suspended by a previous wait(s), wake up process P
      normally, the process waiting the longest gets woken up

## Slide 32: Mutual Exclusion with Semaphores
    process one process two
    while (1){ while (1){
    wait(s); wait(s);
    x = x + 1; x = x + 1;
    signal(s); signal(s);
    } }
initially, s = 1 (this is called a binary semaphore)

## Slide 33: Mutual Exclusion with Semaphores

## Slide 34: Implementing Semaphores
Disable interrupts
  Only works on uniprocessors
Hardware support
  TAS ­ Test and Set instruction
    The following steps are executed atomically
      TEST the operand and set the CPU status flags so that they reflect whether it is zero or non­zero
      Set the operand, so that it is non­zero
Example
  LOOP: TAS lockbyte
  BNZ LOOP
  critical section
  CLR lockbyte
Called a busy-wait
(or a spin-loop)

## Slide 35: The Producer­Consumer Problem
One process produces data, the other consumes it
  (e.g., I/O from keyboard to terminal)
producer(){ consumer(){
while(1){ while(1){
produce; wait(n);
appendToBuffer; takeFromBuffer;
signal(n); consume();
} }
} }
Initially, n = 0;

## Slide 36: Another Producer/Consumer
What if both appendToBuffer and takeFromBuffer cannot overlap in execution
  For example, if buffer is a linked list & a free pool
  Or, multiple producers and consumers
      producer() { consumer() {
      while(1){ while(1){
      produce; wait(n);
      wait(s); wait(s);
      appendToBuffer; takeFromBuffer;
      signal(s); signal(s);
      signal(n); consume();
      } }
      } }
Initially, s = 1, n = 0;

## Slide 37: Bounded Buffer Problem
Assume a single buffer of fixed size
  Consumer blocks (sleeps) when buffer is empty
  Producer blocks (sleeps) when the buffer is full
producer() { consumer() {
while(1) { while(1){
produce; wait(itemReady);
wait(spacesLeft); wait(mutex);
wait(Mutex); takeFromBuffer;
appendToBuffer; signal(mutex);
signal(Mutex); signal(spacesLeft);
signal(itemReady); consume();
} }
} }
Initially, s = 1, n = 0; e = sizeOfBuffer;

## Slide 38: Food for Thought
The Bakery Algorithm
  On arrival at a bakery, the customer picks a token with a number and waits until called
  The baker serves the customer waiting with the lowest number
    (the same applies today at jewelry shop and AAA ;-)
What are condition variables?
  How does the producer block when the buffer is full?
Is there any way to avoid busy-waits in multiprocessor environments?
  Why or why not?

## Slide 39: Atomic SWAP Instruction on the ARM
SWP combines a load and a store in a single, atomic operation
  ADR r0, semaphore
  SWPB r1, r1,[r0]
  SWP loads the word (or byte) from memory location addressed in Rn into Rd and stores the same data type from Rm into the same memory location
  SWP<cond> {B} Rd, Rm, [Rn]

## Slide 40: Summary of Lecture
Context switching = alternating between the different processes or tasks
Scheduling = deciding which task/process to run
  First-come first-served
  Round-robin
  Priority-based
Critical sections = providing adequate memory-protection when multiple tasks/processes run concurrently
  Various solutions to dealing with critical sections