## Slide 1: Interrupts + Serial Communications
Lecture 10

## Slide 2: Summary of Previous Lecture
Timers
Interrupt vs. polled I/O
  Polling the Serial Port – Example with code

## Slide 3: Outline of This Lecture
Interrupts (continued)
  Interrupt handlers
  Interrupts on the X-Board
  Installing and writing interrupt handlers
Serial Communications
  Asynchronous protocols
  Serial port and bit transmission
Detours signify material outside of, but indirect/direct background/review material for, the main lecture
(available in the lecture handout on Blackboard)

## Slide 4: Review of ARM Exceptions

## Slide 5: Review of ARM Interrupts
Vector table
  Reserved area of 32 bytes at the end of the memory map
  One word of space for each exception type
  Contains a Branch or Load PC instruction for the exception handler
Exception modes and registers
  Handling exceptions changes program from user to non-user mode
  Each exception handler has access to its own set of registers
    Its own r13 = stack pointer
    Its own r14 = link register
    Its own SPSR (Saved Program Status Register)
  Exception handlers must save (restore) other register on entry (exit)

## Slide 7: What if Exceptions Happen Simultaneously?

## Slide 8: Enabling IRQ and FIQ
Program Status Register
To disable interrupts, set corresponding “F” or “I” bit to 1
On interrupt, processor does the following
    Switches register banks
    Copies CPSR to SPSR_mode (saves mode, interrupt flags, etc.)
    Changes the CPSR mode bits (M[4:0])
    Disables interrupts
    Copies PC to R14_mode (to provide return address)
    Sets the PC to the vector address of the exception handler
Interrupt handlers must contain code to clear the source of the interrupt
N
31 30 29 28 27 … 8 7 6 5 4 3 2 1 0
Z
C
V
I
F
M4
M3
M2
M1
M0

## Slide 9: Interrupt Details
On an IRQ interrupt, the processor will ...
  If the “I” bit in the CPSR is clear, the current instruction is completed and then the ARM will
    Save the address of the next instruction plus 4 in r14_irq
    Save the CPSR in the SPSR_irq
    Force the CPSR mode bits M[4:0] to 10010 (binary)
This switches the CPU to IRQ mode and then sets the “I” flag to disable further IRQ interrupts
On an FIQ interrupt, the processor will ...
  If the “F” bit in the CPSR is clear and the current instruction is completed, the ARM will
    Save the address of the next instruction plus 4 in r14_fiq
    Force the CPSR mode bits M[4:0] to 10001 (binary)
      This switches the CPU to FIQ mode and then sets the “I” and “F” flags to disable further IRQ or FIQ interrupts

## Slide 10: Interrupt Details
On an IRQ interrupt, if the “I” bit in the CPSR is clear, the current instruction is completed and then the ARM will
  Save the address of the next instruction plus 4 in r14_irq
Doesn’t this mess up the return address?
  See Section 2.6.6 of the ARM Architecture Reference Manual !
    Choice 1 – but return with SUBS PC, r14, #4

## Slide 11: IRQ vs. FIQ
External interrupts that are active LOW
FIQs have higher priority than IRQs
  When multiple interrupts occur, FIQs get serviced before IRQs
  Servicing an FIQ causes IRQs to be disabled until the FIQ handler re-enables them
    CPSR restored from the SPSR at the end of the FIQ handler
How are FIQs made faster?
  They have five extra registers at their disposal, allowing them to store status between calls to the handler
  FIQ vector is the last entry in the vector table
    The FIQ handler can be placed directly at the vector location and run sequentially after the location
    Cache-based systems: Vector table + FIQ handler all locked down into one block

## Slide 12: Interrupt Handlers
When an interrupt occurs, the hardware will jump to an “interrupt handler”
user program
user program
IRQ Interrupt handler
Interrupt
On interrupt, the processor will set the corresponding interrupt bit in the CPSR to disable subsequent interrupts of the same type from occurring.
However, interrupts of a higher priority can still occur.
Task
IRQ
FIQ
time

## Slide 13: Nested/Re-entrant Interrupts
Interrupts can occur within interrupt handlers
user program
user program
IRQ Interrupt handler
Interrupt
On interrupt, the processor will set the corresponding interrupt bit in the CPSR to disable subsequent interrupts of the same type from occurring.
However, interrupts of a higher priority can still occur.
Task
IRQ
FIQ
time
FIQ Interrupt handler
Second
Interrupt

## Slide 14: Timing of Interrupts
Before an interrupt handler can do anything, it must save away the current program's registers (if it touches those registers)
That's why the FIQ has lots of extra registers ­ to minimize CPU context saving overhead
user program
user program
“servicing” interrupt
Interrupt
Task
IRQ
FIQ
time
cpu context saved
cpu context restored
Interrupt response
Interrupt latency

## Slide 15: Interrupts on the X-Board
Intel 80200 Processor has two interrupt inputs
  nIRQ or nFIQ
Interrupt steering function
  Part of the firmware
  Routes the interrupts to the appropriate input
Interrupt status register
  Able to read which interrupts are currently active
Interrupt Mask register
  Used to inhibit an interrupt source from raising the 80200 interrupt input
Can change Interrupt Mask or Steering Register at any time
Question: What happens if an interrupt arrives as you are changing the Interrupt Mask or the Steering Register?

## Slide 16: X-Board Interrupt Controller

## Slide 17: More on X-Board Interrupts
Difference between Interrupt Mask and Interrupt Status Registers
  Interrupt Status Register = status of interrupt source
  Interrupt Mask Register = whether interrupt source is masked from CPU
  An active but masked interrupt will have
    Status Register will reflect that interrupt is active
    Interrupt Mask Register will prevent the interrupt signal from being activated
All interrupts must be cleared at their source
Exception: The software-controllable interrupt
  Provided in addition to the external and internal interrupts
  Activation reflected in the Interrupt Controller’s Status Register
Next Page: Interrupt Controller’s Status Register

## Slide 19: Jumping to the Interrupt Handler
Auto-vectored
  Processor-determined address of interrupt handler based on type of interrupt
  This is what the ARM does
Vectored
  Device supplies processor with address of interrupt handler
Why the different methods?
  If multiple devices uses the same interrupt type (IRQ vs. FIQ), in an Auto-vectored system the processor must poll each device to determine which device interrupted the processor
    This can be time-consuming if there is a lot of devices
  In a vectored system, the processor would just take the address from the device (which dumps the interrupt vector onto a special bus).

## Slide 20: Writing Your Own Interrupt Handler
Use the __irq function declaration keyword
  Preserves all ATPCS corruptible registers
  Preserves all other registers
  Exits the function cleanly (sets PC and CPSR correctly on exit)
Cannot be used for re-entrant interrupt handlers (does not save or restore SPSR)
See ADS_Developer_Guide, Section 5.5 for more details

## Slide 21: Serial Communications

## Slide 22: Serial vs. Parallel
Serial ports
  Universal Asynchronous Receiver/Transmitter (UART): controller
  Takes the computer bus’ parallel data and serializes it
  Transfer rate of 115 Kbps
  Example usage: Modems
Parallel ports
  Sends the 8 bits in parallel
  50-100 KBps (standard), upto 2 MBps (enhanced)
  Example usage: Printers, Zip drives
PARALLEL
SERIAL

## Slide 23: Data Communication
Communications between computer and monitor over serial line
  Data is converted from parallel (bytes) to serial (bits) in the bus interface
  Bits are sent over wire (TX) to terminal (or back from terminal to computer)
  Receiving end (RX) translates bit stream back into parallel data (bytes)
Parallel-to-Serial
Converter
CPU
Serial-to-Parallel
Converter
RX
TX
RX
TX
Computer
Terminal
Serial
Link

## Slide 24: Types of Serial Communication
Two types of configurations
  point­to­point: two end stations communicate as peers
  multi­drop: one device is designated as master (primary), the other devices are slaves (secondaries)
Physical link can consist of either two or four wires
  Two wire link provides signal and ground wires
  Four wire link provides two sets of signal and ground wires
Full­duplex link
  One signal wire is for transmitting, the other for receiving
  Closed loop: individual characters are echoed back to transmitter
  Open loop: data is assumed to reach its destination
Half­duplex link
  One signal wire is for both transmitting and receiving
TX
RX

## Slide 25: Data Modulation
When sending data over serial lines, logic signals are converted into a form the physical media (wires) can support
RS232C uses bipolar pulses
  Any signal greater than +3 volts is considered a mark
  Any signal less than ­3 volts is considered a space
20 mA current loop
  Uses four wires, trasmit+, transmit­, receive+ and receive­
  Voltage is applied at one end and the current travels to the far end, passes through a load resistor and then returns to the transmitter
  HIGHs and LOWs are determined by the presence or absence of 20 mA current
Other schemes modulate the amplitude or frequency of a frequency carrier signal

## Slide 26: Serial Communications Protocols
A Communications protocol is a convention for data transmission that includes such functions as timing, formatting and data representation
Two categories of protocols:
  Asynchronous protocols
  successive data appear in the data stream at arbitrary times, with no specific clock control governing the relative delays in data
  Synchronous protocols
  each successive datum in a stream of data is governed by a master data clock and appears at a specific interval of time
    Often, protocols deliver serial data in 8­bit characters ­­ asynchronous protocols treat each character as an individual message, and the characters appear in the data stream at arbitrary relative times. However, within each character, the bits are transmitted at a fixed predetermined clock rate

## Slide 27: Asynchronous Protocols
Many different types of electrical connection standards
  RS­232­C
  20 mA current loop
  RS­422, RS­423, and RS­499
Timing is the same
  idle line is assumed to be in high (1) state
  each character begins with a zero (0) bit, followed by 8 data bits and then 1, 1­1/2, or 2 closing 1 bits.
  Bits are usually encoded using ASCII (American Standard Code for Information Interchange)
Data
Clock
1
parity
bit
7 data bits
1 or 2
stop
bits
Sampling points

## Slide 28: Asynchronous Protocols (cont’d)
Start (stop) bits identify the beginning (end) of each character ­­ also permits receiver to resynchronize local clock to each new character
  Remember: characters can begin at arbitrary times
Bit Sampling
  Receiver's clock is not identical to the transmitter's clock
  Best if the sample is near the middle of a bit
  Not always possible because of clock differences
  Receiver clock (in relation to transmitter) cannot gain or lose more than 1/2 bit per 10 to 11 clock periods (time to transmit one character)
    Clocks must be accurate to within 5%
  Most receivers use a fast clock to determine the “middle” of a bit
    Typical is 16X clock which can take 16 samples per 1 bit
      Begins by detecting start bit which clears clock counter
      Clock counter increments to 16 for each tick of the receiver clock
      When the counter reaches 8, it has reached the middle of the bit and takes the sample

## Slide 29: Serial Port
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Clock
RxRegister
TxRegister
FIFO Buffer
FIFO Buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Clock
RxRegister
TxRegister
FIFO Buffer
FIFO Buffer
Processor
Peripheral

## Slide 30: Transmitting Bits
7
6
7
5
6
7
4
5
6
7
3
4
5
6
7
2
3
4
5
6
7
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
n
n+1
n+2
n+3
n+4
n+5
n+6
n+7
n+8
Transmitter
Receiver
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
0
1
2
3
4
5
0
1
2
3
4
0
1
2
3
0
1
2
0
1
0
n
n+1
n+2
n+3
n+4
n+5
n+6
n+7
n+8
Interrupt when
Transmitter (Tx) is empty
Interrupt when
Receiver (Rx) is full

## Slide 31: Coping with Errors ­ Parity
A single bit determined by the number of 1's in a word
The simplest form of error detection
Parity bit is appended to each group­of­bits (byte, word)
Odd parity
  Parity bit is chosen to force the number of 1's to be odd
  Example: 0 0 0 0 1 0 1 0
        0 0 0 0 1 0 1 0 1
Even parity
  Parity bit is chosen to force the number of 1's to be even
When receiving data, the receiver will check every group of bits
  Parity checker determines if the parity of a group of bits is correct
  If wrong, an error (exception) will be raised to let the processor and software know an error has occurred in parity bit
parity bit

## Slide 32: Interfacing Serial Data to Microprocessor
Processor has parallel buses for data ­­ need to convert serial data to parallel (and vice versa)
Standard way is with UART
UART ­ Universal asynchronous receiver and transmitter
  USART ­ Universal synchronous and asynchronous receiver and transmitter
Chip Reg
Select
R/W
Control
Tx Data Reg
Status Reg
Control Reg
Rx Data Reg
Tx Shift Reg
Rx Shift Reg
Tx Clock
Rx Clock
IRQ
CTS
RTS
Rx Data
Tx Data
Data
Bus
Buffers
D0-D7

## Slide 33: Summary of Lecture
Interrupts (continued)
  Interrupt handlers
  Nested interrupts
  Interrupts on the X-Board
  Installing and writing interrupt handlers
Serial Communications
  Data communications and modulation
  Asynchronous protocols
  Serial port and bit transmission
Quiz #3