## Slide 1: Interrupts
Fundamental concept in computation
Interrupt execution of a program to “handle” an event
  Don’t have to rely on program relinquishing control
  Can code program without worrying about others
Issues
  What can interrupt and when?
  Where is the code that knows what to do?
  How long does it take to handle interruption?
  Can an interruption be, in turn, interrupted?
  How does the interrupt handling code communicate its results?
  How is data shared between interrupt handlers and programs?

## Slide 2: What is an Interrupt?
Reaction to something in I/O (human, comm link)
Usually asynchronous to processor activities
“interrupt handler” or “interrupt service routine” (ISR) invoked to take care of condition causing interrupt
  Change value of internal variable (count)
  Read a data value (sensor, receive)
  Write a data value (actuator, send)
Main Program
  Instruction 1
  Instruction 2
  Instruction 3
  Instruction 4
  …..
ISR
  Save state
  Instruction 1
  Instruction 2
  Instruction 3
  …..
  Restore state
  Return from Interrupt

## Slide 3: Interrupts
Code sample that does not interrupt
    char SPI_SlaveReceive(void)
    {
    /* Wait for reception complete */
    while(!(SPSR & (1<<SPIF)))
    ;
    /* Return data register */
    return SPDR;
    }
Instead of busy waiting until a byte is received the processor can generate an interrupt when it sets SPIF
    SIGNAL(SIG_SPI) {
    RX_Byte = SPDR
    }

## Slide 4: Saving and Restoring Context
Processor and compiler dependent
Where to find ISR code?
  Different interrupts have separate ISRs
Who does dispatching?
  Direct
    Different address for each interrupt type
    Supported directly by processor architecture
  Indirect
    One top-level ISR
    Switch statement on interrupt type
  A mix of these two extremes?

## Slide 5: Saving and Restoring Context
How much context to save?
  Registers, flags, program counter, etc.
  Save all or part?
  Agreement needed between ISR and program
Where should it be saved?
  Stack, special memory locations, shadow registers, etc.
  How much room will be needed on the stack?
  Nested interrupts may make stack reach its limit – what then?
Restore context when ISR completes

## Slide 6: Ignoring Interrupts
Can interrupts be ignored?
  It depends on the cause of the interrupt
  No, for nuclear power plant temperature warning
  Yes, for keypad on cell phone (human timescale is long)
When servicing another interrupt
  Ignore others until done
  Can’t take too long – keep ISRs as short as possible
    Just do a quick count, or read, or write – not a long computation
Interrupt disabling
  Will ignored interrupt “stick”?
    Rising edge sets a flip-flop
  Or will it be gone when you get to it?
    Level changes again and its as if it never happened
  Don’t forget to re-enable

## Slide 7: Prioritizing Interrupts
When multiple interrupts happen simultaneously
  Which is serviced first?
  Fixed or flexible priority?
Priority interrupts
  Higher priority can interrupt
  Lower priority can’t
Maskable interrupts
  “don’t bother me with that right now”
  Not all interrupts are maskable, some are non-maskable

## Slide 8: Interrupts in the ATmega16
External interrupts
  From I/O pins of microcontroller
Internal interrupts
  Timers
    Output compare
    Input capture
    Overflow
  Communication units
    Receiving something
    Done sending
  ADC
    Completed conversion

## Slide 9: Interrupt Jump Vector Table
Fixed location in memory to find first instruction for each type of interrupt
Only room for one instruction
  JMP to location of complete ISR

## Slide 10: Chain of Events on Interrupt
Finish executing current instruction
Disable all interrupts
Push program counter on to stack
Jump to interrupt vector table
Jump to start of complete ISR
Save any context that ISR may otherwise change
  Registers and flags must be saved within ISR and restored before it returns – this is very important!
Re-enable interrupts if nested interrupts are ok
Complete ISR’s code
Re-enable interrupts upon return
Jump back to next instruction before interruption
Automatic
RETI
Compiler
SEI
CLI

## Slide 11: Shared Data Problem
When you use interrupts you create the opportunity for multiple sections of code to update a variable.
This might cause a problems in your logic if an interrupt updates a variable between two lines of code that are directly dependent on each other (e.g. if statement)
One solution is to create critical sections where you disable the interrupts for a short period of time while you complete your logic on the shared variable cli(); …..critical section code goes here….. sei();

## Slide 12: External Interrupts
Special pins: INT0, INT1, INT2
  Can interrupt on edge or level
Can interrupt even if set to be output pins
  Implements “software interrupts” by setting output

## Slide 13: Closer Look at a Timer/Counter
Timer0/Counter0
  Clear timer on compare match (auto reload)
  Prescaler (divide clock by up to 1024)
  Overflow and compare match interrupts
  Registers
    Configuration
    Count value
    Output compare value

## Slide 14: Timer/Counter Registers
Timer/Counter Control Register TCCR0

## Slide 15: Timer/Counter Registers (cont’d)
Timer/Counter Control Register TCCR0

## Slide 16: Timer/Counter Registers (cont’d)
Timer/Counter Control Register TCCR0

## Slide 17: Timer/Counter Registers (cont’d)

## Slide 18: Setting Register Values
Defined names for each register and bit
  Set timer to clear on match
  Set prescaler to 1024 TCCR0 = (1<<WGM01) | (1<<CS02) | (1<<CS00);
  Set count value to compare against OCR0 = 150;
  Set timer to interrupt when it reaches count TIMSK = (1<<OCIE0);

## Slide 19: Writing an Interrupt Handler in C
Set and clear interrupt enable
  sei();
  cli();
Interrupt handler
  SIGNAL(SIG_OUTPUT_COMPARE0) { i++; }
Setting I/O registers
  TCCR0 = (1<<WGM01) | (1<<CS02) | (1<<CS00);
Enabling specific interrupts
  TIMSK = (1<<OCIE0);

## Slide 20: Switch Debouncing

## Slide 21: A Switch is Pressed, So What???
5V
Vs
t
V
5
0
Problem: Switch Bounce
Initial
Connection
Finally
Contact Closed
Typically 10-20ms
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Debouncing
When a switch (any type) changes state (on -> off or off -> on), it presents a mechanical bouncing which generates a signal similar to the one shown at the right.
The resistor R is needed because the signal S can not be left “floating” in an undefined state when the switch changes from state 1 to 2.
Without debouncing the signal can generate several interrupts (or status changes) corresponding to just one action.
Debouncing consists in “Filtering” the signal S so that a proper operation of the switch action is sensed.
Debouncing can be done in hardware of software
Microcontroller
1
2
C
5V
R
5V
S
Read Key (should be stable)
Techniques that can be used:
If status loop: after first status change, program timer and after elapsed time read key status.
If Interrupt: on first interrupt program timer which will interrupt after elapsed time. Then read key status.
Δt
Δt

## Slide 23: Light Dependent Resistors (LDRs)

## Slide 24: Light Dependent Resistors (LDRs)
Devices whose resistance changes (usually decreases) with light striking it
(also called photocells, photoconductors)
Light striking a semiconducting material can provide sufficient energy to cause electrons to break away from atoms.
Free electrons and holes can be created which causes resistance to be reduced
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Light Dependent Resistors (LDRs)
Typical materials used are Cadmium Sulphide (CdS), Cadmium Selenide (CdSe), Lead Sulphide
With no illumination, resistance can be greater than 1 M (dark resistance).
Resistance varies inversely proportional to light intensity.
Reduces down to 10-100s ohms
100ms/10ms response time
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Light Dependent Resistors (LDRs)
1 M
100k
10k
1k
100
1 10 100 1000 lm/m2
Illumination
Resistance
CdS LDR
Top view
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Light Dependent Resistors (LDRs)
LDRs have a low energy gap
Operate over a wide wavelengths (some, into infrared)
Indium antimonide is good for IR. When cooled is very sensitive, used for thermal scanning of earth’s surface
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Analog to Digital Conversion

## Slide 29: Basic ADC circuits (1)
  Digitizing begins with a ‘start’ pulse
  DAC is ramped up from zero
  counter stopped by comparator when Vin = DAC out
  ADC output is counter value
  Tracking ADC
Simple ramp and comparator ADC
start
Binary output
Unknown
analog
input

## Slide 30: Basic ADC circuits (2)
This ADC circuit is limited and rarely used WHY -
  slow
  variable time to give result
  input signal can vary during digitising
Successive Approximation ADC solves these problems - using
  complex logic to test and retain each DAC bit
  a sample and hold circuit ahead of the comparator

## Slide 31: Successive Approximation ADC
  Fast process - 1 - 100µsecs
  Result always n clocks after start
  Used extensively for 12-16bit DAQ systems

## Slide 32: Flash ADC
  The fastest process <50nsecs
  Limited resolution typically 8 - 10bits
  Half-flash technique is cheaper
Flash
Half-Flash
analog
input
analog
input
Vref
Vref

## Slide 33: A-to-D Conversion Errors

## Slide 34: ATmega16 A-to-D Conversion
Needs a comparator and a D-to-A converter
Takes time to do successive approximation
Interrupt generated when conversion is completed

## Slide 35: A-to-D Conversion on the ATmega16
10-bit resolution (adjusted to 8 bits as needed)
65-260 usec conversion time
8 multiplexed input channels
Capability to do differential conversion
  Difference of two pins
  Optional gain on differential signal (amplifies difference)
Interrupt on completion of A-to-D conversion
0-VCC input range
2*LSB accuracy (2 * 1/1024 = ~0.2%)
  Susceptible to noise – special analog supply pin (AVCC) and capacitor connection for reference voltage (AREF)

## Slide 36: A-to-D Conversion (cont’d)

## Slide 37: A-to-D Conversion (cont’d)
Single-ended or differential
  1 of 8 single-ended
  ADCx – ADC1 at 1x gain
  ADC{0,1} – ADC0 at 10x
  ADC{0,1} – ADC0 at 200x
  ADC{2,3} – ADC2 at 10x
  ADC{2,3} – ADC3 at 200x
  ADC{0,1,2,3,4,5} – ADC2 at 1x

## Slide 38: A-to-D Conversion (cont’d)

## Slide 39: A-to-D Conversion (cont’d)

## Slide 40: A-to-D Conversion (cont’d)

## Slide 41: Writing an Interrupt Handler in C (again)
Ensure main program sets up all registers
Enable interrupts as needed
Enable global interrupts (SEI)
Write handler routine for each enabled interrupt
  What if an interrupt occurs and a handler isn’t defined?
Make sure routine does not disrupt others
  Data sharing problem
  Save any state that might be changed (done by compiler)
Re-enable interrupts upon return
  done by compiler with RETI

## Slide 42: Sleep modes

## Slide 43: Power modes
Processor can go to “sleep” and save power
Different modes put different sets of modules to sleep
  Which one to use depends on which modules are needed to wake up processor
  Timers, external interrupts, ADC, serial communication lines, etc.
set_sleep_mode (mode);
sleep_mode ();

## Slide 44: Power modes (cont’d)

## Slide 45: Power modes (cont’d)
Wake up sources and active clocks