## Slide 1
Introduction to SimpliciTI
Low-power RF protocol from Texas Instruments

## Slide 2
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
2

## Slide 3
What is SimpliciTI?
SimpliciTI is:
– Low Power: a TI proprietary low-power RF network protocol
– Low Cost: uses < 8K FLASH, 1K RAM depending on configuration
– Flexible: simple star w/ extendor and/or p2p communication
– Simple: Utilizes a very basic core API
– Versatile: MSP430+CC110x/2500, CC1110/2510, CC1111/CC2511,
CC2430, CC2520
– Low Power: Supports sleeping devices
3

## Slide 4
Application Areas
SimpliciTI supports:
- alarm & security: occupancy sensors, light sensors, carbon monoxide
sensors, glass-breakage detectors
- smoke detectors
- remote controls
- AMR: gas meters, water meters, e-meters
- home automation: garage door openers, appliances, environmental
devices
4

## Slide 5
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
5

## Slide 6
6
SimpliciTI Network topology
wireless sensing application
• Range can be
extended through
repeaters.
• The circles
represent range of
gateway and
extended range of
repeaters.

## Slide 7
7
SimpliciTI Network topology
Active RF tags
• Active RF tags
typically enter and exit
the network ad-hoc.
• Tags must be able to
quickly associate to
the network while
maintaining low power
consumption.

## Slide 8
SimpliciTI Network topology
Smoke Detector System
C
Gateway
Smoke
Alarm
Smoke
Alarm
Flooded Alarm Message
8
Examples message flows
Optional Access point
Sensor / Extender
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Smoke
Alarm
Alarm Triggered Device

## Slide 9
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
9

## Slide 10
• Network Support
–
–
–
–
–
–
init
ping
link / linklisten
nwk mgmt
send / receive
I/O
• Layers
–
–
–
–
MRFI (“minimal RF interface”)
NWK
nwk applications (modules)
customer applications
Architectural Overview
10

## Slide 11
Application Programming Interface (API)
• initialization
• smplStatus_t SMPL_Init(uint8_t (*callback)(linkID_t));
• linking (bi-directional by default)
• smplStatus_t SMPL_Link(linkID_t *linkID);
• smplStatus_t SMPL_LinkListen(linkID_t *linkID);
• peer-to-peer messaging
• smplStatus_t SMPL_Send(lid, *msg, len);
• smplStatus_t SMPL_Receive(lid, *msg, *len);
• configuration
• smplStatus_t SMPL_Ioctl(object, action, *val);
11

## Slide 12
• operational mode (type)
• power mode (sleep support)
• topology
• addressing / identification
• RAM allocation
– packet size
– buffer sizes
– # supported links (connections)
• security tokens
• messaging (hop ct, repeaters)
• radio (freq, crypto key, modulation,
CCA parameters)
/* FROM smpl_config.dat */
// Number of connections supported
-DNUM_CONNECTIONS=4
// Maximum size of application payload
-DMAX_APP_PAYLOAD=20
// size of low level queues for sent and received frames.
-DSIZE_INFRAME_Q=2
-DSIZE_OUTFRAME_Q=2
// default Link token
-DDEFAULT_LINK_TOKEN=0x01020304
// default Join token
-DDEFAULT_JOIN_TOKEN=0x05060708
// this device's address.
-DTHIS_DEVICE_ADDRESS="{0x79, 0x56, 0x34, 0x12}"
// device type
-DEND_DEVICE
// for End Devices specify the Rx type.
//-DRX_LISTENS
//-DRX_POLLS
//-DRX_NEVER
-DRX_ALWAYS
Simple Configuration
12

## Slide 13
13
Runtime Configuration
• app access to radio controls
• AP nwk mgmt control
• radio frequency
• encryption key
• app access to frame header
Object
IOCTL_OBJ_FREQ
IOCTL_OBJ_CRYPTKEY
IOCTL_OBJ_RAW_IO
IOCTL_OBJ_RADIO
IOCTL_OBJ_AP_JOIN
Description
Get/Set radio frequency
Set encryption key
Application layer access to
the frame header to directly
send or receive a frame.
Application layer access to
some radio controls.
Access Point join-allow
context
Comments
Frequency agility. May be used by
APP or NWK.
Customer may provide external means
for user to set a non-default key.
Requires reset to take effect.
This object is used for example to ping
another device where the network
address of the target device is supplied
directly and not done through the
connection table.
Limited access to radio directly. For
example, sleeping and awakening the
radio and getting signal strength
information.
Interface to control whether Access
Point will allow devices to join or not.

## Slide 14
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
14

## Slide 15
Example
How to configure Access Point
• star hub in the network ( 1 / net )
• always-on (acts as range extender)
• store and fwd for sleeping devices
• linking and token (link and join) mgmt
• AP can implement end device functionality (link listen, receive)
// Initialize the HW/Radio
BSP_Init(); // initialize the BSP (API subject to change)
SMPL_Init(0);
// Handle Linking
SMPL_LinkListen(&linkID1);
// Receive Messages
While (1) {
while((SMPL_SUCCESS == SMPL_Receive(linkID1, msg, &len) {
// do something
}}
15

## Slide 16
Example
How to configure Range Extender
• always-on device
• repeats received frames (with limitations)
• limited to 4 / net (although flexible in design)
// Initialize the HW/Radio
BSP_Init();
SMPL_Init(0);
// No Linking or application level functionality
while(1) ;
16

## Slide 17
17
Example
How to configure End Device
• poll for data
– polling is Port specific
– no data results
in blank (empty)
response
• API e.g. Sequence
– Init (and Join)
– Link (assumes listen)
– Sample Temp
– Send
• option to sleep
void main()
{
linkID_t linkID;
uint32_t temp;
// Initialize the board’s HW
BSP_Init();
SMPL_Init(0);
// link.
SMPL_Link(&linkID);
while (TRUE)
{
// sleep until timer. read temp sensor
MCU_Sleep();
HW_ReadTempSensor(&temp);
if (temp > TOO_HIGH)
{
SMPL_Send(linkID, “Hot!”, 4);
}
if (temp < TOO_LOW)
{
SMPL_Send(linkID, “Cold!”, 5);
}}}

## Slide 18
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
18

## Slide 19
Packet Format
• preamble: hw sync
• sync: hw sync
• length: bytes non-phy
• dstaddr
• srcaddr
• port: app port number
• dev info: capabilities
• tractid: transaction nonce or seq num
• app pyld: 0 <= n <= 52 byte/113 byte
(radio dependent)
• crc: must be valid
19

## Slide 20
ED 1
ED 2
• net address = hw addr (4 byte) + app port
– statically assigned hw addr
– no address resolution mechanism
• byte 1: 0x00, 0xFF – reserved for broadcast
• communication topologies:
RE
ED 1
ED 2
•
store and fwd p2p through AP
•
direct peer-2-peer
•
direct p2p through RE
•
store and fwd p2p through RE and AP
Addressing and Communication
20

## Slide 21
Additional Details
• CCS development environment
• minimal hw abstraction
• no driver support (UART, SPI, LCD, Timers)
• no heap utilization
• no runtime (nwk) context storage
• single thread (app), no tasks or scheduling
• nwk api is synchronous (does not return until
operation is complete)
• retries and acks must be managed by app
21

## Slide 22
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
22

## Slide 23
• MSP-EXP430FG4618 Experimenters Board
– (MSP430FG4618) w/ Socket Interface for CC110x /
CC2500
• eZ430RF-2500
– MSP430F2274 + CC2500
Hardware Support
• CC2510-CC2511DK and CC1110
CC1111DK
• DSSS (MSP430 +CC2420, CC2430)
• CC2520
23

## Slide 24
Outline
• Overview – What is SimpliciTI?
• Device types and network topologies
• SimpliciTI software architecture
• Example: How to configure SimpliciTI devices
• Insight on packet format and addressing
• Supported hardware platforms
• Demonstration: Temp sensor network
24

## Slide 25
25
Example
Hardware configuration

## Slide 26
26
Development Tools
Packet sniffer
• two end devices are
reading their internal
temperature sensor
• 1/sec they report their
value to the access point
• the access point feeds the
data to a terminal window on
the PC via a virtual COM
port
• all RF traffic can be
monitored with the TI
SimpliciTI packet sniffer
Packet sniffer screenshot

## Slide 27
27
Current Consumption
How to estimate and measure?
• Guideline to SimpliciTI current consumption as presented in
application note:
• Wireless Sensor Monitor Using the eZ430-RF2500.
• http://www.ti.com/litv/pdf/slaa378a

## Slide 28
Available examples
Where
SimpliciTI distribution
eZ430-RF2500
What
SimpliciTI examples:
- 2 ED with bi-di
- AP as data hub
- Cascading ED
- Simple polling with AP
- Temp.Sens network with PC
gui
Notes
- Distributed with eZ430-
RF2500.
- Comes with app.note
www.ti.com/simpliciti
28