## Slide 1: Commercial Real-Time Operating Systems Lecture 24

## Slide 2: Outline
Standards
Metrics
RTOSs
  VxWorks
  Embedded Windows platforms
  Linux extensions
  …

## Slide 3: (Traditional) Real-Time Applications
Transportation systems
  Automotives, avionics, railway system, submarines, …
Space-based systems
  Satellite systems, planetary rovers, …
Industrial Automation
  Manufacturing automation (e.g. Bottling factories)
  Process control (e.g. petroleum refinement, temperature control systems, …)
Motion control
  Robotics applications, mechanical pets, …
Data Acquisition systems
  Supervisory control and data acquisition systems (SCADA), Security monitoring systems
Defense/military systems
  Radar systems, Smart weapons, …
+

## Slide 4: Emerging Applications
Cell-phones, VoIP phone, PDA’s
MP3 players
Set-top boxes, Game Consoles
Automotive Systems
Network Elements
Web Servers

## Slide 5: Popular Standards
Real-Time Operating System standards
  IEEE 1003.1b POSIX Real-Time Extensions (www.ieee.org)
  OSEK (automotive real-time OS standard) (www.osek.org)
Real-Time (and Concurrent) Programming Languages
  Real-Time Specification for Java (www.java.com, www.timesys.com)
  Ada 83 and Ada 95
Real-Time Middleware
  Real-Time CORBA (middleware and abstraction of the underlying RTOS)
Networks/buses
  CANbus (Controller Area Network bus)
  TTA: Time-Triggered Architecture (www.tttech.com)
  FlexRay (www.flexray.org)
  ATM or Switched Ethernet
    Priority-based or weighted fair-sharing schemes

## Slide 6: Metrics in Real-Time Systems (1/2)
End-to-end latency:
  E.g. worst-case, average-case, variance, distribution
  Can involve multiple hops (across nodes, links, switches and routers)
  Behavior in the presence or absence of failures
Jitter
Throughput:
  How many X can be processed?
  How many messages can be transmitted?
Survivability:
  How many faults can be tolerated before system failures?
  What functionality gets compromised?

## Slide 7: Metrics in Real-Time Systems (2/2)
Security:
  Can the system’s integrity be compromised?
  Can violations be detected?
Safety:
  Is the system “safe”?
    Can the system get into an ‘unsafe’ state? Has it been ‘certified’?
Maintainability:
  How does one fix problems?
  How does the system get upgraded?
Dynamism and Adaptability:
  What happens when the system mission changes?
  What happens when individual elements fail?
  Can the system reconfigure itself dynamically?
  How does the system behave after re-configuration?

## Slide 8: RTOS Considerations
What processor(s) does it run on?
  8-bit, 16-bit, 32-bit, …
  Intel Pentium® Processor, PowerPC, Arm/StrongArm Intel Xscale®, MIPS, SuperH, …
  IBM and Intel® Network Processors
What board(s) does it run on?
  Complete software package for a particular hardware board is called a BSP (Board Support Package)
What is the software environment?
  Compilers and debuggers
  IDE
    Cross-compilation + symbolic debugging on target?
  Profilers (CPU, memory)
  Test coverage tools
  Native simulation/emulation support?

## Slide 9: Real-Time Operating Systems
Windows platforms
  Embedded XP, Windows CE, Pocket Windows
VxWorks from Wind River Systems (www.windriver.com)
Linux variants
  Blue Cat Linux (www.lynuxworks.com)
  (Embedded) Red Hat Linux (www.redhat.com)
  FSM RT-Linux (www.fsmlabs.com)
  Monta Vista Linux (www.mvista.com)
  TimeSys Linux (www.timesys.com)
LynxOS (www.lynuxworks.com)
QNX (www.qnx.com)
Solaris real-time extensions
TRON
  Embedded OS specification in Japan
  Has multiple profiles for different classes of devices

## Slide 10: Common RTOS Features
Utilities
Bootstrapping support
“Headless” operation
  Display not necessary
APIs (Application Programming Interfaces)
Multiple threads and/or processes
  Fixed priority scheduling is most popular
Mutex/semaphore support likely with priority inheritance support
Inter-process communications
  Message queues
Timers/clock
Graphics support
Device drivers
Network protocol stack

## Slide 11: Emerging RTOS Requirements
Full-featured operating system
Support for new processors and devices
Support for Internet protocols and standards
Support for Multimedia protocols and standards
Support for File Systems
Memory protection
Resource protection, security
Development tools and libraries
GUI Environment
Do this with low and predictable overheads.

## Slide 12: Case Study: Linux in embedded systems

## Slide 13: Why Linux?
Reliable, Full-featured Operating System
  Rich multi-tasking support
  Security, Protection
  Networking Support
    TCP/IP, RSVP, SIP, MPLS, H.323
  Multimedia Support
    JPEG, MPEG, GSM
  Device Drivers
Standard, Known Environment and API’s
  Unix Lineage
    Familiar environment for many users/developers
  POSIX Compliance

## Slide 14: Why Linux?
The Cost Factor
  Free run-time royalties
The Open Source Factor
  A global team of programmers enhancing the environment literally all the time
  Availability of libraries, tools, and device drivers
  Source Code Access allowing “peeking inside the hood” (and customizing as necessary)
The Popularity Factor
  Excellent textbooks and documentation

## Slide 15: Why Linux?
Small Embedded Systems
  Modular Kernel, possible to configure the kernel to suitable size
  Customizable Root File System
  Lots of Utilities
High-End Embedded Systems
  High-Availability
  Clustering
  SMP Support

## Slide 16: Linux API: Tasking
Process
  Encapsulates a thread of control and an address space
    Address space may be shared giving threads in effect
  Schedulable Entity
Threads
  Are processes to the Linux kernel
    Scheduled by the Linux kernel
  Can be created such that they share the address space with the parent process, effectively giving threads

## Slide 17: Linux API: POSIX, SVR4, BSD
POSIX 1003.1.b (Real-Time Extensions)
  Priority Scheduling
  Memory Locking
  Clocks and Timers
  Real-Time Signals
POSIX 1003.1.c (Thread Extensions)
  Using pthreads library
  Thread creation, destruction, etc.
  Mutexes, Condition Variables
SVR4 IPC
  Shared Memory
  Semaphores
Networking:
  BSD Sockets

## Slide 18: Linux Internals Architecture
Device
Drivers
Modules
Core Mechanisms
Process
Scheduler
vfs
mm
ipc
net

## Slide 19: The Real-Time Linux Challenge
How to leverage the advantages of Linux, while making it suitable for real-time systems?

## Slide 20: Approaches to Real-Time Linux
Approaches limiting Real-time and Non Real-time Task Interactions
  Compliant Kernel Approach
    LynxOS/Blue Cat Linux
  Thin Kernel Approach
    RTLinux/RTAI
Approaches that integrate Real-time and Non Real-time tasks
  Core Kernel Approach
    TimeSys Linux, Monta Vista Linux
  Resource Kernel Approach
    TimeSys Linux

## Slide 21: Linux Internals: Scheduling
Schedulable Entities
  Processes
    Real-Time Class: SCHED_FIFO or SCHED_RR
    Time-Sharing Class: SCHED_OTHER
  Real-Time processes have
    Application defined priority
    Higher priority than time-sharing processes
Non Schedulable Entities
  Interrupt Handlers
    Have priorities, and can be nested
  Bottom Halves & Task Queues
    Run on schedule, ret from system call, ret from interrupt

## Slide 22: Linux and Real-Time: Problems
Timer Granularity
  Many real-time tasks are driven by timer interrupts
  In Standard Linux, the timer is set to expire at 10 ms intervals
Scheduler Predictability
  Linux scheduler keeps tasks in an unsorted list
  Requires a scan of all tasks to make a scheduling decision
  Scales poorly as number of tasks increases, and is especially poor for real-time performance
Various subsystems NOT designed for real-time use
  Network protocol stack
  Filesystem
  Windows manager

## Slide 23: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 24: Compliant Kernel Approach
Linux Kernel
(Embedded Applications)
Real-Time Kernel
(Real-Time Applications)
Linux System Call API
Linux System Call API
Linux Development Tools
And Environment
Linux Development Tools
And Environment

## Slide 25: Compliant Kernel Approach
Basic Claim
  Linux is defined by its API and not by its internal implementation
  The real-time kernel is a non Linux kernel
Implications
  No benefits from the Linux kernel
  Not possible to benefit from the Linux kernel evolution
  Not possible to use Linux hardware support
  Not possible to use Linux device drivers

## Slide 26: Compliance
100% Linux API
  Support all of Linux kernel API
Implications
  Any Linux application can run on real-time kernel
    Development can be done on Linux Host, with rich set of host tools for development
  All Linux libraries are trivially available to run on real-time kernel
    Third party software
  Achieving 100% Linux API is non-trivial
    Consider the amount of effort put on Linux kernel development

## Slide 27: Approaches to Real-Time Linux
Dual Kernel Approach
Compliant Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 28: The Thin Kernel Approach
Hardware
Real-Time Kernel (RT-Linux or RTAI)
Real-Time
Task
Real-Time
Task
Real-Time
Task
Linux Kernel
Linux
Process
Linux
Process
User-Level
Kernel-Level
Real-time tasks do NOT use the Linux API or Linux facilities
Failure in any real-time task crashes the entire system

## Slide 29: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 30: Core Kernel Approach
Basic Ideas
  Make the kernel more suitable for real-time
  Ensure that the impact of changes is localized so that
    Kernel upgrades can be easily incorporated
    Kernel reliability and scalability is not compromised
Mechanisms
  Static Configuration
    Can be configured at compile time
  Dynamic Configuration
    Using loadable kernel modules

## Slide 31: Core Kernel Approach
Allows the use of most if not all existing Linux primitives, applications, and tools.
  Need to avoid primitives that can take extended time in the kernel
Allows the use of most existing device drivers written to support Linux.
  Need to avoid poorly written drivers that unfairly hog system resources
Robustness and Reliability
  Core kernel modifications can effect robustness, but source is available

## Slide 32: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 33: Resource Kernel
A Kernel that provides to Applications Timely, Guaranteed, and Enforced access to System Resources
Allows Applications to specify only their Resource Demands, leaving the Kernel to satisfy those Demands using hidden management schemes

## Slide 34: Protection in Resource Kernels
Each application (or a group of collaborating applications) operates in a virtual machine:
  a machine which consists of a well-defined and guaranteed portion of system resources
    CPU capacity, the disk bandwidth, the network bandwidth and the memory resource
Multiple virtual machines can run simultaneously on the same physical machine
  guarantees available to each reserve set is valid despite the presence of other (potentially mis-behaving) applications using other reserve sets

## Slide 35: “Resource Kernel” Architecture
Middleware
Services
CPU
Memory
NetBW
Physical
resources
CPU
Memory
NetBW
CPU
NetBW
Memory
CPU
Memory
NetBW
...
Resource
Kernel
RT Filesystem
Publisher/Subscriber
Services
RT-ORB
QoS Mgr
Real-Time
Java
Apps
Real-Time and Multimedia Applications

## Slide 36: Linux Resource Kernel Architecture
Hardware
Resource
Kernel
Linux
Kernel
Linux
Process
Linux
Process
Linux
Process
Kernel
User-Level
LKM

## Slide 37: Reserves and Resource Sets
Reserve
  A Share of a Single Resource
  Temporal Reserves
    Parameters declare Portion and Timeframe of Resource Usage
      E.g., CPU time, link bandwidth, disk bandwidth
  Spatial Reserves
    Amount of space
      E.g., memory pages, network buffers
Resource Set
  A set of resource reserves

## Slide 38: Summary
The world of embedded real-time is changing, and converging with the
  Desktop world,
  The Enterprise world,
  The Server world,
  The Internet World, etc.
There are 3 dominant platforms
  VxWorks (proprietary)
  Windows variants
  Linux variants
  …