## Slide 1: Overview
Last lecture
  Review of D latches and flip-flops
  T flip-flops and SR latches
  State diagrams
  Asynchronous inputs
Today
  Cascading flip-flops
  Clock skew
  Registers

## Slide 2: Cascading flip-flops
IN
CLK
Q0
Q1
D
Q
D
Q
IN
Q0
Q1
CLK
Example: Shift registers
  First FF acquires IN at rising clock edge
  Second FF acquires Q0 at rising clock edge
>
>
Unlike this figure, draw your clock at the top of the timing diagram

## Slide 3: Cascading flip-flops (con’t)
Flip-flop propagation delays exceed hold times
  Second stage latches its input before input changes
In
Q0
Q1
Clk
tsu
tphl
th
tsu
th
tplh

## Slide 4: Clock skew
Goal: Clock all flip-flops at the same time
  Difficult to achieve in high-speed systems
    Clock delays (wire, buffers) are comparable to logic delays
  Problem is called clock skew
Original state: IN = 0, Q0 = 1, Q1 = 1
Next state: Q0 = 0, Q1 = 0 (should be Q1 = 1)
CLK0 clocks first f/f
CLK1 clocks second f/f
CLK1 should align with
CLK0, but is delayed
due to clock skew
IN
Q0
Q1
CLK0
CLK1

## Slide 5: Registers
Collection of flip-flops with common control
  Store related values (e.g. a binary word)
  Share clock, reset, and set lines
  Examples
    Storage registers, shift registers, counters
R
S
R
S
R
S
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
IN1
IN2
IN3
IN4
R
S
"0"
Example:
A 4-bit
storage
register

## Slide 6: Shift registers
Hold successively sampled input values
  Delays values in time
  Example: 4-bit shift register
    Stores 4 input values in sequence
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 7: Shift-register applications
Parallel-to-serial conversion for signal transmission
Pattern recognition (circuit recognizes 1001)
D
Q
D
Q
D
Q
D
Q
IN
CLK
OUT
parallel inputs
parallel outputs
serial transmission
CLK
CLK

## Slide 8: Counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Ring counter: Sequence is 1000, 0100, 0010, 0001
  Assuming one of these patterns is the starting state
Johnson counter: Sequence is 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 9: Class example: A binary counter
Has logic between flip-flops
  Draw a timing diagram
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
"1”
D1
D2
D3
D4

## Slide 10: Summary: Sequential-logic building blocks
Know latches and flip-flops
  R-S latch
  D latch and D flip-flop
  Master/slave flip-flops
  T flip-flop
Know clocks, timing, timing diagrams
  Flip-flop timing and delay specifications
  Clock skew
Understand asynchronous inputs
  Metastability and how to avoid it
Know basic registers
  Storage registers, shift registers, counters