## Slide 1: Overview
Last lecture
  Introduction to sequential logic and systems
    The basic concepts
    A simple example
Today
  Latches
  Flip-flops
    Edge-triggered D
    Master-slave
  Timing diagrams
  T flip-flops and SR latches

## Slide 2: The D latch
Output depends on clock
  Clock high: Input passes to output
  Clock low: Latch holds its output
Latch are level sensitive and transparent
D
Q
Q
CLK
Input
Output
Output
CLK
D
Qlatch

## Slide 3: The D flip-flop
Input sampled at clock edge
  Rising edge: Input passes to output
  Otherwise: Flip-flop holds its output
Flip-flops are rising-edge triggered, falling-edge triggered, or master-slave
D
Q
Q
CLK
Input
Output
Output
CLK
D
Qff

## Slide 4: Terminology & notation
D
Q
Q
CLK
Input
Output
Output
Falling-edge triggered D flip-flop
D
Q
Q
CLK
Input
Output
Output
Rising-edge triggered D flip-flop
D
Q
Q
CLK
Input
Output
Output
Negative D latch
D
Q
Q
CLK
Input
Output
Output
Positive D latch

## Slide 5: Latches versus flip-flops
behavior is the same unless input
changes while the clock is high
CLK
D
Qff
Qlatch
D
Q
Q
CLK
D
Q
Q
CLK

## Slide 6: The master-slave D
D
Q
CLK
Input
Master D latch
D
Q
Output
Slave D latch
master-slave D flip-flop
Class example: Draw the timing diagram
X

## Slide 7: Flip-flop timing
  Setup time tsu: Amount of time the input must be stable before the clock transitions high (or low for negative-edge triggered FF)
  Hold time th: Amount of time the input must be stable after the clock transitions high (or low for negative-edge triggered FF)
There is a timing "window" around the clock edge during which the input must remain stable
clock
data
D
Q
D
Q
clock
data
changing
stable
data
clock
tsu
th

## Slide 8: Flip-flop timing (cont’d)
th 5ns
tw 25ns
tplh 25nsmax, 13nstyp
tphl 40nsmax, 25nstyp
tsu 20ns
D
CLK
Q
th 5ns
tsu 20ns
Timing constraints
  Must meet setup and hold times
  Must meet minimum clock width
  Will have propagation delays (low to high & high to low)
D
Q
Q
CLK

## Slide 9: Latches versus flip-flops
behavior is the same unless input
changes while the clock is high
CLK
D
Qff
Qlatch
D
Q
Q
CLK
D
Q
Q
CLK

## Slide 10: The master-slave D
D
Q
CLK
Input
Master D latch
D
Q
Output
Slave D latch
master-slave D flip-flop
Class example: Draw the timing diagram

## Slide 11: How do we make a latch?
Two inverters hold a bit
  As long as power is applied
Storing a new memory
  Temporarily break the feedback path
"0"
"1"
"stored bit"
"remember"
"load"
"data"
"stored bit"

## Slide 12: How do we make a D F/F?
Edge triggering is difficult
  Label the internal nodes
  Draw a timing diagram
  Start with Clk=1
Q
D
Clk
W
Y
X
Z
Q’

## Slide 13: T flip-flop
Full name: Toggle flip-flop
Output toggles when input is asserted
  If T=1, then Q  Q' when CLK 
  If T=0, then Q  Q when CLK 
CLK
Q
T
Q
>
Input(t) Q(t) Q(t + t)
0
0
0
0
1
1
1
0
1
1
1
0
Input

## Slide 14: The SR latch
Cross-coupled NOR gates
  Can set (S=1, R=0) or reset (R=1, S=0) the output
Cross-coupled NAND gates
  Can set (S=1, R=0) or reset (R=1, S=0) the output
R
S
Q
Q'
Q
Q'
S'
R'

## Slide 15: SR latch behavior
Truth table and timing
Reset
Hold
Set
Set
Reset
Race
R
S
Q
Q'
100
R
S
Q
Q'
S R Q 0 0 hold 0 1 0 1 0 1 1 1 disallow

## Slide 16: SR latch is glitch sensitive
Static 0 hazards can set/reset latch
  Glitch on S input sets latch
  Glitch on R input resets latch
R
S
Q
Q'
0
0

## Slide 17: Clear and preset in flip-flops
Clear and Preset set flip-flop to a known state
  Used at startup, reset
Clear or Reset to a logic 0
  Synchronous: Q=0 when next clock edge arrives
  Asynchronous: Q=0 when reset is asserted
    Doesn't wait for clock
    Quick but dangerous
Preset or Set the state to logic 1
  Synchronous: Q=1 when next clock edge arrives
  Asynchronous: Q=1 when reset is asserted
    Doesn't wait for clock
    Quick but dangerous