## Slide 1: Overview
Last lecture
  Ant Brain?
Today
  State Minimization
    Row matching method
    Implication chart method
    Observations about minimization and efficiency

## Slide 2: FSM Minimization
Two simple FSMs for odd parity checking

## Slide 3: Collapsing States
We can make the top machine match the bottom machine by collapsing states S0 and S2 onto one state
Notes: If you’re a skeptical sort of person, you might ask, “why would anyone ever design the top state machine?”

## Slide 4: FSM Design on the Cheap
Let’s say we start with this FSM for even parity checking

## Slide 5: FSM Design on the Cheap
Now an enterprising engineer comes along and says, “Hey, we can turn our even parity checker into an odd parity checker by just adding one state.”
Notes: An example this small is a little silly, but this kind of thing really happens on a larger scale

## Slide 6: Two Methods for FSM Minimization
Row matching
  Easier to do by hand
  Misses minimization opportunities
  More pessimistic
Implication table
  Guaranteed to find the most reduced FSM
  More complicated algorithm (but still relatively easy to write a program to do it)
  More optimistic

## Slide 7: A simple problem
Design a Mealy machine with a single bit input and a single bit output. The machine should output a 0, except once every four cycles, if the previous four inputs matched one of two patterns (0110, 1010)
Example input/output trace: in: 0010 0110 1100 1010 0011 … out: 0000 0001 0000 0001 0000 …
Notes: The spaces in the traces are just for readability

## Slide 8: … and a simple solution

## Slide 9: Find matching rows
 |  | Next State |  | Output | 
Input Sequence | Present State | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S7 | S8 | 0 | 0
01 | S4 | S9 | S10 | 0 | 0
10 | S5 | S11 | S12 | 0 | 0
11 | S6 | S13 | S14 | 0 | 0
000 | S7 | S0 | S0 | 0 | 0
001 | S8 | S0 | S0 | 0 | 0
010 | S9 | S0 | S0 | 0 | 0
011 | S10 | S0 | S0 | 1 | 0
100 | S11 | S0 | S0 | 0 | 0
101 | S12 | S0 | S0 | 1 | 0
110 | S13 | S0 | S0 | 0 | 0
111 | S14 | S0 | S0 | 0 | 0

## Slide 10: Merge the matching rows
 |  | Next State |  | Output | 
Input Sequence | Present State | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S7 | S8 | 0 | 0
01 | S4 | S9 | S10’ | 0 | 0
10 | S5 | S11 | S10’ | 0 | 0
11 | S6 | S13 | S14 | 0 | 0
000 | S7 | S0 | S0 | 0 | 0
001 | S8 | S0 | S0 | 0 | 0
010 | S9 | S0 | S0 | 0 | 0
011 or 101 | S10’ | S0 | S0 | 1 | 0
100 | S11 | S0 | S0 | 0 | 0
110 | S13 | S0 | S0 | 0 | 0
111 | S14 | S0 | S0 | 0 | 0

## Slide 11: Merge until no more rows match
 |  | Next State |  | Output | 
Input Sequence | Present State | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S7’ | S7’ | 0 | 0
01 | S4 | S7’ | S10’ | 0 | 0
10 | S5 | S7’ | S10’ | 0 | 0
11 | S6 | S7’ | S7’ | 0 | 0
Not (011 or 101) | S7’ | S0 | S0 | 0 | 0
011 or 101 | S10’ | S0 | S0 | 1 | 0

## Slide 12: The final state transition table
 |  | Next State |  | Output | 
Input Sequence | Present State | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3’ | S4’ | 0 | 0
1 | S2 | S4’ | S3’ | 0 | 0
00 or 11 | S3’ | S7’ | S7’ | 0 | 0
01 or 10 | S4’ | S7’ | S10’ | 0 | 0
Not (011 or 101) | S7’ | S0 | S0 | 0 | 0
011 or 101 | S10’ | S0 | S0 | 1 | 0

## Slide 13: A more efficient solution

## Slide 14: The Implication table method
Here’s a slightly funkier FSM
Notes: You can convince yourself that the row matching method doesn’t work

## Slide 15: Step 1: Draw the table

## Slide 16: Step 2: Consider the outputs

## Slide 17: Step 3: Add transition pairs

## Slide 18: Step 4 (repeated): Consider transitions

## Slide 19: Final reduced FSM

## Slide 20: Minimizing FSMs isn’t always good
Two FSMs for 0->1 edge detection

## Slide 21: An implementation of the first FSM
Notes: Implementation of the other left as an exercise to the reader

## Slide 22: A little perspective
These kinds of optimizations are what CAD(Computer Aided Design)/EDA(Electronic Design Automation) is all about
The interesting problems are almost always computationally intractable to solve optimally
People really care about the automation of the design of billion-transistor chips

## Slide 23: In the next few lectures
More about FSMs
Some methods and tricks for improving them