## Slide 1: Overview
Last lecture
  Sequential Logic Examples
Today
  State encoding
    One-hot encoding
    Output encoding

## Slide 2: State encoding
Assume n state bits and m states
  2n! / (2n – m)! possible encodings [m  n  log2(m)]
    From binomial expansion
    Example: 3 state bits, 4 states, 1680 possible state assignments
Hard problem, with no known algorithmic solution
  Can try heuristic approaches
  Can try to optimize some metric
    FSM size (amount of logic and number of FFs)
    FSM speed (depth of logic and fanout)
    FSM dependencies (decomposition)
Need to consider startup
  Self-starting FSM or explicit reset input

## Slide 3: State-encoding strategies
No guarantee of optimality
  An intractable problem
Most common strategies
  Binary (sequential) – number states as in the state table
  Random – computer tries random encodings
  Heuristic – rules of thumb that seem to work well
    e.g. Gray-code – try to give adjacent states (states with an arc between them) codes that differ in only one bit position
  One-hot – use as many state bits as there are states
  Output – use outputs to help encode states

## Slide 4: One-hot encoding
One-hot: Encode n states using n flip-flops
  Assign a single “1” for each state
    Example: 0001, 0010, 0100, 1000
  Propagate a single “1” from one flip-flop to the next
    All other flip-flop outputs are “0”
The inverse: One-cold encoding
  Assign a single “0” for each state
    Example: 1110, 1101, 1011, 0111
  Propagate a single “0” from one flip-flop to the next
    All other flip-flop outputs are “1”
“almost one-hot” encoding
  Use no-hot (000…0) for the initial (reset state)
  Assumes you never revisit the reset state

## Slide 5: One-hot encoding (con’t)
Often the best approach for FPGAs
  FPGAs have many flip-flops
  One-hot machines use the least next-state logic
Draw FSM directly from the state diagram
  One product term per incoming arc
  But complex state diagram  complex design
One-hot designs have many possible failure modes
  All states that aren’t one-hot
  Can create logic to reset the FSM if it enters illegal state
Large machines require many flip-flops
  Decompose design into smaller one-hot encoded sub-designs
    n+m states for two machines versus n*m states for one

## Slide 6: Vending machine again...
Release item after receiving 15 cents
  Single coin slot for dimes and nickels
    Sensor specifies coin type
  Machine does not give change
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism

## Slide 7: One-hot encoded transition table
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3
0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 – – – – – 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 – – – – – 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 – – – – – 1 0 0 0 – – 1 0 0 0 1
present state inputs next state output Q3Q2Q1Q0 D N D3 D2D1D0 open

## Slide 8: One-hot encoded vending machine
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3

## Slide 9: Designing from the state diagram
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D
D' N'
D' N'
D' N'
1
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3

## Slide 10: Output encoding
Reuse outputs as state bits
  Why create new functions when you can use outputs?
  Bits from state assignments are the outputs for that state
    Take outputs directly from the flip-flops
ad hoc - no tools
  Yields small circuits for most FSMs
  Fits nicely with synchronous Mealy machines

## Slide 11: Digital combination lock again...
An output-encoded FSM
  Punch in 3 values in sequence and the door opens
  If there is an error the lock must be reset
  After the door opens the lock must be reset
  Inputs: sequence of number values, reset
  Outputs: door open/close
reset
value
open/closed
new
clock

## Slide 12: Separate data path and control
Design datapath first
  After the state diagram
  Before the state encoding
Control has 2 outputs
  Mux control to datapath
  Lock open/closed
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
controller
mux control
clock
4
4
4
4
4

## Slide 13: Draw the state diagram
closed
closed
mux=C1
start
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S0
S1
S2
S3
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open

## Slide 14: Design the datapath
C1
C2
C3
comparator
equal
multiplexer
mux control
4
4
4
4
4
value
C1i
C2i
C3i
mux control
valuei
equal
Choose simple control
  3-wire mux for datapath
    Control is 001, 010, 100
  Open/closed bit for lock state
    Control is 0/1

## Slide 15: Output encode the FSM
FSM outputs
  Mux control is 100, 010, 001
  Lock control is 0/1
State are: S0, S1, S2, S3, or ERR
  Can use 3, 4, or 5 bits to encode
  Have 4 outputs, so choose 4 bits
    Encode mux control and lock control in state bits
    Lock control is first bit, mux control is last 3 bits
    S0 = 0001 (lock closed, mux first code)
    S1 = 0010 (lock closed, mux second code)
    S2 = 0100 (lock closed, mux third code)
    S3 = 1000 (lock open)
    ERR = 0000 (error, lock closed)

## Slide 16: FSM has 4 state bits and 2 inputs...
Output encoded!
  Outputs and state bits are the same
How do we minimize the logic?
  FSM has 4 state bits and 2 inputs (equal, new)
  6-variable kmap?
Notice the state assignment is close to one-hot
  ERR state (0000) is only deviation
  Is there a clever design we can use?

## Slide 17: Preset and Reset?
closed
closed
mux=C1
start
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S0
S1
S2
S3
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open
Assume flip-flops have preset & reset inputs
Can we encode the ERR state as reset?

## Slide 18: Answer: Yes!
closed
closed
mux=C1
start
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S0
S1
S2
S3
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open
D0 = Q0N’
D1 = Q0EN + Q1N’
D2 = Q1EN + Q2N’
D3 = Q2EN + Q3
Preset0 = start
Preset1,2,3 = 0
Reset0 = start’(E’N + (Q0+Q1+Q2+Q3)’)
Reset1,2,3 = start + (E’N + (Q0+Q1+Q2+Q3)’)

## Slide 19
D0 = Q0N’
D1 = Q0EN + Q1N’
D2 = Q1EN + Q2N’
D3 = Q2EN + Q3
Preset0 = start
Preset1,2,3 = 0
Reset0 = start’(E’N + (Q0+Q1+Q2+Q3)’)
Reset1,2,3 = start + (E’N + (Q0+Q1+Q2+Q3)’)

## Slide 20: FSM design: A 5-step process
1. Understand the problem
  – State diagram and state-transition table
2. Determine the machine’s states
  – Consider missing transitions: Will the machine start?
  – Minimize the state diagram: Reuse states where possible
3. Encode the states
  – Encode states, outputs with a reasonable encoding choice
  – Consider the implementation target
4. Design the next-state logic
  – Minimize the combinational logic
  – Choices made in steps 2 & 3 affect the logic complexity
5. Implement the FSM