## Slide 1: Overview
Last lecture
  Timing diagrams
  Multilevel logic
    Multilevel NAND/NOR conversion
  Hazards
Today
  "Switching-network" logic blocks
    Multiplexers/selectors
    Demultiplexers/decoders
  Programmable logic devices (PLDs)
    Regular structures for 2-level logic

## Slide 2: Switching-network logic blocks
Multiplexer
  Routes one of many inputs to a single output
  Also called a selector
Demultiplexer
  Routes a single input to one of many outputs
  Also called a decoder
multiplexer
demultiplexer
control
control
We construct these
devices from:
(1) logic gates
(2) networks of tran-
sistor switches

## Slide 3: Rationale: Sharing complex logic functions
Share an adder: Select inputs; route sum
multiple inputs
multiple output destinations
MUX
A
B
Sum
A0 A1
Sa
Ss
Sb
B0 B1
MUX
DEMUX
Z0 Z1
single adder

## Slide 4: Multiplexers
Basic concept
  2n data inputs; n control inputs ("selects"); 1 output
  Connects one of 2n inputs to the output
  “Selects” decide which input connects to output
  Two alternative truth-tables: Functional and Logical
Example: A 2:1 Mux
Z = SIn1 + S'Ino
Functional truth table
S Z 0 In0 1 In1
In1 In0 S Z 0 0 0 0 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
Logical truth table
I0
S
I1
Z

## Slide 5: Logic-gate implementation of multiplexers
2:1 mux
4:1 mux
I0
I1
I2
I3
S0 S1
I0
S
I1
I0
S
I1
Z
Z
Z

## Slide 6: Multiplexers (con't)
2:1 mux: Z = S'In0 + SIn1
4:1 mux: Z = S0'S1'In0 + S0'S1In1 + S0S1'In2 + S0S1In3
8:1 mux: Z = S0'S1'S2'In0 + S0'S1S2In1 + ...
I0 I1 I2 I3 I4 I5 I6 I7
S0 S1 S2
8:1 mux
Z
I0 I1 I2 I3
S0 S1
4:1 mux
Z
I0 I1
S0
2:1 mux
Z

## Slide 7: Cascading multiplexers
Can form large multiplexers from smaller ones
  Many implementation options
Z
4:1 mux
S2
2:1 mux
I4 I5 I6 I7
S0 S1
4:1 mux
S0
Z
S1 S2
4:1 mux
2:1 mux
2:1 mux
2:1 mux
2:1 mux
I4 I5
I2 I3
I0 I1
I6 I7
8:1 mux
8:1 mux
I0 I1 I2 I3

## Slide 8: Multiplexers as general-purpose logic
A 2n:1 mux can implement any function of n variables
  A lookup table
  A 2n – 1:1 mux also can implement any function of n variables
Example: F(A,B,C) = m0 + m2 + m6 + m7 = A'B'C' + A'BC' + ABC' + ABC = A'B'(C') + A'B(C') + AB(0) + AB(1)
A B C F 0 0 0 1 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 1 1 1 1 1
C' C' 0 1
S1
S0
F
0 1 2 3
4:1 MUX
C' C' 0 1
0 1 2 3 4 5 6 7
1 0 1 0 0 0 1 1
S2
8:1 MUX
S1
S0
F
A B C
A B

## Slide 9: Multiplexers as general-purpose logic
Implementing a 2n:1 mux as a function of n–1 variables
  (n-1) mux control variables S0 – Sn–1
  One data variable Sn
  Four possible values for each data input: 0, 1, Sn, Sn'
  Example: F(A,B,C,D) implemented using an 8:1 mux
Choose A,B,C as
control variables
Choose D as a
data variable
0 1 2 3 4 5 6 7
1 D 0 1 D' D D' D'
A
8:1
MUX
B
C
F
D
1 0 1 1
1 0 0 0
1 1 0 1
0 1 1 0
AB
CD
A
00
01
11
10
00
01
11
10
C
B
S2
S1
S0
F=A’B’C’(1)+A’B’C(D)+A’BC’(0)+A’BC(1)
+AB’C’(D’)+AB’C(D)+ABC’(D’)+ABC(D’)
F = A’B’C’+A’CD+B’CD+AC’D’+BCD’

## Slide 10: Demultiplexers
Basic concept
  Single data input; n control inputs (“selects”); 2n outputs
  Single input connects to one of 2n outputs
  “Selects” decide which output is connected to the input
  When used as a decoder, the input is called an “enable” (G)
1:2 Decoder:
Out0 = G  S'
Out1 = G  S
2:4 Decoder:
Out0 = G  S1'  S0'
Out1 = G  S1'  S0
Out2 = G  S1  S0'
Out3 = G  S1  S0
3:8 Decoder:
Out0 = G  S2'  S1'  S0'
Out1 = G  S2'  S1'  S0
Out2 = G  S2'  S1  S0'
Out3 = G  S2'  S1  S0
Out4 = G  S2  S1'  S0'
Out5 = G  S2  S1'  S0
Out6 = G  S2  S1  S0'
Out7 = G  S2  S1  S0

## Slide 11: Logic-gate implementation of demultiplexers
1:2 demux
Out0
G
S
Out1
S1
Out2
Out3
Out0
G
Out1
S0
2:4 demux

## Slide 12: Demultiplexers as general-purpose logic
A n:2n demux can implement any function of n variables
  Use variables as select inputs
  Tie enable input to logic 1
  Sum the appropriate minterms (extra OR gate)
demultiplexer “decodes”
appropriate minterms
from the control signals
C
A
B
0 A'B'C' 1 A'B'C 2 A'BC' 3 A'BC 4 AB'C' 5 AB'C 6 ABC' 7 ABC
S2
3:8
Demux
S1
S0
1

## Slide 13: Demultiplexers as general-purpose logic
Example
F1 = A'BC'D + A'B'CD + ABCD
F2 = ABC'D' + ABC
F3 = (A'+B'+C'+D')
A
B
0 A'B'C'D' 1 A'B'C'D 2 A'B'CD' 3 A'B'CD 4 A'BC'D' 5 A'BC'D 6 A'BCD' 7 A'BCD 8 AB'C'D' 9 AB'C'D 10 AB'CD' 11 AB'CD 12 ABC'D' 13 ABC'D 14 ABCD' 15 ABCD
4:16 Demux
Enable = 1
C
D
F1
F2
F3

## Slide 14: Cascading demultiplexers
5:32 demux
0 A'B'C'D'E' 1 2 3 4 5 6 7
S2
3:8
Demux
S1
S0
A
B
0 1 2 3
S1
2:4
Demux
S0
F
E
C
D
0 1 2 3 4 5 6 7 ABCDE
S2
S1
S0
0 1 2 A'BC'DE' 3 4 5 6 7
S2
S1
S0
E
C
D
0 AB'C'D'E' 1 2 3 4 5 6 7 AB'CDE
S2
S1
S0
3:8
Demux
3:8
Demux
3:8
Demux

## Slide 15: Programmable logic (PLAs & PALs )
• • •
• • •
inputs
outputs
product terms
AND array
OR array
Concept: Large array of uncommitted AND/OR gates
  Actually NAND/NOR gates
  You program the array by making or breaking connections
    Programmable block for sum-of-products logic

## Slide 16: All two-level logic functions are available
You "program" the wire connections
A 3-input, 5-term,
4-function PLA

## Slide 17: Sharing product terms
Example: F0 = A + B'C' F1 = AC' + AB F2 = B'C' + AB F3 = B'C + A
Personality matrix:
1 = asserted in term
0 = negated in term
– = does not participate
inputs
1 = term connected to output
0 = no connection to output
outputs
product inputs outputs
term A B C F0 F1 F2 F3 AB 1 1 – 0 1 1 0 B'C – 0 1 0 0 0 1 AC' 1 – 0 0 1 0 0 B'C' – 0 0 1 0 1 0 A 1 – – 1 0 0 1
Reuse
terms

## Slide 18: Programming the wire connections
  Fuse: Comes connected; break unwanted connections
  Anti-fuse: Comes disconnected; make wanted connections
A
B
C
F1
F2
F3
F0
AB
B'C
AC'
B'C'
A
  F0 = A + B'C'
  F1 = AC' + AB
  F2 = B'C' + AB
  F3 = B'C + A