## Slide 1: Overview
Last lecture
  Logic simplification
    Boolean cubes
    Karnaugh maps
Today
  Incompletely specified functions
  Design examples
  k-maps for POS minimization

## Slide 2: Incompletely specified functions
Functions of n inputs have 2n possible configurations
  Some combinations may be unused
  Call unused combinations “don’t cares”
  Exploit don’t cares during logic minimization
  Don’t care  no output
Example: A BCD increment-by-1
  Function F computes the next number in a BCD sequence
    If the input is 00102, the output is 00112
  BCD encodes decimal digits 0–9 as 00002–10012
    Don’t care about binary numbers 10102–11112

## Slide 3: Truth table for a BCD increment-by-1
A B C D W X Y Z 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
off-set for W: m0–m6, m9
on-set for W: m7 and m8
Don't care set for W:
We don't care
about the output values
INPUTS OUTPUTS

## Slide 4: Notation
Don't cares in canonical forms
  Three distinct logical sets
    {on}, {off}, {don’t care}
Canonical representations of a BCD increment-by-1
  Minterm expansion
    W = m7+m8+d10+d11+d12+d13+d14+d15
  Maxterm expansion
    W = M0•M1•M2•M3•M4•M5•M6•M9•D10•D11•D12•D13•D14•D15

## Slide 5: Karnaugh maps and don't cares
Can treat don't cares as 0s or 1s
  Depending on which is more advantageous
F(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  Example: Minimize F with and without don't cares
0 0 X 0
1 1 X 1
1 1 0 0
0 X 0 0
AB
CD
A
B
D
00
01
11
10
00
01
11
10
C
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10

## Slide 6: Karnaugh maps and don't cares (con’t)
F(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
  F = A'D + B'C'D without using don't cares
  F = A'D + C'D using don't cares
0 0 X 0
1 1 X 1
1 1 0 0
0 X 0 0
AB
CD
A
B
D
00
01
11
10
00
01
11
10
C
Assign X == "1"  allows a 2-cube rather than a 1-cube

## Slide 7: Design example: A two-bit comparator
block diagram
truth table
Need a 4-variable Karnaugh map for each of the 3 output functions
LT EQ GT
A B C D LT EQ GT
0 0 0 0 0 1 0
0 1 1 0 0
1 0 1 0 0
1 1 1 0 0
0 1 0 0 0 0 1
0 1 0 1 0
1 0 1 0 0
1 1 1 0 0
1 0 0 0 0 0 1
0 1 0 0 1
1 0 0 1 0
1 1 1 0 0
1 1 0 0 0 0 1
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
AB < CD AB = CD AB > CD
A
B
C
D

## Slide 8: Two-bit comparator (con’t)
LT = ?
D
0 0 0 0
1 0 0 0
1 1 0 1
1 1 0 0
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D
0 1 1 1
0 0 1 1
0 0 0 0
0 0 1 0
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D
1 0 0 0
0 1 0 0
0 0 1 0
0 0 0 1
AB
CD
A
00
01
11
10
00
01
11
10
C
B
K-map for EQ
K-map for LT
K-map for GT
EQ = ?
GT = ?
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10

## Slide 9: Two-bit comparator (con’t)
LT = A'B'D+A'C+B'CD
D
0 0 0 0
1 0 0 0
1 1 0 1
1 1 0 0
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D
0 1 1 1
0 0 1 1
0 0 0 0
0 0 1 0
AB
CD
A
00
01
11
10
00
01
11
10
C
B
D
1 0 0 0
0 1 0 0
0 0 1 0
0 0 0 1
AB
CD
A
00
01
11
10
00
01
11
10
C
B
GT = BC'D'+AC'+ABD'
EQ = A'B'C'D'+A'BC'D+ABCD+AB'CD'
= (A xnor C)•(B xnor D)

## Slide 10: Two-bit comparator (con’t)
Two ways to implement EQ:
A B C D
EQ
EQ
XNOR approach looks simpler
But XNORs are complex
Example: XNOR constructed
  from 3 simple gates
EQ = A'B'C'D'+A'BC'D+ABCD+AB'CD'
= (A xnor C) •(B xnor D)

## Slide 11: Two-bit comparator design

## Slide 12: Design example: Two-bit multiplier
A2 A1 B2 B1 P8 P4 P2 P1
0 0 0 0 0 0 0 0
0 1 0 0 0 0
1 0 0 0 0 0
1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 0 0 1
1 0 0 0 1 0
1 1 0 0 1 1
1 0 0 0 0 0 0 0
0 1 0 0 1 0
1 0 0 1 0 0
1 1 0 1 1 0
1 1 0 0 0 0 0 0
0 1 0 0 1 1 1 0 0 1 1 0
1 1 1 0 0 1
P1 P2 P4
P8
A1 A2
B1 B2
block diagram
truth table
Need a 4-variable Karnaugh map for each of the 4 output functions

## Slide 13
Two-bit multiplier (cont'd)
K-map
for P4
0 0 0 0
0 0 0 0
0 0 0 1
0 0 1 1
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 1 1 0
0 1 1 0
0 0 0 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 0 0 0
0 0 1 0
0 0 0 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
K-map
for P8
K-map
for P1
K-map
for P2

## Slide 14
Two-bit multiplier (cont'd)
0 0 0 0
0 0 0 0
0 0 0 1
0 0 1 1
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 1 1 0
0 1 1 0
0 0 0 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 0 0 0
0 0 1 0
0 0 0 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
B1
A2A1
B2B1
A2
00
01
11
10
00
01
11
10
B2
A1
P8=A2A1B2B1
P2=A2'A1B2 +A1B2B1' +A2B2'B1 +A2A1'B1
P4=A2B2B1' +A2A1'B2
P1=A1B1

## Slide 15: Two-bit multiplier design
Draw the circuit schematic
  P8=A2A1B2B1
  P4=A2B2B1'+A2A1'B2
  P2=A2'A1B2+A1B2B1'+A2B2'B1+A2A1'B1
  P1=A1B1

## Slide 16: Design example: BCD increment by 1
I8 I4 I2 I1 O8 O4 O2 O1 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
O1 O2 O4
O8
I1 I2 I4
I8
block diagram
truth table
Need a 4-variable Karnaugh map for each of the 4 output functions

## Slide 17: BCD increment by 1 (con’t)
O8
O4
O2
O1
0 0 X 1
0 0 X 0
0 1 X X
0 0 X X
I1
I8
I2
I4
0 0 X 0
1 1 X 0
0 0 X X
1 1 X X
0 1 X 0
0 1 X 0
1 0 X X
0 1 X X
1 1 X 1
0 0 X 0
0 0 X X
1 1 X X
I1
I8
I2
I4
I1
I8
I2
I4
I1
I8
I2
I4
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10

## Slide 18: BCD increment by 1 (con’t)
O8
O4
O2
O1
0 0 X 1
0 0 X 0
0 1 X X
0 0 X X
I1
I8
I2
I4
0 0 X 0
1 1 X 0
0 0 X X
1 1 X X
0 1 X 0
0 1 X 0
1 0 X X
0 1 X X
1 1 X 1
0 0 X 0
0 0 X X
1 1 X X
I1
I8
I2
I4
I1
I8
I2
I4
I1
I8
I2
I4
We greatly simplify
the logic by using
the don’t cares

## Slide 19: BCD increment by 1 design
Draw the circuit schematic
  O8 = I4I2I1 + I8I1'
  O4 = I4I2' + I4I1' + I4'I2I1
  O2 = I8'I2'I1 + I2I1'
  O1 = I1'

## Slide 20: Loose end: POS minimization using k-maps
Using k-maps for POS minimization
  Encircle the zeros in the map
  Interpret indices complementary to SOP form
1 0 0 1
0 1 0 0
1 1 1 1
1 1 1 1
AB
CD
A
B
D
00
01
11
10
00
01
11
10
C
F = (B’+C+D)(B+C+D’)(A’+B’+C)
Check using de Morgan’s on SOP
F’ = BC’D’+B’C’D+ABC’
(F’)’ = (BC’D’+B’C’D+ABC’)’
(F’)’ = (BC’D’)’+(B’C’D)’+(ABC’)’
F = (B’+C+D)(B+C+D’)(A’+B’+C)