## Slide 1: Number systems
Last lecture
  Course overview
  The Digital Age
Today’s lecture
  Binary numbers
  Base conversion
  Number systems
    Twos-complement
  A/D and D/A conversion
Notes: Class rule: Interrupt when you don’t understand why we are doing something

## Slide 2: Digital
Digital = discrete
  Binary codes (example: BCD)
  Decimal digits 0-9
  DNA nucleotides
Binary codes
  Represent symbols using binary digits (bits)
Digital computers:
  I/O is digital
    ASCII, decimal, etc.
  Internal representation is binary
    Process information in bits
Decimal
Symbols
0
1
2
3
4
5
6
7
8
9
BCD
Code
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001

## Slide 3: The basics: Binary numbers
Bases we will use
  Binary: Base 2
  Octal: Base 8
  Hexadecimal: Base 16
Positional number system
  1012= 1×22 + 0×21 + 1×20
  638 = 6×81 + 3×80
  A116= 10×161 + 1×160
Addition and subtraction
1011
+ 1010
10101
1011
– 0110
0101

## Slide 4: Binary → hex/decimal/octal conversion
Conversion from binary to octal/hex
  Binary: 10011110001
  Octal: 10 | 011 | 110 | 001=23618
  Hex: 100 | 1111 | 0001=4F116
Conversion from binary to decimal
  1012= 1×22 + 0×21 + 1×20 = 510
  63.48 = 6×81 + 3×80 + 4×8–1 = 51.510
  A116= 10×161 + 1×160 = 16110

## Slide 5: Decimal→ binary/octal/hex conversion
Why does this work?
  N=5610=1110002
  Q=N/2=56/2=111000/2=11100 remainder 0
Each successive divide liberates an LSB

## Slide 6: Number systems
How do we write negative binary numbers?
Historically: 3 approaches
  Sign-and-magnitude
  Ones-complement
  Twos-complement
For all 3, the most-significant bit (msb) is the sign digit
  0 ≡ positive
  1 ≡ negative
Learn twos-complement
  Simplifies arithmetic
  Used almost universally

## Slide 7: Sign-and-magnitude
The most-significant bit (msb) is the sign digit
  0 ≡ positive
  1 ≡ negative
The remaining bits are the number’s magnitude
Problem 1: Two representations for zero
  0 = 0000 and also –0 = 1000
Problem 2: Arithmetic is cumbersome

## Slide 8: Ones-complement
Negative number: Bitwise complement positive number
  0011 ≡ 310
  1100 ≡ –310
Solves the arithmetic problem
Remaining problem: Two representations for zero
  0 = 0000 and also –0 = 1111

## Slide 9: Twos-complement
Negative number: Bitwise complement plus one
  0011 ≡ 310
  1101 ≡ –310
Number wheel
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
 Only one zero!
 msb is the sign digit
 0 ≡ positive
 1 ≡ negative

## Slide 10: Twos-complement (con’t)
Complementing a complement  the original number
Arithmetic is easy
  Subtraction = negation and addition
    Easy to implement in hardware

## Slide 11: Miscellaneous
Twos-complement of non-integers
  1.687510 = 01.10112
  –1.687510 = 10.01012
Sign extension
  Write +6 and –6 as twos complement
    0110 and 1010
  Sign extend to 8-bit bytes
    00000110 and 11111010
Can’t infer a representation from a number
  11001 is 25 (unsigned)
  11001 is –9 (sign magnitude)
  11001 is –6 (ones complement)
  11001 is –7 (twos complement)

## Slide 12: Twos-complement overflow
Summing two positive numbers gives a negative result
Summing two negative numbers gives a positive result
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
6 + 4 ⇒ –6
–7 – 3 ⇒ +6

## Slide 13: Twos-complement overflow (cont’d)
Correct results
Incorrect results
Overflow condition
  Carry from 2sb-msb and carry from msb-Cout are different
0011 +3
+ 0010 +2
0101 +5
0110 +6
+ 0100 +4
1010 –6
1111 –1
+ 1010 –6
1 1001 –7
1001 –7
+ 1010 –6
1 0011 +3
2sb-msb msb-Cout Overflow
0 0 0
0 1 1
1 0 1
1 1 0

## Slide 14: Gray and BCD codes
Decimal
Symbols
0
1
2
3
4
5
6
7
8
9
BCD
Code
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
Decimal
Symbols
0
1
2
3
4
5
6
7
8
9
Gray
Code
0000
0001
0011
0010
0110
0111
0101
0100
1100
1101

## Slide 15: The physical world is analog
Digital systems need to
  Measure analog quantities
    Speech waveforms, etc
  Control analog systems
    Drive motors, etc
How do we connect the analog and digital domains?
  Analog-to-digital converter (ADC or A/D)
    Example: CD recording
  Digital-to-analog converter (DAC or D/A)
    Example: CD playback

## Slide 16: Sampling
Quantization
  Conversion from analog to discrete values
Quantizing a signal
  We sample it
Datel Data Acquisition and Conversion Handbook

## Slide 17: Conversion
Encoding
  Assigning a digital word to each discrete value
Encoding a quantized signal
  Encode the samples
  Typically Gray or binary codes
Datel Data Acquisition and Conversion Handbook