## Slide 1: Overview
Last lecture
  Introduction to finite state machines
    State diagrams
  Counters as finite state machines
    Counter design
Today
  Finish counter design
    Our last design example
    Self-starting counters
  Introduction to finite-state machines
    Moore versus Mealy machines
    Synchronous Mealy machines
    Example: A parity checker

## Slide 2: Review: Counter design procedure
1. Draw a state diagram
2. Draw a state-transition table
3. Encode the next-state functions
  Minimize the logic using k-maps
4. Implement the design
Example: A 5-state counter

## Slide 3: Example: A 5-state counter
000
010
011
101
110
Step 1: State diagram
Step 2: State transition table
  Assume D flip-flops
Counter repeats 5 states in sequence
  Sequence is 000, 010, 011, 101, 110, 000 (not binary)
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 – – –
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 – – –
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 – – –
Present State Next State

## Slide 4: 5-state counter (con’t)
Step 3: Encode the next state functions
C
B
A
0 0 0 X
X 1 X 1
C+
C
B
A
1 1 0 X
X 0 X 1
B+
C
B
A
0 1 0 X
X 1 X 0
A+
A+ = BC'
C+ = A
B+ = B' + A'C'

## Slide 5: 5-state counter (con’t)
Step 4: Implement the design

## Slide 6: 5-state counter (con’t)
001
100
111
Does our counter get
stuck in invalid states???
Is our design robust?
  What if the counter starts in a 111 state?
000
010
011
101
110

## Slide 7: 5-state counter (con’t)
Back-annotate our design to check it
000
010
011
101
110
Draw state diagram
Fill in state transition table
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 1 1 0
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 1 0 0
Present State Next State
001
100
111
The proper methodology is to design your counter to be self-starting
A+ = BC'
C+ = A
B+ = B' + A'C'

## Slide 8: Self-starting counters
Invalid states should always transition to valid states
  Assures startup
  Assures bit-error tolerance
Design your counters to be self-starting
  Draw all states in the state diagram
  Fill in the entire state-transition table
  May limit your ability to exploit don't cares
    Choose startup transitions that minimize the logic

## Slide 9: Next subject: Finite-state machines
Generalize the counter-design methodology
  State machines have input signals
  State machines have complex transitions
Finite-state machines control digital systems
  The core of digital design

## Slide 10: Finite state machines
FSM: A system that visits a finite number of logically distinct states
Counters are simple FSMs
  Outputs and states are identical
  Visit states in a fixed sequence
FSMs are more complex than counting
  Outputs can depend on current state and on inputs
  State sequencing depends on current state and on inputs

## Slide 11: Generalized FSM model
Inputs
Outputs
Next State
Current State
output logic
Next-state logic
State variables (state vector) holds circuit state
  Stored in registers
Combinational logic computes next state and outputs
  Next state is a function of current state and inputs
  Outputs are functions of
    Current state (Moore machine)
    Current state and inputs (Mealy machine)

## Slide 12: Moore versus Mealy machines
outputs
state feedback
inputs
reg
combinational logic for next state
logic for outputs
Moore machine
Outputs are a function
of current state
Outputs change
synchronously with
state changes
Mealy machine
Outputs depend on state
and on inputs
Input changes can cause immediate output changes
(asynchronous)
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs

## Slide 13: Example: Moore versus Mealy
D
Q
Q
D
Q
Q
D
Q
Q
D
Q
Q
A
B
clock
out
D
Q
Q
D
Q
Q
A
B
clock
out
Circuits recognize AB=10 followed by AB=01
  What kinds of machines are they?

## Slide 14: Specifying outputs for a Moore machine
Output is a function of state only
  Specify output in the state bubble
  Example: Detector for 01 or 10
D/1
E/1
B/0
A/0
C/0
1
0
0
0
0
1
1
1
1
0
reset
current next current reset input state state output
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B D 0
0 0 C E 0
0 1 C C 0
0 0 D E 1
0 1 D C 1
0 0 E B 1
0 1 E D 1

## Slide 15: Specifying outputs for a Mealy machine
Output is a function of state and inputs
  Specify outputs on transition arcs
  Example: Detector for 01 or 10
current next current reset input state state output
B
A
C
0/1
0/0
0/0
1/1
1/0
1/0
reset/0
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B C 1
0 0 C B 1
0 1 C C 0

## Slide 16: Comparing Moore and Mealy machines
Moore machines
  + Safer do use because outputs change at clock edge
  – May take additional logic to decode state into outputs
Mealy machines
  + Typically have fewer states
  + React faster to inputs — don't wait for clock
  – Asynchronous outputs can be dangerous
We will often design synchronous Mealy machines
  Design a Mealy machine
  Then register the outputs

## Slide 17: Synchronous (registered) Mealy machine
Registered state and registered outputs
  No glitches on outputs
  No race conditions between communicating machines
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
reg

## Slide 18: FSM design
Generalized counter design
  Counter-design procedure
    1. State diagram
    2. State-transition table
    3. Next-state logic minimization
    4. Implement the design
  FSM-design procedure
    1. State diagram and state-transition table
    2. State minimization
    3. State assignment (or state encoding)
    4. Next-state logic minimization
    5. Implement the design

## Slide 19: Example: A parity checker
Serial input string
  OUT=1 if odd # of 1s in input
  OUT=0 if even # of 1s in input
Present Input Next Present
State State Output
Even 0 Even 0
Even 1 Odd 0
Odd 0 Odd 1
Odd 1 Even 1
1. State diagram and state-transition table
Moore-machine state diagram

## Slide 20: Parity checker (con’t)
2. State minimization: Already minimized
  Need both states (even and odd)
  Use one flip-flop
3. State assignment (or state encoding)
Present Input Next Present
State State Output
0 0 0 0
0 1 1 0
1 0 1 1
1 1 0 1
Assignment
Even  0
Odd  1

## Slide 21: Parity checker (con’t)
4. Next-state logic minimization
  Assume D flip-flops
  Next state = (present state) XOR (present input)
  Present output = present state
5. Implement the design
D
Q
Q
CLK
Input
Output

## Slide 22: Implementation
D Q
Q
Can map FSMs to programmable logic devices
  Macro-cell = DFF + two-level logic
Other options: Gate arrays, semicustom ICs, etc.