## Slide 1: Overview
Last lecture
  Introduction to finite-state machines
    Moore versus Mealy machines
    Synchronous Mealy machines
    Example: A parity checker
Today
  Example: A sequence detector FSM
  Example: A vending machine FSM
  FSMs in Verilog

## Slide 2: FSM design
FSM-design procedure
  1. State diagram and state-transition table
  2. State minimization
  3. State assignment (or state encoding)
  4. Minimize next-state logic
  5. Implement the design

## Slide 3: Example: Sequence detector
Design a circuit to detect 3 or more 1’s in a bit string
  Assume Moore machine
  Assume D flip-flops
  Assume flip-flops have a reset

## Slide 4: 1. State diagram and state-transition table
B/0
C/0
A/0
D/1
1
0
0
1
1
1
reset
0
0
current next current reset state input state output
1 – – A 0
0 A 0 A 0
0 A 1 B 0
0 B 0 A 0
0 B 1 C 0
0 C 0 A 0
0 C 1 D 0
0 D 0 A 1
0 D 1 D 1

## Slide 5: 2. State minimization & 3. State encoding
State diagram is already minimized
Try a binary encoding
B/0
C/0
A/0
D/1
1
0
0
1
1
1
reset
0
0
current next current reset state input state output
1 – – 00 0
0 00 0 00 0
0 00 1 01 0
0 01 0 00 0
0 01 1 10 0
0 10 0 00 0
0 10 1 11 0
0 11 0 00 1
0 11 1 11 1

## Slide 6: 4. Minimize next-state logic
M
L
In
0 0 0 0
0 1 1 1
MSB+
M
L
In
0 0 0 0
1 0 1 1
LSB+
M
L
In
0 0 1 0
0 0 1 0
OUT+
Out+ = ML
MSB+ = LIn + MIn
LSB+ = L'In + MIn
Notation
M := MSB
L := LSB
In := Input

## Slide 7: 5. Implement the design

## Slide 8: Design example: A vending machine
Release item after receiving 15 cents
  Single coin slot for dimes and nickels
    Sensor specifies coin type
  Machine does not give change
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism

## Slide 9: 1a. State diagram
Consider input sequences
  3 nickels
  2 nickels, dime
  nickel, dime
  dime, nickel
  two dimes
Draw state diagram
  Assume Moore machine
  Inputs: N, D, reset
  Output: Open
S0
Reset
N
S1
S2
S3
S4
S5
S6
S7
N
N
N
D
D
D
[open]
[open]
[open]
[open]
S8
[open]
D

## Slide 10: 1b. Symbolic state-transition table
present inputs next present state D N state output 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1

## Slide 11: 2. State minimization
Reuse states where possible
  Notice we can use the deposited coin values for states
  State is the same if we input 2 nickels or 1 dime
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D

## Slide 12: 3. State encoding
Encode states uniquely
  4 states:
    2 bits minimum
    4 bits maximum
  Look for optimal encoding
  Assume D flip-flops
present state inputs next state present Q0 Q1 D N P1 P0 output 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1

## Slide 13: 4. Minimize the logic
N
0 0 1 1
0 1 1 1
X X X X
1 1 1 1
Q1Q0
DN
Q1
00
01
11
10
00
01
11
10
D
Q0
K-map for P1
K-map for P0
N
0 1 1 0
1 0 1 1
X X X X
0 1 1 1
Q1Q0
DN
Q1
00
01
11
10
00
01
11
10
D
Q0
K-map for Open
N
0 0 1 0
0 0 1 0
X X X X
0 0 1 0
Q1Q0
DN
Q1
00
01
11
10
00
01
11
10
D
Q0
P1 = Q1 + D + Q0N
P0 = Q0'N + Q0N' + Q1N + Q1D
OPEN = Q1Q0
if FFs do not have a reset pin then
P1 = reset'(Q1 + D + Q0N)
P0 = reset'(Q0'N + Q0N' + Q1N + Q1D)

## Slide 14: 5. Implement the design
P1 = Q1 + D + Q0N
P0 = Q0'N + Q0N' + Q1N + Q1D
OPEN = Q1Q0

## Slide 15: Retime design
OPEN is delayed by AND gate after Q1 and Q0
  Can remove this delay by retiming
    Move output logic (AND gate) to eliminate delay
  OPEN = Q1Q0 = (Q1+D+Q0N)(Q0'N+Q0N'+Q1N+Q1D)
Original Design Retimed Design

## Slide 16: Moore versus Mealy vending machine
Moore machine
Mealy machine
D/1
D/0
0¢
Reset
5¢
10¢
15¢
N'D'/0
N'D'/0
N'D'/0
–/1
N+D
D
D
0¢
[0]
Reset
5¢
[0]
10¢
[0]
15¢ [1]
N
N
N'D'
N'D'
N'D'
N+D/1
N/0
N/0

## Slide 17: Hardware Description Languages and Sequential Logic
Flip-flops
  representation of clocks - timing of state changes
  asynchronous vs. synchronous
FSMs
  structural view (FFs separate from combinational logic)
  behavioral view (synthesis of sequencers – not in this course)
Data-paths = data computation (e.g., ALUs, comparators) + registers
  use of arithmetic/logical operators
  control of storage elements

## Slide 18: Example: reduce-1-string-by-1
Remove one 1 from every string of 1s on the input
1
0
0
0
1
1
zero [0]
one1 [0]
two1s
[1]
1/0
0/0
0/0
1/1
zero [0]
one1 [0]
Moore
Mealy

## Slide 19: Verilog FSM - Reduce 1s example
`define zero 0 `define one1 1 `define two1s 2 module reduce (clk, reset, in, out); input clk, reset, in; output out; reg out; reg [2:1] state; // state variables reg [2:1] next_state; always @(posedge clk) if (reset) state = `zero; else state = next_state;
state assignment
Moore machine
1
0
0
0
1
1
zero [0]
one1 [0]
two1s
[1]

## Slide 20: Moore Verilog FSM (cont’d)
always @(in or state)
case (state) `zero: // last input was a zero begin if (in) next_state = `one1; else next_state = `zero; end `one1: // we've seen one 1 begin if (in) next_state = `two1s; else next_state = `zero; end `two1s: // we've seen at least 2 ones begin if (in) next_state = `two1s; else next_state = `zero; end endcase
crucial to include all signals that are input to state determination
note that output depends only on state
always @(state) case (state) `zero: out = 0; `one1: out = 0; `two1s: out = 1; endcase
endmodule

## Slide 21: Mealy Verilog FSM
7
module reduce (clk, reset, in, out); input clk, reset, in; output out; reg out; reg state; // state variables reg next_state; always @(posedge clk) if (reset) state = `zero; else state = next_state; always @(in or state) case (state) `zero: // last input was a zero begin out = 0; if (in) next_state = `one; else next_state = `zero; end `one: // we've seen one 1 if (in) begin next_state = `one; out = 1; end else begin next_state = `zero; out = 0; end endcase endmodule
1/0
0/0
0/0
1/1
zero
one1

## Slide 22: Synchronous Mealy Machine
module reduce (clk, reset, in, out); input clk, reset, in; output out; reg out; reg state; // state variables always @(posedge clk) if (reset) state = `zero; else case (state) `zero: // last input was a zero begin out = 0; if (in) state = `one; else state = `zero; end `one: // we've seen one 1 if (in) begin state = `one; out = 1; end else begin state = `zero; out = 0; end endcase endmodule