## Slide 1: Overview
Last lecture
  Incompletely specified functions
Today
  Verilog
    Structural constructs
    Describing combinational circuits

## Slide 2: Ways of specifying circuits
Schematics
  Structural description
  Describe circuit as interconnected elements
    Build complex circuits using hierarchy
    Large circuits are unreadable
HDLs
  Hardware description languages
    Not programming languages
    Parallel languages tailored to digital design
  Synthesize code to produce a circuit

## Slide 3: Hardware description languages (HDLs)
Abel (~1983)
  Developed by Data-I/O
  Targeted to PLDs
  Limited capabilities (can do state machines)
Verilog (~1985)
  Developed by Gateway (now part of Cadence)
  Syntax similar to C
  Moved to public domain in 1990
VHDL (~1987)
  DoD sponsored
  Syntax similar to Ada

## Slide 4: Verilog versus VHDL
Both “IEEE standard” languages
Most tools support both
Verilog is “simpler”
  Less syntax, fewer constructs
VHDL is more structured
  Can be better for large, complex systems
  Better modularization

## Slide 5: Simulation and synthesis
Simulation
  “Execute” a design to verify correctness
Synthesis
  Generate a physical implementation from HDL code
Synthesis
HDL
Description
Gate or
Transistor
Description
Simulation
Simulation
Physical
Implementation
Functional
Validation
Functional/
Timing
Validation
Real
Chip!
Notes: Physical Implementation sometimes called a “netlist”

## Slide 6: Simulation and synthesis (con’t)
Simulation
  Models what a circuit does
    Multiply is “*”, ignoring implementation options
  Can include static timing
  Allows you to test design options
Synthesis
  Converts your code to a netlist
    Can simulate synthesized design
  Tools map your netlist to hardware
Simulation and synthesis in the CSE curriculum
  CSE370: Learn simulation
  CSE467: Learn synthesis

## Slide 7: Simulation
You provide an environment
  Using non-circuit constructs
    Active-HDL waveforms, Read files, print
  Using Verilog simulation code
    A “test fixture”
Simulation
Test Fixture
(Specification)
Circuit Description
(Synthesizeable)
Note: We will ignore timing and test benches until next Verilog lecture

## Slide 8: Specifying circuits in Verilog
There are three major styles
  Instances ‘n wires
  Continuous assignments
  “always” blocks
wire E;
and g1(E,A,B);
not g2(Y,C);
or g3(X,E,Y);
wire E;
assign E = A & B;
assign Y = ~C;
assign X = E | Y;
reg E, X, Y;
always @ (A or B or C)
begin
E = A & B;
Y = ~C;
X = E | Y;
end
“Structural”
“Behavioral”
Notes: Structural
  Describe explicit circuit elements
  Describe explicit connections between elements
    Connections between logic gates
  Just like schematics, but using text
Behavioral
  Describe circuit as algorithms/programs
    What a component does
    Input/output behavior
  Many possible circuits could have same behavior
    Different implementations of a Boolean function

## Slide 9: Data types
Values on a wire
  0, 1, x (unknown or conflict), z (tristate or unconnected)
Vectors
  A[3:0] vector of 4 bits: A[3], A[2], A[1], A[0]
    Unsigned integer value
    Indices must be constants
  Concatenating bits/vectors
    e.g. sign extend
      B[7:0] = {A[3], A[3], A[3], A[3], A[3:0]};
      B[7:0] = {4{A[3]}, A[3:0]};
  Style: Use a[7:0] = b[7:0] + c; Not a = b + c;
  Legal syntax: C = &A[6:7]; // logical and of bits 6 and 7 of A

## Slide 10: Data types that do not exist
Structures
Pointers
Objects
Recursive types
(Remember, Verilog is not C or Java or Lisp or …!)

## Slide 11: Numbers
Format: <sign><size><base format><number>
14
  Decimal number
–4’b11
  4-bit 2’s complement binary of 0011 (is 1101)
12’b0000_0100_0110
  12 bit binary number (_ is ignored)
3’h046
  3-digit (12-bit) hexadecimal number
Verilog values are unsigned
  C[4:0] = A[3:0] + B[3:0];
    if A = 0110 (6) and B = 1010(–6), then C = 10000 (not 00000)
    B is zero-padded, not sign-extended

## Slide 12: Operators
Similar to C operators

## Slide 13: Two abstraction mechanisms
Modules
  More structural
  Heavily used in 370 and “real” Verilog code
Functions
  More behavioral
  Used to some extent in “real” Verilog, but not much in 370

## Slide 14: Basic building blocks: Modules
// first simple example
module smpl (X,Y,A,B,C);
input A,B,C;
output X,Y;
wire E
and g1(E,A,B);
not g2(Y,C);
or g3(X,E,Y);
endmodule
  Instanced into a design
    Never called
  Illegal to nest module defs.
  Modules execute in parallel
  Names are case sensitive
  // for comments
  Name can’t begin with a number
  Use wires for connections
  and, or, not are keywords
  All keywords are lower case
  Gate declarations (and, or, etc)
    List outputs first
    Inputs second

## Slide 15: Modules are circuit components
  Module has ports
    External connections
    A,B,C,X,Y in example
  Port types
    input
    output
    inout (tristate)
  Use assign statements for Boolean expressions
    and  &
    or  |
    not  ~
// previous example as a
// Boolean expression
module smpl2 (X,Y,A,B,C);
input A,B,C;
output X,Y;
assign X = (A&B)|~C;
assign Y = ~C;
endmodule

## Slide 16: Structural Verilog
module xor_gate (out,a,b); input a,b; output out; wire abar, bbar, t1, t2; not inva (abar,a); not invb (bbar,b); and and1 (t1,abar,b); and and2 (t2,bbar,a); or or1 (out,t1,t2);
endmodule
8 basic gates (keywords):
and, or, nand, nor
buf, not, xor, xnor

## Slide 17: Behavioral Verilog
module full_addr (Sum,Cout,A,B,Cin); input A, B, Cin; output Sum, Cout; assign {Cout, Sum} = A + B + Cin; endmodule
A
B
Cin
Cout
Sum
Adder
Describe circuit behavior
  Not implementation
{Cout, Sum} is a concatenation

## Slide 18: Behavioral 4-bit adder
module add4 (SUM, OVER, A, B);
input [3:0] A;
input [3:0] B;
output [3:0] SUM;
output OVER;
assign {OVER, SUM[3:0]} = A[3:0] + B[3:0];
endmodule
“[3:0] A” is a 4-wire bus labeled “A”
Bit 3 is the MSB
Bit 0 is the LSB
Can also write “[0:3] A”
Bit 0 is the MSB
Bit 3 is the LSB
Buses are implicitly connected
  If you write BUS[3:2], BUS[1:0]
  They become part of BUS[3:0]

## Slide 19: Continuous assignment
assign A = X | (Y & ~Z);
assign B[3:0] = 4'b01XX;
assign C[15:0] = 4'h00ff;
assign #3 {Cout, Sum[3:0]} = A[3:0] + B[3:0] + Cin;
arithmetic operator
multiple assignment (concatenation)
Gate delay (used by simulator)
Boolean operators (~ for bit-wise negation)
bits can assume four values (0, 1, X, Z)
variables can be n-bits wide (MSB:LSB)
Assignment is continuously evaluated
  Corresponds to a logic gate
  Assignments execute in parallel
Notes: Verilog is an event driven simulator
When an assignment variable changes, code executes
In an always block, code only executes when the triggers change

## Slide 20: Example: A comparator
module Compare1 (Equal, Alarger, Blarger, A, B); input A, B; output Equal, Alarger, Blarger; assign Equal = (A & B) | (~A & ~B); assign Alarger = (A & ~B); assign Blarger = (~A & B); endmodule
Top-down design and bottom-up design are both okay
 module ordering doesn’t matter
 because modules execute in parallel

## Slide 21: Comparator example (con’t)
// Make a 4-bit comparator from 4 1-bit comparators module Compare4(Equal, Alarger, Blarger, A4, B4); input [3:0] A4, B4; output Equal, Alarger, Blarger; wire e0, e1, e2, e3, Al0, Al1, Al2, Al3, B10, Bl1, Bl2, Bl3; Compare1 cp0(e0, Al0, Bl0, A4[0], B4[0]); Compare1 cp1(e1, Al1, Bl1, A4[1], B4[1]); Compare1 cp2(e2, Al2, Bl2, A4[2], B4[2]); Compare1 cp3(e3, Al3, Bl3, A4[3], B4[3], ); assign Equal = (e0 & e1 & e2 & e3); assign Alarger = (Al3 | (Al2 & e3) |
(Al1 & e3 & e2) |
(Al0 & e3 & e2 & e1)); assign Blarger = (~Alarger & ~Equal); endmodule

## Slide 22: Sequential assigns don’t make any sense
assign A = X | (Y & ~Z);
assign B = W | A;
assign A = Y & Z;
“Reusing” a variable in several assign statements is not allowed

## Slide 23: Always Blocks
reg A, B, C;
always @ (W or X or Y or Z)
begin
A = X | (Y & ~Z);
B = W | A;
A = Y & Z;
if (A & B) begin
B = Z;
C = W | Y;
end
end
Sensitivity list
Variables that appear on the left hand side in an always block must be declared as “reg”s
Statements in an always block are executed in sequence
All variables must be assigned on every control path!!! (otherwise you get the dreaded “inferred latch”)

## Slide 24: Functions
module and_gate (out, in1, in2); input in1, in2; output out;
assign out = myfunction(in1, in2);
function myfunction;
input in1, in2;
begin
myfunction = in1 & in2;
end
endfunction
endmodule
Benefit:
Functions force a result
 Compiler will fail if function
does not generate a result
Use functions for complex combinational logic

## Slide 25: Sequential Verilog-- Blocking and non-blocking assignments
always @(posedge CLK) begin temp = B; B = A; A = temp; end
always @(posedge CLK) begin A <= B; B <= A; end
Blocking assignments (Q = A)
  Variable is assigned immediately
    New value is used by subsequent statements
Non-blocking assignments (Q <= A)
  Variable is assigned after all scheduled statements are executed
    Value to be assigned is computed but saved for later
  Usual use: Register assignment
    Registers simultaneously take new values after the clock edge
Example: Swap

## Slide 26: Sequential Verilog-- Assignments- watch out!
reg B, C, D;
always @(posedge clk) begin B <= A; C <= B; D <= C; end
reg B, C, D;
always @(posedge clk) begin B = A; C = B; D = C; end
Blocking versus Non-blocking

## Slide 27: Verilog tips
Do not write C-code
  Think hardware, not algorithms
    Verilog is inherently parallel
    Compilers don’t map algorithms to circuits well
Do describe hardware circuits
  First draw a dataflow diagram
  Then start coding
References
  Tutorial and reference manual are found in ActiveHDL help
  And in today’s reading assignment
  “Starter’s Guide to Verilog 2001” by Michael Ciletti
  copies for borrowing in hardware lab
Notes: When you get more experience, you don’t actually need to draw the diagram, but you still think that way

## Slide 28: Summary of two-level combinational-logic
Logic functions and truth tables
  AND, OR, Buf, NOT, NAND, NOR, XOR, XNOR
  Minimal set
Axioms and theorems of Boolean algebra
  Proofs by re-writing
  Proofs by perfect induction (fill in truth table)
Gate logic
  Networks of Boolean functions
  NAND/NOR conversion and de Morgan’s theorem
Canonical forms
  Two-level forms
  Incompletely specified functions (don’t cares)
Simplification
  Two-level simplification (K-maps)

## Slide 29: Solving combinational design problems
Step 1: Understand the problem
  Identify the inputs and outputs
  Draw a truth table
Step 2: Simplify the logic
  Draw a K-map
  Write a simplified Boolean expression
    SOP or POS
    Use don’t cares
Step 3: Implement the design
  Logic gates and/or Verilog