## Slide 1: Overview
Last lecture
  Latches
  Flip-flops
    Edge-triggered D
    Master-slave
  Timing diagrams
Today
  Sequential Verilog

## Slide 2: Variables
wire
  Connects components together
reg
  Saves a value
    Part of a behavioral description
  Does NOT necessarily become a register when you synthesize
    May become a wire
The rule
  Declare a variable as reg if it is a target of an assignment statement inside an always block
    Continuous assign doesn’t count

## Slide 3: Sequential Verilog
Sequential circuits: Registers & combinational logic
  Use positive edge-triggered registers
  Avoid latches and negative edge-triggered registers
Register is triggered by “posedge clk”
module register(Q, D, clock); input D, clock; output Q; reg Q; always @(posedge clock) begin
Q <= D;
end
endmodule
Example: A D flip-flop
A real register. Holds Q between clock edges

## Slide 4: always block
A construct that describes a circuit’s behavior
  Can contain multiple statements
  Can contain if, for, while, case
  Triggers at the specified conditions
  begin/end groups statements within always block
module register(Q, D, clock); input D, clock; output Q; reg Q; always @(posedge clock) begin
Q <= D;
end
endmodule

## Slide 5: always example
module and_gate(out, in1, in2); input in1, in2; output out; reg out; always @(in1 or in2) begin
out = in1 & in2;
end
endmodule
Not a real register!!
Holds assignment in always block
specifies when block is executed i.e. triggered by changes in in1 or in2
The compiler will not synthesize this code to a register, because out changes whenever in1 or in2 change. Can instead simply write
wire out, in1, in2;
and (out, in1, in2);

## Slide 6: Incomplete sensitivity list or incomplete assignment
module and_gate (out, in1, in2); input in1, in2; output out; reg out; always @(in1) begin
out = in1 & in2;
end
endmodule
What if you omit an input trigger (e.g. in2)
  Compiler will insert a latch to hold the state
  Becomes a sequential circuit — NOT what you want
2 rules:
1) Include all inputs in the trigger list
2) Use complete assignments
 Every path must lead to an assignment for out
 Otherwise out needs a state element
Real state!! Holds out because in2 isn’t specified in always sensitivity list

## Slide 7: Assignments
Be careful with always assignments
  Which of these statements generate state?
always @(c or x) begin if (c) begin
value = x;
end
y = value;
end
always @(c or x) begin value = x;
if (c) begin
value = 0;
end
y = value;
end
always @(c or x) begin if (c)
value = 0;
else if (x)
value = 1;
end
always @(a or b) f = a & b & c;
end
2 rules:
1) Include all inputs in the sensitivity list
2) Use complete assignments
 Every path must lead to an assignment for out
 Otherwise out needs a state element

## Slide 8: Another way: Use functions
module and_gate (out, in1, in2); input in1, in2; output out;
assign out = myfunction(in1, in2);
function myfunction;
input in1, in2;
begin
myfunction = in1 & in2;
end
endfunction
endmodule
Benefits:
Functions force a result
 Compiler will fail if function
does not generate a result
 If you build a function wrong
the circuit will not synthesize.
If you build an always block
wrong you get a register
Functions for combinational logic
  Functions can’t have state

## Slide 9: if
// Simple 4-1 mux
module mux4 (sel, A, B, C, D, Y);
input [1:0] sel; // 2-bit control signal
input A, B, C, D;
output Y;
reg Y; // target of assignment
always @(sel or A or B or C or D)
if (sel == 2’b00) Y = A;
else if (sel == 2’b01) Y = B;
else if (sel == 2’b10) Y = C;
else if (sel == 2’b11) Y = D;
endmodule
Same as C if statement
 Single if statements synthesize to multiplexers
 Nested if /else statements usually synthesize to logic

## Slide 10: if (another way)
// Simple 4-1 mux
module mux4 (sel, A, B, C, D, Y);
input [1:0] sel; // 2-bit control signal
input A, B, C, D;
output Y;
reg Y; // target of assignment
always @(sel or A or B or C or D)
if (sel[0] == 0)
if (sel[1] == 0) Y = A;
else Y = B;
else
if (sel[1] == 0) Y = C;
else Y = D;
endmodule

## Slide 11: case
// Simple 4-1 mux
module mux4 (sel, A, B, C, D, Y);
input [1:0] sel; // 2-bit control signal
input A, B, C, D;
output Y;
reg Y; // target of assignment
always @(sel or A or B or C or D)
case (sel)
2’b00: Y = A;
2’b01: Y = B;
2’b10: Y = C;
2’b11: Y = D;
endcase
endmodule
case executes sequentially
 First match executes
 Don’t need to break out of case
case statements synthesize to muxes

## Slide 12: case (another way)
// Simple 4-1 mux
module mux4 (sel, A, B, C, D, Y);
input [1:0] sel; // 2-bit control signal
input A, B, C, D;
output Y;
assign out = mymux(sel, A, B, C, D);
function mymux;
input [1:0] sel, A, B, C, D;
begin
case (sel)
2’b00: mymux = A;
2’b01: mymux = B;
2’b10: mymux = C;
2’b11: mymux = D;
endcase
end
endfunction
endmodule
Note: You can define a function in a file
Then include it into your Verilog module

## Slide 13: default case
// Simple binary encoder (input is 1-hot)
module encode (A, Y);
input [7:0] A; // 8-bit input vector
output [2:0] Y; // 3-bit encoded output
reg [2:0] Y; // target of assignment
always @(A)
case (A)
8’b00000001: Y = 0;
8’b00000010: Y = 1;
8’b00000100: Y = 2;
8’b00001000: Y = 3;
8’b00010000: Y = 4;
8’b00100000: Y = 5;
8’b01000000: Y = 6;
8’b10000000: Y = 7;
default: Y = 3’bx; // Don’t care about other cases
endcase
endmodule
If you omit the default, the compiler will create a latch for Y
 Either list all 256 cases
 Or use a function (compiler will
warn you of missing cases)

## Slide 14: case executes sequentially
// Priority encoder
module encode (A, Y);
input [7:0] A; // 8-bit input vector
output [2:0] Y; // 3-bit encoded output
reg [2:0] Y; // target of assignment
always @(A)
case (1’b1)
A[0]: Y = 0;
A[1]: Y = 1;
A[2]: Y = 2;
A[3]: Y = 3;
A[4]: Y = 4;
A[5]: Y = 5;
A[6]: Y = 6;
A[7]: Y = 7;
default: Y = 3’bx; // Don’t care when input is all 0’s
endcase
endmodule
Case statements execute sequentially
 Take the first alternative that matches

## Slide 15: for
// simple encoder
module encode (A, Y);
input [7:0] A; // 8-bit input vector
output [2:0] Y; // 3-bit encoded output
reg [2:0] Y; // target of assignment
integer i; // Temporary variables for program
reg [7:0] test;
always @(A) begin
test = 8b’00000001;
Y = 3’bx;
for (i = 0; i < 8; i = i + 1) begin
if (A == test) Y = i;
test = test << 1; // Shift left, pad with 0s
end
end
endmodule
for statements synthesize as cascaded combinational logic
 Verilog unrolls the loop
Notes: Note the “integer”

## Slide 16: Verilog while/repeat/forever
while (expression) statement
  execute statement while expression is true
repeat (expression) statement
  execute statement a fixed number of times
forever statement
  execute statement forever

## Slide 17: Blocking and non-blocking assignments
always @(posedge CLK) begin temp = B; B = A; A = temp; end
always @(posedge CLK) begin A <= B; B <= A; end
Blocking assignments (Q = A)
  Variable is assigned immediately
  New value is used by subsequent statements
Non-blocking assignments (Q <= A)
  Variable is assigned after all scheduled statements are executed
  Value to be assigned is computed but saved for later
Example: Swap

## Slide 18: Blocking and non-blocking assignments
reg B, C, D;
always @(posedge clk) begin B <= A; C <= B; D <= C; end
reg B, C, D;
always @(posedge clk) begin B = A; C = B; D = C; end

## Slide 19: Swap
always @(posedge CLK) begin A = B; end
always @(posedge CLK) begin B = A; end
always @(posedge CLK) begin A <= B; end
always @(posedge CLK) begin B <= A; end
The following code executes incorrectly
  One block executes first
  Loses previous value of variable
Non-blocking assignment fixes this
  Both blocks are scheduled by posedge CLK

## Slide 20: A simple stateful example
module stateful_and (out, in, clk); input in, clk; output out; reg out; always @(posedge clk) begin
out <= in & out;
end
endmodule

## Slide 21: Parallel versus serial execution
assign statements are implicitly parallel
  “=” means continuous assignment
  Example assign E = A & D; assign A = B & C;
  A and E change if B changes
always blocks execute in parallel
  always @(posedge clock)
Procedural block internals not necessarily parallel
  “=” is a blocking assignment (sequential)
  “<=” is a nonblocking assignment (parallel)
  Examples of procedures: always, function, etc.

## Slide 22: Synthesis examples
wire [3:0] x, y, a, b, c, d;
assign apr = ^a;
assign y = a & ~b;
assign x = (a == b) ?
a + c : d + a;
x
+
+
==
a
b
c
d
x
+
==
a
b
c
d