## Slide 1: Overview
Last lecture
  Sequential Logic Examples
Today
  State encoding
    One-hot encoding
    Output encoding
    FSM partitioning

## Slide 2: State encoding
Assume n state bits and m states
  2n! / (2n – m)! possible encodings [m  n  log2(m)]
    From binomial expansion
    Example: 3 state bits, 4 states, 1680 possible state assignments
Hard problem, with no known algorithmic solution
  Can try heuristic approaches
  Can try to optimize some metric
    FSM size (amount of logic and number of FFs)
    FSM speed (depth of logic and fanout)
    FSM dependencies (decomposition)
Need to consider startup
  Self-starting FSM or explicit reset input

## Slide 3: State-encoding strategies
No guarantee of optimality
  An intractable problem
Most common strategies
  Binary (sequential) – number states as in the state table
  Random – computer tries random encodings
  Heuristic – rules of thumb that seem to work well
    e.g. Gray-code – try to give adjacent states (states with an arc between them) codes that differ in only one bit position
  One-hot – use as many state bits as there are states
  Output – use outputs to help encode states

## Slide 4: One-hot encoding
One-hot: Encode n states using n flip-flops
  Assign a single “1” for each state
    Example: 0001, 0010, 0100, 1000
  Propagate a single “1” from one flip-flop to the next
    All other flip-flop outputs are “0”
The inverse: One-cold encoding
  Assign a single “0” for each state
    Example: 1110, 1101, 1011, 0111
  Propagate a single “0” from one flip-flop to the next
    All other flip-flop outputs are “1”
“almost one-hot” encoding
  Use no-hot (000…0) for the initial (reset state)
  Assumes you never revisit the reset state

## Slide 5: One-hot encoding (con’t)
Often the best approach for FPGAs
  FPGAs have many flip-flops
  One-hot machines use the least next-state logic
Draw FSM directly from the state diagram
  One product term per incoming arc
  But complex state diagram  complex design
One-hot designs have many possible failure modes
  All states that aren’t one-hot
  Can create logic to reset the FSM if it enters illegal state
Large machines require many flip-flops
  Decompose design into smaller one-hot encoded sub-designs
    n+m states for two machines versus n*m states for one

## Slide 6: Vending machine again...
Release item after receiving 15 cents
  Single coin slot for dimes and nickels
    Sensor specifies coin type
  Machine does not give change
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism

## Slide 7: One-hot encoded transition table
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3
0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 – – – – – 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 – – – – – 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 – – – – – 1 0 0 0 – – 1 0 0 0 1
present state inputs next state output Q3Q2Q1Q0 D N D3 D2D1D0 open

## Slide 8: One-hot encoded vending machine
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3

## Slide 9: Designing from the state diagram
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D
D' N'
D' N'
D' N'
1
D0 = Q0D’N’
D1 = Q0N + Q1D’N’
D2 = Q0D + Q1N + Q2D’N’
D3 = Q1D + Q2D + Q2N + Q3
OPEN = Q3

## Slide 10: Output encoding
Reuse outputs as state bits
  Why create new functions when you can use outputs?
  Bits from state assignments are the outputs for that state
    Take outputs directly from the flip-flops
ad hoc - no tools
  Yields small circuits for most FSMs
  Fits nicely with synchronous Mealy machines

## Slide 11: FSM partitioning
Break a large FSM into two or more smaller FSMs
Rationale
  Less states in each partition
    Simpler minimization and state assignment
    Smaller combinational logic
    Shorter critical path
  But more logic overall
Goal
  Minimize communication between partitions
    Minimize wires & I/O
Partitions are synchronous
  Same clock!!!

## Slide 12: Example: Partition the machine
C1
C2
C3
C4
C5
S1
S3
S2
S6
S4
S5
Partition into two halves

## Slide 13: Introduce idle states
C1
C2
C5•S2
S6
S4
S5
SB
C1•S1
C3•S2+ C4•S3
(C1•S1+ C3•S2+
C4•S3+
C5•S2)’
C4
S1
S3
S2
SA
C2•S6
C3+C5
(C2•S6)’
SA and SB handoff control between machines
C1
C2
C3
C4
C5
S1
S3
S2
S6
S4
S5

## Slide 14: Partitioning rules
S1
S6
C1
SA
S1
C1
S1
S6
C2
SA
S1
C2•S6
Rule #1: Source-state transformation
Replace by transition to idle state (SA)
Rule #2: Destination state transformation
Replace with exit transition from idle state

## Slide 15: Partitioning rules (con’t)
S2
S3
S5
S4
C4
C5
C3
S2
S3
SA
C3+C5
C4
S5
S4
C5•S2
SB
C3•S2 +
C4•S3
SA
S1
C2•S6
C2•S6
Rule #3: Multiple transitions with same source or destination
Source  Replace by transitions to idle state (SA)
Destination  Replace with exit transitions from idle state
Rule #4: Hold condition for idle state
OR exit conditions and invert

## Slide 16: Mealy versus Moore partitions
Mealy machines undesirable
  Inputs can affect outputs immediately
    “output” can be a handoff to another machine!!!
  Inputs can ripple through several machines in one clock cycle
Moore or synchronized Mealy desirable
  Input-to-output path always broken by a flip-flop
  But…may take several clocks for input to propagate to output
    Output may derive from other side of a partition

## Slide 17: Example: Six-state up/down counter
D
U
S0
S2
S1
S5
S3
S4
U
U
U
U
U
D
D
D
D
D
Break into 2 parts
U  count up
D  count down

## Slide 18: Example: 6 state up/down counter (con’t)
D•S0
U
S5
S3
S4
U
U
U•S2
D
D
D
SB
(D•S0+
U•S2)’
D•S3
U
S0
S2
S1
U
U
U•S5
D
D
D
SA
(D•S3 +
U•S5)’
Count sequence S0, S1, S2, S3, S4, S5
  S2 goes to SA and holds, leaves after S5
  S5 goes to SB and holds, leaves after S2
  Down sequence is similar

## Slide 19: Minimize communication between partitions
Ideal world: Two machines handoff control
  Separate I/O, states, etc.
Real world: Minimize handoffs and common I/O
  Minimize number of state bits that cross boundary
  Merge common outputs
Look for:
  Disjoint inputs used in different regions of state diagram
  Outputs active in only one region of state diagram
  Isomorphic portions of state diagram
    Add states, if necessary, to make them so
  Regions of diagram with a single entry and single exit point

## Slide 20: Sequential logic: What you should know
Sequential logic building blocks
  Latches (R-S and D)
  Flip-flops (master/slave D, edge-triggered D & T)
  Latch and flip-flop timing (setup/hold time, prop delay)
  Timing diagrams
  Flip-flop clocking
  Asynchronous inputs and metastability
  Registers

## Slide 21: Sequential logic: What you should know
Counters
  Timing diagrams
  Shift registers
  Ripple counters
  State diagrams and state-transition tables
  Counter design procedure
    1. Draw a state diagram
    2. Draw a state-transition table
    3. Encode the next-state functions
    4. Implement the design
  Self-starting counters

## Slide 22: Sequential logic: What you should know
Finite state machines
  Timing diagrams (synchronous FSMs)
  Moore versus Mealy versus registered Mealy
  FSM design procedure
    1. Understand the problem (state diagram & state-transition table)
    2. Determine the machine’s states (minimize the state diagram)
    3. Encode the machine’s states (state assignment)
    4. Design the next-state logic (minimize the combinational logic)
    5. Implement the FSM
  FSM design guidelines
    Separate datapath and control
  One-hot encoding
  FSM partitioning procedure