## Slide 1: Overview
Last lecture
  Adders
Today
  Introduction to sequential logic and systems
    The basic concepts
    A simple example

## Slide 2: Sequential versus combinational
B
A
C
clock
Apply fixed inputs A, B
Wait for clock edge
Observe C
Wait for another clock edge
Observe C again
Combinational: C will stay the same
Sequential: C may be different

## Slide 3: Sequential logic
Two types
  Synchronous = clocked
  Asynchronous = self-timed
Has state
  State = memory
Employs feedback
Assumes steady-state signals
  Signals are valid after they have settled
  State elements hold their settled output values

## Slide 4: Sequential versus combinational (again)
Combinational systems are memoryless
  Outputs depend only on the present inputs
Sequential systems have memory
  Outputs depend on the present and the previous inputs
Inputs
Outputs
System
Inputs
Outputs
System
Feedback

## Slide 5: Synchronous sequential systems
Memory holds a system’s state
  Changes in state occur at specific times
  A periodic signal times or clocks the state changes
  The clock period is the time between state changes
period
duty cycle = pulsewidth/period
(here it is 50%)
pulsewidth
B
A
C
clock
State changes occur at rising edge of clock
clock

## Slide 6: Steady-state abstraction
Outputs retain their settled values
  The clock period must be long enough for all voltages to settle to a steady state before the next state change
B
A
C
clock
clock
C
Settled value
Clock hides transient behavior

## Slide 7: Example: A sequential system
Door combination lock
  Enter 3 numbers in sequence and the door opens
  If there is an error the lock must be reset
  After the door opens the lock must be reset
  Inputs: Sequence of numbers, reset
  Outputs: Door open/close
  Memory: Must remember the combination

## Slide 8: Understand the problem
Consider I/O and unknowns
  How many bits per input?
  How many inputs in sequence?
  How do we know a new input is entered?
  How do we represent the system states?
reset
value
open/closed
new
clock

## Slide 9: Implement using sequential logic
Behavior
  Clock tells us when to look at inputs
    After inputs have settled
  Sequential: Enter sequence of numbers
  Sequential: Remember if error occurred
Need a finite-state diagram
  Assume synchronous inputs
  State sequence
    Enter 3 numbers serially
    Remember if error occurred
  All states have outputs
    Lock open or closed
reset
value
open/closed
new
clock

## Slide 10: Finite-state diagram
States: 5
  Each state has outputs
Outputs: open/closed
Inputs: reset, new, results of comparisons
  Assume synchronous inputs
closed
closed
closed
C1== value & new
C2== value & new
C3== value & new
C1!= value & new
C2!= value & new
C3!= value & new
closed
reset
not new
not new
not new
S1
S2
S3
OPEN
ERR
open
We use state diagrams to represent sequential logic
System transitions between finite numbers of states

## Slide 11: Separate data path and control
Data path
  Stores combination
  Compares inputs with combination
Control
  Finite state-machine controller
  Control for data path
  State changes clocked
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
controller
mux control
clock
4
4
4
4
4

## Slide 12: Refine diagram; generate state table
Refine state diagram to include internal structure
Generate state table
closed
closed
mux=C1
reset
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S1
S2
S3
OPEN
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open
reset new equal state state mux open/closed 1 – – – S1 C1 closed 0 0 – S1 S1 C1 closed 0 1 0 S1 ERR – closed 0 1 1 S1 S2 C2 closed ... 0 1 1 S3 OPEN – open ...
next

## Slide 13: Encode state table
State can be: S1, S2, S3, OPEN, or ERR
  Need at least 3 bits to encode: 000, 001, 010, 011, 100
  Can use 5 bits: 00001, 00010, 00100, 01000, 10000
  Choose 4 bits: 0001, 0010, 0100, 1000, 0000
Output to mux can be: C1, C2, or C3
  Need 2 or 3 bits to encode
  Choose 3 bits: 001, 010, 100
Output open/closed can be: Open or closed
  Need 1 or 2 bits to encode
  Choose 1 bit: 1, 0

## Slide 14: Encode state table (con’t)
reset new equal state state mux open/closed 1 – – – 0001 001 0 0 0 – 0001 0001 001 0 0 1 0 0001 0000 – 0 0 1 1 0001 0010 010 0 ... 0 1 1 0100 1000 – 1 ...
next
Good encoding choice!
  Mux control is identical to last 3 state bits
  Open/closed is identical to first state bit
  Output encoding  the outputs and state bits are the same

## Slide 15: Implementing the controller

## Slide 16: Implementing the controller
reset
open/closed
new
equal
mux control
clock
comb. logic
state
special circuit element, called a register, for storing inputs when
told to by the clock
We will learn how to design the controller given the encoded state-transition table

## Slide 17: Designing the datapath
C1
C2
C3
comparator
equal
multiplexer
mux control
4
4
4
4
4
value
C1i
C2i
C3i
mux control
valuei
equal
  Four 3:1 multiplexers
    2-input ANDs and 3-input OR
  Four single-bit comparators
    2-input XNORs
  4-input AND

## Slide 18: Where did we use memory?
Memory: Stored combination, state (errors or successes in past inputs)
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
equal
controller
mux control
clock

## Slide 19: Where did we use feedback?
Feedback: Comparator output ("equal" signal)
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
equal
controller
mux control
clock

## Slide 20: Where did we use clock?
Clock synchronizes the inputs
  Accept inputs when clock goes high
Controller is clocked
  Mux-control and open/closed signals change on the clock edge
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
equal
controller
mux control
clock

## Slide 21: Then next 5 weeks...
We learn the details
  Latches, flip-flops, registers
  Shift registers, counters
  State machines
  Timing and timing diagrams
  Synchronous and asynchronous inputs
    Metastability
  Clock skew
  Moore and Mealy machines
  One-hot encoding
  More...