## Slide 1: Overview
Last lecture
  State encoding
    One-hot encoding
    Output encoding
Today:
  Optimizing FSMs
    Pipelining
    Retiming
    Partitioning
  Conclusion of sequential logic

## Slide 2: Definitions
Latency: Time to perform a computation
  Data input to data output
Throughput: Input or output data rate
  Typically the clock rate
Combinational delays drive performance
  Define d  delay through slowest combinational stage n  number of stages from input to output
  Latency  n * d (in sec)
  Throughput  1/d (in Hz)

## Slide 3: Pipelining
What?
  Subdivide combinational logic
  Add registers between logic
Why?
  Trade latency for throughput
  Increased throughput
    Reduce logic delays
    Increase clock speed
  Increased latency
    Takes cycles to fill the pipe
  Increase circuit utilization
    Simultaneous computations
Logic Reg
Logic Reg Logic Reg

## Slide 4: Pipelining
When?
  Need throughput more than latency
    Signal processing
  Logic delays > setup/hold times
  Acyclic logic
Where?
  At natural breaks in the combinational logic
  Adding registers makes sense
Reg Logic Reg

## Slide 5: Pipelining example

## Slide 6: Pipelining and clock skew
Which is faster?
Which is safer?

## Slide 7: Retiming
Pipelining adds registers
  To increase the clock speed
Retiming moves registers around
  Reschedules computations to optimize performance
    Minimize critical path
    Optimize logic across register boundaries
    Reduce register count
  Without altering functionality

## Slide 8: Retiming in a nutshell
Change position of FFs
  For speed
  To suit implementation target
Retiming modifies state assignment
  Preserves FSM functionality
b
a
?
a
a
b
b
a
b
×

## Slide 9: Retiming groundrules
Rules:
  Remove one register from each input and add one to each output
  Remove one register from each output and add one to each input
Combinational logic
Register

## Slide 10: Retiming examples
Reduce register count
Change output delays
a
b
d
x
D Q
a
b
d
x
D Q
D Q

## Slide 11: Optimal pipelining
  Add registers
  Use retiming to optimize location
8
7
13
10
5
6
8
7
13
10
5
6
Input
Input
Output
Output
Added registers
for pipelining

## Slide 12: Example: Digital correlator
+
+


+


yt
xt
a0
a1
a2
a3
yt = (xt, a0) + (xt–1, a1) + (xt–2, a2) + (xt–3, a3)
  (x, a) = 1 if x = a; 0 otherwise
Input
Output

## Slide 13: Example: Digital correlator (cont’d)
+
+


+


+
+


+


Original design
cycle time = 24
Retimed design
cycle time = 13
Delays: Comparator = 3; adder = 7
Input
Output
Input
Output

## Slide 14: FSM partitioning
Break a large FSM into two or more smaller FSMs
Rationale
  Less states in each partition
    Simpler minimization and state assignment
    Smaller combinational logic
    Shorter critical path
  But more logic overall
Goal
  Minimize communication between partitions
    Minimize wires & I/O
Partitions are synchronous
  Same clock!!!

## Slide 15: Example: Partition the machine
C1
C2
C3
C4
C5
S1
S3
S2
S6
S4
S5
Partition into two halves

## Slide 16: Introduce idle states
C1
C2
C5•S2
S6
S4
S5
SB
C1•S1
C3•S2+ C4•S3
(C1•S1+ C3•S2+
C4•S3+
C5•S2)’
C4
S1
S3
S2
SA
C2•S6
C3+C5
(C2•S6)’
SA and SB handoff control between machines
C1
C2
C3
C4
C5
S1
S3
S2
S6
S4
S5

## Slide 17: Partitioning rules
S1
S6
C1
SA
S1
C1
S1
S6
C2
SA
S1
C2•S6
Rule #1: Source-state transformation
Replace by transition to idle state (SA)
Rule #2: Destination state transformation
Replace with exit transition from idle state

## Slide 18: Partitioning rules (con’t)
S2
S3
S5
S4
C4
C5
C3
S2
S3
SA
C3+C5
C4
S5
S4
C5•S2
SB
C3•S2 +
C4•S3
SA
S1
C2•S6
C2•S6
Rule #3: Multiple transitions with same source or destination
Source  Replace by transitions to idle state (SA)
Destination  Replace with exit transitions from idle state
Rule #4: Hold condition for idle state
OR exit conditions and invert

## Slide 19: Mealy versus Moore partitions
Mealy machines undesirable
  Inputs can affect outputs immediately
    “output” can be a handoff to another machine!!!
  Inputs can ripple through several machines in one clock cycle
Moore or synchronized Mealy desirable
  Input-to-output path always broken by a flip-flop
  But…may take several clocks for input to propagate to output
    Output may derive from other side of a partition

## Slide 20: Example: Six-state up/down counter
D
U
S0
S2
S1
S5
S3
S4
U
U
U
U
U
D
D
D
D
D
Break into 2 parts
U  count up
D  count down

## Slide 21: Example: 6 state up/down counter (con’t)
D•S0
U
S5
S3
S4
U
U
U•S2
D
D
D
SB
(D•S0+
U•S2)’
D•S3
U
S0
S2
S1
U
U
U•S5
D
D
D
SA
(D•S3 +
U•S5)’
Count sequence S0, S1, S2, S3, S4, S5
  S2 goes to SA and holds, leaves after S5
  S5 goes to SB and holds, leaves after S2
  Down sequence is similar

## Slide 22: Minimize communication between partitions
Ideal world: Two machines handoff control
  Separate I/O, states, etc.
Real world: Minimize handoffs and common I/O
  Minimize number of state bits that cross boundary
  Merge common outputs
Look for:
  Disjoint inputs used in different regions of state diagram
  Outputs active in only one region of state diagram
  Isomorphic portions of state diagram
    Add states, if necessary, to make them so
  Regions of diagram with a single entry and single exit point

## Slide 23: Sequential logic: What you should know
Sequential logic building blocks
  Latches (R-S and D)
  Flip-flops (master/slave D, edge-triggered D & T)
  Latch and flip-flop timing (setup/hold time, prop delay)
  Timing diagrams
  Flip-flop clocking
  Asynchronous inputs and metastability
  Registers

## Slide 24: Sequential logic: What you should know
Counters
  Timing diagrams
  Shift registers
  Ripple counters
  State diagrams and state-transition tables
  Counter design procedure
    1. Draw a state diagram
    2. Draw a state-transition table
    3. Encode the next-state functions
    4. Implement the design
  Self-starting counters

## Slide 25: Sequential logic: What you should know
Finite state machines
  Timing diagrams (synchronous FSMs)
  Moore versus Mealy versus registered Mealy
  FSM design procedure
    1. Understand the problem (state diagram & state-transition table)
    2. Determine the machine’s states (minimize the state diagram)
    3. Encode the machine’s states (state assignment)
    4. Design the next-state logic (minimize the combinational logic)
    5. Implement the FSM
  FSM design guidelines
    Separate datapath and control
  One-hot encoding
  Pipelining and retiming basics