## Slide 1: Boolean algebra
Last lecture
  Binary numbers
  Base conversion
  Number systems
    Twos-complement
  A/D and D/A conversion
Today’s lecture
  Boolean algebra
    Axioms
    Useful laws and theorems
    Simplifying Boolean expressions
  Lab-- What is a circuit?
Class rule: Interrupt when you don’t understand why we are doing something
Notes: Class rule: Interrupt when you don’t understand why we are doing something

## Slide 2: Major topic: Combinational logic
Axioms and theorems of Boolean algebra
Logic functions and truth tables
  AND, OR, Buffer, NAND, NOR, NOT, XOR, XNOR
Gate logic
  Networks of Boolean functions
Canonical forms
  Sum of products and product of sums
Simplification
  Boolean cubes and Karnaugh maps
  Two-level simplification

## Slide 3: Combinational versus sequential
B
A
C
Clock
Combinational: Memoryless
  Apply fixed inputs A, B
  Wait for clock edge
  Observe C
  Wait for another clock edge
  Observe C again: C will stay the same
Sequential: With Memory
  Apply fixed inputs A, B
  Wait for clock edge
  Observe C
  Wait for another clock edge
  Observe C again: C may be different

## Slide 4: Boolean algebra
A Boolean algebra comprises...
  A set of elements B
  Binary operators {+ , •}
  A unary operation { ' }
…and the following axioms
  1. The set B contains at least two elements {a b} with a  b
  2. Closure: a+b is in B a•b is in B
  3. Commutative: a+b = b+a a•b = b•a
  4. Associative: a+(b+c) = (a+b)+c a•(b•c) = (a•b)•c
  5. Identity: a+0 = a a•1 = a
  6. Distributive: a+(b•c)=(a+b)•(a+c) a•(b+c)=(a•b)+(a•c)
  7. Complementarity: a+a' = 1 a•a' = 0

## Slide 5: Digital (binary) logic is a Boolean algebra
Substitute
  {0, 1} for B
  AND for • Boolean Product
  OR for + Boolean Sum
  NOT for '
All the axioms hold for binary logic
Definitions
  Boolean function
    Maps inputs from the set {0,1} to the set {0,1}
  Boolean expression
    An algebraic statement of Boolean variables and operators

## Slide 6: AND, OR, Not
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X
Y
Z
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
Z
AND X•Y XY
OR X+Y
NOT X X'
X Y 0 1 1 0
X
Y

## Slide 7: Logic functions and Boolean algebra
X Y X' Y' X • Y X' •Y' Z 0 0 1 1 0 1 1 0 1 1 0 0 0 0 1 0 0 1 0 0 0
1 1 0 0 1 0 1
X Y X' Z 0 0 1 0 0 1 1 1 1 0 0 0
1 1 0 0
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
Any logic function that is expressible as a truth table can be written in Boolean algebra using +, •, and '
Z=X•Y
Z=X'•Y
Z=(X•Y)+(X' •Y')

## Slide 8: Two key concepts
Duality (a meta-theorem— a theorem about theorems)
  All Boolean expressions have logical duals
  Any theorem that can be proved is also proved for its dual
  Replace: • with +, + with •, 0 with 1, and 1 with 0
  Leave the variables unchanged
de Morgan’s Theorem
  Procedure for complementing Boolean functions
  Replace: • with +, + with •, 0 with 1, and 1 with 0
  Replace all variables with their complements

## Slide 9: Useful laws and theorems
Identity: X + 0 = X Dual: X • 1 = X
Null: X + 1 = 1 Dual: X • 0 = 0
Idempotent: X + X = X Dual: X • X = X
Involution: (X')' = X
Complementarity: X + X' = 1 Dual: X • X' = 0
Commutative: X + Y = Y + X Dual: X • Y = Y • X
Associative: (X+Y)+Z=X+(Y+Z) Dual: (X•Y)•Z=X•(Y•Z)
Distributive: X•(Y+Z)=(X•Y)+(X•Z) Dual: X+(Y•Z)=(X+Y)•(X+Z)
Uniting: X•Y+X•Y'=X Dual: (X+Y)•(X+Y')=X

## Slide 10: Useful laws and theorems (con’t)
Absorption: X+X•Y=X Dual: X•(X+Y)=X
Absorption (#2): (X+Y')•Y=X•Y Dual: (X•Y')+Y=X+Y
de Morgan's: (X+Y+...)'=X'•Y'•... Dual: (X•Y•...)'=X'+Y'+...
Duality: (X+Y+...)D=X•Y•... Dual: (X•Y•...)D=X+Y+…
Multiplying & factoring: (X+Y)•(X'+Z)=X•Z+X'•Y
  Dual: X•Y+X'•Z=(X+Z)•(X'+Y)
Consensus: (X•Y)+(Y•Z)+(X'•Z)= X•Y+X'•Z
  Dual: (X+Y)•(Y+Z)•(X'+Z)=(X+Y)•(X'+Z)

## Slide 11: Proving theorems
Example 1: Prove the uniting theorem-- X•Y+X•Y'=X
  Distributive X•Y+X•Y' = X•(Y+Y') Complementarity = X•(1) Identity = X
Example 2: Prove the absorption theorem-- X+X•Y=X
  Identity X+X•Y = (X•1)+(X•Y) Distributive = X•(1+Y) Null = X•(1) Identity = X

## Slide 12: Proving theorems
Example 3: Prove the consensus theorem-- (XY)+(YZ)+(X'Z)= XY+X'Z
  Complementarity XY+YZ+X'Z = XY+(X+X')YZ + X'Z
  Distributive = XYZ+XY+X'YZ+X'Z
    Use absorption {AB+A=A} with A=XY and B=Z
  = XY+X'YZ+X'Z
  Rearrange terms = XY+X'ZY+X'Z
    Use absorption {AB+A=A} with A=X'Z and B=Y
  XY+YZ+X'Z = XY+X'Z

## Slide 13: de Morgan’s Theorem
Use de Morgan’s Theorem to find complements
Example: F=(A+B)•(A’+C), so F’=(A’•B’)+(A•C’)
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
A B C F’
0 0 0 1
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1 0

## Slide 14: Logic simplification
Use the axioms to simplify logical expressions
  Why? To use less hardware
Example: A two-level logic expression Z = A'BC + AB'C' + AB'C + ABC' + ABC = AB'C + AB'C' + A'BC + ABC' + ABC rearrange = AB'(C + C') + A'BC + AB(C' + C) distributive = AB' + A'BC + AB comp. = AB' + AB + A'BC rearrange = A(B' + B) + A'BC distributive = A + A'BC comp.
    Use absorption #2D {(X •Y')+Y=X+Y} with X=BC and Y=A
  Z = A + BC

## Slide 15: Example: A full adder
1-bit binary adder
  Inputs: A, B, Carry-in
  Outputs: Sum, Carry-out
A B Cin S Cout
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A'BCin + AB'Cin + ABCin' + ABCin
S = A'B'Cin + A'BCin' + AB'Cin' + ABCin
A
B
Cin
Cout
Sum
Adder

## Slide 16: Simplifying the carry-out function
Cout = A'BCin + AB'Cin + ABCin' + ABCin = A'BCin + AB'Cin + ABCin' + ABCin + ABCin = A'BCin + ABCin + AB'Cin + ABCin' + ABCin = (A'+A)BCin + AB'Cin + ABCin' + ABCin = (1)BCin + AB'Cin + ABCin' + ABCin = BCin + AB'Cin + ABCin' + ABCin + ABCin = BCin + AB'Cin + ABCin + ABCin' + ABCin = BCin + A(B'+B)Cin + ABCin' + ABCin = BCin + A(1)Cin + ABCin' + ABCin = BCin + ACin + AB(Cin'+Cin) = BCin + ACin + AB(1) = BCin + ACin + AB
associative
idempotent

## Slide 17: Some notation
Priorities:
Variables are sometimes called literals

## Slide 18: Lab
What is a circuit?

## Slide 19: A Circuit
+
VR
VD
I
Current is the flow of charge
  Assume positively charged particles
    Real physical current is negatively charged electrons
  Units are amps; we will use mA (10–3A) or µA (10–6A)
Voltage is a measure of potential energy
  Work that can be done by the electrons
  Must always have a reference; we will use ground
  Units are volts; we will use V or mV (10–3V)
Vcc
GND