## Slide 1: Overview
Last lecture
  PLDs
  ROMs
  Tristates
  Design examples
Today
  Adders
    Ripple-carry
    Carry-lookahead
    Carry-select
  Parallel prefix trees
  The conclusion of combinational logic!!!

## Slide 2: Arithmetic circuits
General-purpose building blocks
  Critical components in processor datapaths
    Adders
    Multipliers (integer, floating-point)
    ALUs
  Perform most computer instructions
  Time  space tradeoff
    Fast circuits usually require more logic

## Slide 3: Binary half adder
1-bit half adder
  Computes sum, carry-out
    No carry-in
  Sum = A'B + AB' = A xor B
  Cout = AB
A B S Cout 0 0 0 0 0 1 1 0 1 0 1 0 1 1 0 1
A
B
Cout
Sum
Half
Adder

## Slide 4: Binary full adder
A B Cin S Cout 0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
1-bit full adder
  Computes sum, carry-out
    Carry-in allows cascaded adders
  Sum = Cin xor A xor B
  Cout = ACin + BCin + AB
A
B
Cin
Cout
Sum
Full
Adder

## Slide 5: Full adder: Alternative implementation
Multilevel logic
  Slower
  Fewer gates
    2 XORs, 2 ANDs, 1 OR
Sum = (A  B)  Cin
Cout = ACin + BCin + AB
  = (A  B)Cin + AB
A
B
A xor B
Cin
A xor B xor Cin
Sum
Cout
(A xor B)Cin
AB
Sum
Cout
Half Adder
Sum
Cout
Half Adder
A B Cin S Cout Cout 0 0 0 0 0 0 0 0 1 1 0 0 0 1 0 1 0 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 0 1 1 1 1 0 0 1 1 1 1 1 1 1 1

## Slide 6: 2-bit ripple-carry adder
A1
B1
Cout
Cin
Sum1
A
Sum
Cout
Cin
B
1-Bit Adder
A2
B2
Sum2
Cout
Cin
0
Overflow

## Slide 7: 4-bit ripple-carry adder/subtractor
A
B
Cout
Sum
Cin
0
1
0  Add 1  Subtract
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0
Circuit adds or subtracts
  2s complement: A – B = A + (–B) = A + B' + 1
Note: Can replace 2:1 muxes with XOR gates

## Slide 8: Problem: Ripple-carry delay
Carry propagation limits adder speed
@0
@0
Cout takes two gate delays
Cin arrives late
A0
B0
Cin
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
@0
@2N
@0
@2N
@0
@0
@2N
@2N+1
@2N+2

## Slide 9: Ripple-carry adder timing diagram
T0
T2
T4
T6
T8
S0, C1 Valid
S1, C2 Valid
S2, C3 Valid
S3, C4 Valid
Critical delay
  Carry propagation
  1111 + 0001 = 10000 is worst case

## Slide 10: One solution: Carry lookahead logic
A0
B0
Cin
S0 @2
A1
B1
C1 @3
S1 @4
A2
B2
C2 @3
S2 @4
A3
B3
C3 @3
S3 @4
C4 @3
C4 @3
Compute all the carries in parallel
  Derive carries from the data inputs
    Not from intermediate carries
    Use two-level logic
  Compute all sums in parallel
Cascade simple adders to make large adders
Speed improvement
  16-bit ripple-carry: ~32 gate delays
  16-bit carry-lookahead: ~8 gate delays
Issues
  Complex combinational logic

## Slide 11: A Digression: Linear chains vs. trees
Lets say we want to implement an 8-input Or function with only 2-input gates Gates: 7 Max delay: 7

## Slide 12: Linear chains vs. trees, part 2
Now consider the tree version Gates: 7 Max delay: 3

## Slide 13: And now we change the problem slightly
Build a circuit that takes 8 single bit inputs and calculates the Or of the first 2, the Or of the first 3, the Or of the first 4, and so on, up to the Or of all 8 Gates: 7 Max delay: 7

## Slide 14: The tree version of the prefix circuit
Gates: 12 Max delay: 3
Notes: The gates highlighted in blue are the original tree

## Slide 15: Full adder again
A
B
A xor B
Cin
A xor B xor Cin
Cout
Cin(A xor B)
AB
Sum
Cout
Half Adder
Sum
Cout
Half Adder

## Slide 16: Carry-lookahead logic
Carry generate: Gi = AiBi
  Generate carry when A = B = 1
Carry propagate: Pi = Ai xor Bi
  Propagate carry-in to carry-out when (A xor B) = 1
Sum and Cout in terms of generate/propagate:
  Si = Ai xor Bi xor Ci = Pi xor Ci
  Ci+1= AiBi + Ci(Ai xor Bi) = Gi + CiPi

## Slide 17: Carry-lookahead logic (cont’d)
Re-express the carry logic in terms of G and P
  C1 = G0 + P0C0
  C2 = G1 + P1C1 = G1 + P1G0 + P1P0C0
  C3 = G2 + P2C2 = G2 + P2G1 + P2P1G0 + P2P1P0C0
  C4 = G3 + P3C3 = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0C0
Implement each carry equation with two-level logic
  Derive intermediate results directly from inputs
    Rather than from carries
  Allows "sum" computations to proceed in parallel

## Slide 18: Implementing the carry-lookahead logic
C1
C0
C0
P0
P0
G0
G0
P1
P1
G1
C2
C0
P0
G0
P1
P1
G1
P2
P2
P2
G2
C3
G3
C0
P0
G0
P1
P1
G1
P2
P2
P2
G2
P3
P3
P3
P3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
Logic complexity
increases with
adder size

## Slide 19: Cascaded carry-lookahead adder
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@4
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4 four-bit adders with internal carry lookahead
  Second level lookahead extends adder to 16 bits

## Slide 20: Another solution: Carry-select adder
4-Bit Adder [3:0]
C0
C4
4-bit adder [7:4]
0
C8
1
C8
five 2:1 muxes
0
1
0
1
0
1
0
1
adder high
adder low
0
1
4-bit adder [7:4]
C8
S7
S6
S5
S4
S3
S2
S1
S0
Redundant hardware speeds carry calculation
  Compute two high-order sums while waiting for carry-in (C4)
  Select correct high-order sum after receiving C4

## Slide 21: Scaling of carry-select adders
Size: roughly twice the size of a ripple-carry Delay: delay through a 4-bit ripple-carry plus the multiplexor path highlighted in blue (3 2-1 multiplexors, in this example)

## Slide 22: We've finished combinational logic...
What you should know
  Twos complement arithmetic
  Truth tables
  Basic logic gates
  Schematic diagrams
  Timing diagrams
  Minterm and maxterm expansions (canonical, minimized)
  de Morgan's theorem
  AND/OR to NAND/NOR logic conversion
  K-maps, logic minimization, don't cares
  Multiplexers/demultiplexers
  PLAs/PALs
  ROMs
  Adders