## Slide 1: Overview
Last lecture
  State Minimization
Today
  Sequential Logic Examples

## Slide 2: Sequential logic examples
Basic design approach: a 4-step design process
Hardware description languages and finite state machines
Implementation examples and case studies
  complex counter
  traffic light controller
  door combination lock

## Slide 3: General FSM design procedure
(1) Determine inputs and outputs
(2) Determine possible states of machine
  – state minimization
(3) Encode states and outputs into a binary code
  – state assignment or state encoding
  – output encoding
  – possibly input encoding (if under our control)
(4) Realize logic to implement functions for states and outputs
  – combinational logic implementation and optimization
  – choices made in steps 2 and 3 can have large effect on resulting logic

## Slide 4: Complex counter
Mode Input M
0
0
1
1
1
0
0
Current State
000
001
010
110
111
101
110
Next State
001
010
110
111
101
110
111
A synchronous 3-bit counter has a mode control M
  when M = 0, the counter counts up in the binary sequence
  when M = 1, the counter advances through the Gray code sequence binary: 000, 001, 010, 011, 100, 101, 110, 111 Gray: 000, 001, 011, 010, 110, 111, 101, 100
Valid I/O behavior (partial)

## Slide 5: Complex counter (state diagram)
Deriving state diagram
  one state for each output combination
  add appropriate arcs for the mode control
S0 [000]
S1 [001]
S2 [010]
S3 [011]
S4 [100]
S5 [101]
S6 [110]
S7 [111]
reset
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1

## Slide 6: Complex counter (state encoding)
Verilog description including state encoding
module string (clk, M, rst, Z0, Z1, Z2);
input clk, X, rst;
output Z0, Z1, Z2;
reg state[0:2];
‘define S0 = [0,0,0];
‘define S1 = [0,0,1];
‘define S2 = [0,1,0];
‘define S3 = [0,1,1];
‘define S4 = [1,0,0];
‘define S5 = [1,0,1];
‘define S6 = [1,1,0];
‘define S7 = [1,1,1];
assign Z0 = state[0];
assign Z1 = state[1];
assign Z2 = state[2];
always @(posedge clk) begin
if rst state = ‘S0;
else
case (state)
‘S0: state = ‘S1; ‘S1: if (M) state = ‘S3 else state = ‘S2; ‘S2: if (M) state = ‘S6 else state = ‘S3; ‘S3: if (M) state = ‘S2 else state = ‘S4; ‘S4: if (M) state = ‘S0 else state = ‘S5; ‘S5: if (M) state = ‘S4 else state = ‘S6; ‘S6: state = ‘S7; ‘S7: if (M) state = ‘S5 else state = ‘S0; endcase
end
endmodule

## Slide 7: Traffic light controller as two communicating FSMs
TS/ST
S1
TS'
–/ST
S1a
S1b
S1c
traffic light controller
timer
TL
TS
ST
Without separate timer
  S0 would require 7 states
  S1 would require 3 states
  S2 would require 7 states
  S3 would require 3 states
  S1 and S3 have simple transformation
  S0 and S2 would require many more arcs
    C could change in any of seven states
By factoring out timer
  greatly reduce number of states
    4 instead of 20
  counter only requires seven or eight states
    12 total instead of 20

## Slide 8: Traffic light controller FSM
module FSM(HR, HY, HG, FR, FY, FG, ST, TS, TL, C, reset, Clk); output HR; output HY; output HG; output FR; output FY; output FG; output ST; input TS; input TL; input C; input reset; input Clk; reg [6:1] state; reg ST;
`define highwaygreen 6'b001100 `define highwayyellow 6'b010100 `define farmroadgreen 6'b100001 `define farmroadyellow 6'b100010
assign HR = state[6]; assign HY = state[5]; assign HG = state[4]; assign FR = state[3]; assign FY = state[2]; assign FG = state[1];
specify state bits and codes for each state as well as connections to outputs
Specification of inputs, outputs, and state elements

## Slide 9: Traffic light controller FSM (cont’d)
initial begin state = `highwaygreen; ST = 0; end always @(posedge Clk) begin if (reset) begin state = `highwaygreen; ST = 1; end else begin ST = 0; case (state) `highwaygreen: if (TL & C) begin state = `highwayyellow; ST = 1; end `highwayyellow: if (TS) begin state = `farmroadgreen; ST = 1; end `farmroadgreen: if (TL | !C) begin state = `farmroadyellow; ST = 1; end `farmroadyellow: if (TS) begin state = `highwaygreen; ST = 1; end endcase end end endmodule
case statement triggerred by clock edge

## Slide 10: Timer for traffic light controller
module Timer(TS, TL, ST, Clk); output TS; output TL; input ST; input Clk; integer value; assign TS = (value >= 4); // 5 cycles after reset assign TL = (value >= 14); // 15 cycles after reset always @(posedge ST) value = 0; // async reset always @(posedge Clk) value = value + 1; endmodule
Another FSM

## Slide 11: Complete traffic light controller
module main(HR, HY, HG, FR, FY, FG, reset, C, Clk); output HR, HY, HG, FR, FY, FG; input reset, C, Clk; Timer part1(TS, TL, ST, Clk); FSM part2(HR, HY, HG, FR, FY, FG, ST, TS, TL, C, reset, Clk); endmodule
Tying it all together (FSM + timer)
traffic light controller
timer
TL
TS
ST

## Slide 12: Communicating finite state machines
machines advance in lock step
initial inputs/outputs: X = 0, Y = 0
CLK FSM1 X FSM2 Y
A
A
B
C
D
D
FSM 1
FSM 2
X
Y
Y==1
A [1]
Y==0
B [0]
Y==0
X==1
C [0]
X==0
X==0
D [1]
X==1
X==0
One machine's output is another machine's input

## Slide 13: Data-path and control
"puppet"
"puppeteer who pulls the strings"
control
data-path
status info and inputs
control signal outputs
state
Digital hardware systems = data-path + control
  datapath: registers, counters, combinational functional units (e.g., ALU), communication (e.g., busses)
  control: FSM generating sequences of control signals that instructs datapath what to do next

## Slide 14: Digital combinational lock
Door combination lock:
  punch in 3 values in sequence and the door opens; if there is an error the lock must be reset; once the door opens the lock must be reset
  inputs: sequence of input values, reset
  outputs: door open/close
  memory: must remember combination or always have it available
  open questions: how do you set the internal combination?
    stored in registers (how loaded?)
    hardwired via switches set by user

## Slide 15: Implementation in software
integer combination_lock ( ) {
  integer v1, v2, v3;
  integer error = 0;
  static integer c[3] = 3, 4, 2;
  while (!new_value( ));
  v1 = read_value( );
  if (v1 != c[1]) then error = 1;
  while (!new_value( ));
  v2 = read_value( );
  if (v2 != c[2]) then error = 1;
  while (!new_value( ));
  v3 = read_value( );
  if (v2 != c[3]) then error = 1;
  if (error == 1) then return(0); else return (1);
}

## Slide 16: Determining details of the specification
reset
value
open/closed
new
clock
How many bits per input value?
How many values in sequence?
How do we know a new input value is entered?
What are the states and state transitions of the system?

## Slide 17: Digital combination lock state diagram
States: 5 states
  represent point in execution of machine
  each state has outputs
Transitions: 6 from state to state, 5 self transitions, 1 global
  changes of state occur when clock says its ok
  based on value of inputs
Inputs: reset, new, results of comparisons
Output: open/closed
closed
closed
closed
C1==value & new
C2==value & new
C3==value & new
C1!=value & new
C2!=value & new
C3!=value & new
closed
reset
not new
not new
not new
S1
S2
S3
OPEN
ERR
open

## Slide 18: Data-path and control structure
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
controller
mux control
clock
4
4
4
4
4
Data-path
  storage registers for combination values
  multiplexer
  comparator
Control
  finite-state machine controller
  control for data-path (which value to compare)

## Slide 19: State table for combination lock
Finite-state machine
  refine state diagram to take internal structure into account
  state table ready for encoding

## Slide 20: Encodings for combination lock
mux is identical to last 3 bits of state open/closed is identical to first bit of state
therefore, we do not even need to implement FFs to hold state, just use outputs
reset
open/closed
new
equal
controller
mux control
clock
Encode state table
  state can be: S1, S2, S3, OPEN, or ERR
    needs at least 3 bits to encode: 000, 001, 010, 011, 100
    and as many as 5: 00001, 00010, 00100, 01000, 10000
    choose 4 bits: 0001, 0010, 0100, 1000, 0000
  output mux can be: C1, C2, or C3
    needs 2 to 3 bits to encode
    choose 3 bits: 001, 010, 100
  output open/closed can be: open or closed
    needs 1 or 2 bits to encode
    choose 1 bit: 1, 0

## Slide 21: Data-path implementation for combination lock
C1
C2
C3
comparator
equal
multiplexer
mux control
4
4
4
4
4
value
C1i
C2i
C3i
mux control
value
equal
Multiplexer
  easy to implement as combinational logic when few inputs
  logic can easily get too big for most PLDs

## Slide 22: Data-path implementation (cont’d)
C1
C2
C3
comparator
equal
multiplexer
mux control
4
4
4
4
4
value
C1i
C2i
C3i
mux control
value
equal
+
oc
open-collector connection
(zero whenever one connection is zero, one otherwise – wired AND)
tri-state driver
(can disconnect from output)
Tri-state logic
  utilize a third output state: “no connection” or “float”
  connect outputs together as long as only one is “enabled”
  open-collector gates can only output 0, not 1
    can be used to implement logical AND with only wires

## Slide 23: Tri-state gates
In OE Out X 0 Z 0 1 0 1 1 1
non-inverting
tri-state buffer
100
In
OE
Out
The third value
  logic values: “0”, “1”
  don't care: “X” (must be 0 or 1 in real circuit!)
  third value or state: “Z” — high impedance, infinite R, no connection
Tri-state gates
  additional input – output enable (OE)
  output values are 0, 1, and Z
  when OE is high, the gate functions normally
  when OE is low, the gate is disconnected from wire at output
  allows more than one gate to be connected to the same output wire
    as long as only one has its output enabled at any one time (otherwise, sparks could fly)
In
Out
OE

## Slide 24: Tri-state and multiplexing
when Select is high Input1 is connected to F
when Select is low Input0 is connected to F
this is essentially a 2:1 mux
OE
OE
F
Input0
Input1
Select
When using tri-state logic
  (1) make sure never more than one "driver" for a wire at any one time (pulling high and low at the same time can severely damage circuits)
  (2) make sure to only use value on wire when its being driven (using a floating value may cause failures)
Using tri-state gates to implement an economical multiplexer

## Slide 25: Open-collector gates and wired-AND
open-collector NAND gates
with ouputs wired together
using "wired-AND" to form (AB)'(CD)'
Open collector: another way to connect gate outputs to the same wire
  gate only has the ability to pull its output low
  it cannot actively drive the wire high (default – pulled high through resistor)
Wired-AND can be implemented with open collector logic
  if A and B are "1", output is actively pulled low
  if C and D are "1", output is actively pulled low
  if one gate output is low and the other high, then low wins
  if both gate outputs are "1", the wire value "floats", pulled high by resistor
    low to high transition usually slower than it would have been with a gate pulling high
  hence, the two NAND functions are ANDed together

## Slide 26: Digital combination lock (new data-path)
C1
C2
C3
comparator
value
equal
multiplexer
mux control
4
4
4
4
4
ld1
ld2
ld3
Decrease number of inputs
Remove 3 code digits as inputs
  use code registers
  make them loadable from value
  need 3 load signal inputs (net gain in input (4*3)–3=9)
    could be done with 2 signals and decoder (ld1, ld2, ld3, load none)