## Slide 1: Overview
Last lecture
  Finished counter design
    Design example
    Self-starting counters
Today
  Introduction to finite-state machines
    Moore versus Mealy machines
    Synchronous Mealy machines
    Example: A parity checker

## Slide 2: Finite state machines
FSM: A system that visits a finite number of logically distinct states
Counters are simple FSMs
  Outputs and states are identical
  Visit states in a fixed sequence
FSMs are more complex than counting
  Outputs can depend on current state and on inputs
  State sequencing depends on current state and on inputs

## Slide 3: Generalized FSM model
Inputs
Outputs
Next State
Current State
output logic
Next-state logic
State variables (state vector) holds circuit state
  Stored in registers
Combinational logic computes next state and outputs
  Next state is a function of current state and inputs
  Outputs are functions of
    Current state (Moore machine)
    Current state and inputs (Mealy machine)

## Slide 4: Moore versus Mealy machines
outputs
state feedback
inputs
reg
combinational logic for next state
logic for outputs
Moore machine
Outputs are a function
of current state
Outputs change
synchronously with
state changes
Mealy machine
Outputs depend on state
and on inputs
Input changes can cause immediate output changes
(asynchronous)
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs

## Slide 5: Example: Moore versus Mealy
D
Q
Q
D
Q
Q
D
Q
Q
D
Q
Q
A
B
clock
out
D
Q
Q
D
Q
Q
A
B
clock
out
Circuits recognize AB=10 followed by AB=01
  What kinds of machines are they?

## Slide 6: Specifying outputs for a Moore machine
Output is a function of state only
  Specify output in the state bubble
  Example: Detector for 01 or 10
D/1
E/1
B/0
A/0
C/0
1
0
0
0
0
1
1
1
1
0
reset
current next current reset input state state output
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B D 0
0 0 C E 0
0 1 C C 0
0 0 D E 1
0 1 D C 1
0 0 E B 1
0 1 E D 1

## Slide 7: Specifying outputs for a Mealy machine
Output is a function of state and inputs
  Specify outputs on transition arcs
  Example: Detector for 01 or 10
current next current reset input state state output
B
A
C
0/1
0/0
0/0
1/1
1/0
1/0
reset/0
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B C 1
0 0 C B 1
0 1 C C 0

## Slide 8: Comparing Moore and Mealy machines
Moore machines
  + Safer do use because outputs change at clock edge
  – May take additional logic to decode state into outputs
Mealy machines
  + Typically have fewer states
  + React faster to inputs — don't wait for clock
  – Asynchronous outputs can be dangerous
We will often design synchronous Mealy machines
  Design a Mealy machine
  Then register the outputs

## Slide 9: Synchronous (registered) Mealy machine
Registered state and registered outputs
  No glitches on outputs
  No race conditions between communicating machines
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
reg

## Slide 10: FSM design
Generalized counter design
  Counter-design procedure
    1. State diagram
    2. State-transition table
    3. Next-state logic minimization
    4. Implement the design
  FSM-design procedure
    1. State diagram and state-transition table
    2. State minimization
    3. State assignment (or state encoding)
    4. Next-state logic minimization
    5. Implement the design

## Slide 11: Example: A parity checker
Serial input string
  OUT=1 if odd # of 1s in input
  OUT=0 if even # of 1s in input
Present Input Next Present
State State Output
Even 0 Even 0
Even 1 Odd 0
Odd 0 Odd 1
Odd 1 Even 1
1. State diagram and state-transition table
Moore-machine state diagram

## Slide 12: Parity checker (con’t)
2. State minimization: Already minimized
  Need both states (even and odd)
  Use one flip-flop
3. State assignment (or state encoding)
Present Input Next Present
State State Output
0 0 0 0
0 1 1 0
1 0 1 1
1 1 0 1
Assignment
Even  0
Odd  1

## Slide 13: Parity checker (con’t)
4. Next-state logic minimization
  Assume D flip-flops
  Next state = (present state) XOR (present input)
  Present output = present state
5. Implement the design
D
Q
Q
CLK
Input
Output

## Slide 14: Implementation
D Q
Q
Can map FSMs to programmable logic devices
  Macro-cell = DFF + two-level logic
Other options: Gate arrays, semicustom ICs, etc.

## Slide 15
Figure 1. The general form of a sequential circuit.
Combinational
circuit
Flip-flops
Clock
Q
W
Z
Combinational
circuit

## Slide 16
Figure 2. Sequences of input and output signals.
Clockcycle:
t
0
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
w
:
0
1
0
1
1
0
1
1
1
0
1
z
:
0
0
0
0
0
1
0
0
1
1
0

## Slide 17
Figure 3. State diagram of a simple sequential circuit.
C
z
1
=

Reset
B
z
0
=

A
z
0
=

w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=

## Slide 18
Figure 4. State table.
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1

## Slide 19
Figure 5. A general sequential circuit.
Combinational
circuit
Combinational
circuit
Clock
y
2
z
w
y
1
Y
1
Y
2

## Slide 20
Figure.6. A state-assigned table.
Present
Next state
state
w
=
0
w
=
1
Output
y
2
y
1
Y
2
Y
1
Y
2
Y
1
z
A
00
00
01
0
B
01
00
10
0
C
10
00
10
1
11
dd
dd
d

## Slide 21
Figure 7. Derivation of logic expressions.
w
00
01
11
10
0
1
0
1
0
y
2
y
1
Y
1
wy
1
y
2
=
w
00
01
11
10
0
1
0
d
1
d
y
2
y
1
Y
2
wy
1
y
2
wy
1
y
2
+
=
d
d
0
0
0
0
0
0
1
0
1
0
1
0
d
y
1
z
y
1
y
2
=
0
1
y
2
Y
1
wy
1
y
2
=
Y
2
wy
1
wy
2
+
=
z
y
2
=
w
y
1
y
2
+
(
)
=
Ignoring don't cares
Using don't cares

## Slide 22
Figure 8. Sequential circuit derived in Figure 7.

## Slide 23
Figure 9. Verilog code for the FSM in Figure 3.
module simple (Clock, Resetn, w, z);
input Clock, Resetn, w;
output z;
reg [2:1] state, NextState;
parameter [2:1] stateA = 2'b00, stateB = 2'b01, stateC = 2'b10;
// Define the next state combinational circuit
always @(w or state)
case (state)
stateA : if (w) NextState = stateB;
else NextState = stateA;
stateB : if (w) NextState = stateC;
else NextState = stateA;
stateC : if (w) NextState = stateC;
else NextState = stateA;
default: NextState = 2'bxx;
endcase
// Define the sequential block
always @(negedge Resetn or posedge Clock)
if (Resetn == 0) state <= stateA;
else state <= NextState;
// Define output
assign z = (state == stateC);
endmodule