## Slide 1: Overview
Last lecture
  Sequential Verilog
Today
  Review of D latches and flip-flops
  T flip-flops and SR latches
  State diagrams
  Asynchronous inputs

## Slide 2: Latches versus flip-flops
behavior is the same unless input
changes while the clock is high
CLK
D
Qff
Qlatch
D
Q
Q
CLK
D
Q
Q
CLK

## Slide 3: The master-slave D
D
Q
CLK
Input
Master D latch
D
Q
Output
Slave D latch
master-slave D flip-flop
Class example: Draw the timing diagram

## Slide 4: How do we make a latch?
Two inverters hold a bit
  As long as power is applied
Storing a new memory
  Temporarily break the feedback path
"0"
"1"
"stored bit"
"remember"
"load"
"data"
"stored bit"

## Slide 5: How do we make a D F/F?
Edge triggering is difficult
  Label the internal nodes
  Draw a timing diagram
  Start with Clk=1
Q
D
Clk
W
Y
X
Z
Q’

## Slide 6: T flip-flop
Full name: Toggle flip-flop
Output toggles when input is asserted
  If T=1, then Q  Q' when CLK 
  If T=0, then Q  Q when CLK 
CLK
Q
T
Q
>
Input(t) Q(t) Q(t + t)
0
0
0
0
1
1
1
0
1
1
1
0
Input

## Slide 7: The SR latch
Cross-coupled NOR gates
  Can set (S=1, R=0) or reset (R=1, S=0) the output
Cross-coupled NAND gates
  Can set (S=1, R=0) or reset (R=1, S=0) the output
R
S
Q
Q'
Q
Q'
S'
R'

## Slide 8: SR latch behavior
Truth table and timing
Reset
Hold
Set
Set
Reset
Race
R
S
Q
Q'
100
R
S
Q
Q'
S R Q 0 0 hold 0 1 0 1 0 1 1 1 disallow

## Slide 9: SR latch is glitch sensitive
Static 0 hazards can set/reset latch
  Glitch on S input sets latch
  Glitch on R input resets latch
R
S
Q
Q'
0
0

## Slide 10: Clear and preset in flip-flops
Clear and Preset set flip-flop to a known state
  Used at startup, reset
Clear or Reset to a logic 0
  Synchronous: Q=0 when next clock edge arrives
  Asynchronous: Q=0 when reset is asserted
    Doesn't wait for clock
    Quick but dangerous
Preset or Set the state to logic 1
  Synchronous: Q=1 when next clock edge arrives
  Asynchronous: Q=1 when reset is asserted
    Doesn't wait for clock
    Quick but dangerous

## Slide 11: State diagrams
How do we characterize logic circuits?
  Combinational circuits: Truth tables
  Sequential circuits: State diagrams
First draw the states
  States  Unique circuit configurations
Second draw the transitions between states
  Transitions  Changes in state caused by inputs

## Slide 12: Example: SR latch
Begin by drawing the states
  States  Unique circuit configurations
  Possible values for feedback (Q, Q')
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
Q Q' 1 1
R
S
Q
Q'

## Slide 13: Example: SR latch
Now draw the state transitions
  Labeling inputs
R
S
Q
Q'
possible oscillation between states 00 and 11
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
Q Q' 1 1
SR=00
SR=11
SR=00
SR=10
SR=01
SR=00
SR=10
SR=00
SR=01
SR=11
SR=11
SR=10
SR=01
SR=01
SR=10
SR=11

## Slide 14: Observed SR latch behavior
The 1–1 state is transitory
  Either R or S “gets ahead”
  Latch settles to 0–1 or 1–0 state ambiguously
  Race condition  non-deterministic transition
    Disallow (R,S) = (1,1)
R
S
Q
Q'
SR=00
SR=10
Q Q' 0 1
Q Q' 1 0
SR=10
SR=01
SR=00
SR=01

## Slide 15: System considerations
Use edge-triggered flip-flops wherever possible
  Avoid latches
  Most common: Master-slave D
Basic rules for correct timing
  Clock flip-flops synchronously (all at the same time)
    No flip-flop changes state more than once per clock cycle
    FF propagation delay > hold time
  Avoid mixing positive-edge triggered and negative-edge triggered flip-flops in the same circuit

## Slide 16: Asynchronous inputs
Clocked circuits are synchronous
  Circuit changes state only at clock edges
  Signals (voltages) settle in-between clock edges
Unclocked circuits or signals are asynchronous
  No master clock
  Real-world inputs (e.g. a keypress) are asynchronous
Synchronous circuits have asynchronous inputs
  Reset signal, memory wait, user input, etc.
  Inputs “bounce”
  Inputs can change at any time
    We must synchronize the input to our clock
    Inputs will violate flip-flop setup/hold times

## Slide 17: Debouncing
Switch inputs bounce
  i. e. don’t make clean transitions
Can use SR latch for debouncing
  Eliminates dynamic hazards
  “Cleans-up” inputs
R
S
Q
Q'
3.3V
3.3V
0V
3.3V
0V
1
0
1
0

## Slide 18: Synchronizer failure
Occurs when FF input changes near clock edge
  Input is neither 1 or 0 when clock goes high
  Output may be neither 0 or 1
    May stay undefined for a long time
  Undefined state is called metastability
logic 0
logic 1
D
CLK
Q

## Slide 19: Minimizing synchronizer failures
Failure probability can never be 0
  Can make it small
  Cascade two (or more) flip-flops
    Effectively synchronizes twice
    Both would have to fail for system to fail
D
D
Q
asynchronous
input
synchronized
input
Clk
Q

## Slide 20: Handling asynchronous inputs
Never fan-out asynchronous inputs
  Synchronize at circuit boundary
  Fan-out synchronized signal
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
Synchronizer