## Slide 1: Computer Organization: A real processor
UW CSE
MIPS 2000

## Slide 2: Background
UW CSE
We have built a model processor in ActiveHDL
  You get to make it work
Heavily based on MIPS2000
  Described by Patterson & Hennessy
Single-cycle design
  All operations take 1 (long) cycle

## Slide 3: Instruction Set Specs
UW CSE
32 registers
Load-Store Architecture
Word Addressing
3 Formats for Instructions
  Register to Register
  Immediate
  Jump

## Slide 4: Instruction Encodings
CSE370 - Computer Organization
<number>
Three principal types (32 bits in each instruction) type op rs rt rd shift funct R(egister) 6 5 5 5 5 6 I(mmediate) 6 5 5 16- immediate J(ump) 6 26- immediate
Some of the instructions add 6’h00 rs rt rd 6’h20 rd = rs + rt sub 6’h00 rs rt rd 6’h22 rd = rs - rt and 6’h00 rs rt rd 6’h24 rd = rs & rt or 6’h00 rs rt rd 6’h25 rd = rs | rt slt 6’h00 rs rt rd 6’h2a rd = (rs < rt) lw 6’h23 rs rt offset rt = mem[rs + offset] sw 6’h2b rs rt offset mem[rs + offset] = rt beq 6’h04 rs rt offset pc = pc + offset, if (rs == rt) addi 6’h08 rs rt offset rt = rs + offset j 6’h02 target address pc = target address halt 6’h3f - stop execution until reset
R
I
J

## Slide 5: Mips2000
UW CSE

## Slide 6: Program Counter
UW CSE
assign offset = {{16{Inst[15]}},Inst}; // sign extend the immediate
assign Branch = Next + offset;
assign Jump = {Next[31:26],Inst[25:0]}; // used by J instruction
// There are 4 possible sources for PC
// 0. PC = Next (Move to next Instruction)
// 1. PC = Next + offset (Conditional Branch)
// 2. PC = Reg (Jump to Register value)
// 3. PC = Next[31:26],jump_target( J instruction)
assign PC = (PCSel[1])?
((PCSel[0])? Jump : Reg) : ((PCSel[0])? Branch : Next);

## Slide 7: Controller
UW CSE
Skeleton Code:
…
ADDI: begin
wrDataSel = 2'bxx;
mw = 1'bx;
mr = 1'bx;
PCSel = 2'bxx;
srcB = 1'bx;
regWrite = 1'bx;
wrRegSel = 2'bxx;
op = 6'bxxxxxx;
end

## Slide 8: Register File
UW CSE
// decide which register is the one that might be written to (depends on instruction)
// 00 – rd, 01 – rt, 1X – hardwired to 31 for JAL
assign wrReg = wrRegSel[1] ?
5'b11111 : (wrRegSel[0] ? rd : rt);
// do two reads and, optionally, one write with the register file
// read two registers and send them to the ALU
assign RegA = RegFile[rs];
assign RegB = RegFile[rt];
// write into a register (but not the register storing our constant 0)
always @(posedge clk) begin
if (regWrite && (wrReg != 0)) begin
RegFile[wrReg] = WriteData;
end
end

## Slide 9: ALU
UW CSE
// use srcB to select between RegB and Imm
assign B = (srcB === 0)? RegB : Imm;
always @(A or B or op) begin
case (op)
6'b000001: result = A + B;
…
default: result = 32'hxxxxxxxx;
endcase
zero = (result == 32'h00000000);
neg = result[31];
end

## Slide 10: Data Memory
UW CSE
Address from ALU
Data from Reg B
Memory-Mapped I/O
  SW to xFFFFFFF
  Buffers / Displays
  (See dmemory.v for more)

## Slide 11: Miscellaneous
UW CSE
WrRegSel:
  // wrDataSel
  // 00: Out = ALU
  // 01: Out = MEM
  // 1X: Out = PC + 1
SignExtender:
convert 16-bit to 32-bit

## Slide 12: Global View
UW CSE

## Slide 13: R-Format Operations
UW CSE
Func | Operation | PC | comment
ADD | rd = rs + rt | PC++ | 
SUB | rd = rs – rt | PC++ | 
SLT | rd = (rs < rt) ? 1 : 0 | PC++ | Set on less than
JR | No change | PC=rs | Jump to Register

## Slide 14: I-Format Ops:
UW CSE
 | Operation | PC | Comment
ADDI | rt = rs+SE(imm) | PC++ | 
ORI | rt = rs ¦ imm | PC++ | 
LUI | rt = imm << 16 | PC++ | Load upper immed
LW | rt = MEM[rs+se(imm)] | PC++ | 
SW | MEM[rs+se(imm)] = rt | PC++ | 
BEQ | (rs == rt)? | PC+1+(0¦imm) | 

## Slide 15: J-Format Ops:
UW CSE
Func | Operation | PC | comment
J |  | PC = target | a.k.a GOTO
JAL | r31 = PC+1 | PC = target | Jump and Link
JAL stores next address, jumps to target (a.k.a fn call )

## Slide 16: Final Tips:
UW CSE
Verilog uses “?” for Don’t Cares
Waveforms will make things easier
Be sure to set clk and reset
Simulation: 14000ns limit-- longer, controller is broken
Don't use opcode defs from 378 text-- ours are different.

## Slide 17: Programming Example
UW CSE
Given: A is an array of size B
Goal: Compute
Lets use a for loop …

## Slide 18: In Assembly Language:
UW CSE
Variables  Registers
Array Access  Load (name+offset)
Minimal Control Structures
  Branches ( A < B, A >= B, A != B)
  Jumps

## Slide 19: C to ASM
UW CSE
High Level Language
C = 0;
for(i = 0; i < B; i = i+1) {
C = C + A[i];
}
Psuedo-Asm
C = 0;
i = 0;
Loop: bge i, B, Exit
temp = A+i
temp2 = load 0(temp)
C = C + temp2;
i = i + 1;
j Loop
Exit: …

## Slide 20: ASM to RTL
UW CSE
r3 = r0, PC++
r4 = r0, PC++
Loop: PC =
( r4 ≥ r2) ? Exit : PC+1
r6 = MEM[r4+r1 ],PC++
r3 = r3 + r6, PC++
r4 = r4 + 1, PC++
PC = LOOP
Exit:
C = 0;
i = 0;
Loop: bge i, B, Exit
temp = load A[i];
C = C + temp;
i = i + 1;
j Loop
Exit: …