## Slide 1: Overview
Last lecture
  Verilog
Today
  Timing diagrams
  Multilevel logic
    Multilevel NAND/NOR conversion
  Hazards

## Slide 2: Timing diagrams
F
A
B
C
D
time
“Sideways” truth tables
  Show time-response of circuits
    Real gates have real delays
  Example: A' • A = 0
    Delays cause transient F=1
Some texts call timing diagrams “waveforms”

## Slide 3: Example: F=A+BC in 2-level logic
minimized product-of-sums
F1
F2
F3
B
C
A
F4
canonical product-of-sums
minimized sum-of-products
canonical sum-of-products

## Slide 4: Timing diagram for F = A + BC
Time waveforms for F1 – F4 are identical
  Except for timing hazards (glitches)
  More on this shortly...

## Slide 5: Multilevel logic
Basic idea: Simplify logic using >2 gate levels
  Time–space (speed versus gate count) tradeoff
Two-level logic usually
  Has smaller delays (faster circuits)
    But more gates and more wires (more circuit area)
    Sometimes has large fan-ins (slow)
  Easier to eliminate hazards
Multilevel logic usually
  Has fewer gates (smaller circuits)
    But can be slower (more gate delays)
  Harder to eliminate hazards

## Slide 6: Multilevel logic example
Function X
  SOP: X = ADF + AEF + BDF + BEF + CDF + CEF + G
    X is minimized!
    Six 3-input ANDs; one 7-input OR; 25 wires
  Multilevel: X = (A+B+C)(D+E)F + G
    Factored form
    One 3-input OR, two 2-input OR's, one 3-input AND; 10 wires
A
B C
D E F G
X
3-level circuit
X = (A+B+C)(D+E)F + G

## Slide 7: Multilevel NAND/NAND conversion
F = A(B+CD) + BC'
original
AND-OR network
introduce bubbles
(conserve inversions)
Level 1 Level 2 Level 3 Level 4
A
C
D
B
B
C'
F
A
C
D
B
B
C'
F

## Slide 8: Multilevel NOR/NOR conversion
F = A(B+CD) + BC'
original
AND-OR network
introduce bubbles
(conserve inversions)
Level 1 Level 2 Level 3 Level 4
A
C
D
B
B
C'
F
A
C
D
B
B
C'
F

## Slide 9: Generic multilevel conversion
F = ABC + BC + D = AX + X + D
D'
A
X'
B
C
F
D'
A
X
B
C
F
X'
(a)
(c)
(b)
(d)
A
X
B
C
D
F
original circuit
A
X
B
C
D
F
add double bubbles at inputs
distribute bubbles
some mismatches
insert inverters to fix mismatches

## Slide 10: Issues with multilevel design
No global definition of “optimal” multilevel circuit
  Optimality depends on user-defined goals
  Synthesize an implementation that meets design goals
Synthesis requires CAD-tool help
  No simple hand methods like K-maps
  CAD tools manipulate Boolean expressions
    Factoring, decomposition, etc.
  Covered in more detail in CSE467

## Slide 11: Multilevel logic summary
Advantages over 2-level logic
  Smaller circuits
  Reduced fan-in
  Less wires
Disadvantages w.r.t 2-level logic
  More difficult design
  Less powerful optimizing tools
  Dynamic hazards
What you should know for CSE370
  The basic multilevel idea
  Multilevel NAND/NAND and NOR/NOR conversion

## Slide 12: Hazards/glitches
Hazards/glitches: Undesired output switching
  Occurs when different pathways have different delays
  Wastes power; causes circuit noise
  Dangerous if logic makes a decision while output is unstable
  Dangerous if using asynchronous circuits
Solutions
  Design hazard-free circuits
    Difficult when logic is multilevel
  Wait until signals are stable
  Use synchronous circuits

## Slide 13: Types of hazards
1
0
0
1
1
0
0
1
1
0
0
0
1
1
Static 1-hazard
  Output should stay logic 1
  Gate delays cause brief glitch to logic 0
Static 0-hazard
  Output should stay logic 0
  Gate delays cause brief glitch to logic 1
Dynamic hazards
  Output should toggle cleanly
  Gate delays cause multiple transitions

## Slide 14: Static hazards
Occur when a literal and its complement momentarily assume the same value
  Through different paths with different delays
  Causes an (ideally) static output to glitch
F
A
B
S
S'
F
static-0 hazard
A
S
B
S'
A multiplexer

## Slide 15: Dynamic hazards
Occur when a literal assumes multiple values
  Through different paths with different delays
  Causes an output to toggle multiple times
B2
A
C
B1
F
Dynamic hazard
B3
A
C
B
F
1
2
3
Dynamic hazards

## Slide 16: Eliminating static hazards
In 2-level logic circuits
  Assuming single-bit changes
Key idea: Glitches happen when a changing input spans separate k-map encirclements
  Example: 1101 to 0101 change can cause a static-1 glitch
A
C'
A'
D
F
0 0 1 1
1 1 1 1
1 1 0 0
0 0 0 0
AB
CD
B
D
00
01
11
10
00
01
11
10
C
A
F = AC' + A'D

## Slide 17: Eliminating static hazards (con’t)
Solution: Add redundant k-map encirclements
  Ensure that all single-bit changes are covered
  First eliminate static-1 hazards: Use SOP form
  Still need to eliminate static-0 hazards: Use POS form
A
C'
A'
D
F
0 0 1 1
1 1 1 1
1 1 0 0
0 0 0 0
AB
CD
B
D
00
01
11
10
00
01
11
10
C
A
C'
D
F = AC' + A'D + C'D

## Slide 18: Summary of hazards
We can eliminate static hazards in 2-level logic
  For single-bit changes
  Eliminating static hazards also eliminates dynamic hazards
Hazards are a difficult problem
  Multiple-bit changes in 2-level logic are hard
  Static hazards in multilevel logic are harder
  Dynamic hazards in multilevel logic are harder yet
CAD tools and simulation/testing are indispensable
  Test vectors probe a design for hazards