## Slide 1: Overview
Last lecture
  Cascading flip-flops
  Clock skew
  Registers
Today
  Introduction to finite state machines
    State diagrams
  Counters as finite state machines
    Counter design

## Slide 2: State machines
Combinational Logic
Storage Elements
Outputs
State Outputs
State Inputs
Inputs
Combinational logic and storage elements
  Localized feedback loops
  Choice of storage elements alters the logic
    D flip-flop, T flip-flop, etc.

## Slide 3: Asynchronous versus synchronous
Asynchronous
  State changes occur when state inputs change
  Feedback elements may be wires or delays
Synchronous
  State changes occur synchronously
  Feedback elements are clocked
Clock
Combinational Logic
Combinational Logic
Synchronous
Asynchronous

## Slide 4: Finite-state machines
In = 0
In = 1
In = 0
In = 1
100
010
110
111
001
States: Possible storage-element values
Transitions: Changes in state
  Clock synchronizes the state changes
Sequential logic
  Sequences through a series of states
  Based on inputs and present state

## Slide 5: Drawing state diagrams
100
110
111
011
101
010
000
001
0
1
1
1
1
1
1
1
0
0
0
0
0
1
0
0
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
CLK
Show input values on transition arcs
Show output values in state nodes

## Slide 6: Begin by studying counters
010
100
110
011
001
000
101
111
3-bit up-counter
Simple state machines
  Output is the counter’s state
Next state is well defined
  Does not depend on input (no inputs)

## Slide 7: Counter design procedure
1. Draw a state diagram
2. Draw a state-transition table
3. Encode the next-state functions
  Minimize the logic using k-maps
4. Implement the design
Example: Design the 3-bit up counter

## Slide 8: 1. Draw a state diagram
010
100
110
011
001
000
101
111
3-bit up-counter

## Slide 9: 2. Draw a state-transition table
Like a truth-table
  State encoding is easy for counters  Use count value
current state next state 0 000 001 1 1 001 010 2 2 010 011 3 3 011 100 4 4 100 101 5 5 101 110 6 6 110 111 7 7 111 000 0
010
100
110
011
001
000
101
111
3-bit up-counter

## Slide 10: 3. Encode the next state functions
Assume D flip-flops as state elements
C3 C2 C1 N3 N2 N1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0
0 0 1 1 0 1 0 1
C2
C3
C1
N3
1 1 1 1 0 0 0 0
C2
C3
C1
N1
0 1 1 0 1 0 0 1
C2
C3
C1
N2
N1 := C1'
N2 := C1C2' + C1'C2
:= C1 xor C2
N3 := C1C2C3' + C1'C3 + C2'C3
:= C1C2C3' + (C1' + C2')C3
:= (C1C2) xor C3

## Slide 11: 4. Implement the design
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
CLK
"1"
3 flip-flops hold state
  Counter is synchronously clocked
Minimized logic computes next state

## Slide 12: Class example
Redesign the 3-bit up counter using T flip-flops
1. Draw a state diagram
2. Draw a state-transition table
3. Encode the next-state functions
  Minimize the logic using k-maps
4. Implement the design

## Slide 13: 1. Draw a state diagram
010
100
110
011
001
000
101
111
3-bit up-counter

## Slide 14: 2. Draw a state-transition table
Like a truth-table
  State encoding is easy for counters  Use count value
current state next state 0 000 001 1 1 001 010 2 2 010 011 3 3 011 100 4 4 100 101 5 5 101 110 6 6 110 111 7 7 111 000 0
010
100
110
011
001
000
101
111
3-bit up-counter
Name:____________________

## Slide 15: 3. Encode the next state functions
T flip-flops
C2
C3
C1
T3
C2
C3
C1
T1
C2
C3
C1
T2
T1 :=
T
Q
C3 C2 C1 N3 N2 N1 T3 T2 T1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0
T2 :=
T3 :=
T
Q
T
Q
T
Q
C1
C2
C3
CLK
4. Implement the design: