## Slide 1: Computer organization
CSE370 - Computer Organization
<number>
Computer design – an application of digital logic design procedures
Computer = processing unit + memory system
Processing unit = control + datapath
Control = finite state machine
  inputs = machine instruction, datapath conditions
  outputs = register transfer control signals, ALU operation codes
  instruction interpretation = instruction fetch, decode, execute
Datapath = functional units + registers
  functional units = ALU, multipliers, dividers, etc.
  registers = program counter, shifters, storage registers

## Slide 2: Structure of a computer
CSE370 - Computer Organization
<number>
central processing unit (CPU)
instruction unit – instruction fetch and interpretation FSM
execution unit – functional units
and registers
address
read/write
data
Processor
Memory
System
Block diagram view
control signals
data conditions
Data Path
Control

## Slide 3: Registers
CSE370 - Computer Organization
<number>
LD asserted during a lo-to-hi clock transition loads new data into FFs
OE asserted causes FF state to be connected to output pins; otherwise they are left unconnected (high impedance)
OE
Q7
Q6
Q5
Q4
Q3
Q2
Q1
Q0
LD
D7
D6
D5
D4
D3
D2
D1
D0
CLK
Selectively loaded – EN or LD input
Output enable – OE input
Multiple registers – group 4 or 8 in parallel

## Slide 4: Register transfer
CSE370 - Computer Organization
<number>
Point-to-point connection
  dedicated wires
  muxes on inputs of each register
Common input from multiplexer
  load enables for each register
  control signals for multiplexer
Common bus with output enables
  output enables and load enables for each register
rt
MUX
rs
MUX
rd
MUX
R4
MUX
rs
MUX
rt
rd
R4
BUS
rs
rt
rd
R4

## Slide 5: Register files
CSE370 - Computer Organization
<number>
RE
RB
RA
WE
WB
WA
D3
D2
D1
D0
Q3
Q2
Q1
Q0
Collections of registers in one package
  two-dimensional array of FFs
  address used as index to a particular word
  can have separate read and write addresses so can do both at same time
4 by 4 register file
  16 D-FFs
  organized as four words of four bits each
  write-enable (load)
  read-enable (output enable)

## Slide 6: Memories
CSE370 - Computer Organization
<number>
RD
WR
A9
A8
A7
A6
A5
A4
A3
A2
A2
A1
A0
IO3
IO2
IO1
IO0
Larger collections of storage elements
  implemented not as FFs but as much more efficient latches
  high-density memories use 1 to 5 switches (transitors) per memory bit
Static RAM – 1024 words each 4 bits wide
  once written, memory holds forever (not true for denser dynamic RAM)
  address lines to select word (10 lines for 1024 words)
  read enable
    same as output enable
    often called chip select
    permits connection of many chips into larger array
  write enable (same as load enable)
  bi-directional data lines
    output when reading, input when writing

## Slide 7: Instruction sequencing
CSE370 - Computer Organization
<number>
Example – an instruction to add the contents of two registers (Rx and Ry) and place result in a third register (Rz)
Step 1: get the ADD instruction from memory into an instruction register
Step 2: decode instruction
  instruction in IR has the code of an ADD instruction
  register indices used to generate output enables for registers Rx and Ry
  register index used to generate load signal for register Rz
Step 3: execute instruction
  enable Rx and Ry output and direct to ALU
  setup ALU to perform ADD operation
  direct result to Rz so that it can be loaded into register

## Slide 8: Instruction types
CSE370 - Computer Organization
<number>
Data manipulation
  add, subtract
  increment, decrement
  multiply
  shift, rotate
  immediate operands
Data staging
  load/store data to/from memory
  register-to-register move
Control
  conditional/unconditional branches in program flow
  subroutine call and return

## Slide 9: Elements of the control unit (aka instruction unit)
CSE370 - Computer Organization
<number>
Standard FSM elements
  state register
  next-state logic
  output logic (datapath/control signalling)
  Moore or synchronous Mealy machine to avoid loops unbroken by FF
Plus additional "control" registers
  instruction register (IR)
  program counter (PC)
Inputs/outputs
  outputs control elements of data path
  inputs from data path used to alter flow of program (test if zero)

## Slide 10: Instruction execution
CSE370 - Computer Organization
<number>
Reset
Initialize Machine
Register- to-Register
Branch Not Taken
Branch Taken
Control state diagram (for each diagram)
  reset
  fetch instruction
  decode
  execute
Instructions partitioned into three classes
  branch
  load/store
  register-to-register
Different sequence through diagram for each instruction type
Init
Fetch Instr.
XEQ Instr.
Load/ Store
Branch
Incr. PC

## Slide 11: Data path (hierarchy)
CSE370 - Computer Organization
<number>
Cin
Ain
Bin
Sum
Cout
FA
HA
Ain
Bin
Sum
Cin
Cout
HA
Arithmetic circuits constructed in hierarchical and modular fashion
  each bit in datapath is functionally identical
  4-bit, 8-bit, 16-bit, 32-bit datapaths

## Slide 12: Data path (ALU)
CSE370 - Computer Organization
<number>
32
32
A
B
S
Z
N
Operation
32
ALU block diagram
  input: data and operation to perform
  output: result of operation and status information

## Slide 13: Data path (ALU + registers)
CSE370 - Computer Organization
<number>
32
Z
N
OP
32
AC
REG
32
32
Accumulator
  special register
  one of the inputs to ALU
  output of ALU stored back in accumulator
One-address instructions
  operation and address of one operand
  other operand and destination is accumulator register
  AC <– AC op Mem[addr]
  "single address instructions” (AC implicit operand)
Multiple registers
  part of instruction used to choose register operands

## Slide 14: Data path (bit-slice)
CSE370 - Computer Organization
<number>
2 bits wide
1 bit wide
Bit-slice concept – replicate to build n-bit wide datapaths
CO
CI
ALU
AC
R0
from memory
rs
rt
rd
CO
ALU
AC
R0
from memory
rs
rt
rd
CI
ALU
AC
R0
from memory
rs
rt
rd

## Slide 15: Instruction path
CSE370 - Computer Organization
<number>
Program counter (PC)
  keeps track of program execution
  address of next instruction to read from memory
  may have auto-increment feature or use ALU
Instruction register (IR)
  current instruction
  includes ALU operation and address of operand
  also holds target of jump instruction
  immediate operands
Relationship to data path
  PC may be incremented through ALU
  contents of IR may also be required as input to ALU – immediate operands

## Slide 16: Data path (memory interface)
CSE370 - Computer Organization
<number>
Memory
  separate data and instruction memory (Harvard architecture)
    two address busses, two data busses
  single combined memory (Princeton architecture)
    single address bus, single data bus
Separate memory
  ALU output goes to data memory input
  register input from data memory output
  data memory address from instruction register
  instruction register from instruction memory output
  instruction memory address from program counter
Single memory
  address from PC or IR
  memory output to instruction and data registers
  memory input from ALU output

## Slide 17: Block diagram of processor (Harvard)
CSE370 - Computer Organization
<number>
Control FSM
16
16
Z
N
OP
16
AC
REG
16
load
path
store path
Data Memory
(16-bit words)
16
16
OP
16
PC
IR
16
data
addr
rd wr
Inst Memory
(8-bit words)
data
addr
Register transfer view of Harvard architecture
  which register outputs are connected to which register inputs
  arrows represent data-flow, other are control signals from control FSM
  two MARs (PC and IR)
  two MBRs (REG and AC)
  load control for each register

## Slide 18: Block diagram of processor (Princeton)
CSE370 - Computer Organization
<number>
16
Z
N
OP
8
AC
REG
16
16
load
path
store path
Data Memory
(16-bit words)
16
OP
16
PC
IR
16
16
data
addr
rd wr
MAR
Control FSM
Register transfer view of Princeton architecture
  which register outputs are connected to which register inputs
  arrows represent data-flow, other are control signals from control FSM
  MAR may be a simple multiplexer rather than separate register
  MBR is split in two (REG and IR)
  load control for each register

## Slide 19: A simplified processor data-path and memory
CSE370 - Computer Organization
<number>
Harvard architecture
Register file
Instruction register
Modeled after MIPS rt2000 (used in 378 textbook by Patterson & Hennessy)
a 32-bit machine

## Slide 20: A simplified processor data-path and memory
CSE370 - Computer Organization
<number>

## Slide 21: Processor control
CSE370 - Computer Organization
<number>
Combinational Controller– decodes instruction and sets control lines
Single cycle per instruction
This is what you will finish in HW 8

## Slide 22: Processor instructions
CSE370 - Computer Organization
<number>
Three principal types (32 bits in each instruction) type op rs rt rd shift funct R(egister) 6 5 5 5 5 6 I(mmediate) 6 5 5 16- immediate J(ump) 6 26- immediate
Some of the instructions add 6’h00 rs rt rd 6’h20 rd = rs + rt sub 6’h00 rs rt rd 6’h22 rd = rs - rt and 6’h00 rs rt rd 6’h24 rd = rs & rt or 6’h00 rs rt rd 6’h25 rd = rs | rt slt 6’h00 rs rt rd 6’h2a rd = (rs < rt) lw 6’h23 rs rt offset rt = mem[rs + offset] sw 6’h2b rs rt offset mem[rs + offset] = rt beq 6’h04 rs rt offset pc = pc + offset, if (rs == rt) addi 6’h08 rs rt offset rt = rs + offset j 6’h02 target address pc = target address halt 6’h3f - stop execution until reset
R
I
J

## Slide 23: Tracing an instruction's execution
CSE370 - Computer Organization
<number>
Instruction: r3 = r1 + r2 R 0 rs=r1 rt=r2 rd=r3 funct=0
Phase 1. instruction fetch
  Clock PC register for memory address bus
  Instruction memory outputs next instruction
  configure PCsel to select new value NEXT
Phase 2. instruction decode
  op-code bits of IR are input to control FSM
  rest of IR bits encode the operand addresses (rs and rt)
    these go to register file
Phase 3. instruction execute
  set up ALU inputs
  configure ALU to perform ADD operation
  configure register file to store ALU result (rd)

## Slide 24: Tracing an instruction's execution (cont’d)
CSE370 - Computer Organization
<number>
1. Instruction fetch
  Clock PC register for memory address bus
  Instruction memory outputs next instruction
  configure PCsel to select new value NEXT

## Slide 25: Tracing an instruction's execution (cont’d)
  op-code bits of IR are input to controller
  rest of IR bits encode the operand addresses (rs and rt)
    these go to register file
CSE370 - Computer Organization
<number>
2. Instruction decode

## Slide 26: Tracing an instruction's execution (cont’d)
CSE370 - Computer Organization
<number>
3. Instruction execute
  set up ALU inputs
  configure ALU to perform ADD operation
  configure register file to store ALU result

## Slide 27: Register-transfer-level description
CSE370 - Computer Organization
<number>
Control
  transfer data between registers by asserting appropriate control signals
Register transfer notation - work from register to register
  instruction fetch: mabus  PC; – move PC to memory address bus (PCmaEN, ALUmaEN) memory read; – assert memory read signal (mr, RegBmdEN) IR  memory; – load IR from memory data bus (IRld) op  add – send PC into A input, 1 into B input, add (srcA, srcB0, scrB1, op) PC  ALUout – load result of incrementing in ALU into PC (PCld, PCsel)
  instruction decode: IR to controller values of A and B read from register file (rs, rt)
  instruction execution: op  add – send regA into A input, regB into B input, add (srcA, srcB0, scrB1, op) rd  ALUout – store result of add into destination register (regWrite, wrDataSel, wrRegSel)

## Slide 28: Register-transfer-level description (cont’d)
CSE370 - Computer Organization
<number>
How many states are needed to accomplish these transfers?
  data dependencies (where do values that are needed come from?)
  resource conflicts (ALU, busses, etc.)
In our case, All operations take 1 (long) cycle
How do we set all of the control signals to be output by the state machine?
  depends on the type of machine (Mealy, Moore, synchronous Mealy)

## Slide 29: FSM controller for CPU (skeletal Moore FSM)
CSE370 - Computer Organization
<number>
instruction execution
instruction decode
LW
SW
ADD
J
reset
First pass at deriving the state diagram (Moore machine)
  these will be further refined into sub-states
instruction fetch

## Slide 30: FSM controller for CPU (reset and inst. fetch)
CSE370 - Computer Organization
<number>
Assume Moore machine
  outputs associated with states rather than arcs
Reset state and instruction fetch sequence
On reset (go to Fetch state)
  start fetching instructions
  PC will set itself to zero mabus  PC; memory read; IR  memory data bus; PC  PC + 1;
reset
instruction fetch
Fetch

## Slide 31: FSM controller for CPU (decode)
CSE370 - Computer Organization
<number>
Operation decode state
  next state branch based on operation code in instruction
  read two operands out of register file
    what if the instruction doesn’t have two operands?
instruction decode
Decode
branch based on value of Inst[31:26] and Inst[5:0]
add

## Slide 32: FSM controller for CPU (instruction execution)
CSE370 - Computer Organization
<number>
For add instruction
  configure ALU and store result in register rd  A + B
  other instructions may require multiple cycles
instruction execution
add

## Slide 33: FSM controller for CPU (add instruction)
CSE370 - Computer Organization
<number>
Putting it all together and closing the loop
  the famous instruction fetch decode execute cycle
reset
instruction fetch
Fetch
instruction decode
Decode
add
instruction execution
add

## Slide 34: FSM controller for CPU
CSE370 - Computer Organization
<number>
Now we need to repeat this for all the instructions of our processor
  fetch and decode states stay the same
  different execution states for each instruction
    some may require multiple states if available register transfer paths require sequencing of steps